## Slide 1: Overcoming challenges: leveraging machine learnings for efficient modeling of divertor plasmas
Ben Zhu1*, Menglong Zhao1, Harsh Bhatia1, Xue-qiao Xu1, David Eldon2, Peer-Timo Bremer1, William Meyer1, Thomas Rognlien1, Hyungho Lee3, and Junghoo Hwang4
1Lawrence Livermore National Laboratory
2General Atomics
3Korean Institute of Fusion Energy
4Korea Advanced Institute of Science and Technology
*zhu12@llnl.gov
IAEA Workshop on Artificial Intelligence for Accelerating Fusion and Plasma Science
Vienna, Austria
November 28, 2023

## Slide 2: Outline
Motivation
  Why efficient divertor models benefit magnetic confinement fusion (MCF)?
Summary and future work
ML model for detachment control
  How about solving the real-world problems? i.e., to provide a proper model for advancing model-based detachment controller.
Proof-of-principle study
  Does divertor plasma have low-dimensional latent space representation that can facilitate ML model development?

## Slide 3: Particle & heat exhaust in magnetic confinement fusion devices
  In toroidal devices, a substantial amount of fusion power will be deposited to a narrow region on divertors.
  Divertor plasma is complicated – multi-ion plasma couples atomic, neutral, molecular dynamics.

## Slide 4: A gap between fusion performance and exhaust
credit to David Eldon (General Atomics)
One challenge of reactor-grade MCF devices is to bridge the gap between fusion performance and heat exhaust:
  a large radiative cooling fraction (e.g., 60~90%), or detachment is required to avoid divertor/PFC damage
  impurity seeding degrades core plasma
Integrated core-pedestal-SOL/divertor models are needed to
  identify “sweet spots” in operation space
  demonstrate means to access and maintain in such a desired state

## Slide 5: The need of fast, robust and reliable divertor plasma models
Device design
Scenario development
Operation control
Loss of critical in-situ diagnostics in future reactors
Desired divertor model
Speed
Accuracy
Semi-analytical models (e.g., 2PM): fast but not accurate, depends on empirical fitting coefficients
Transport models (e.g., SOLPS, UEDGE): sensitive to initial conditions, takes days to months
mins-hrs
fairly high
sec-mins
~1-10ms
reasonable

## Slide 6: Plasma state has low-dimensional latent space representation
An efficient data-driven surrogate model to
  predict divertor plasma condition without doing actual simulations
  leverage the “latent space” (LS) concept
  obtain projection relation (NNs) between three different descriptions of plasma state
Anirudh et al., “Improved surrogates in inertial confinement fusion with manifold and cycle consistencies”, Prod. National Academy of Sciences, 117 9741 (2020)

## Slide 7: Outline
Motivation
  Why efficient divertor models benefit magnetic confinement fusion (MCF)?
Summary and future work
ML model for detachment control
  How about solving the real-world problems? i.e., to provide a proper model for advancing model-based detachment controller.
Proof-of-principle study
  Does divertor plasma have low-dimensional latent space representation that can facilitate ML model development?

## Slide 8: A pilot project based on 1D UEDGE transport model
Proof-of-principle study
simple yet contains essential divertor plasma/neutral physics
efficient – a few mins per run
LLNL’s in-house expertise
Diagnostics set y includes four scalars and one array
radiation profile (30 elements)

## Slide 9: Over one million 1D UEDGE simulations were performed
Results presented here are based on ~170k runs.
data set 1 (111,598 cases): for training and validation of beta-VAE (y->z->y’) and MLP (x->z)
data set 2 (57,655 cases): for validation of combine model (x->z->y’)
DIII-D like configuration with three varying input parameters x
“detached” and “attached” cases are labeled by the electron temperature at divertor
  Labeling won’t affect the model performance.

## Slide 10: LSRs are identified via 𝛽-variational auto-encoder (𝛽-VAE)
𝛽-VAE is chosen to regularize latent space distributions (for reducing MLP error in next stage).
40+4 elements input y to 6 dimensional LSR z, compression rate ~7.
AE loss
Kullback-Leibler divergence

## Slide 11: Detached and attached cases are well-separated in latent space
Detached and attached divertor plasmas have different distributions in certain latent space dimension; and are clustered in t-SNE visualization.

## Slide 12: Combined forward prediction model (x->z->y’) works well
The coefficient of determination, R2, is between 0.978 to 0.999 for all four scalars and maximum radiation amplitude in both detached and attached plasmas.

## Slide 13: Statistically small relative errors (except for peak radiation amplitude)
Four scalars
  error close to Gaussian distribution
  standard deviation is a few precent
  a few outliers
  attached cases are more accurate
Radiation info
  peak amplitude is least accurate
  location is well predicted
  not follow Gaussian distribution

## Slide 14: Mis-classification rate is as low as 0.2%
25 out of 29,187
35 out of 28,468
Despite being a proof-of-concept study, this divertor model based on 1D simulations
  contains more physics and provide more info than the semi-analytical 2-Point Model (2PM).
has wrong temperature cliff threshold; over-predicts radiation power density.

## Slide 15: ML model meets the requirements of integrated modeling
Speed: over 104 times faster than simulation even without any optimization
Robustness: not sensitive to initial condition
Accuracy: statistic-wise, predictions of four scalers have a few precents relative error; peak radiation amplitude is less accurate, but the location prediction is good
number of cases | 1 | 10 | 100 | 1,000 | 10,000 | 100,000
speed (ms) | 36 | 37 | 42 | 51 | 178 | 2,259

## Slide 16: Outline
Motivation
  Why efficient divertor models benefit magnetic confinement fusion (MCF)?
Summary and future work
ML model for detachment control
  How about solving the real-world problems? i.e., to provide a proper model for advancing model-based detachment controller.
Proof-of-principle study
  Does divertor plasma have low-dimensional latent space representation that can facilitate ML model development?

## Slide 17: Status and challenges of divertor plasma detachment control
Ravensbergen et al., Nature Comm., 12 1105 (2021)
Real-time feedback control of divertor plasma detachment is an active research area.
  [TCV] control C-III emission (detachment) front
  [KSTAR] control attachment fraction
Eldon et al., PPCF, 64 075002 (2022)
However, reactor-grade devices require more sophisticated detachment control
  loss of in-situ diagnostics
  multiple control objectives
  better to develop a model-based control algorithm instead of using empirical coefs.

## Slide 18: Desired SOL/divertor plasma parameters and NN architectures
Desired plasma condition prediction (y)
  Heat load at inner and outer divertors
  Jsat at inner and outer divertors
  Te at inner and outer divertors
  Radiation info. (divertor radiated power, and the detachment/radiation front location)
  Upstream density and temperature profile
Key detachment related discharge parameters (x)
  Total power injection (real-time control)
  Core plasma density (real-time diagnostic)
  Impurity species and fraction (estimate  upgrade to seeding rate)
  Diffusion coefficients (empirical estimate on real-time control)
3
2
1
1
2
3
1
heat exhaust
particle exhaust
core/fusion perf.

## Slide 19: Neural network architectures
Desired plasma condition prediction (y)
  Heat load at inner and outer divertors
  Jsat at inner and outer divertors
  Te at inner and outer divertors
  Radiation info. (divertor radiated power, and the detachment/radiation front location)
  Upstream density and temperature profile
multi-modal encoder
multi-modal decoder
Architecture of multi-modal (MM) data-driven surrogate model
Key detachment related discharge parameters (x)
  Total power injection
  Core plasma density
  Impurity species and fraction
  Diffusion coefficients

## Slide 20: Data generation with 2D UEDGE transport model
24,000 2D UEDGE simulations based on KSTAR #22849_5600 equilibrium were preformed with randomly sampled inputs
Synthetic diagnostics then extract desired edge/divertor plasma condition for control purpose, including
  Inner and outer divertor profiles
  Edge and divertor region radiated power fraction, radiation front location, and peak amplitude
  Outboard midplane profiles
x

## Slide 21: Multi-modal 𝛽-variational auto-encoder
Multi-modal 𝛽-VAE is used to identify reduced LSR.
  upstream and downstream plasma profiles are handled by separated CNNs
  moderate overall compression rate ~ 10: 20x8+5 = 165 DOFs -> 16 LS dimensions
  a small 𝛽 to regularize LSR distribution

## Slide 22: Plasma states in latent space representation
Similar to 1D study, detached and attached divertor plasmas have different distributions in certain latent space dimensions; but are less well separated in t-SNE visualization.
Label cases with Te,osp<5eV as “detached”

## Slide 23: Combined surrogate model performance
Accuracy: most quantities are within 25% relative error margin.
Speed: 105-6x speed-up; ~10 ms vs ~1 hour if this simulation converges.
1
3
2
1
1

## Slide 24: Surrogate model successfully predicts detachment onset
Attached plasma
Detached plasma
ML model
UEDGE

## Slide 25: Summary and future work
Efficient divertor models are critical for MFE research.
Divertor plasma has low-dimensional latent space representation (LSR).
  fast and reliable surrogate model via LSR;
  manifold consistent prediction of multi-modal data set (e.g., images, spectra, …) for general MFE applications.
A protype surrogate model for KSTAR detachment control is developed.
  prediction of upper steam and divertor plasma conditions as well as the radiation info.
  quasi-real-time (~10 ms), <25% error margin
  plan for initial deployment/validation on PCS next year
A project on FPP divertor design will start soon.