## Slide 2: Controlling Investment Risks by Integrating Decommissioning by Design in SMR Development
Click to edit Master title style
Aliki van Heek
Nuclear-21
www.nuclear-21.net
IAEA International Conference on Small Modular Reactors and their Applications
Vienna, Austria
21-25 October, 2024

## Slide 3
Decommissioning costs as SMR investment risk
SMR offer the potential for safer, more flexible, and cost-effective energy solutions
BUT realization has been slow
WHY: perceived investment risk
  uncertainties around RoI and liabilities
  Liability of this paper: plant at the end of its operational life.
IAEA SMR Booklet 2022: 84 SMR designs
  4 in operation
  8 mention mention any form of decommissioning plan
    limited to spent fuel
    traditional methods like entombment at the plant site
    transportation to “globally accepted recycling centers”
investor hesitation
Notes: Industrial (non-state) clients even more

## Slide 4
Current decommissioning and dismantling practice
Decommissioning phases:
  Pre-decommissioning: planning and securing regulatory approvals, including developing detailed decommissioning plans and safety protocols.
  Shutdown: halting reactor operations and starting decontamination to reduce radiation levels.
  Dismantling: disassembling the reactor; managing the resulting radioactive waste.
  Site cleanup: removing remaining radioactive materials, demolishing structures, restoring the site for future use.
Duration 15 - 20 years
Costs 0.5 – 2 B$
change
needed
Notes: Costs according to IAEA

## Slide 5
SMR clients
Electric utility
Energy intensive industry
→ more dependent on private sector investments
Notes: This approach has been championed by various industry experts and is being gradually adopted in new reactor designs.
Examples: left, Callaway NPP, USA; right, Chemelot industrial cluster, The Netherlands

## Slide 6
Current decommissioning and dismantling practice and costs
Case Switzerland:
Cost estimates per plant: 560 - 930 MCHF (600 – 990 M€)
Uncertainties 19 - 28% of total cost estimate
    forecast inaccuracies
    potential hazards
    general safety surcharge
OECD NEA, Addressing Uncertainties in Cost Estimates for Decommissioning Nuclear Facilities, 2017.

## Slide 7: So.. What do do?
Click to edit Master title style

## Slide 8
De-risking SMR decommissioning
Recognized Cost Reduction Strategies
  Decommissioning in series
  Decommissioning by design
  Building Information Management
Optimizing SMR Decommissioning Practices
  Building Information Management expansion
  Design for disassembly
  Minimize on-site work – use modular features

## Slide 9
Decommissioning in series
Example study on 335 MWe SMR:
  cost reduction factors of
    0.78 by series of 4
    0.81 by design features to minimize radiation levels or contamination
  Not yet making up for loss of economy of scale:
    (decommissioning cost of 4 SMR) = 2 * (decommissioning cost of 1 large reactor)
Larger series of same SMR design needed for more cost reduction.
Illustration with
cost reduction graph
Locatelli, L., Mancini, M., Competitiveness of Small-Medium, New Generation Reactors: a Comparative Study on Decommissioning, Proceedings of ICONE17, Brussels, Belgium, 2009.

## Slide 10
Decommissioning by design
Design nuclear facilities with their eventual decommissioning in mind
Best practices and lessons learned from past experiences to optimize the final phase of a reactor’s lifecycle, aiming to
  reduce radiation exposure,
  minimize radioactive waste, and
  ease the burden on waste facilities and future generations.
Not only physical design features, also structuring businesses to plan/conduct decommissioning activities.
Upfront planning of components decontamination, free-release and recycling → waste volume reduction.
Nuclear Decommissioning, IAEA Bulletin, IAEA, Vienna, April 2023
Notes: This approach has been championed by various industry experts and is being gradually adopted in new reactor designs.

## Slide 11
Building Information Management (BIM)
3D models: digital representation of the physical and functional characteristics of a facility
  shared knowledge resource for information about facility
  reliable basis for decisions during its lifecycle from inception to demolition.
allows for
  precise planning and visualization of decommissioning activities.
  simulation of different scenarios: optimization of workflows, identification of potential issues before they arise.
facilitates the management of radioactive waste by tracking materials location, condition and radiological data.
BUT: investment in software acquisition and staff training needed
Notes: facilitates the management of radioactive waste … ensuring compliance with regulatory requirements.

## Slide 12
BIM expansion
BIM has already become a mandatory practice in the construction industry → will also be used in SMR construction process.
Design and construction models can be expanded throughout the operational period to include detailed material and radiological data
  activation and contamination levels
Estimate from construction industry: using BIM can save around 20% in capital costs due to better project scope understanding and reduced contingencies.
Expanding to decommissioning phase: cost estimate uncertainties can be significantly reduced.
Notes: Design and construction models … the decommissioning process can be streamlined upfront and risks will be much reduced.
Uncertainties in the cost estimate: in the Swiss case ranging from 19% to 28%.

## Slide 13
Design for disassembly (DfD)
  Core principle: to design with the end of life in mind
    ensuring materials and components can be easily dismantled, removed and repurposed.
  SMR modular design essential for DfD:
    reactor modules can be transported back to the factory for decommissioning
      → reducing onsite workload
    integrating design elements allowing for straightforward disassembly and safe removal of components
      using standardized, easily separable materials
      implementing construction techniques that facilitate dismantling
        not only metals and plastics but also concrete.
  Additional feature on top of construction industry practice:
      Reduction of radiation exposure risks
      Minimization of amounts of radioactive waste
  This approach supports:
      sustainability by promoting material reuse but also
      compliance with regulatory frameworks from the start
decommissioning cost reduction
mitigates long-term investment risks
Notes: Already an existing concept in the construction world: An architectural and engineering approach aimed at facilitating the deconstruction of buildings and other structures to maximize the reuse and recycling of materials.

## Slide 14
Minimize on-site work
  For SMR:
    front-end assembly is planned to be centralized in factory halls,
    → decommissioning process should also be centralized.
  Conducting as much of the dismantling work as possible off-site in controlled factory environments can reduce on-site activities, lower radiation exposure risks, and minimize logistical challenges.
  This approach leverages the modular nature of SMRs, allowing components to be transported to specialized facilities for disassembly and processing.
  Not entirely new: steam generators from regular PWR are already transported across Europe to a dismantling site in Sweden
Notes: Cyclife

## Slide 15
Conclusion
Incorporating decommissioning considerations into the design phase is critical for SMRs.
Borrow from construction industry:
  Building Information Management (BIM)
  Design for Disassembly (DfD)
Key elements of designing SMR with decommissioning in mind:
  Modular construction
  Material selection
  Documentation and data management
→ reduction of investment risk
    real
    perceived

## Slide 16: Thank you for your attention!
Click to edit Master title style
Aliki van Heek
vanheek@nuclear-21.net
www.nuclear-21.net