## Slide 2: The Development Status of Innovative SMR and Future Plan
S. HEO, S.G. LIM and H.G. KIM
Innovative SMR Development Agency,
Republic of KOREA

## Slide 3
Introduction of i-SMR Development
i-SMR(170MWe)
SMART(100MWe)
APR1400 & APR+(1500MWe)
Passive systems
iPOWER(1250MW, Passive PWR)
Proven Tech. of Large Commercial PWR
World’s first standard design Approval SMR (2012)
More Safe
More Economical
More Flexible

## Slide 4
Development Goals - Safety
CDF < 1.0e-9 / RY
EPZ
< site boundary
Safety
Elimination of LOCA by integrated reactor
Passive safety system with natural circulation
Safety system without safety-class DC power
Reduced the likelihood of failure
Seismic Design 0.5g
Underground reactor
Seismic design of major equipment
Reduction of radioactive leakage
Small reactor
Low accident probability
Steel containment

## Slide 5
Development Goals - Economics
Reduction in construction volume
Design simplification of system
Multiple modules in a single reactor building
Modularization and factory manufacturing
Design optimization for inland transportation
Reduced construction time and cost
Significant reduction in operators
3 operators in one integrated MCR for multiple modules
Autonomous/Automatic operation and operate support system
Digital twin and predictive preventive maintenance
Construction unit price < $3,500/kWe
Power generation unit price < $65/MWh

## Slide 6
Top-Tier Requirements
Boron free operation
Flexible utilization
Flexibility
Economic
Overnight cost : $3,500 /kWe
LCOE : LCOE $65 /MWh
Construction time ≤ 24 month (First module)
Modularization and factory manufacturing
- component design optimization considering inland transportation
Integrated PWR
Power : 170 MWe
Design Life : 80 years
Seismic design : 0.5g
Safety
CDF : 1.0 × 10-9 /M·Y
EPZ : Within site boundary
Grace time : over 72 hrs
Fully passive safety system without AC/DC power
General
Refueling cycle ≥ 24 months

## Slide 7
i-SMR Design Features (1/2)
Integrated module reactor
Minimization of rad-waste by boron free operation
Elimination of pipe break
Elimination of CEA ejection by In-vessel CEDM
Optimization of economics by module manufacture & RCP
Enhanced thermal margin
RCP
CSB
UGS
IV-CEDM
Helical Coil
Once-through SG
PZR
Steel CV
Schematic diagram of RV and CV
RV

## Slide 8
i-SMR Design Features (2/2)
PAFS
PCCS
PECCS
Emergency Cooling Tank
Full passive safety system with dry containment vessel
Practical elimination of severe accident
Independent module arrangement
Flexible utilization
(Load following operation or hydrogen or heat)

## Slide 9
Regulatory Challenges for Standard Design Approval
• Flexible Utilization
• Separate review for Reactor
module / Plant / Site
• Regulation by principles
• 3 Crews Operation
• EPZ Elimination
Module
Design
Pre-
Review
Innovative
Design
• Communication with Developer and Regulator
• Effectiveness of Pre-review
Plant
Site
Module

## Slide 10
Organization for SMR development & commercialization
Robust Supply Chain
More than 500 nuclear plant parts suppliers
i-SMR
Development
Agency
DOOSAN
EQUIPMENT SUPPLY
Construction Co.
CONSTRUCTION
KEPCO E&C
A/E + NSSS DESIGN
KNF
CORE DESIGN,
NUCLEAR FUEL
KHNP
Utility
KAERI
Nuclear R&D
Public Sector
Private Sector
All key nuclear organizations in Korea are actively participating in i-SMR development.

## Slide 11
Milestone of i-SMR Development
Government funding and Pre-design review start in 2023.
Standard Design Approval by 2028 and Construction permit by 2030
Commercial operation of first module by 2034
2023
2024
2025
2026
2027
2028
Nuclear Design
Final Safety Analysis
Separate Effect Test Integral Effect Test
Standard
Design
2029
2030
2034
Design Spec.
Pre-design Review
SSAR
First Module Installation
Licensing
Business model setup
Construction Permit
Deployment
Standard design Approval
2033
2032
2031
Site preparation

## Slide 12
Thank you
THINK SAFETY