## Slide 1: HEXANA : a sodium advanced modular reactor for sustainable industrial decarbonization
P. Gauthé, J.B. Droin, H. Polge, P. Andreucci, S. Nizou

## Slide 2: No climate solution without industry decarbonization
of required energy is heat
3/4
of the needed heat is >400°C
50%
of global CO2 emissions come from industry
43%
of industrial energy is driven by fossil fuels
90%

## Slide 3: Why does the Gen-IV Sodium Fast Reactor technology is a good candidate among other Gen-III SMR ?
Delivery of high T° heat to the industries, in complement to electricity…
  Direct process heat delivery on a wide temperature range (70-500°C)
  Can be completed by electrical heating and/or H2 if needed, with a very good efficiency
  Also enables heat storage for flexibility and decoupling issues
… and because it’s a sustainable solution
  Good for climate and ecology (spent fuel as a ressource, less waste, less water)
  Good for countries (energy independence)
  Good for industries (stable OPEX, long term guaranteed prices)
  Good for the nuclear industry (makes nuclear sustainable)

## Slide 4: Why does the Gen-IV Sodium Fast Reactor technology is a good candidate among other Gen-IV systems ?
For its maturity and credibility!
Fuel & Materials
  Qualified, manufacturable, and recyclable MOX fuel
  Reactor structure materials identified and qualified
Ecosystem
  Well-known and mature industrial ecosystem (Framatome, CEA, EDF, ORANO…)
  Strong expertise related to the ASTRID project
Core proven technology
  >400 years of global operational feedback
  50 years of R&D in France, Operation of Phenix and SuperPhenix
1967
RAPSODIE
Proof of concept
40 MWth
SFR feasibility
1986
SUPERPHENIX
Industrial FOAK
1200 Mwe
Industrial feasibility of large SFR
1973
PHENIX
Prototype
250 Mwe
MOX fuel, material and components qualification

## Slide 5: HEXANA : An innovative architecture for modular and flexible energy production
Heat storage module
2 nuclear modules of 400MW thermal power
Heat
Flexible power generation
Industrial clusters
500 °C
300 °C
90 °C
Constant power
Variable power provided by heat storage
Modular
Flexible
Integrated
Tailor-made power levels
90°C to 500°C
Large industrial applications
Hydrogen, steel, ammonia, e-fuels, etc.
On-site production
Integrated into industrial clusters

## Slide 6: BOP Architecture
CONDENSOR
SODIUM-SALT HEAT EXCHANGER
STEAM GENERATOR
HOT TANK
510°C
COLD TANK
300°C
SODIUM SECONDARY LOOPS
STORAGE SALT LOOP
WATER-STEAM LOOP
530°C
480°C
180 bar
510°C
435°C
238°C
300°C
0.05 bar
455 MW
800 MW
345 MWe

## Slide 7: Use cases modelisation
OBJECTIVE : optimize the direct heat supply
Rankine PCS design
Thermoptim simulation for steady-state
Modelica simulation for dynamic transients

## Slide 8: Theoretical case : small direct heat demand
30 MWth of heat demand with two temperatures
Optimisation of Rankine PCS design
Conclusion : in this case, it’s better to take the heat directly from the storage system without modification of a standard PCS system

## Slide 9: Interest of the HEXANA storage system
Sell energy when it’s expensive, store when it’s cheap
Public subsidies for capacity and grid security
CAPEX reduction (no pressure)
Concept assessed by HEXANA team since 2017
GW scale industrial thermal storage already operating worldwide
Different backups or innovative tracks
Flexibility of energy supply
Decoupling between the nuclear site and industrial site
Enhanced siting possibilities
Decoupling between industrial risks and the reactor
Elimination of interaction between sodium and water or any pressurized fluid
Industrial needs
Safety
Profitability
Maturity

## Slide 10: Heat storage design and strategy
Buffer approach : delay the import or export of power to ro from the grid
Load following approach : follow the demand in electricity of the industrial and minimize the import and export link to and from the grid
In each use case, the goal is to design the right size of the thermal storgae to meet the demand without overinvesting

## Slide 11: Conclusion : Why is HEXANA a relevant solution to decarbonize industrial hubs?
Compatible with industrial needs
  Relevant size & power (modular concept)
  Continuous energy delivery thanks to module twinning
  Multi-energetic and integrated production (for ex: desalination + H2 + preheating + elec -> steel)
Enable to meet climate targets
  Higher energetic efficiency than Gen-III reactors thanks to the high temperature
  Less need for water
  Ultra low carbon energy (<3 geqCO2/kWh)
  Can replace gas a back-up systems
  Reliable, predictible and guaranteed energy prices on several decades
  Independant from any fuel importations and from the Uranium market evolutions (fast reactor)
   Geopolitically resilient technology
  Base-load nuclear operation + high flexibility thanks to storage = optimized plant capacity factor
   increased revenue + increased lifetime
Ease the integration of renewables onsite
  Absorption of intermittency thanks to heat storage
  Possibility to store extra energy in the storage during renewables overproduction periods
   HEXANA can play the role of an industrial hub energy stabilizer (without significant grid reinforcement measures)