## Slide 1
Overview of Modified Design Features of SMART-C
October 23, 2024
Min Young Park
Korea Atomic Energy Research Institute

## Slide 2
Introduction
01
Overview of SMART
02
Key Design Features of SMART-C
03
Summary
04

## Slide 3
Introduction
01

## Slide 4
SMART
Introduction
01
Advanced Integral PWR
TYPE
THERMAL POWER
365 MW
SMART
System-integrated Modular Advanced ReacTor
NAME

## Slide 5
Cogeneration
Introduction
01
Electricity Generation
and Desalination or District Heating
PURPOSE
Sea
Water
Fresh
Water
Electricity
Steam
Steam
Transformer
Hot Water Heat supply
Desalination Plant
100 MWe
40,000 t/day

## Slide 6
Development chronicle
Introduction
01
Integral Reactor
World First
SDA
SMART
PPE Project
Conceptual design
of SMART
Basic design
of SMART
SMART Prototype
SMART Preliminary feasibility study
Safety enhancement
SMART Standard Design Approval
Technology Optimization
SMART Pre-project Engineering
Standard design of SMART100
19.1~24.09
15.12~18.11
07.7~08.12
09.1~12.7
12.3~16.2
06.7~07.6
02.7~06.2
99.4~02.3
97.7~99.3

## Slide 7
Overview of SMART
02

## Slide 8
Overview of SMART (1/2)
02
CRDM
Pressurizer
RCP
Steam Nozzle
UGS
CSB
Feedwater Nozzle
FMHA
Core
ICI Nozzle
57 fuel assembly
Cylindrical low enriched uranium oxide pellets
CORE
4 canned motor pump
Horizontally mounted
Reactor Coolant Pump
8 cassettes
Once-through type with helically coiled tubes
Steam Generator
Maintain the coolant in a saturated state
Wet thermal insulator is installed
Pressurizer
SG

## Slide 9
Overview of SMART (2/2)
02
Passive Residual Heat Removal System
Passive Safety Injection System
Containment Pressure and Radioactivity Suppression System
CORE
To maintain a reactor in the safe condition for 72 hours without any operator action at the postulated design basis accidents.
All safety systems can operate not depending on electrical power from emergency diesel generator for 72 hours.
Safety-grade batteries provide necessary DC power for valve initiation and post accident monitoring.
FEATURE
PSIS
PRHRS
CPRSS

## Slide 10
Overview of SMART-C
02
SMART100
SMART100
365 MWt
110 MWe
PWR
Integral
About 4.6 m
30 months
Block type helically coiled SG
Passive (2 SIT trains)
Battery
DC power + natural circulation
72 hour
< 1.0X10-7/RY
Reduced arch-shaped rectangular
Thermal power
Electric output
Reactor type
Reactor configuration
Reactor size (diameter)
Refueling cycle
SG type
Safety system
Emergency power
Driving force
Operator action
SMART-C
Core Damage frequency
SMART-C
365 MWt
110 MWe
PWR
Integral
About 6 m
30 months
Cassette type helically coiled SG
Passive (4 SIT trains)
Battery
DC power + natural circulation
72 hour
< 1.0X10-7/RY
Arch-shaped rectangular
Containment building

## Slide 11
Key Design Features of SMART-C
03

## Slide 12
Steam Generator
Key Design Features of SMART-C
03
  Volume and weight reduction of reactor vessel by 45%
    For portability and cost-effectiveness
    Achieved through modification in steam generator design
      8 cassette type SGs to block type SG
    Reactor vessel diameter has decreased from 6 m to 4.55 m
Steam generator
Steam generator
SMART100
SMART-C
Bad space efficiency
Relatively easy to install and dismantle
Maximize space efficiency
Difficult to install and dismantle

## Slide 13
Safety Injection
Key Design Features of SMART-C
03
  Simplification of passive safety system
    Reduction in number of trains from 4 to 2
    Implementation of the two-stage SIT
      CMT and SIT merged into a single tank (TSIT)
    High/low flow injection achieved by implementing independent injection line with different orifices (with different flow resistances)
Conceptual design of two-stage SIT

## Slide 14
Summary
04

## Slide 15
PRESENTATION TITLE
Summary
01
  KAERI developed an integral type PWR, SMART
    SMART and SMART100 has gained standard design approval in 2012 and 2024, respectively.
  One of the most promising SMRs
    High degree of development completeness (SDA)
    Safe and innovative SMR
    Wide range of applications, including the potential for cogeneration
  Variation of SMART has been proposed, SMART-C
    Enhanced portability and economic viability
      Through SG and safety system modification
  Further studies (detail design) will be conducted on SMART-C and the feasibility in various industrial fields will be evaluated

## Slide 16
THANK YOU
0 m
5 m
10 m
15 m
20 m
25 m
SMART
SMART100
SMART-C
110MWe
SMART-C
SMART100
110MWe
SMART
100MWe