## Slide 2: Classification Requirements for Floating Nuclear Power Plants (FNPPs)
American Bureau of Shipping (ABS)
Meg Dowling
Derek Novak
Jin Wang

## Slide 3: Contents
Maritime Demand for Decarbonization
Maritime Regulatory Framework
Regulations for Commercial Nuclear Maritime Applications
ABS Requirements for Nuclear Power Systems
  Stakeholder Roles
  Risk Assessment
  Marine and Nuclear System Interface
3 | Classification Requirements for Floating Nuclear Power Plants (FNPPs) Track A.4 - 185

## Slide 4
Maritime Demand for Decarbonization
4 | Classification Requirements for Floating Nuclear Power Plants (FNPPs) Track A.4 - 185
International Maritime Organization (IMO) targets eliminating all greenhouse gases from shipping by 2050
Mid-term measures must be adopted in the 2030s

## Slide 5
Maritime Demand for Decarbonization
5 | Classification Requirements for Floating Nuclear Power Plants (FNPPs) Track A.4 - 185

## Slide 6
Maritime Regulatory Framework
6 | Classification Requirements for Floating Nuclear Power Plants (FNPPs) Track A.4 - 185
International Maritime Organization (IMO)
Codes and standards for commercial vessels endorsed and implemented by member States
Classification Societies (Class)
International Association of Classification Societies (IACS)
Non-Governmental Organizations (NGOs)
Establish and administer standards for design, construction and survey
Appointed by flag Administrations as Recognized Organization (RO) to perform statutory inspections
Notes: 174 Member States and other Non-Governmental Organizations
For Classification Societies,
Class Certificate demonstrating Compliance issued by Classification Society

## Slide 7
Requirements for Nuclear Propulsion
7 | Classification Requirements for Floating Nuclear Power Plants (FNPPs) Track A.4 - 185
International Regulations
International Convention for the Safety of Life at Sea (SOLAS) Chapter VIII: Nuclear Ships
Classification Rules
Notes: Outdated
Old, PWR-Based, But not bad thinking…
Established set of requirements, including goals and technical requirements from which functional requirements could be derived by nuclear and maritime experts.

## Slide 8
ABS Requirements for Nuclear Power
8 | Classification Requirements for Floating Nuclear Power Plants (FNPPs) Track A.4 - 185
Non-nuclear propulsion maritime applications (i.e., FNPPs)
Mandatory Power Service (Nuclear) Notation
Suitable for any type of nuclear technology
Designated interface between stakeholders according to marine or nuclear service

## Slide 9: Stakeholder Roles
9 | Classification Requirements for Floating Nuclear Power Plants (FNPPs) Track A.4 - 185
Flag Administration
Classification Society
Nuclear Regulator
Port Authorities/Port States, Coastal States and Port State Administration
© Adam Melnyk/Shutterstock
© EtiAmmos/Shutterstock
Notes: Flag Administration
- The national authority with whom the vessel is registered
Classification Society
-Flag-Administration designated recognized organization (RO) for design review and approval, as well as audits, survey and inspection.
Nuclear Regulator
- Independent agency of a national authority that has authority over the approval and licensure of nuclear reactors and related systems.
Port Authorities/Port States, Coastal States and Port State Administrations
- Appropriate authority of the country in which the vessel is operating, stationed, or laid up.
Port State Administration may also be the appropriate authority of the country:
● in which the vessel is constructed (nation of construction);
● where the vessel is serviced or maintained, either in a floating condition or in drydock; or
● where the vessel may be deactivated and decommissioned.

## Slide 10
Unit Safety
Risk Assessments
10 | Classification Requirements for Floating Nuclear Power Plants (FNPPs) Track A.4 - 185
Considerations for Maritime Applications
Nuclear Hazards Imposed on Marine Safety
Radioactivity
Thermal Energy
Corrosive Materials
Marine Systems
Nuclear Systems
Marine Hazards Imposed on Nuclear Safety
Structural Loads
Motions
Onboard Fire
External Hazards
Mooring
Notes: Goals and Objectives
Aid in decision making to introduce risk-reduction measures
Demonstrate that the risks involved with NPPs have been evaluated resolve any adverse effect to the security of life, property, and the natural environment.
Use acceptable and recognized risk analysis techniques to determine that there are no unacceptable risks to the asset, people or the environment.

## Slide 11
Interface Document
11 | Classification Requirements for Floating Nuclear Power Plants (FNPPs) Track A.4 - 185
Establish Technical Agreement Among Stakeholders
Notes: Describe the marine and nuclear systems
Stakeholders whose approvals are necessary
The responsibilities assigned to the Stakeholders
Form the technical agreement between stakeholders to confirm that all parties involved understand and accept the distribution of responsibilities.

## Slide 12: Key Takeaways
12 | Classification Requirements for Floating Nuclear Power Plants (FNPPs) Track A.4 - 185
Classification functions as RO of flag Administration
ABS class requirements allows for any type of nuclear technology for FNPP use
Process involves nuclear regulator to license reactor(s)
Risk assessment informs design decisions
Interface document must be developed and agreed upon to establish the division of responsibility between review and approval authorities

## Slide 13: Thank You