## Slide 2: Decarbonizing refining processes SMR deployment paving the way to synthetic fuels
Vienna, 24th October 2024
Eleonora Lambridis, Head of Innovation Lab

## Slide 3: Global reliance on fossil fuels
IEA (2021), Total primary energy supply by fuel, 1971 and 2019, IEA, Paris https://www.iea.org/data-and-statistics/charts/total-primary-energy-supply-by-fuel-1971-and-2019, Licence: CC BY 4.0
Oil
Coal
Natural gas
Nuclear
Biofuels
Other renewables
Hydro
Main non-energy uses: lubricants, asphalt, waxes, naphtha, surface coating, resins, foams, fibres, plastics,…

## Slide 4: Compatibility of SMRs with industrial heat
Reengineering
Top-up heat
Part supply
On-site retrofit
Plug-in
>1000°C
Top-up heat required or via syngas production
<1000°C
Very High Temperature Gas
compatible
<550°C
Molten salt, Liquid metal compatible
<250°C
Light Water Reactor compatible
District Heating
Paper
Refineries
Soda ash
(Petro)chemical clusters
Ceramic
Cu, Ni
Lime
Aluminium
Ammonia
Steel
Cement
Glass
Max process temperature
Coupling complexity
Hydrogen low t°
Hydrogen high t°
Caption
Current Gen early adopters
Next Gen early adopter
Next Gen late adopter
Opportunistic
>40 GWth
>20 GWth
>10 GWth
<10 GWth
Atomistic

## Slide 5: Lifecycle of Petroleum Products
Extraction and production of crude oil
Refining
Energy needs:
Few 10MWe
100-1000 MWth
Transportation
End-use Crude oil derivatives (fuels) used in transportation sector

## Slide 6: Complexity of installations
Main opportunities to decarbonise the process at the level of inputs and outputs:
Decarbonising the steam production
Acting on exhaust gases
Source: Wikipedia

## Slide 7: Energy balance
Refinery Products
Crude Oil
Natural Gas
LPG
CO gas
H2 from CRU
Tail gas
Fuel Gas Mix Drum
H2 to process / Waste
CO Gas to Boiler

## Slide 8: CO2 mass balance
Stacks from different units

## Slide 9: Premises & key principles
Nuclear energy is a new technology to be introduced within a refinery ecosystem, hence the “path of least resistance” principle should be applied, meaning that:
The planification of energy assets transition should be graded as to leave room for “learning by doing”;
Priority should be put on the conversion of assets requiring few to no re-engineering as to minimize complexity and capex investment;
With the disruption of the current Product & Energy balance, applications bringing additional value (new cash-flow streams) should be prioritized.
As crude oil derivatives market is changing and uncertain (e.g. expected decrease of gasoline consumption vs. expected increased demand for Sustainable Aviation Fuel), special attention should be put on: scalability, options and exit doors.
<
<
Investment
Conversion

## Slide 10
Electrolysis
Exhaust Gas
Fluid Catalytic Cracking
Regenerator
Reverse Water Gas Shift
C1-C5
C(s)
CO2
Fischer-Tropsch
Power
Power
O2
CO
H2
H2
H2
C10H22 | Crude
Pyrolysis
Membrane

## Slide 11: Key takeaway on hazard assessment Safety analysis have concluded that external hazards from H2 (Jet fire, Fire ball, Explosion) is not a showstopper for close co-localization (~100m required)
Chart: 
Chart: Distance [m]
Chart: Distance [m]
| 0 | 1.2636919343272 | 2.5273838686543999 | 3.7910758029816001 | 5.05476773730879 | 6.3184596716359902 | 7.5821516059631904 | 8.8458435402903905 | 10.1095354746176 | 11.3732274089448 | 12.636919343272 | 13.9006112775992 | 15.1643032119264 | 16.4279951462536 | 17.691687080580799 | 18.955379014908001 | 20.219070949235199 | 21.482762883562401 | 22.7464548178896 | 24.010146752216802 | 25.273838686544 | 26.537530620871198 | 27.8012225551984 | 29.064914489525599 | 30.328606423852801 | 31.592298358179999 | 32.855990292507201 | 34.119682226834399 | 35.383374161161598 | 36.647066095488803 | 37.910758029816002 | 39.1744499641432 | 40.438141898470299 | 41.701833832797497 | 42.965525767124703 | 44.229217701451901 | 45.4929096357791 | 46.756601570106298 | 48.020293504433504 | 49.283985438760702 | 50.5476773730879 | 51.811369307415099 | 53.075061241742297 | 54.338753176069503 | 55.602445110396701 | 56.866137044723899 | 58.129828979051098 | 59.393520913378303 | 60.657212847705502 | 61.9209047820327
H2 pipeline breach (DN150, 40 bar) | 27.623 | 32.4854 | 35.4527 | 35.4417 | 33.6637 | 31.3512 | 29.1138 | 27.2577 | 26.896 | 26.4204 | 25.8834 | 25.4015 | 24.9188 | 24.3166 | 23.6748 | 23.058 | 22.4322 | 21.801 | 21.1666 | 20.5329 | 20.0412 | 19.2632 | 18.6328 | 18.0072 | 17.3879 | 16.7763 | 16.1739 | 15.5819 | 15.0017 | 14.4342 | 13.8806 | 13.3417 | 12.8183 | 12.3109 | 11.8199 | 11.3457 | 10.8884 | 10.4482 | 10.0249 | 9.6183 | 9.2284 | 8.8547 | 8.4991 | 8.1565 | 7.829 | 7.5161 | 7.2172 | 6.9319 | 6.6596 | 6.3998
H2 pipeline breach (DN300, 40 bar) | 39.6051 | 42.863 | 46.3669 | 45.8548 | 42.9662 | 39.5097 | 36.2999 | 33.5427 | 32.0112 | 31.1446 | 30.249 | 29.3437 | 28.5697 | 27.705 | 26.8143 | 25.9508 | 25.0897 | 24.2393 | 23.3908 | 22.6966 | 21.8329 | 20.9157 | 20.1187 | 19.3381 | 18.5751 | 17.831 | 17.1069 | 16.4038 | 15.7225 | 15.0636 | 14.4277 | 13.815 | 13.2257 | 12.6598 | 12.1171 | 11.5973 | 11.1001 | 10.625 | 10.1713 | 9.7385 | 9.3283 | 8.935 | 8.5603 | 8.2037 | 7.8643 | 7.5415 | 7.2343 | 6.9422 | 6.6643 | 6.4
CH4 pipeline breach (DN250, 15 bar) | 128.9149 | 138.5429 | 109.3233 | 92.3772 | 78.1147 | 68.3118 | 61.2619 | 55.9349 | 51.7663 | 48.3902 | 45.5938 | 43.1919 | 41.107 | 39.2595 | 37.5874 | 36.0505 | 34.6169 | 33.2767 | 31.9753 | 30.7125 | 29.494 | 28.3019 | 27.1306 | 25.9774 | 24.8393 | 23.7208 | 22.6206 | 21.5414 | 20.4857 | 19.4563 | 18.4561 | 17.4882 | 16.5866 | 15.6885 | 14.7997 | 13.9805 | 13.2007 | 12.4611 | 11.7609 | 11.0997 | 10.4763 | 9.8896 | 9.3382 | 8.8204 | 8.3348 | 7.8797 | 7.4533 | 7.054 | 6.7119 | 6.4001

## Slide 12: Conclusion
Refineries need to undergo a deep and thorough conversion process in order to make the 4th industrial revolution reliant on carbon-neutral energy sources.
A major challenge is imposed by the need for reliable and abundant energy supply, where Small Modular Reactors can be a major solution.
Tractebel’s investigation of existing assets revealed no technical or regulatory obstacles to integrating SMRs with refineries.
Such transformation process should follow the “path of least resistance”.

## Slide 13: Unfolding the vision of advanced nuclear
Notes: With the roadmap for BE