## Slide 1: Developing Regulatory Framework for SMRs in Finland
Overview of activities

## Slide 2: Contents
Emergence of SMRs
Regulatory reform
  New licensing process
Competence building
Experiences from design reviews
EPZ changes
Seismic design criteria

## Slide 3: Emergence of SMRs challenges our assumptions and regulatory model
New applications beyond electricity production, such as district heating and industrial processes
New stakeholders
  Municipalities and industrial enterprises as possible new licensees
  Startup vendors
Proximity to population centers or industrial facilities
Serial production of reactor components

## Slide 4: Regulatory reform

## Slide 5: Regulatory reform: towards a more risk-oriented approach
Various drivers behind the reform
Emergence of SMRs and non-light water reactors
Changing operating environment and new business models
Legislative complexities and some outdated frameworks from the 1980s
Objective is to create enabling regulations
A single, flexible set of goal-based regulations for all reactor types
Less prescriptive requirements to allow for more latitude
Safety and licensee responsibility paramount

## Slide 6: New licensing process aims to provide ways for project de-risking
Challenges with the current model
  Decision-in-Principle (DiP) requires significant investment early without certainty
  Site-specific design basis approved late, impacting project feasibility
  Lack of a formalized pre-licensing process
Proposed changes
  DiP without a technology – focus on political decision, applicant capability
  EIA required before construction license (CL) phase
  Site-specific design basis approval before CLA
  Introduction of conceptual design review

## Slide 7: Path to construction license
Decision in Principle (DiP)
Overall good of the society
Applicant’s competence
Waste management plan
Site approval by STUK
Site-specific requirements for the facility design
Land-use planning
In good time before the construction license phase
Applicant A
Applicant B
Applicant C
Conceptual review by STUK
Evaluation of the facility design and safety principles
Capabilities of the vendor, partners, and supply chain
In good time before the construction license phase
Safety and design of the facility as required, detailed and assessed
Adaptation of the planned facility to the site and production purpose
Capabilities and readiness for the implementation and construction
Siting risk management
Design risk management
Political risk management
Implementation risk management
Environmental impact assessment (EIA)
Construction license
Land-use planning
Applicant A*
Notes: All three required for CLA, but can have different applicant

## Slide 8: Competence building

## Slide 9: Road map to build knowledge on SMRs and non-LWRs
Knowledge building supports design reviews and regulatory reform
Light water reactors a priority – they seem most likely
Non-LWR technologies ranked in importance – based on industry projects in Finland

## Slide 10: Design reviews as a way of competence building
Fortum feasibility study looks at large LWRs and SMRs
  Current licensee Fortum has requested us to review certain parts of specific designs
  Increased understanding of the designs
  Valuable input for the regulatory reform - topics have challenged our thinking
Observing Rolls-Royce SMR GDA in UK
Steady Energy LDR-50 conceptual design review
  LDR-50 district heating SMR
  First example of a conceptual design review
  Learning from a real-world application of SMR design review

## Slide 11: Changes to regulation

## Slide 12: EPZ regulation changed to be more flexible
Previous Model had fixed sizes – PAZ (5 km) and EPZ (20 km)
New approach is a case-by-case evaluation
  Based on licensee application and demonstration
Allows SMRs to be sited closer to population if safety is ensured and demonstrated
  Facilitates land-use planning
The definition of PAZ and EPZ has not changed
  Outside of PAZ, the radiation dose to an unprotected person does not exceed 1 Sv within 10 hours from the beginning of exposure. Based on IAEA Safety Standard GSR Part 7
  EPZ: a high probability that there will be no need to take urgent protective measure for the population, to limit the stochastic effects of ionising radiation outside of EPZ.
  It must be demonstrated that, in the event of an accident, the radiation dose of an unprotected person outside the EPZ will not exceed 10 mSv within 48 hours of the start of exposure.

## Slide 13: Creation of common seismic design criteria facilitates SMR deployment while maintaining safety
Low seismic activity, but uncertainties in seismic hazard assessments
Leads to lengthy and costly seismic surveys for new licensees
Common seismic design criteria
Seismic hazard maps and criteria specific to Finland
Encode into regulation
Best practices and experiences from countries with higher seismic risks