## Slide 1: DIII-D Runaway Electron Mitigation Coil Modeling and RE transport calculations with ASCOT5
V.A. Izzo (Fiat Lux)
A. Battey, C. Hansen (Columbia University)
Acknowledgement (ASCOT5 help): K. Särkimäki
Work supported by DOE-FES

## Slide 2: Key points
NIMROD was used to model the DIII-D nonlinear plasma response to the planned runaway electron mitigation coil (REMC)
  NIMROD includes RE drift orbit calculation, but follow only a small fixed starting population that is lost as the simulation progresses
A workflow was developed to post-process NIMROD results with the ASCOT5 orbit following code
  Resulting diffusion coefficients are compared for different plasma shapes, different RE energies and pitches, and full vs. drift orbits

## Slide 3: The DIII-D REMC
See: D.B. Weisberg et al (2021) Nucl. Fusion 61 106033
An inboard-wall runaway electron mitigation coil (REMC) has been designed for DIII-D, consisting of a single helical turn connected by a single vertical leg
Current in the coil is driven passively by the CQ loop-voltage to produce large 3D magnetic perturbations to help deconfine REs in the CQ phase
Inboard wall design was chosen for DIII-D due to tendency of CQ plasmas to limit on the inner wall

## Slide 4: REMC response is modeled with ThinCurr
time [ms]
Ip [MA]
IREMC [MA]
IREMC(Ip) fit
coil is here
|Bpol|
Simulation boundary
ThinCurr models the coil and surrounding conducting structures with a series of coupled circuit equations
Model of conducting structures captures major features like portholes
Filament representation of plasma allow prescribed current rampdown
3D fields at LCFS from ThinCurr are extrapolated to NIMROD boundary for time-dependent Bn boundary conditions
Coil current as a function of plasma current is also taken from ThinCurr

## Slide 5: NIMROD results for IWL plasma
9/2
8/2
4/1
6/1
5/1
ThinCurr fields
Vacuum fields
ThinCurr fields
Vacuum fields
ThinCurr fields have more n=2 than coil vacuum fields and produce earlier island overlap
Oscillatory loss rate associates with break-up of successive rational surfaces

## Slide 6: Results for LSN plasma with TQ, comparing ideal and resistive wall
Ideal
w/ REMC
No REMC
resistive
Wth [MJ] & Ip [MA]
Ip
Emag.n=1
Wth
Emag,n=1 [kJ]
Large quantity of Ne is deposited across the whole cross-section (poloidally and toroidally uniform)
Resistive & Ideal wall cases, w/ and w/o REMC are run
RW cases have vwall = 100 m/s ( = /0)

## Slide 7: Resistive wall is particularly important when REMC is on
Ideal
w/ REMC
No REMC
resistive
All RE test particles are lost due to the TQ MHD in every case
In each case, new population is launched 0.5 ms after initial loss (allow some time to re-heal)
Loss fraction after 0.5 ms is in ~97%-99% range for three cases: RW slightly better than IW. REMC better than not.
REMC + RW exceeds 99.9% loss

## Slide 8: The ASCOT5 code for RE orbits calculations
https://github.com/ascot4fusion/ascot5

## Slide 9: ASCOT analysis was done for SPARC

## Slide 10: ASCOT5 diffusion coefficients from IWL case
 All markers have pitch -0.99 and are drift orbit calculations
0.1 MeV
30.0 MeV
Log10(D m2/s)
Log10(D m2/s)

## Slide 11: Comparison of drift vs. full-orbit
 All markers have pitch -0.99 and energies of 0.1 MeV
Full orbits
(Drift – Full / Drift)
Log10(D m2/s)
Log10((D1-D2)/D1 m2/s)

## Slide 12
Variation of pitch angle
 All markers have full-orbit integration and energies of 0.1 MeV
p||/p = -0.7
(p70 – p99 / p99)

## Slide 13: ASCOT transport results for LSN plasma
0.1 MeV
30.0 MeV

## Slide 14: Summary of ASCOT5 results
Diffusion coefficients calculated for a range of energies, pitch angles, full vs. drift orbits, and two plasma shapes
  Full orbits show 10’s%-O(1) differences from drift orbits
  Similar change as pitch is varied
  High energies show less small-scale structure associated due to islands than low energies
  Largest diffusion in the thermal quench phase when TQ is included
Coefficients can be incorporated into 1D model for RE evolution

## Slide 15: Incorporation of ADAS atomic data into NIMROD disruption calculations
V.A. Izzo (Fiat Lux)

## Slide 16: ADAS rates replace KPRAD
KPRAD coronal non-equilibrium rates were initially incorporated into NIMROD in 2006; depend only on plasma temperature
  Coding uses logarithmic-polynomial fits
ADAS collisional-radiative rates are now incorporated using Aurora
  Full ADAS rates can be used when available, otherwise open-ADAS is accessed
  Density and temperature-dependent rates are evaluated with bicubic splines

## Slide 17: Comparison of Ar MGI into DIII-D
Ar MGI simulation run halfway through the TQ
Wth (MJ)
KPRAD
ADAS
Prad (W)
KPRAD
ADAS
Time [ms]
Time [ms]

## Slide 18: Comparison of Ne MGI into DIII-D
Time [ms]
Time [ms]
Wth (MJ)
KPRAD
Full ADAS
Prad (W)
KPRAD
Full ADAS
Open-ADAS
Open-ADAS

## Slide 19: Summary of ADAS/KPRAD comparison
Ar data from ADAS and open-ADAS is identical; radiation rate differ very slightly from KPRAD, but very similar evolution up to midpoint of TQ
Ne datasets from ADAS and open ADAS differ, but are close; KPRAD rates differ more than for Ar
  Higher KPRAD radiation rates at early times leads to faster TQ onset