## Slide 1
Development and preliminary calibration of an off-normal warning system for SPARC
A.R. Saperstein, R. Sweeney, D. Boyer, A. Kumar, Z. Keith, H. Wietfeldt, A. Maris, A. Wang, M. Pharr, C. Rea
3rd Technical Meeting on Plasma Disruptions and their Mitigation – 4 September 2024

## Slide 2: Creation of a cross-institutional team for the development of SPARC’s Off-Normal Warning System
Dan Boyer
CFS
Ryan Sweeney
Cristina Rea (PI)
MIT
Alex Saperstein (PA)
Arunav Kumar (PA)
William Wei (PA)
Andrew Maris (GS)
Henry Wietfeldt (GS)
Zander Keith (GS)
Columbia
Matt Pharr (GS)
Nik Logan (PI)
EPFL
Alessandro Pau (PI)
And we welcome more collaborators!!
Allen Wang (GS)

## Slide 3: Overview
Scope of SPARC’s Off-Normal Warning (ONW) system
Progress on its development
  ONW system structure
  Creation of Off-Normal Event (ONE)-specific warnings

## Slide 4
Scope of SPARC’s Off-Normal Warning (ONW) system

## Slide 5: The ONW system will play two crucial roles in SPARC operations
Plasma control
  Integration into the Plasma Control System
  Identify when a disruption may be imminent and decide on a response based on the risk to the device
Scenario design
  Integration into Pulse-Planning workflow
  Identify the cause(s) of plasma disruptions and identify scenarios that may be less disruptive for future campaigns

## Slide 6: SPARC’s ONW systems need to address several ITER-relevant challenges specific to high-power devices
SPARC has a “Disruption Budget”
  The number of disruptions (cumulative thermal loads) the tokamak is designed to withstand
The budget needs to be managed early in operation
  This requires the ONW system to be ready provided a limited amount of data
  This will be a stress test of cross-machine transferability for both physics and data-driven models
  This is an opportunity to test the implementation of adaptive training
    Which has been explored on JET [1,2], EAST [3], ASDEX [4]
There will be little (if any) room to commission the warning system at high performance
  The risk associated with an un-mitigated disruption may be too great
The ONW system needs to be tunable assuming limited performance info
  The performance of the system can be unclear when running in mostly closed-loop
  However, this is also an opportunity to explore the cost-benefit analysis of running in open-loop
[1] Murari, A. et al Nat Commun 15, 2424 (2024)
[2] R. Rossi et al 2024 Nucl.Fusion 64 046017
[3] arXiv:2404.08241v2
[4] B. Cannas et al 2010 Nucl.Fusion 50 075004

## Slide 7: These challenges set some priorities in development
Operator friendly
  When a warning fails, it needs to be clear why, as well as how to update it
  The triggering of a warning should make it clear why a plasma disrupted, and suggest how to adjust the scenario for the next pulse
Starting development with physics-driven warning models
  Provides the clear tuning knobs and interpretability for the low-data budget available early on
Followed by data-driven warning models
  This is expected to provide higher accuracy and better warning-times provided enough data
Closed-loop and real-time Off-Normal SIMulations (ONSIMs) will be used to relieve the burden of needing real SPARC data
  SPARC data + physics knowledge can potentially fill in unexplored regions of stability-space without explicit experimentation
  Can potentially implement data earlier with the help of ONSIMs

## Slide 8
Progress on development
ONW system structure

## Slide 9: Each Off-Normal Event (ONE) has its own ONW module containing control-focused detectors within it
Disruption Mitigation System (DMS)
Optimal threshold
Optimal threshold
ONE
Appropriate Detector(s)
Control response(s)
Optimized threshold(s)
Warning Time [au]
Counts
Disruption
[5, 6]
[5] J. Vega et al 2024 Nucl.Fusion 64 046010
[6] M Maraschek et al 2018 PlasmaPhys.Control.Fusion 60 014047
Avoidance
VDEs

## Slide 10: Different control responses may have different optimization metrics
A common set of performance metrics to all optimizations is the True Positive Rate (TPR) and False Positive Rate (FPR)
  TPR = Frequency that the model correctly identifies an event
  FPR = Frequency that the model falsely identifies an event
A flexible optimization metric has been developed for the Disruption Mitigation System (DMS) warnings based on the expected cumulative disruption loads
  DMS Metric
  mitigation efficiency natural disruptivity
  Optimization looks for minimum in DMS Metric
DMS Metric [MJ/shot]
Performance Metrics
False Positive Rate (FPR)
True Positive Rate (TPR)
Notes: These are all functions of the warning threshold chosen
⟨𝐷⟩ is the most important metric to optimize, as it affects the disruption budget

## Slide 11: We use an extension of Gerhardt’s Points-Based model for establishing warning thresholds
The original Point-Based model [7] maps thresholds points for each input and then sums them
  Contours of constant sums draw stability boundaries
  Used with success on NSTX by both Gerhardt [7] and DECAF [8]
The extension to this model implemented here makes the point-assignments more continuous, and easily tunable
2* primary tuning knobs
  Weight (), shape (): set FPR  points mapping
    sets the weight of each input
    sets the shape of the profile
Points
[ - ]
Point Mapping
[ - ]
[ - ]
,
[7] S.P. Gerhardt et al 2013 Nucl. Fusion 53 063021
[8] S.A. Sabbagh et al Phys. Plasmas 30, 032506 (2023)
Notes: 𝒘 sets the weight of each input (increase to make warnings uniformly more sensitive to this input)
𝒔 sets the shape of the 𝑝𝑜𝑖𝑛𝑡𝑠 profile (increase to make warnings more sensitive to stricter thresholds than more relaxed ones)
Decrease to make warnings more uniformly sensitive to all inputs

## Slide 12
Progress on development
Creation of ONW modules

## Slide 13: ONW detector development workflow
Operational Tuning
Manual tuning and adaptive training
SPARC Plasma Control System
(thresholds, points)
Aggregate threshold
ONSIMs
Generate synthetic data by simulating SPARC’s ONEs`
Create Detector
Identify inputs you want to use and performance metrics you want to optimize
Experimental Demonstration (C-Mod + others)
Demonstrate performance on an existing machine(s) and identify distribution
Impurity Accumulation Events (IAEs): DMS
VDEs: DMS, Avoidance
TMs
IAEs: DMS
Demonstration
Implementation
SPARC Training
SPARC Data
IAEs: DMS
VDEs: DMS, Avoidance
IAEs: DMS

## Slide 14: DMS detector for Impurity Accumulation Events (IAEs) has been demonstrated on C-Mod
[9] R. Rossi et al 2024 Nucl. Fusion 64 046017
Event Duration Distribution
Warning-time Distribution
Labeling Performance
FPR
Stability Boundary
TPR
Success with and [9] as IAE DMS observers
  Radiative cooling timescale
  FPR,TPR
Warning-time distribution is limited by distribution of radiated collapse durations on Alcator C-Mod
But should scale well to SPARC for longer ’s
DMS Metric [MJ/shot]

## Slide 15: DMS detector for VDEs has been demonstrated on C-Mod
Success with and as VDE DMS observers
  FPR,TPR
Better localized warning-time distribution
  But still limited by short event durations
  Which should scale optimistically to SPARC as well for lower ’s
Warning-time Distribution
Labeling Performance
Event Duration Distribution
FPR
Stability Boundary
TPR
DMS Metric [MJ/shot]

## Slide 16: ONW detector development workflow
Operational Tuning
Manual tuning and adaptive training
SPARC Plasma Control System
(thresholds, points)
Aggregate threshold
ONSIMs
Generate synthetic data by simulating SPARC’s ONEs`
Create Detector
Identify inputs you want to use and performance metrics you want to optimize
Experimental Demonstration (C-Mod + others)
Demonstrate performance on an existing machine(s) and identify distribution
Impurity Accumulation Events (IAEs): DMS
VDEs: DMS, Avoidance
TMs
IAEs: DMS
Demonstration
Implementation
SPARC Training
SPARC Data
IAEs: DMS
VDEs: DMS, Avoidance
IAEs: DMS

## Slide 17: DMS detector for IAEs has been tested in simulated SPARC-like environment
We have introduced IAEs and generated a database of stable and disruptive shots
A DMS detector has been trained/tested on this database
The performance is reasonable, but the physics fidelity needs to be improved to get more appropriate thresholds
Simulated Database
FPR
TPR
time [s]
DMS Metric [MJ/shot]

## Slide 18: Summary
The structure for SPARC’s ONW system has been mostly established
  Control-response structure for ONW modules
  Detectors are designed to meet specific warning-time distributions
  A tunable extension of the Points-Based model is used for triggering warnings
ONW modules for IAEs, VDEs, and TMs are currently in development
  DMS detectors for IAEs and VDEs are working well on C-Mod, and scale optimistically to SPARC
  An IAE warning module has been tested on preliminary simulations of a SPARC-like environment
  An Avoidance detector for VDEs is also in the works See talk after this one
Coming soon
  Collaboration with EPFL to integrate ONW development with DEFUSE, and benchmark these physics-driven models against existing scalings and data-driven models
  Planning to test ONW system during ramp-up and ramp-down

## Slide 19
Extra slides

## Slide 20: Other optimization metrics considered
Expected cumulative loads per shot
    average un-mitigated disruption load [J or N /shot]
  Expected cumulative loads over lifetime
    x number of shots
Other* relevant metrics
  (FPR,TPR) - generic model performance
  - controllability performance
  ONW Failure Rate (OFR) - operation-time performance
  Average disruptive load - machine safety performance
False Positive Rate (FPR)
True Positive Rate (TPR)
DMS Metric [MJ/shot]
OFR [-]
Average warning-time [\30ms]

## Slide 21: Other physics-driven models considered
Several simple and interpretable models were investigated
  Independent thresholds
  Disruptivity
  Regression
  (Gerhardt’s) Points-Based model
Why the Points-Based model?
  It has similar performance and interpretability to Disruptivity, but scales better at larger dimensionality and is much more flexible to tuning

## Slide 22: More detailed Points-model explanation
Identify relevant thresholds for each input based on their associated FPR
(Updated by re-training)
Reward lower FPRs with more points
Set by
(Updated by tuning)
Map thresholds points
Generate contours of constant
(Updated by optimizing relevant metric)

## Slide 23: Example ONW module output (IAE DMS detector on C-Mod)
Traces of physics inputs
Trajectory in stability-space
1120131012
Warnings

## Slide 24: List of ONEs to be addressed for SPARC
List based on deVries 2011
Priority
  1) Likely to come up in nominal operation
    1-H) … nominal H-mod operation
  2) Unlikely to come up in nominal operation
IAEs
  SPARC scenarios are expected to operate at higher
  Sensitivity to impurity seeding issues
VDEs
  High-ish elongation ()
LMs
  Generic disruption precursor
Event | Abbr. | Priority
Impurity Accumulation Events | IAE | 1
Vertical Displacement Event | VDE | 1
Locked Modes | LMs | 1
Rotating Tearing Modes | RMs | 1
Error Field Locked Modes | EFLMs | 1
Sawtooth Crashes | ST | 1
Inboard/Outboard Shift |  | 1
Detachment |  | 1
Edge Localized Modes | ELMs | 1-H
HL back-transition |  | 1-H
Density Limit | DL | 2
Internal Transport Barrier collapse | ITB | 2
Low safety factor | LOQ | 2
Flux consumption |  | 2

## Slide 25: POPSIM + ONSIMs
POPSIM = time-dependent POPCON
  POPSIM is a control-oriented tokamak plasma simulation toolbox built in the machine-learning framework JAX
  Currently being developed at MIT in collaboration with CFS
Off-Normal Events SIMulations (ONSIMs) are being added to POPSIM
  Physics fidelity is being improved to meet ONSIM needs
Plasma Simulator
POPSIM
ONSIMs
Plasma Control System
PCS
ONW Modules