## Slide 1: Prediction and validation of disruption-induced eddy currents and forces within engineering design cycles using ThinCurr and TokaMaker
Chris Hansen1, A. Battey1, A. Braun1, N. DaSilva1, S. Guizzo1, J. Levesque1, R. Sweeney2, M. Lagieski2, G. Subbotin3,
M. Nurgaliev3, S. Miller1, and C. Paz-Soldan1
1- Columbia University
2- Commonwealth Fusion Systems
3- Next Step Fusion

## Slide 2: Outline
Modeling disruptive forces in 2D
  TokaMaker: Axisymmetric model
  Modeling to inform NTT design
  Modeling to inform ARC design
Modeling disruptive forces in 3D
  ThinCurr: 3D thin-wall model
  Validation with commercial tools
  Modeling to inform SPARC/ARC design
Design and validation on HBT-EP REMC
  Coil design and installation update
  Initial model validation
Summary and Conclusions

## Slide 3: The tools discussed today are available in the open-source Open FUSION Toolkit
Fully open-source on GitHub
  All tools share the same codebase
  Python/Fortran/C/C++
  Downloadable binaries
  Contributions welcome!
Finite elements on unstructured grids
  Direct meshing from CAD
Current physics tools
  TokaMaker: Axisymmetric equilibrium
  ThinCurr: 3D thin-wall E-M modeling
  MUG: 3D time-dependent MHD
  Marklin: 3D Ideal MHD equilibria (const. 𝜆)
Guizzo et al., PPCF (2024)
Battey et al., NF (2023)
Hansen et al., CPC (2024)
Hansen et al., PoP (2015)
https://hansec.github.io/OpenFUSIONToolkit/

## Slide 4: Outline
Modeling disruptive forces in 2D
  TokaMaker: Axisymmetric model
  Modeling to inform NTT design
  Modeling to inform ARC design
Modeling disruptive forces in 3D
  ThinCurr: 3D thin-wall model
  Validation with commercial tools
  Modeling to inform SPARC/ARC design
Design and validation on HBT-EP REMC
  Coil design and installation update
  Initial model validation
Summary and Conclusions

## Slide 5: TokaMaker is a time-dependent Grad-Shafranov code that captures axisymmetric eddy current dynamics
1- Hansen et al., Comput. Phys. Commun. (2024)
Time-dependent Grad-Sharfanov code
  Unstructured triangular grid
  Variable order finite elements
  Python interface with compiled backend
Currently being applied to device design
  Stability/control (eg. passive structures)
  Magnetic system
Axisymmetric eddy currents can be captured in forward and inverse equilibria
  Fully meshed, thick-wall representation
  Self-consistent evolution or specified sources
Guizzo et al., PPCF (2024)

## Slide 6: TokaMaker was used to assess forces on passive components during CQ events as part of NTT design
TokaMaker has been used to inform magnetic and early structural design for Next Step Fusion’s Negative Triangularity Tokamak (NTT)
  Native NT tokamak
  Focused on control development
Forces evaluated for characteristic CQ events as design evolved
  Changes to stability plates, VV, etc.
  Direct integration with CAD models
Scoping, design, and loads within a single tool
  Equilibrium design (PFs, limiter, etc.)
  Stability (linear and nonlinear)
  Forces (static and dynamic)
2- Publication in preparation

## Slide 7: TokaMaker is also being scoped to assess forces during CQ events as part of preliminary ARC design
TokaMaker models are created directly from IDS-like device description
A variety of disruption-relevant events can be modeled
  VDE, CQ, TQ/β-collapse, etc.
  Self-consistent or fixed plasma evolution
  Fast simulations: O(10 s) on a laptop

## Slide 8: Outline
Modeling disruptive forces in 2D
  TokaMaker: Axisymmetric model
  Modeling to inform NTT design
  Modeling to inform ARC design
Modeling disruptive forces in 3D
  ThinCurr: 3D thin-wall model
  Validation with commercial tools
  Modeling to inform SPARC/ARC design
Design and validation on HBT-EP REMC
  Coil design and installation update
  Initial model validation
Summary and Conclusions

## Slide 9: ThinCurr models inductive coupling between currents in the thin-wall limit using a finite element method
ThinCurr is primarily designed to solve inductive-resistive current dynamics in 3D
  Time-domain, frequency-domain, eigenvalues
ThinCurr utilizes a Boundary Finite Element (BFEM) approach
  Current represented using a scalar potential
  Green’s function maps to any point in space
3- Publication in preparation

## Slide 10: ThinCurr utilizes HODLR approximation to improve scalability of BFEM for large models
Hierarchical Off-Diagonal Low-Rank (HODLR) approximation is used for L matrix
  Adaptive Cross-Approximation (ACA) is used to iteratively form low-rank blocks
Scaling is dramatically improved from O(N2) to O(N log(N)) for both memory and time
  Expands access to much larger models of a given system
  Applicable to B-field reconstruction as well
HODLR/ACA has some overhead, but break even occurs fairly quickly
  Implementation can be optimized further
Eigenvalue solve
Time-domain solve

## Slide 11: ThinCurr currents and loads have been validated with commercial analysis software (Ansys)
ThinCurr currents and forces were validated against axisymmetric Ansys model of SPARC
  Excellent match in current and forces
  Ansys challenging for large 3D models
  ThinCurr can model full machine; necessary for low-n features (eg. REMC)

## Slide 12: ThinCurr enables prediction of a variety of disruption loads throughout the machine design process
Induced eddy currents
  Vessel, PFC, and REMC design
  Forces and heating
Inductive voltages
  Diagnostic and component design
  Insulation requirements and short failure analysis
Direct iteration with engineering workflows
  Meshing directly from CAD
  Export of results to Ansys mechanical analysis in progress
3- Battey et al., Nucl. Fusion (2024)

## Slide 13: ThinCurr is being used in early vessel design for ARC to assess disruption loads from inductive coupling
Model of ARC VV evaluated on design iteration timescale
  Current models are axisymmetric
  Same description as TokaMaker models
  Ports and other 3D structures in future
Disruptions evaluated using filament grid for plasma
  Flexible for many types of CQ, VDE, etc.
  Generate from reduced models or plasma predictions (TokaMaker, M3D-C1, etc.)
Workflows to use output in commercial thermo-mechanical (Ansys) analysis underway

## Slide 14: Further model reduction is possible for many design cases, enabling extremely lightweight models
Large-scale CQ dynamics only couple well to a handful of vessel eigenmodes
  High grid resolution adds very fast modes that don’t contribute much
  Many modes are orthogonal to plasma model (filaments)
Reduced models built from O(100) eigenmodes perform well in design contexts
  O(1) inductive limit modes for fast dynamics
  Computed once and used many times
Reduced models accelerate simulations to O(1-10 s) for even reactor-scale devices
  Enable real time usage (eg. eddy current reconstruction)

## Slide 15: Outline
Modeling disruptive forces in 2D
  TokaMaker: Axisymmetric model
  Modeling to inform NTT design
  Modeling to inform ARC design
Modeling disruptive forces in 3D
  ThinCurr: 3D thin-wall model
  Validation with commercial tools
  Modeling to inform SPARC/ARC design
Design and validation on HBT-EP REMC
  Coil design and installation update
  Initial model validation
Summary and Conclusions

## Slide 16: HBT-EP has installed a first of a kind Runaway Electron Mitigation Coil* for studying design considerations
HBT-EP is a small tokamak focused on understanding and control of 3D MHD
  Circular, high-aspect ratio
  20 segment adjustable first wall
  High-resolution magnetic feedback coilset
HBT-EP has recently completed installation of an REMC in vessel
  HFS and LFS† coils
  Passively and actively driven
  1/1 or 2/1 configurations (m/n)
* - No true runaways in HBT-EP
† - LFS coil completion in 2025
HBT-EP Typical Parameters | 
R0 | 92 cm
a | 15 cm
IP | ≤ 20 kA
BT | 0.35 T
𝛕pulse | 5 - 10 ms
Te | ≤ 150 eV

## Slide 17: ThinCurr workflow used for DIII-D/SPARC REMCs also utilized on HBT-EP to optimize coil and support validation
Coil designs couple well to disrupting plasmas with ~20% plasma current conversion
  Coupling weakly dependent on coil position
  Coupling can be changed by modifying vessel electrical connections
Disruptions in HBT-EP progress toward the HFS
  Every shot ends in a disruption

## Slide 18: Broad mode spectrum is predicted in REMC-generated field; adjustable with wall movement
HFS and LFS coils are designed for a dominant m/n = 1/1 structure
  Broad spectrum from discrete coil position
  Control coils provide cross-comparison
Walls generate additional poloidal variation in applied field on plasma
  Adjustable for LFS by moving wall segments
Coil Only
Full model

## Slide 19: The HFS and LFS* REMCs have been installed in HBT-EP and preparations are now underway for plasma operation
* - LFS coil completion in 2025

## Slide 20: Initial vacuum tests have been completed to confirm expected performance of HFS coil with active drive
An external high-power supply was used to drive the HFS coil in vacuum
  1.2 kA achievable with available supplies
  Sufficient for plasma response studies
ThinCurr predictions using the baseline design provide a reasonable match to “as built”
  Preliminary L error < 25%
  More precise measurements needed
  Calibrated resistivity and inductance to be used for plasma studies
Additional tests are planned this month (pre-APS meeting)
  Vacuum: OH/PF coupling
  Plasma: Disruptions
Rnom
Rmeas
Active
Passive

## Slide 21: Summary and conclusions
A hierarchy of tools for assessing loads in disruptive CQs due to inductive effects is available in the Open FUSION Toolkit
  TokaMaker, ThinCurr (full and reduced models)
Tools can couple to relevant engineering workflows (eg. CAD) and obtain results on design-relevant timescales without the use of HPC
  Axisymmetric calculations run in O(10 s) and share platform with equilibrium design
  3D calculations run in O(10 m) for full calculations on workstation hardware
  Reduced 3D calculations run in O(10 s) while retaining design-level fidelity
Tools are being successfully applied to design of public and private devices and components
  Validation performed with commercial tools and experimental data
Initial HBT-EP REMC is installed and undergoing tests in preparation for upcoming first plasma operations

## Slide 22: Backup Slides

## Slide 23: The HFS and LFS REMCs have been installed in HBT-EP and preparations are now underway for plasma operation

## Slide 24: For general surfaces element space must be supplemented to account for topology
For multiply connected surfaces the potential must be multi-valued
  Insert elements to represent “jumps” in potential on unique loops
  Called “secular” terms in SIMSOPT
These correspond to “holes” in the surface
  Unique “cycles”, which define a basis for the topology
If a volume is fully enclosed an element must be removed
  Enclosing a volume makes the inductance matrix singular
  Net flux must be zero

## Slide 25: Matrix blocks associated with off-diagonal interactions exhibit low-rank structure
Scalability of problems can
  N-body problem; O(N2), O(Δx4) matrix size
Sub-blocks of matrix exhibit low-rank structure
  Interactions at long range quickly decay
Controlled approximation of the matrix by truncating these low-rank blocks
  Use SVD to compress blocks
Same observation leads to Fast Multipole Method (FMM)

## Slide 26: Adaptive Cross Approximation is a technique to iteratively build a low-rank approximation of a matrix
ACA+ provides an approach to iteratively approximate a matrix through sampling
  Series of rank-1 updates from candidate rows/cols
  Randomly selected starting point, then target largest elements
  Recompress after with SVD (small matrix)
Recursively sub-divide geometry in space
  Determine far-field interactions on each level
  All levels: Apply ACA+ to far-field blocks
  Lowest level: SVD compress near blocks; keep full block for self-interaction
Hopefully only need to compute and store a small fraction of full matrix

## Slide 27: Figures bank for Chris - Anson