## Slide 1: Cross Tokamak Disruption Prediction with Different Methods and from Different Perspectives
Wei Zheng, Fengming Xue, Zhongyong Chen, Chengshuo Shen, Dalong Chen, Bihao Guo, Xinkun Ai, Ming Zhang, Nengchao Wang, Yonghua Ding, Zhipeng Chen, Zhoujun Yang, Yuan Pan, Biao Shen, Bingjia Xiao
With help from J-TEXT, EAST and HL-2A team

## Slide 2: Agenda
Why do we need cross tokamak disruption prediction
Related works
J-TEXT’s efforts on cross tokamak disruption prediction
Integrated Disruption Prediction Strategy

## Slide 3: Agenda
Why do we need cross tokamak disruption prediction
Related works
J-TEXT’s efforts on cross tokamak disruption prediction
Integrated Disruption Prediction Strategy

## Slide 4: The Problem of ML Based Disruption Prediction
Disruption is everyday routine😀
Disruption is not that big a deal
One runaway discharge will do the job 😟
It needs disruption data from the target machines
  Machine Learning is data driven.
  For future tokamak reactors it’s hard to provide enough disruption data before it damages itself.
  How to use the existing tokamaks to build a model that works on future reactors?
Train: J-TEXT
Test: EAST
Test: J-TEXT
AUC: 0.98
AUC: 0.64

## Slide 5: Agenda
Why do we need cross tokamak disruption prediction
Related works
J-TEXT’s efforts on cross tokamak disruption prediction
Integrated Disruption Prediction Strategy

## Slide 6: Deep Learning with Mixing Data
J. Kates-Harbeck, et al., Nature, 2019.
With a glimpse of the target tokamak
  CNN+LSTM deep neural net model, FRNN
  Training set mainly built on existing Tokamaks
  Add a tiny amount of data from target machine
  With deep learning, “Magic happened”
A Glimpse=
5 Disruption
+
16 Safe shots

## Slide 7: More Delicate Ways of Mixing Data
J. X. Zhu, et al., "Hybrid deep-learning architecture for general disruption prediction across multiple tokamaks," Nucl. Fusion, 2020
Mixing lots of disruption from existing with lots of safe shots from target
  CNN+GRU deep learning model
  Best case: All disruptive from existing machines + All safe shots from new+20 disruption from new
  New machine cannot provide disruption, but they can provide safe shots
  Add non-disruption from existing machines harms the model performance
  The disruptive characteristics are machine-independent

## Slide 8: More Delicate Ways of Mixing Data
J. Zhu, et al., "Scenario adaptive disruption prediction study for next generation burning-plasma tokamaks," Nucl. Fusion, vol. 61, 2021.
Scenario adaptive disruption prediction
  Different mixing techniques based on discharge scenario
  Best case: HP from existing machine + LP from target machine
  Existing machine can provide the HP disruptions, while target machine can withstand LP disruptions

## Slide 9: Disruption Bench
Spangher, et al. 2024. Pre-print.
Spangher, et al propose a benchmark to standardize the evaluation of cross-tokamak disruption prediction models
  Targeted specific at test how well models trained on existing data can make predictions about a new tokamak.
  Designed standard training set compositions to simulate different stages of tokamak operation.

## Slide 10: Transfer Learning
Mixing
Currently most cross tokamak disruption prediction is done by mixing data from the target tokamak:
  Carefully designing a new data set to approximate the target data set
  Also known as instance based transfer learning
Cross tokamak disruption prediction is a transfer learning problem

## Slide 11: More on mixing
  Training data: Mixing lots of LP data from HL-2A with a fraction of HP data (10 shots) did improve the performance significantly
  But, the contributing features are different, some even contradict each other
  Mixing really requires carefully selected data to minimize negative effect.
Lp-Model
Lp-Model
Hp-Model
Hp-Model
Low performance
discharges
High performance
discharges
  Training set: Mixture of lots of LP shots and 10 HP shots
  Test set: HP shots only

## Slide 12: Agenda
Why do we need cross tokamak disruption prediction
Related works
J-TEXT’s efforts on cross tokamak disruption prediction
Integrated Disruption Prediction Strategy

## Slide 13: J-TEXT’s efforts
  Transfer learning disruption prediction
  Instance based transfer learning
  Feature based transfer learning
  Parameter based transfer learning
Low performance discharges
High performance discharges
  Training set:
    Mixture of lots of LP shots and 10 HP shots
  Test set:
    HP shots only

## Slide 14: Instance Based Transfer
  How to reduce the negative effect of mixing data when there is contradicting features in different operation range?
  Using Model explanation to reduce the contradiction features and samples
Remove contradicting features
Signal drop | H-set auc(mix)
Remove contradicting features | 0.82
Remove non-contradicting features | 0.715
Baseline (full features) | 0.81
Remove contradicting features, gains performance
Remove non-contradicting features, reduces performance
Remove contradicting samples
sample reserve SHAP value | H-set auc(mix)
[-1.5, 1.5] ~approx. remove 20% | 0.761
[-1，1] ~approx. remove 50% | 0.678
[-0.5, 0.5 ] ~approx. remove 90% | 0.719
But remove contradicting sample does not gain performance

## Slide 15: Instance Based Transfer
  Tradaboost to adjust the weight of each sample
  Moreover, using previous SHAP value to set initial weight of each shot further improves the performance
Training Case | TPR | FPR | BA
Lots of HP shots (Target) | 0.96 | 0.28 | 0.84
Just Mix | 0.75 | 0.19 | 0.78
Tradaboost | 0.95 | 0.28 | 0.84
Tradaboost with initial weights | 0.95 | 0.23 | 0.86
  Tradaboost to adjust the sample weights iteratively to optimize the performance in the target domain.

## Slide 16
  Transfer learning disruption prediction
  Instance based transfer learning
  Feature based transfer learning
  Parameter based transfer learning
  Training set:
    Lots of J-TEXT shots
    10-20 EAST shots
  Test set:
    EAST shots only

## Slide 17: The Key of Transfer learning
Reduces source and target divergence
Reduces source error
J. Wang, et al. arXiv:2103.03097, 01 3 2021
  To increase the performance on future reactors, it needs to increase the performance on existing tokamak, and reduce the difference between existing and future machines

## Slide 18: Transfer Based on Machine Independent features
First, feature engineering:
  Extract machine independent disruption related features
  Reduce source domain error as well as source and target divergence
Types of features | Feature tag | Impact on disruption
MHD instabilities related | mode_number_m, mode_number_n | 2/1 magnetic island growth; Multi-magnetic island overlap; Locked mode
 | n=1 amplitude | 
 | FFTMir_abs, FFTMir_fre | 
 | Mir_VV | 
Radiation related | P_rad, SXR_core, CIII | Edge cooling; MARFE
 | axuv_array_kurt(skew, var) | 
 | sxr_array_kurt(skew, var) | 
Density related | sum_ne | Density limit disruption
 | ne | 
 | ne_array_kurt(skew, var) | 
PCS related | bt, ip | Plasma current limit disruption
 | Ihfp, Ivfp, vl | VDE; Plasma out of control
 | Ihfp_diff, Ivfp_diff, ip_diff | 
 | dr, dz | 
Got better performance than raw data with less data
C. Shen, et al., Nuclear Fusion, 63 046024, 2023

## Slide 19: Transfer Based on Machine Independent features
Then, domain adaptation-CORAL:
  With a few shots from the target tokamak, you can transform the source tokamak features into target tokamak feature spaces
  Train a model with transformed source data, it will work on target tokamak
Case No. | EAST Data | Data Strategy | CORAL Strategy | AUC
1 | None | / | / | 0.642
2 | 1896 (355) | All EAST | / | 0.936
3 | 0 (10) | Mixing | / | 0.764
4 | 0 (10) | CORAL | Unsupervised | 0.797
5 | 0 (10) | CORAL | Supervised | 0.890
CORAL only need 10 disruptions from EAST
Huge improvement over mixing -10 shots- 0.76->0.89
C. Shen, et al., Nuclear Fusion, accepted, 2024
B. Sun, et al., AAAI 30, 2016
Notes: (a-c) Illustration of CORrelation ALignment (CORAL) for Domain Adaptation: (a) The original source and target domains have different distribution covariances, despite the features being normalized to zero mean and unit standard deviation. This presents a problem for transferring classifiers trained on source to target. (b) The same two domains after source decorrelation, i.e. removing the feature correlations of the source domain. (c) Target re-correlation, adding the correlation of the target domain to the source features. After this step, the source and target distributions are well aligned and the classifier trained on the adjusted source domain is expected to work well in the target domain. (d) One might instead attempt to align the distributions by whitening both source and target. However, this will fail since the source and target data are likely to lie on different subspaces due to domain shift.

## Slide 20
  Transfer learning disruption prediction
  Instance based transfer learning
  Feature based transfer learning
  Parameter based transfer learning

## Slide 21: Deep Transfer Learning, Pre-train, Fine tune
  Lower level layers extract low level patterns which is shared between tokamaks;
  Possible to pre-train a feature extractor on lots of data from existing machines.
  Then fine tune it on limited target machine data
J-TEXT Data | EAST Data | Layers Frozen | Unfreeze | AUC | Remark
None | 1896 (355) | / | / | 0.821 | EAST full data baseline
494 (189) | 20 (10) | CNNs | No | 0.811 | Best practice
494 (189) | 20 (10) | / | / | 0.661 | Mixing J-TEXT and EAST
None | 20 (10) | / | / | 0.615 | 20 discharges from EAST
494 (189) | None | / | / | 0.611 | Only J-TEXT model
  Reaching similar performance as EASAT full data baseline using only 20 EAST discharges
W. Zheng, F. Xue, et al. Communication Physics, 6, 181 (2023).

## Slide 22: J-TEXT’s Efforts
  Besides transfer learning disruption prediction
    Anomaly detection disruption prediction

## Slide 23: Anomaly detection disruption prediction
Future reactors cannot provide disruption data
What if we can train a predictor with only safe shots
  But, you can’t get lots of safe shots without any disruption!
  But we found: Different shots have different precursor onset time
  Using fixed precursor onset time labeling is not optimal
  Using anomaly labeled precursor can improve the supervised learning predictors’ performance
[1] Ai, X.K., et al.,. Nuclear Engineering and Technology, 2023.

## Slide 24: Agenda
Why do we need cross tokamak disruption prediction
Related works
J-TEXT’s efforts on cross tokamak disruption prediction
Integrated Disruption Prediction Strategy

## Slide 25: The Problem of Transfer Learning
It still needs data from the target machine although not much
Will ITER be able to provide those data?
  FP: 0.1-1 MA circular limiter plasma. Disruption is OK, but is it useful for later stages?
  PFPO-1/2: 7.5-15 MA unmitigated disruption is barely acceptable
  FPO: Will it be a new machine again?
Each stage is like a new machine

## Slide 26: Integrated Disruption Prediction Strategy
Using different methods at different stages of tokamak operation to achieve different disruption prediction goals

## Slide 27: Integrated Disruption Prediction Strategy
An Adaptive model that predicts the next shot from the first shot
Basic protection
From the 1st shot
Disruption Budget Consumption Guided
Operation
Generate training data without destroying the reactor
Domain Generalization
Model
High Performance Disruption Prediction Model
Train with limited generated data and lots of data from existing tokamaks
Better protection

## Slide 28: Adaptive training
Murari, A., et al., Nuclear Fusion. 2019
A. Murari, et al, Nucl. Fusion, 2020
We do not need a model that can predict every shot, just predicting the next shot is enough
  Adaptively train the model to predicting shots in near future
  The model is pre-trained on existing tokamaks
  Can be re-trained after the first safe and disruptive discharge
  Is re-trained after meeting some criteria, like, an alarm is triggered or missed.

## Slide 29: Adaptive training from scratch
Pre-train an anomaly detection model from existing machine
Inference on the 1st shot
Fine tune on the new shots
Inference on the next shot
Modified loss, support positive samples, but still can be trained with ONLY negative samples
How this is gonna work?
Deployed on the new machine
The model can be fine tuned with only safe shots
When there is a missed alarm, it can also contribute

## Slide 30: Adaptive training from scratch
The model is pre-trained on J-TEXT with both disruptions and safe shots
The model can be fine tuned with 1 shot, no matter if it is a disruption or not
After each shot the model is retrained with available future reactor (EAST) data
With existing tokamak’s (J-TEXT) model weight as initial weight, it works from very 1st shot.

## Slide 31: Integrated Disruption Prediction Strategy
An Adaptive model that predicts the next shot from the first shot
Basic protection
From the 1st shot
Disruption Budget Consumption Guided
Operation
Generate training data without destroy the reactor
Domain Generalization
Model
High Performance Disruption Prediction Model
Train with limited generated data and lots of data from existing tokamaks
Better protection

## Slide 32: Disruption Budget Consumption Guided Operation
Each shot is given a Disruption Budget Consumption (DBC) based on the potential disruption damage
Try to cover as wide operation regime as possible with low DBC
With disruption prediction and DMS, DBC can be kept even lower
M. Lehnen et al 26th IAEA Fusion Energy Conference (FEC 2016)
Calculate DBC for each shot
k is safe shot discount rate, 1 for disruption, 0.2 for safe shot
Just toy example for demonstration

## Slide 33: Disruption Budget Consumption Guided Operation
You can get a high performance model even with much less DBC
Just preliminary results, for demonstration
DBC | 62198 | 61793 | 61323 | 38121 | 30719 | 23978
shots | 827 | 827 | 827 | 827 | 827 | 827
Disrup. ratio | 0.265 | 0.265 | 0.265 | 0.265 | 0.265 | 0.265
AUC | 0.88 | 0.88 | 0.85 | 0.86 | 0.90 | 0.87
DBC | 69593 | 69593 | 69593 | 69593
shots | 910 | 718 | 625 | 478
Disrup. ratio | 0.256 | 0.289 | 0.298 | 0.323
AUC | 0.9 | 0.84 | 0.76 | 0.69
You can generate more and better data for training a better mode with the same DBC
So, you can get better and more data with less damage, if you plan your shots considering DBC

## Slide 34: Integrated Disruption Prediction Strategy
An Adaptive model that predicts the next shot from the first shot
Basic protection
From the 1st shot
Disruption Budget Consumption Guided
Operation
Generate training data without destroy the reactor
Domain Generalization
Model
High Performance Disruption Prediction Model
Train with limited generated data and lots of data from existing tokamaks
Better protection

## Slide 35: Domain Generalization Model
There are a common rule that disruption on all tokamak follows:
  Trained on many existing tokamaks, a model may learn the common rule
  The model has 2 tasks, one to predict the disruption, the other try to tell which machine does the data come from
  Via domain adversarial training DANN

## Slide 36: Domain Generalization Model
With sufficient J-TEXT+HL-2A data (source) and little bit of EAST data (target):
  DANN enforced the model to learn a representation that is common between J-TEXT and HL-2A
  The result is much better then just transfer from one machine to another
 | J-TEXT | HL2A | EAST
Training Set | 1021 | 474 | 20
Validation Set | 0 | 0 | 20
Test Set | 0 | 0 | 506
Cases | TPR | FPR | AUC
DA1 Mixing | 65.05% | 15.04% | 0.7937
DA2 MMD | 82.11% | 20.89% | 0.8492
DA3 DANN | 82.63% | 22.47% | 0.8724
DA4 EA | 83.68% | 40.19% | 0.8141
DA5 EA+MMD | 81.05% | 32.28% | 0.7986
DA6 EA+DANN | 81.58% | 28.48% | 0.8210
Just preliminary results, better performance expected

## Slide 37: Domain Generalization Model
What’s more interesting:
  Even with no target data at all, the model still kinda works, but not as good
 | J-TEXT | HL2A | EAST
Training Set | 1021 | 474 | 0
Validation Set | 255 | 115 | 0
Test Set | 0 | 0 | 506
Cases (0 shot) | TPR | FPR | AUC
DG1 Mixing | 60.00% | 11.39% | 0.8009
DG2 MMD | 74.74% | 25.95% | 0.8115
DG3 DANN | 90.00% | 31.01% | 0.8343
Just preliminary results, better performance expected

## Slide 38: Domain Generalization Model
Cross tokamak disruption database
  With“IAEA CRP Artificial Intelligence for Accelerating Fusion R&D”Collaborated with MIT, IAEA and ITU,
  An open database of J-TEXT，HL-2A，Alcator C-Mod was built with JDDB tools；
  An open challenge was organized by ITU, attracted many from non-fusion communities.
  This is a good starting point, but this is far from done.
Cross tokamak disruption prediction challenge with MIT, IAEA and ITU

## Slide 39: The Next Step
A large multi-tokamak database is needed
  Many tokamaks, complete diagnostics, complete metadata
  Standard tooling for model development and benchmarking
  With very large data, a tokamak large foundation model could be built
Explainable model is needed
  Explainable models can let us assess the performance on unseen tokamaks before we have any test data
  Disruption prediction model are getting better, so should our understanding about disruptions
All require in-depth collaborations of us

## Slide 40
Thank for your attention

## Slide 41: Adaptive training from scratch
About the Very 1st shot
  Everything from the new machine looks like an anomaly.
  But disruption looks even more abnormal, it can be detected
  It used the first part of the discharge to get used to the new scenario