## Slide 1: TOWARDS A LONG PULSE ECRH SYSTEM FOR WEST
J-M. Bernard1*, L.Delpech1, J.Barra1, F.Bouquey1, F.Clairet1, E.Corbel1, L.Doceul1, F.Durand1, R.Dumont1, T.Fonghetti1, P.Garibaldi1, G.Giruzzi1, S.Girard1, P.Magaud1, P.Maget1, X.Regal-Mezin1, P.Mollard1, D.Mouyon1, L.Nicolas1, X. Mezin1 , P.Thrierr1, E Velly1, and the WEST team**
1 CEA, IRFM, F-13108 Saint-Paul-lez-Durance, France
2 *Corresponding Author, **http://west.cea.fr/WESTteam

## Slide 2: OUTLINE
Introduction of WEST Heating System
ECRH system Presentation
Long pulse operation is a challenge
Conclusion

## Slide 3: Introduction of WEST Heating Systems
1

## Slide 4: 1- WEST Heating system introduction
LH1 (FAM)
(Full Active Multi-junction)
LH2 (PAM)
Passive Active Muti-junction
IC1
IC2
IC3
  Up to 13 MW RF Heating & CD
  LHCD system
    2 launchers
      LH1 at 4 MW/ 1000 s
      LH2 at 3 MW / 1000 s
  ICRH system
      3 antennas (1 MW / 1000 s each)
  ECRH
    This presentation
ECRH
[X. Regal Mézin this meeting]

## Slide 5: ECRH system presentation
2

## Slide 6: Main Features
  Increase the operational domain in full W environment
    Increasing central electron heating
    Reduced W contamination
    Ease access to H-mode
  3 gyrotrons, 1 MW / 1000 s each (Thales)
  Operational Frequency 105 GHz
  Transmission line waveguides Ø 63,5 mm (General Atomics)
  One dummy load for gyrotrons commissioning (Calabazas Creeks corp..)
[ Integrated Modeling P Manas 2021 ]

## Slide 7: Description of the system
Power dummy load
Plasma
Antenna
GYR1
GYR2
GYR3
RF SWITCH
High power supplies
Cooling loop
CODAC and interlocks
Vacuum system
Transmission line
Gyrotrons
Torus hall
Transmitter
RF SWITCH
RF SWITCH
POLARIZER
POLARIZER
POLARIZER
Plant Control System
Belows
Belows
Belows
DC Break
DC Break
DC Break
Valves
Valves
Valves
RF SWITCH

## Slide 8: Layout of the gyrotron hall and transmission lines
1st Gyrotron
TH1511
Waveguides
Cooling pipes
MOU
Power Load
CODAC Cubicles
Magnet
3 Gyrotrons
Hall

## Slide 9: Antenna
  6 water cooled mirrors (3 fixed / 3 steerable)
  Frame and internal ss waveguides are not water cooled yet
  Thermo couple embbeded for thermography
  Current limitation 1 MW/10 s for each line
  In vessel calibration of the steerable mirrors done this spring 2024
Miror position | Angular variation | Tolérencies
Upper | Toroidaly ± 25° Poloidaly +11°/-17° | Toroidaly ~ ± 0,4° Poloidaly ~ ± 0,6°
Equatorial | Toroidaly ± 25° Poloidaly ± 17° | 
Lower | Toroidaly ± 25° Poloidaly +17°/-11° | 
Equatorial steerable mirror
Lower steerable mirror
Upper steerable mirror

## Slide 10: Main results of commissionning of the first Gyrotron
  At KIT on Fulgor Test bed
  1 MW / 3 ms achieved in december 2023
  Infrared measurement at output of gyrotron
  Calculated modal purity better than 96 %
  Oscillation at 105 GHz
  1 MW / 2,5 s June 2024
  Frequency shift 212 MHz @ 1 MW power
Infrared measurement at output of gyrotron
RF Beam Propagation

## Slide 11: Long pulse operation a challenge
3

## Slide 12: Two Water loops will be used
  First one used for high pressure drop components and low flow rate
    Small components: Waveguides, Elbows...
    10 bar
    ~98 m3/h
  Second one used for low pressure drop but high flow rate
    Large components: Gyrotrons, water load
    6 bar
    ~340 m3/h
Piping and Instrumentation Diagram (P&ID)
(Upgrade under work)

## Slide 13: Power supply an other challenge
Need permanant energy source for long pulse
  A dedicated distribution network exists at IRFM at 400 kV
Transformer of 90 MW for poloidal coils and heating systems.
For ECRH
  (efficiency ~50 %)
  3 gyrotrons of 3 MW = 6 MW of power supply 1000 s
Transformer 400 kV / 66 kV

## Slide 14: RF components and transmission lines
Design of the load to be validated
long pulse operation (Water cooled)
Part of waveguides (Water cooled)
Valves, Belows and DC break (Not cooled yet)

## Slide 15: Interlocks and CODAC
  Each Gyrotron is equipped with 45 thermocouples
  Monitoring of the output power by
    Calorimetry
    Millimeter wave measurements
  Monitoring the Spectral purity
    with down converter and fast acquisition oscilloscope
  Fast safety card
    Mode loss detection
    Over heating on gyrotron / Transmission lines / antenna
    Arc detection (MOU, TL )
    Over voltage/over current
    Gyrotron Vacuum fault
  Data acquisition
    ~1 Mo/s
    1Go / 1000 s

## Slide 16: Conclusion
4

## Slide 17: Conclusion
  3 MW / 1000 s ECRH system is under construction
    It will increase the WEST operational domain.
  First Gyrotron validated on short pulse duration
    Need more commissionning for long pulse
  1000 sec is a real challenge regarding the auxiliaries
    increase the complexity, but available at IRFM
  The antenna, and some RF line components are not yet cooled
    Need some future upgrade
  The first shot with ECRH in WEST
    Foreseen by the end of this year
  The second and third gyrotron are foreseen to be integrated next year

## Slide 18: Thank you for your attention
  This meeting
    P.Manas ”Long pulse operation in a W environment : feedback from WEST”
    X.Regal Mézin ”Lower Hybrid current drive long pulse operation state of the art on WEST”
    R/Nouilletas “Long pulse operation in a W environment : feedback from WEST”
    T.Fonghetti « WEST operational domain predictions of L-mode non-inductive discharges with an integrated modeling approach”
    L.meunier « WEST: the challenges of reaching 100% of actively cooled components for long pulse operation”
    V. Lamaison ”WEST – operation of long pulse fusion Tokamak”
  Fusion engineering and design:
    A new 3MW ECRH system at 105 GHz for WEST (https://doi.org/10.1016/j.fusengdes.2022.113360).
    Operational domain for the new 3MW/1000s ECRH System on WEST (https://doi.org/10.1051/epjconf/202327702006)