## Slide 1: Long-pulse operation in the fully metallic tokamak WEST: control and scenario development
Rémy Nouailletas, P. Moreau, R. Mitteau, S. Kerboua Benlarbi, C. Reux, A. Gallo, D. Weldon, P. Maget, A. Ekedahl, B. Santraine and the WEST team
Technical Meeting on Long-Pulse Operation of Fusion Devices
Vienna, Austria from 14 to 18 October 2024

## Slide 2: Outline
Controlling a plasma during long-duration, what’s so difficult?
Controlling the loop voltage
Monitoring plasma facing components
Long-duration scenario: WEST recipes
Conclusion / Perspectives

## Slide 3: Difficulty of long-duration plasma
Reach plasma duration close to the internal plasma dynamic time constant is the easy part of long-duration scenario
After addressing this noble core physic issues, the dirty work starts:
  Save the magnetic flux
  Keep the plasma MHD free
  Avoid impurity pollution (outgassing)
  Deal with slag, dust
  Deal with steady-state limits of the machine
  Learn to cross fingers

## Slide 4: Outline
Controlling a plasma during long-duration, what’s so difficult?
Controlling the loop voltage
Monitoring plasma facing components
Long-duration scenario: WEST recipes
Conclusion / Perspectives

## Slide 5: Loop voltage feedback control
The duration of the pulse is directly linked to the flux consumption. At very low loop voltage, a small offset implies a very large variation of the pulse duration.
Efficient loop voltage control is required but without plasma current, deviations of which are linked to plasma resistance increase
Thus dual Ip/Vloop control is required:
  The plasma current is controlled using LH power
  The loop voltage is controlled using the Central Solenoid Voltage
Fpmin
t
Δt
WEST#59183
WEST flight simulator
PLH [kW]

## Slide 6: Outline
Controlling a plasma during long-duration, what’s so difficult?
Controlling the loop voltage
Monitoring plasma facing components
Long-duration scenario: WEST recipes
Conclusion / Perspectives

## Slide 7: Monitoring Plasma Facing Components
Long-duration plasmas reveal long time-scale dynamics:
  PFC components can take hundred of seconds to reach steady-state temperatures (1) although they are actively cooled
  Some temperatures increase during the full discharge and require specific analysis (flakes, reflection…) (2)
Regions of Interest: Temperatures against soft limits (dashed red) and hard limits (solid yellow) on LH1 launcher WEST #59763
(1)
(2)
LH1 launcher and ROI definition
ROI6.3
ROI6.3
ROI6.2
ROI6.2
ROI6.1
ROI6.1
ROI6.3

## Slide 8: Monitoring Plasma Facing Components
To avoid reaching temperature limits and melting PFCs, feedback control is engaged to reduce the power request when PFC temperatures are approaching their respective limits:
  Electron ripple losses coming from LH power ramp-up
  Overheat upper diverter pipe leading to water leak risk
  PCS decreases LH power requests proportionally to temperature excursion until safe wall conditions are back

## Slide 9: Outline
Controlling a plasma during long-duration, what’s so difficult?
Controlling the loop voltage
Monitoring plasma facing components
Long-duration scenario: WEST recipes
Conclusion / Perspectives

## Slide 10: Long-duration scenario: WEST recipes
Long-duration scenario should
  Minimizes the flux consumption
  Uses a plasma shape compatible with steady-state capability of the coils
  Heats the plasma without heating the PFCs…
  Set a q profile that is MHD free
  Take care of all thermal limits that can be reached (cooling loops, semi-inertial hidden elements…)
On WEST:
  The iron core of the machine saves flux  good for long-pulse 
  PF coils are actively water-cooled  they could be steady-state for a range of current 
  The CS current should be closed to 0 during flat-top  the X-point formation and the early phases of the discharge should be well designed to reach this target at the beginning of the flat-top 
  LH launchers don’t drive current at the plasma center  very hard to get stable and MHD free plasma current profile 
J.M. Bernard: Towards a long-pulse ECRH system for WEST (15th October, 16:10)
X. Regal-Mezin: Lower Hybrid current drive long-pulse operation state of art on WEST (15th October, 16:55)

## Slide 11: Ramp-up
Start with the maximal flux value available (IG0 = 35 kA)
Plasma current overshoot to 400 kA and then synchronized decrease to 280 kA with LH power ramp-up  sharp density current profile to avoid tearing mode
Reach |IG0 | < 5 kA when at the beginning of the flat-top  compatible with steady-state value of the cooling loop
P. Manas: Long-pulse operation in a W environment : feedback from WEST (14th October, 16:10)
T. Fonghetti: WEST operational domain predictions of L-mode non-inductive discharges with an integrated modeling approach (17th October, 10:35)
WEST#59763

## Slide 12: Flattop first part
Constant density
Start of Vloop/Ip control mode (transition to improve)
Long decrease of the plasma current from 280 kA to 270 kA during 50 s
Long decrease of the loop voltage (feedback control) from 10 mV to 3 mV during 50 s
Aim: keep a stable q profile free of MHD
Ip/Vloop control start
WEST#59763

## Slide 13: Flattop second part
Because of the long-time dynamics of the interactions between the wall and the plasma, there is no plasma steady-state, strictly speaking
  Decrease injected gas flow to 0 to keep density constant  Outgassing of passive elements?
  Increase of Zeff  Impurity source?
  Slow increase of the LH power to keep the loop voltage and plasma current constant (feedback control)
Feedback control could minimize the impact of these dynamics keeping the main parameters constant, however the cure can be worse than the disease.
Parameters | Variation between 80s and 345s
Ip | 1.1%
Vloop | 5.2% (0.15mV)
Plh | 7.0%
Cu/ne | 4.3%
ne | 0.95%
qD2 | 98.7%
Zeff | 16.0%
Te0 | 1.7%
Impurity increase
Zeff and plasma resistivity increase
Ip/Vloop control increases LH power
Copper erosion increase
L. Meunier: WEST: the challenges of reaching 100% of actively cooled components for long-pulse operation (16th October, 11:55)
WEST#59763

## Slide 14: Plasma end
Even 0 injected gas flow can’t compensate for the outgassing
Density continues to increase
The Greenwald limit is reached and the plasma disrupts
With each long-duration plasma attempt, the outgassing seems to be less and less important
Plasmas longer than 3 minutes seem to clean the components that were not very well baked, effectively conditioning the machine
WEST#59763

## Slide 15: Reproduce long-duration pulse
Achieving a long-duration plasma has strong impact on the wall conditioning
Several plasmas are required to recover good conditions for a new try
Several random events could end the discharge prematurely (slag, dust…)
New control room strategy:
  Succeed on a long-duration plasma (i.e. >3min)
  Run an ohmic pulse at 500 kA until a detached plasma is achieved
  Retry a long-duration plasma
  Wash, rinse, repeat…
Pulse number | Duration | Comment
59756 | 27,5s | Warm-up
59757 | 298s | Good first try
59758 | 0s | Non Sustainable Breakdown (NSB)
59759 | 3,5s | Early disruption with LH ramp-up
59760 | 0s | No gas
59761 | 3,5 | Early disruption
59762 | 106s | Detached but survived
59763 | 364s | Record !
59764 | 0s | NSB
5976559768 | 3,5s | Early disruptions with LH ramp-up
59769 | 10s | Ohmic, Detached
59770 | 12s | Ohmic Detached but better
5977159777 | Max: 115s | Scenario lower density (MHD issue)
59778 | 60s | Repeat 59763
59778 | 3,5s | Repeat 59763 (Early disruption)
59780 | 182s | Repeat 59763
V. Lamaison: WEST: Long-pulse operation in a tokamak (16th October, 11:30)

## Slide 16: Outline
Controlling a plasma during long-duration, what’s so difficult?
Controlling the loop voltage
Monitoring plasma facing components
Long-duration scenario: WEST recipes
Conclusion / Perspectives

## Slide 17: Conclusion
On WEST, dynamics between the wall and the plasma could have a huge time constant (>1min) and become more relevant than plasma core dynamics
Several controllers have been implemented to deal with these dynamics and try to reach steady-state
However several main parameters don’t reach steady-state despite a flattop of about 300 s
Repeating long-duration plasmas is also a challenge because of the legacy left by each attempt

## Slide 18: Perspectives
Future fusion power plants will be dirty machines:
  Weak pumping in front of plasma volume
  PFCs subject to erosion/deposit cycles
  Air/water leaks despite all the promises
But should perform plasma during several minutes with a satisfactory reproduction rate
We need to learn to operate dirty machine:
  Feedback control to avoid vicious circles  Control models to simulate several minutes of plasma, integrate wall/plasma interaction into the models
  Systems to recover/maintain the wall conditioning during the plasma discharge  Injection Powder Dropper
  Scenarios with plasma robust to events (Slag, dust…)  Sacrifice the performance target to increase robustness

## Slide 19: Thank you for your attention
Technical Meeting on Long-Pulse Operation of Fusion Devices
Vienna, Austria from 14 to 18 October 2024

## Slide 20: WEST CODAC Overview
20
Message system/
Ethernet network
Timing system network
Real time network
DDIV1/2
DPOLO
DGAZ
DFCI
DHYB
DFCE
Supervision
Timing system unit
(APILOT)
Database
Diagnostics
(DMAG,…)
PCS
Poloidal system supply
Divertor coils supply
ICRH
hardware
LH
hardware
Gas injection
hardware
ECRH
hardware
Actuators major faults
Permission flag
Direct link with the hardware layer
Converter
Optic fibers
Copper cables

## Slide 21: PCS Overview
DCS server
DCS
Shared memory
Fueling control
Magnetic control
Dolphin Gateway
Communication with RT network
Pulse schedule files
Diagnostics
Actuators
Supervision
Database
Timing system unit
Timing system network
Real time network
Ethernet network
Segment manager
TIPC
ChronoPCI AP
Communication with Timing system network
Heating permission flag
Heating control
Reference generator
WESTbox
Pulse data files
Cycle Master
TIPC
WEST PCS on DCS (Discharge Control System: AUG real time framework)
Segment based approach
Controllers developed using Matlab Simulink and Compiler toolbox
Gateway between DCS and WEST CODAC using WESTbox
TIPC

## Slide 22: Monitoring Plasma Facing Components: example
Electron ripple losses coming from LH power ramp-up
Overheat upper diverter pipe leading to water leak risk
PCS decreases LH power requests proportionally to temperature excursion until safe wall conditions are back

## Slide 23: Loop voltage feedback control
Based on a Tokamak transformer model, the following equations are defined to design the controller
On flattop, two decoupled PID controllers are enough to reach the desired references without offset
The controller has been assessed and tuned on the WEST flight simulator (FEEQS+0D flux consumption model).
Basic request redistribution on the two LH launchers have been implemented to optimize the total power request against different events:
  Saturation
  PFC overheating
  Copper impurity
  Arcing
After a couple of tests for final tuning, the controller is now used routinely for long-duration pulse
WEST flight simulator
PLH [kW]