## Slide 1
Overview of the MAST Upgrade Physics Programme: Testing novel concepts at low aspect ratio to inform future devices
J. R. Harrison on behalf of the MAST Upgrade team

## Slide 2: Thank you to collaborating institutes

## Slide 3
R = 0.8m
a = 0.5m
Capable of studying high performance ST plasmas
Ip ≤ 2 MA (1 MA to date)
B ≤ 0.8 T (0.72T)
τpulse ≤ 5s (1.2s)
Te,core ≤ 2.0 keV
Ti,core ≤ 3.0 keV
Advanced shaping capabilities
Can vary core and divertor shaping independently
Single and double null
  2.5
-0.3 <  < 0.55
Vpl = 8 m3
Flexible heating
On-axis and off-axis NBI
PNBI  2.5 MW per beam
Produces super Alfvénic fast ions

## Slide 4: MAST Upgrade programme contributes to the physics basis for future devices
Recent advances on MAST Upgrade support the physics basis for future devices, emphasising aspects where it can uniquely contribute:
Understanding confinement and stability at high performance
q profile tailoring toward scenario optimisation
Optimising power exhaust between and during transients with alternative divertor configurations
Expanding the ST operating space into ELM-free edge and pedestal regimes
ITER Tokamak (https://fusionforenergy.europa.eu/the-device/)

## Slide 5: MAST Upgrade programme contributes to the physics basis for future devices
ITER Tokamak (https://fusionforenergy.europa.eu/the-device/)
Recent advances on MAST Upgrade support the physics basis for future devices, emphasising aspects where it can uniquely contribute:
Understanding confinement and stability at high performance
q profile tailoring toward scenario optimisation
Optimising power exhaust between and during transients with alternative divertor configurations
Expanding the ST operating space into ELM-free edge and pedestal regimes

## Slide 6: Scenario development has improved reliability and performance
MAST-U research is underpinned by high-performance, reproducible plasma scenarios
Robust breakdown and ramp-up informed by DYON and CREATE-BD modelling
Early neutral beam injection to maintain an elevated monotonic q profile avoids internal reconnection events
Thermal confinement large in agreement with ITER scaling, gradually degraded by 2/1 mode
Core
q=2
see K-T Kim – Fri 11:00 oral

## Slide 7: Prevalent performance-limiting instabilities are 2/1 modes
Performance of NBI heated H-modes is typically limited by the presence of m/n=2/1 tearing modes
Mode is excited and persists when local minimum in the current density J coincides with q=2 surface
Core
q=2
q=2

## Slide 8: Evidence for flux pumping observed maintaining q0~1
On-axis safety factor, q0, is typically above 1 in the absence of sawteeth, indicative of a flux pumping mechanism when on-axis and off-axis neutral beam heating is applied
Operating space in sawtoothing and flux pumping regimes has been identified
Rotational coupling between q=1, q=2 surfaces during flux pumping, suggesting differential rotation between them plays a role
Shot 47020
Measurement
TRANSP
see S. Blackmore – Wed. AM poster

## Slide 9: MAST-U Experiments Test Limits of Local Gyrokinetic Models
see D. Kennedy – Fri 9:10 oral
High beta (N~4) experiments have accessed a regime where local gyrokinetic simulations exhibit high fluxes and do not saturate
Threshold to access regime where Maxwell stress is comparable to Reynolds stress
  Ideal ballooning stability used as a proxy
MAST-U can access this regime due to high flow shear
  Gyrokinetic simulations predict high fluxes when flow shear is omitted
Shot 48657, 600ms
S
T
A
B
L
E

## Slide 10: MAST Upgrade programme contributes to the physics basis for future devices
ITER Tokamak (https://fusionforenergy.europa.eu/the-device/)
Recent advances on MAST Upgrade support the physics basis for future devices, emphasising aspects where it can uniquely contribute:
Understanding confinement and stability at high performance
q profile tailoring toward scenario optimisation
Optimising power exhaust between and during transients with alternative divertor configurations
Expanding the ST operating space into ELM-free edge and pedestal regimes

## Slide 11: Impact of cryopumping is localised to the lower divertor chamber
Up to 50% reduction in lower divertor neutral pressure, main chamber and upper divertor are unaffected
Hotter, less detached divertor conditions in the lower divertor
Lower divertor
Upper divertor
see Q. Xia – Fri AM poster

## Slide 12: Fuelling location significantly affects the separatrix density
see Q. Xia – Fri AM poster
Fuelling impact on upstream density primarily impacted by fuelling location rather than divertor configuration or cryopump
SOLPS simulations recover the trend but significantly overestimate divertor neutral pressures compared to experiment

## Slide 13: Plasma-Molecule Interactions Influence Divertor Detachment
Inclusion of vibrationally rates of plasma-neutral interactions can reduce the predicted detachment threshold by SOLPS-ITER by ~20% in MAST-U conditions
Elevated D2 rotational temperature is observed as the outer divertors detach on MAST-U and TCV, indicates momentum transfer from plasma to neutrals
J. Bryant et al., Nucl. Fusion 65 036025 (2025)
N Osborne et al., Plasma Phys. Control. Fusion 66 025008 (2024)

## Slide 14: Detachment control via real-time imaging has been demonstrated
Super-X and extended leg divertors have reduced sensitivity of the detachment front position to changes in gas fuelling than a conventional divertor
Tightly baffled divertor chambers enable decoupling of the detachment state of the upper and lower divertors when using D2 fuelling
  Impurities that escape the divertor chambers can reduce this decoupling
B. Kool et al. Nat Energy (2025)

## Slide 15: Detachment control via real-time imaging has been demonstrated
Physics-based control of the ionisation front position has been demonstrated via imaging of D2 Fulcher band emission in Super-X and extended divertor configurations

## Slide 16: Tightly Baffled Divertors Enable Independent Detachment Control
Applying detachment control to upper and lower divertors enables their detachment state to be varied independently with D2 fuelling in NBI heated L-mode experiments
Control of the density of the plasma core can be performed independently of detachment state of both divertors
Upper divertor
Plasma core
Lower divertor

## Slide 17: Radiation front position is unstable in the inner divertor legs
The advancement of the radiation front from the lower inner target to the X-point is tracked with imaging bolometry
At the inner divertor leg, the radiation front jumps from the target to the X-point
There is a gradual movement of the radiation front along the conventional outer divertor leg
Highlights a key role of B field gradients to passively stabilise movement of the detachment front
X-point
Target
Unstable
X-point
Target
ne,sep (1019 m-3)
B = 1.6 T
B = 0.9 T
B = 0.7 T
B = 0.9 T
destabilising
stabilising
F. Federici et al., NME 43 101940 (2025)
B. Lipschultz et al., Nucl. Fusion 56 056007 (2016)

## Slide 18: Development of divertor configurations accelerated with Tokamak Exhaust Designer
O. Bardsley et al., PPCF 66 055006 (2024)
Exploits spherical harmonics to represent flux from poloidal shaping coils to accelerate calculations
Enables the development of feedforward and feedback divertor shape controllers
Linear constraints are easily accommodated to specify the position of the separatrix and null points, flux expansion, etc within machine limits

## Slide 19: Core-Edge Integration Observed with X-Point Target Divertor Configuration
Modest impact of outer divertor configuration on the edge pedestal or global confinement
  Consistent with a fixed ionisation front position as X-point target is formed, upstream of the secondary nulls
  Te along outer divertor legs lower in the X-point target (< 1 eV) than in the Super-X configuration (~1-1.5 eV)
Core
q=2
X-point
target
see K. Verhaegh – Wed 2:20pm oral

## Slide 20
Evidence for Stronger Plasma-Neutral Interactions in X-point Target Configuration
Divertor density profiles inferred from are significantly broader in the X-point target configuration, promoting stronger plasma neutral interactions
[T. Wijkamp, 2023, NF; N. Lonigro, 2025, PPCF]

## Slide 21: Buffering of transient heat loads observed in the Super-X configuration
see R. Scannell – Wed. PM poster
Divertor entrance
Divertor target
The interaction of sawteeth and ELMs with detached Super-X divertor configurations reveal complex dynamics

## Slide 22: Buffering of transient heat loads observed in the Super-X configuration
see R. Scannell – Wed. PM poster
The interaction of sawteeth and ELMs with detached Super-X divertor configurations reveal complex dynamics
Incoming transient can burn through the neutral buffer near the target
Dα, Dβ emission from the divertor leg remains elevated after transient has reached the strike point, showing an elevated neutral buffer due to recycling of the transient
Ratio of D2 Fulcher emission at target and upstream used to quantify degree of buffering
Divertor entrance
Divertor target

## Slide 23: Buffering of transient heat loads observed in the Super-X configuration
Power loads due to ELMs and sawteeth with < 2 kJ energy can be fully buffered with similar dependence of buffering on divertor neutral pressure
Partial buffering is observed of transients of up to 5 kJ
Buffering is more effective in the Super-X configuration due to geometric expansion of the divertor target
Fully buffered
Partially
buffered
Fully buffered
Partially
buffered
see R. Scannell – Wed. PM poster

## Slide 24: X-point radiator established with N2 seeding for the first time in an ST
Radiation localised near the lower X-point in single null, more broadly distributed radiation on the high-field side in double null
Onset of X-point radiator regime coincides with reduction in energy confinement (H98y,2 1.0  0.8)
  Higher N2 seeding results in H-L back-transition in single-null or onset of ELM-free pedestal regime in double-null
  Inner and outer divertor power loads significantly reduced
Double null
Single null

## Slide 25: MAST Upgrade programme contributes to the physics basis for future devices
ITER Tokamak (https://fusionforenergy.europa.eu/the-device/)
Recent advances on MAST Upgrade support the physics basis for future devices, emphasising aspects where it can uniquely contribute:
Understanding confinement and stability at high performance
q profile tailoring toward scenario optimisation
Optimising power exhaust between and during transients with alternative divertor configurations
Expanding the ST operating space into ELM-free edge and pedestal regimes

## Slide 26: Small ELM regimes accessed at high shaping
Type-II ELMy regime is observed at high squareness and triangularity
At lower shaping, type-I ELMs are typically observed
Chart: Triangularity
| 0.54049999999999998 | 0.58400000000000007 | 0.49399999999999999 | 0.47899999999999998 | 0.53500000000000003 | 0.49 | 0.47950000000000004 | 0.4355 | 0.46 | 0.42549999999999999 | 0.51149999999999995 | 0.50349999999999995 | 0.47599999999999998 | 0.41300000000000003 | 0.47350000000000003 | 0.40800000000000003 | 0.52899999999999991 | 0.52400000000000002 | 0.3775 | 0.45950000000000002 | 0.47499999999999998 | 0.44700000000000001 | 0.40449999999999997 | 0.38250000000000001 | 0.42649999999999999 | 0.48799999999999999
 | 0.074748 | 0.022681 | -0.20351 | -0.2607 | -0.016582 | -0.22143 | -0.14376 | -0.26923 | -0.154 | -0.25216 | -0.074624 | -0.0020717 | 0.065359 | -0.023411 | -0.17961 | -0.00036457 | -0.22143 | -0.21205 | 0.046581 | -0.019996 | -0.10023 | -0.11815 | -0.011461 | -0.043896 | 0.048288 | -0.20522
Type-II ELMy / QCE regime

## Slide 27: Absence of ELMs observed at negative triangularity for the first time in an ST
Transition from type-III to ELM-free edge has been observed at sufficiently negative triangularity
First observation in a low aspect ratio tokamak
Transition to ELM-free regime occurs at CRIT ~ -0.06
Closure of access to region of 2nd ballooning stability precedes transition to ELM-free edge, unlike TCV, DIII-D
ELM-free
A.O. Nelson et al Nucl. Fusion 64 124004 (2024)

## Slide 28: Initial evidence of RMP ELM suppression for the first time in an ST
ELM mitigation with static and rotating n=1 RMPs has been observed in double null
ELMs suppression with RMPs observed for the first time in a spherical tokamak
  Observed using RMPs with dominant n=3 component applied to single null plasmas
  Absence of ELMs accompanied by density pump-out and strong rotation braking
  Persistence of Te pedestal shows plasma remains in H mode

## Slide 29: Enhancements to MAST Upgrade in 2027 enable access to reactor-relevant regimes
1.8MW electron Bernstein wave system
Testing reactor-relevant heating and current drive schemes
Access to higher , PSOL, lower * to study confinement, stability and power exhaust
Additional 5MW neutral beam heating
Status of EBW system
P. Jacquet – Thu. AM poster
Aiming to develop STEP physics basis
H. Wilson – Sat. 14:20 oral

## Slide 30: MAST-U Contributions to IAEA FEC
Wed AM Poster | S. Blackmore et al. | Investigation of the magnetic flux pumping effect in MAST Upgrade
Wed 14:20 Oral | K. Verhaegh et al. | The physics basis for implementing Alternative Divertor Configurations on reactors
Wed PM Poster | R. Scannell et al. | Impact of transient heat load on the detached MAST Upgrade Super-X divertor
Thu AM Poster | P. Jacquet et al. | The construction and commissioning of the Electron Bernstein Wave Heating and Current Drive System for MAST-U
Fri AM Poster | Q. Xia et al. | Cryopump and fuelling location impacts on upstream density and detachment on MAST-U
Fri 9:10 Oral | D. Kennedy et al. | A Tale of Two (Viso)cities Electromagnetic Turbulence and Transport Bifurcations: Implications for Next-Generation Fusion Power Plants
Fri PM Poster | P. Sharma et al. | Developing open machine learning benchmarks for tokamak event prediction from MAST
Sat. 9:10 Oral | L. Frassinetti et al. | Peeling limited pedestals in JET, MAST-U and TCV: effect of density and isotope mass in deuterium and tritium-rich plasma on pedestal structure and stability and validation of pedestal predictions for ITER

## Slide 31
Backup slides

## Slide 32: Neutrals have a significant effect on the edge pedestal
Te,OMP (eV)
ne,OMP (1019 m-3)
Div. Closure
Div. closure
Div. puff
Div. puff
OSP pos.
Fixed HFS puff
D+ (s-1)
D (s-1)
Div. puff
OSP pos.
HFS
LFS
HFS puff
HFS + div. puff
D
D+
Improved divertor closure raises Te,ped, reduces ne,ped raising pe,ped
Reducing divertor closure and/or increasing fuelling from divertors has the opposite effect
Diffusive model does not capture degradation of Te,ped. Data guiding development of EPED+SOLPS predictive pedestal model

## Slide 33: Bi-directional GAEs observed for the first time
Sub-cyclotron frequency Alfvén eigenmodes (AEs) observed in beam-heated pulses.
  Small frequency gap between bands identifies these as GAEs rather than CAEs (supported by CSCAS and MISHKA modelling).
FILD measurements indicate GAEs drive fast ion losses.
M.B. Dreval et al 2025 Nucl. Fusion 65 016043
750 kA Ip: co- and counter-propagating GAEs
450 kA Ip: only counter-propagating GAEs
Beam energy 63 kV
Pitch angle 55 degrees
FIDASIM orbit tracing for 63 keV, 55° pitch shows ions at s=0.3, corresponding to co-propagating GAEs.

## Slide 34: A novel diamond-based proton detector improves robustness of charged fusion product measurements
Proton detector is mounted on the reciprocating arm and measures in-vacuum, 20 cm – 30 cm from the LCFS.
Measures 3 MeV protons from the d(d,p)t fusion reaction.
A. Aboutaleb et al. Rev. Sci. Instrum. 95, 083522 (2024)
Diamond detector does not suffer dropouts as probe is moved closer to the plasma.
Thicker entry foil required to improve Si detector reliability.
Results in qualitative agreement with neutron camera and fission chamber and show sawteeth as in magnetics and SXR.

## Slide 35: Scenario development has improved reliability and performance
Scenarios with elevated q profiles have been developed to study confinement and stability properties
No limiter phase to improve plasma purity
Strong shaping (~2.5) supports sustainment of an elevated q profile
  q0 > 2.0 for 0.4 (0.2s with lower shaping)
Early heating and L-H transition to maintain low li and good vertical stability at high 
Relatively high plasma volume (10 m3 cf 8 m3) reduces power density and confinement
Core
q=2