## Slide 1: The physics basis for implementing alternative divertor configurations on reactors
K. Verhaegh, C. Theiler, D. Brida, et al.
Eindhoven University of Technology
k.h.a.verhaegh@tue.nl
30th IAEA Fusion Energy Conference, Chengdu, China

## Slide 2: Towards fusion power plants
ITER – under construction (2033-2039)
Q (energy out / energy in) =10
(EU-)DEMO – under design (>2040)
Q=25 (300-500 MW electricity)
SPARC (CFS - US) (construction 2026)
Q>2
ARC (CFS – US) (planned 2030s)
100s MW electricity
STEP (UK) – (under design <2040)
>0 MW electricity
BEST (China) (construction 2027)
Q=5
CFETR (China) (planned 2030s)
Q=13 (891 MW electricity)
Working towards fusion reactors -> private & public sector

## Slide 3: Power exhaust – a common challenge towards fusion energy
Order-of-magnitude heat flux reductions required !
Unmitigated heat flux reactor: >> 100 MW/m2
Tolerable engineering limit: < 5-10 MW/m2
Heat flux
reduction
Impurity power dissipation
Detachment (5 eV) -> power, particle, mom. Loss
But, requires massive impurity & fuel injection
    Deteriorates core performance
    Reactor extrapolations uncertain
    Careful control required (slow actuators)
Can exhaust be tackled in a reactor ?
  New solutions as risk mitigation
N2, Ne, Ar, …
D2, …
Solution: Detachment !
~x4
>x10
MAST-U Ray-tracing
Conventional

## Slide 4: Power exhaust – a common challenge towards fusion energy
N2, Ne, Ar, …
D2, …
Reactor power exhaust challenge daunting especially for compact designs
Order-of-magnitude heat flux reductions required !
Unmitigated heat flux reactor: >> 100 MW/m2
Tolerable engineering limit: < 5-10 MW/m2
MAST-U Conventional
Can exhaust be tackled in a reactor ?
  New solutions as risk mitigation
Exhaust more daunting for compact designs
  New solutions needed as baseline

## Slide 5: ADCs can provide solutions !
Detached !
Total flux expansion ‘Super-X Divertor’
‘Conventional’
MAST-U
‘Super-X’
MAST-U
C. Theiler, et al. 2017, Nucl. Fusion
Conventional
‘X-Point Target’
Reimerdes, et al. 2013, NF
‘Snowflake’
Tackle power exhaust challenge with magnetic topology
Continuum of options from small to extreme: (leg length, baffling, flux expansion, secondary nulls, …)
Poloidal flux expansion ‘X-Divertor’

## Slide 6: ADCs can provide solutions !
C. Theiler, et al. 2017, Nucl. Fusion
Conventional
‘X-Point Target’
Reimerdes, et al. 2013, NF
‘Snowflake’
Total flux expansion ‘Super-X Divertor’
(MAST-U)
Tackle power exhaust challenge with magnetic topology
Continuum of options from small to extreme: (leg length, baffling, flux expansion, secondary nulls, …)
J. Harrison, et al. 2024, PPCF
ADCs can be achieved + may pose benefits
Poloidal flux expansion ‘X-Divertor’
ADCs
    Promising benefits ?
    Added engineering complexity

## Slide 7: Progress in ADC research through EUROfusion
TCV (>2017)
EPFL, Switzerland See C. Theiler, et al.
Extreme shaping flexibility
MAST Upgrade (>2020) UKAEA, UK See J. Harrison, et al.
Extreme shaping + baffling integration
WEST (>2025) See J. Harrison, et al.
Asdex Upgrade (>2025) See J. Harrison, et al.
ASDEX Upgrade (>2025)
IPP, Germany See T. Pütterich, et al.
WEST (>2025)
CEA, France See J. Bucalossi, et al.
New upper divertor -> study ADCs at high power
Long pulse double-null
This talk
Ongoing / future
Combine unique features EUROfusion tokamaks -> take ADCs from concept to reactor maturity

## Slide 8: Author list
WEST (>2025) See J. Harrison, et al.
Asdex Upgrade (>2025) See J. Harrison, et al.
K. Verhaegh1, C. Theiler2, D. Brida3, M. Carpita2, O. Février2, P. Figueiredo6,1 , A. Hakola4, J. Harrison5, B. Kool6,1, K. Lee2, T. Lunt3, N. Lonigro8,5, D. Moiraf7, D. Moulton5, B. Sieglin3, M, Zurita2, F. Albrecht3, C. Beckley5, M. van Berkel6,1, C. Bowman5, B. Brown2, M. Czarski9, G. Derks6, R. Ducker2, G. Durr-Legoupil-Nicoud2, F. Federici10, N. Fedorczak7, J. Flanagan11, S. Henderson5, Z. Huang5, D. Greenhouse8, J. Karhunen4, S. Kachkanov5, S. Kobussen6,1, B. Labit2, H. Lindl2, B. Lipschultz8, J. Lovell10, A. Mancini3, S. Menmuir5, R. Mishra9, R. Morgan2, K. Murray11, P. Muscente13, N. Osborne5, E. Pawelec12, O. Pan3, A. Perek2, H. Reimerdes2, P. Ryan5, R. Scannell5, S. Silburn5, E. Tonello2, A. Tookey5, M. Wigram13, M. Winkel1, T. Wijkamp6, Q. Xia5, L. Xiang5 , the ASDEX Upgrade Team14, the MAST Upgrade team15, the TCV team16, the WEST team17, the EUROfusion WPTE team18
1
2,16
3,14
5,15
6
4
7,17
10
13
11
9
12
8
18
14 See author list of T. Putterich, et al. this conference
15 See author list of J.R. Harrison, et al. this conference
16 See author list of C. Theiler, et al. this conference
17 See author list of J. Bucalossi, et al. this conference
Team effort !
55 authors
13 institutes
5 consortia

## Slide 9: Progress in ADC research through EUROfusion
Past
ADCs can be achieved + may pose benefits
WEST (>2025) See J. Harrison, et al.
Asdex Upgrade (>2025) See J. Harrison, et al.
Major benefits for reactor integration
without adverse core impact
Multiple ADCs obtain similar benefits
Moderate shaping can improve exhaust
Present
We understand the physics behind it
Harness for divertor optimisation
Improve physics basis ITER & beyond
Combine unique features EUROfusion tokamaks -> take ADCs from concept to reactor maturity
Future
Reactor-relevant PSOL/R

## Slide 10: Progress in ADC research through EUROfusion
EUROfusion philosophy:
  Combine unique traits fusion devices
ADCs -> solutions to optimise
May pose some benefits
C. Theiler, et al. 2017, NF
….
Large benefits for reactor integration
Steady-state, control & transient management
Understand those benefits
Use to optimise divertor design reactors
Power exhaust benefits
Tangible benefits for reactor integration without adverse core impact

## Slide 11: Power exhaust benefits – detachment access
MAST-U
Conventional CD
Super-X SXD
Low ne, sep / high PSOL (1.5 MW) -> challenge divertor (PSOL / R λq ne, sep2)
Similar results in H-mode (3.5+ MW)
Attached (CD)
Detached (SXD)
B 
X-point
h𝜈
h𝜈
h𝜈
Impurity
Radiation
Detachment
h𝜈
Ionisation
Benefits without core degradation
Detachment onset reduction
Detachment window increase (> x3.5)
Detachment front (Lpol)
Detachment
Lower detach. onset -> less imp. needed
Consistent with (EU-)DEMO Super-X sims. [L. Xiang, et al. NF, 2021]
Core Greenwald fraction (%)

## Slide 12: Power exhaust benefits – detachment access
MAST-U
[K. Verhaegh, et al. 2025, Commun. Phys]
Conventional CD
Elongated ED
Super-X SXD
Benefits without core degradation
Detachment onset reduction
Detachment window increase (> x3.5)
Super-X benefits maintained in less extreme shape
B 
X-point
h𝜈
h𝜈
h𝜈
Impurity
Radiation
Detachment
h𝜈
Ionisation
Detachment front (Lpol)
Detachment
Core Greenwald fraction (%)
Total flux expansion ED < STEP ! Similar to DEMO SXD & ARC (!)
Total flux expansion

## Slide 13: TCV’s X-Point Target Divertor
TCV
[K. Lee, et al. 2025, Phys. Rev. Lett.]
Discovery of the X-Point Target Radiator (XPTR) regime
  Strong power dissipation – x-point radiator structure in secondary null
  Localised power dissipation without XPR risks
X-Point Target Radiator discovered on TCV – localised power dissipation in secondary null
X-Point Target – Featured in SPARC & ARC

## Slide 14: TCV’s X-Point Target Divertor
TCV
Discovery of the X-Point Target Radiator (XPTR) regime
  Strong power dissipation – x-point radiator structure in secondary null
  Localised power dissipation without XPR risks
XPT benefits maintained at highest power/low density (PSOL / R λq ne, sep2)
High power XPT could be detached at higher power with less impurity injection (!)
Conventional
Attached
X-Point Target Detached
X-Point Target – detached where conventional attached !
x 2.2 seeding
x 3 heating
CIII emission front ~ 5-9 eV
X-Point Target Radiator discovered on TCV – localised power dissipation in secondary null
X
X
Detachment

## Slide 15: Power exhaust benefits – improved detachment
Two different concepts -> similar power exhaust benefits !
MAST-U & TCV
Benefits without core degradation
Detachment onset reduction
Detachment window increase (> x3.5)
Reduced heat loads
[K. Lee, et al. 2025, Phys. Rev. Lett]
[K. Verhaegh, et al. 2025, Commun. Phys]
Power exhaust benefits
CD
ED
SXD (MAST-U)
XPT (TCV)
Possibility to combine ADC features !
[N. Lonigro, et al. AAPPS-DPP, 2025]
Total flux expansion, …
Add secondary null (X-Point Target)
MAST-U
SXD + XPT

## Slide 16: Power exhaust benefits – reduced sensitivity
Benefits without core degradation
Detachment onset reduction
Detachment window increase (> x3.5)
Reduced heat loads
Reduced detachment sensitivity (x5)
MAST-U & TCV
B 
X-point
h𝜈
h𝜈
h𝜈
Impurity
Radiation
Detachment
h𝜈
Ionisation
Detachment front (Lpol)
Detachment less sensitive to core (!)
Conventional (CD)
Elongated (ED)
Super-X (SXD)
X-Point Target
[K. Lee, et al. 2025, Phys. Rev. Lett]
[K. Verhaegh, et al. 2025, Commun. Phys]
Power exhaust benefits
Total flux expansion, …
Add secondary null (X-Point Target)
CD
ED
SXD (MAST-U)
XPT (TCV)
SXD, ED & XPT – all three strongly reduced core sensitivity !

## Slide 17: Reduced sensitivity -> improved resilience to perturbations
MAST-U
Actuator response
Quasi-steady
state
Slow transients (power exhaust control ?)
Passive absorption reliance
ADCs can greatly boost passive absorption (!)
[B. Kool, et al. 2025, Nat. Energy]
Dynamic perturbation
CD – very sensitive (MAST-U)
D2 Fulcher emission – ionisation proxy
Fast transients (too fast to actuate on
Conventional divertor
B 
X-point
h𝜈
h𝜈
h𝜈
Impurity
Radiation
Detachment
h𝜈
Ionisation
Detachment front (Lpol)
Lpol (m)
Lpol
Fueling
(1021 part./s)

## Slide 18: Reduced sensitivity -> improved resilience to perturbations
MAST-U & TCV
Actuator response
Quasi-steady
state
Slow transients (power exhaust control !)
Passive absorption reliance
ADCs can greatly boost passive absorption (!)
[B. Kool, et al. 2025, Nat. Energy]
Dynamic perturbation
CD – very sensitive (MAST-U)
ED/SXD – very insensitive
XPT – very, very insensitive
ADCs can act as shock absorber -> give actuators more time for control
Fast transients (too fast to actuate on
CD sensitivity
Reduced sensitivity
No sensitivity
Super-X Divertor
Lpol
Lpol (m)
Fueling
(1021 part./s)

## Slide 19: ADCs can aid power exhaust control
Actuator response
Quasi-steady
state
Fast transients (too fast to actuate on
Slow transients (power exhaust control !)
Passive absorption reliance
MAST-U
D2 Fulcher emission – ionisation proxy
[B. Kool, et al. 2025, Nat. Energy]
B 
X-point
h𝜈
h𝜈
h𝜈
Impurity
Radiation
Detachment
h𝜈
Ionisation
Detachment front (Lpol)
Detachment front controlled in real-time in MAST-U SXD and ED
Not possible in MAST-U CD due to sensitivity
Higher fidelity detachment control possible in MAST-U ADC’s, but impossible in MAST-U CD (!)
ADCs can act as shock absorber -> give actuators more time for control
Lpol (m)
Lpol

## Slide 20: ADCs can improve handling of fast transients
[B. Kool, et al. 2025, Nat. Energy]
Actuator response
Quasi-steady
state
Fast transients (too fast to actuate on)
Slow transients (power exhaust control)
Passive absorption reliance
ADCs can improve handling of fast transients
Conventional CIII reaches target
87081
1.5254s
XPT
CIII emission reaches 2d X-point
87080
1.4070s
Transient buffering also observed in MAST-U Super-X (see R. Scannell, et al.)
TCV
[M. Zurita, et al. APS, 2025
Preliminary
[J. Flanagan, et al. Nucl. Fusion 2025]

## Slide 21: Progress in ADC research through EUROfusion
EUROfusion philosophy:
  Combine unique traits fusion devices
ADCs -> solutions to optimise
May pose some benefits
C. Theiler, et al. 2017, NF
….
Large benefits for reactor integration
Steady-state, control & transient management
Understand those benefits
Use to optimise divertor design reactors
Physics basis of ADCs
What drives these benefits and how can we harness that knowledge ?
We now have validated tools for ADC implementation !
We now understand why
The most successful cases work so well
Other configs. yielded less benefits
Consistent with simulations (!)
Magnetic topology (total flux expansion & secondary null)
  Detachment access & reduced sensitivity
Divertor (poloidal) leg length/volume
  Power/particle losses
Neutral baffling
  Decouples divertors from core
  Enables shaping benefits to be obtained

## Slide 22: We understand why and when ADCs yield big benefits (!)
Some ADCs yielded less benefits than expected but we understand why
Benefits poloidal flux expansion TCV relatively small
  Drift simulations reproduce results
Benefits Super-X TCV relatively small
  Baffling not as strong -> neutral escape -> flows -> negate SXD benefit [M. Carpita, et al. 2024, NF]
WEST (>2025) See J. Harrison, et al.
Asdex Upgrade (>2025) See J. Harrison, et al.
TCV
NO
DRIFTS
SOLPS-ITER
DRIFTS
[M. Carpita, et al. AAPS, 2025]
Validation of the importance of including drifts exhaust modelling
To be validated
Preliminary
Validated tools/sims. for ADC implementation !
We now understand why
The most successful cases work so well
Other configurations yielded less benefits
Neutral baffling
Maximises plasma-neutr. Inter. & decouples divertor-core
Enables divertor shape detachment benefits
[E. Tonello, et al. this conference]
?
No change !

## Slide 23: Reduced model: magnetic topology drives detachment front
Divertor (poloidal) leg length/volume
  Power/particle losses
Divertor topology (total flux expansion & secondary null)
  Detachment access & reduced sensitivity
Neutral baffling (similar neutral pressure CD & ED & SXD )
  Enables shaping benefits to be obtained
MAST-U + TCV
DLS prediction (calibrated to CD detachment onset)
Reduced models enable exploring balance exhaust benefits & engineering complexity
Core Greenwald fraction (%)
Detachment front (Lpol) (m)
Neutral baffling
Maximises plasma-neutr. Inter. & decouples divertor-core
Enables divertor shape detachment benefits
Preliminary
DLS: Relative , given , function of only geometry
Detachment front as function of only shape (DLS) [Lipschultz, 2017, NF; Cowley, 2023 NF; Myatra, 2023, NF]
Predicts detachment onset, window & sensitivity
Agrees with experiments
B 
X-point
Impurity
Radiation
Ionisation
Detachment

## Slide 24: Analysis: neutral buffer -> deepens detachment
Plasma parameters similar at same poloidal distance to X-point
Longer divertor legs ( ED & SXD ) + baffling
more ion sinks & mom. Losses -> deeper detachment
MAST-U
Novel Insights -> Novel Solutions
12
Ion sources / sinks
B 
h𝜈
h𝜈
B 
h𝜈
h𝜈
X-point
B 
B 
B 
B 
[N. Osborne, et al. 2025, NF]
[K. Verhaegh, et al. 2025, Commun. Phys.]
B 
B 
Detached -
Plasma-neutr.
Neutral baffling
Maximises plasma-neutr. Inter. & decouples divertor-core
Enables divertor shape detachment benefits
B 
B 
B 
B 
B 
B 
Detached -
Plasma-neutr.

## Slide 25: ADCs as understanding & model validation tool
WEST (>2025) See J. Harrison, et al.
Asdex Upgrade (>2025) See J. Harrison, et al.
MAST-U + TCV
ADC research can help tackling gaps in general power exhaust understanding & model validation
ITER and beyond
Example emissivity
[Wijkamp, 2023, NF]
Default rate
New rate
SOLPS-ITER simulations
[J. Karhunen, D. Moulton, et al.]
Example 2: ADC research highlighted errors plasma-neutral interactions exhaust modelling
Example 1: Validation of the importance of drifts in exhaust modelling
[E. Tonello, et al. this conference]
Validate importance of drifts in exhaust simulations
  Necessary to reproduce TCV results
Extrapolating reactor simulations (STEP) shows significant impact
Errors:
>200% ion sinks
200-800% dissociation
[K. Verhaegh, et al. 2025, Commun. Phys.]
Validation of the importance of including drifts exhaust modelling
[Verhaegh, et al. 2024, NF]

## Slide 26: Next steps: ADCs at reactor-relevant power
WEST (>2025) See J. Harrison, et al.
Asdex Upgrade (>2025) See J. Harrison, et al.
ADC configurations tested up to 20 MW input power (!) on ASDEX Upgrade
AUG
ADC geometries obtained (camera + magnetic reconstruction) – analysis underway
[D. Brida, et al. APS, 2025]
[T. Lunt, et al. IAEA Div Conc, 2025]
[B. Sieglin, et al. EPS, 2025]
Snowflake ADCs achieved at high power
Preliminary
Conventional
(upper single null)
Snowflake minus
(upper single null)
[Zammuto, et al. 2021, FED]
(See T. Lunt, et al. this conference)
MAST-U + TCV – up to 4-5 MW

## Slide 27: Next steps: ADCs at reactor-relevant power
WEST (>2025) See J. Harrison, et al.
Asdex Upgrade (>2025) See J. Harrison, et al.
Prepare for DTT to push ADCs to even higher power (42.5 MW)
DTT
DTT Timeline
[F. Crisanti, et al. 2024, Nucl. Fusion]
Now Construction
2029 Commissioning & test 17.5 MW
2034 Relevant-power studies 26.5 MW
2038 DEMO-like divertor test 42.5 MW
Divertor Test Tokamak (DTT) equilibria [DTT research plan]
ADC configurations tested up to 20 MW input power (!) on ASDEX Upgrade
MAST-U + TCV – up to 4-5 MW
ADC equilibria (EU-)DEMO [H. Reimerdes, et al. 2020, NF]

## Slide 28: Take away message
Tangible power exhaust benefits for reactors
  Not only limited to lower heat loads
  More flexibility for steady-state solution, exhaust control, transients, ….
We understand the physics of these benefits
  Continuum of ADCs provides these benefits
  Enable balancing engineering complexity and power exhaust benefits
Magnetic topology as a tool for model validation and general divertor optimisation
ADCs -> towards reactor implementation