## Slide 1: Hierarchy of turbulent transport models with the SOLEDGE3X code
H. Bufferand
M. Capasso, G. Ciraolo, H. Corvoysier, J. Denis, N. Fedorczak, Ph. Ghendrih, E. Havlíčková, D. S. de Oliveira, N. Rivals, S. Sureshkumar, P. Tamain, N. Varadarajan, Y. Marandet, R. Düll, I. Kudashev, F. Schwander, E. Serre, H. Yang and the TCV team
This work has been carried out within the framework of the EUROfusion Consortium, funded by the European Union via the Euratom Research and Training Programme (Grant Agreement No 101052200 — EUROfusion). Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the European Union or the European Commission. Neither the European Union nor the European Commission can be held responsible for them.

## Slide 2: Outline
Introduction to the hierarchy of turbulence models
Implementation in the SOLEDGE3X code
Application to TCV-X21 reference scenario

## Slide 3: Introduction to the hierarchy of turbulence models
1

## Slide 4: Example from the neutral fluid community
Underlying model: Navier-Stokes equations
Turbulence key properties (in 3D):
  Mixing effect
  Well characterized energy spectrum
Turbulence numerical modelling hierarchy:
Energy injection
(large scales)
Inertial range
(energy cascade)
Dissipation
(small scales)

## Slide 5: Example from the neutral fluid community
Underlying model: Navier-Stokes equations
Turbulence key properties (in 3D):
  Mixing effect
  Well characterized energy spectrum
Turbulence numerical modelling hierarchy:
Numerically resolved
Energy injection
(large scales)
Inertial range
(energy cascade)
Dissipation
(small scales)
DNS
Reynolds-Averaged Navier-Stokes
Large Eddy Simulation
Direct Numerical Simulation
Fidelity

## Slide 6: Example from the neutral fluid community
Underlying model: Navier-Stokes equations
Turbulence key properties (in 3D):
  Mixing effect
  Well characterized energy spectrum
Turbulence numerical modelling hierarchy:
Energy injection
(large scales)
Inertial range
(energy cascade)
Dissipation
(small scales)
Numerically
resolved
Model estimated
LES
Reynolds-Averaged Navier-Stokes
Large Eddy Simulation
Direct Numerical Simulation
Fidelity

## Slide 7: Example from the neutral fluid community
Underlying model: Navier-Stokes equations
Turbulence key properties (in 3D):
  Mixing effect
  Well characterized energy spectrum
Turbulence numerical modelling hierarchy:
Energy injection
(large scales)
Inertial range
(energy cascade)
Dissipation
(small scales)
Model estimated
RANS
Reynolds-Averaged Navier-Stokes
Large Eddy Simulation
Direct Numerical Simulation
Fidelity
Efficiency
Model used:
Empirical effective turbulent viscosity
Semi-empirical: , , RSM
Mean-field simulations
Turbulence simulations

## Slide 8: Hierachy of models in edge plasma community
Underlying model: Braginskii’s equations
Complex turbulence properties in strongly magnetized plasma
  Mixing effect (enhanced transport)
  Strong interaction between large scale flows and turbulent structures  transport barrier
Hierarchy of models for turbulence:
Models for effective turbulent diffusivities:
  Empirical: ad-hoc diffusivities to match experimental profiles
  Semi-empirical reduced models for turbulence:
 | Transport codes | Turbulence codes
Physical model | Mean-field (2D or 3D) Empirical or semi-empirical Multi-physics (neutrals, impurities…) | First principle modelling
Purposes | Experiment interpretation Plasma scenario design (exhaust) | Predictive modelling (, threshold…)
Examples | SOLPS-ITER, EDGE2D, EMC3, SONIC, SOLEDGE3X… | GBS, GRILLIX, HERMES-3, SOLEDGE3X…
 | Transport codes | Turbulence codes
Physical model | Mean-field (2D or 3D) Empirical or semi-empirical Multi-physics (neutrals, impurities…) | First principle modelling
Purposes | Experiment interpretation Plasma scenario design (exhaust) | 
Examples | SOLPS-ITER, EDGE2D, EMC3, SONIC, SOLEDGE3X… | GBS, GRILLIX, HERMES-3, SOLEDGE3X…
SOLEDGE3X ITER transport simulation [Rivals et al., Nucl. Fusion 65, 2025]
SOLEDGE3X WEST turbulent simulation [Bufferand et al. Nucl. Fusion 61, 2021]
    Two equations models:
      [Baschetti et al., Nucl. Fusion 61(2021)]
      [Coosemans et al., Contrib. Plasma Phys. 60 (2020)]
    Predator-Prey models [Miki et al., Phys. Plasmas 19 (2012)]
    …

## Slide 9: Implementation in the SOLEDGE3X code
2

## Slide 10: SOLEDGE3X: a versatile fluid code for edge plasma modelling
Drift-fluid code based on Braginskii’s equations with Zhdanov closure terms for multi-component plasma
Up to the first wall modelling thanks to immersed boundary conditions
Kinetic neutrals via coupling with EIRENE
Applications: 2D/3D transport AND 3D turbulent simulations
More info: www.soledge3x.com
Example of application to turbulent simulation of a Deuterium & Carbon plasma on TCV
Neutrals simulated with EIRENE
Radiation by sputtered carbon

## Slide 11: Reduced -equation turbulence model for mean-field simulations
One equation model based on estimating turbulent kinetic energy
Effective turbulent diffusivity proportional to :
Drive governed by interchange growth rate:
Saturation set empirically with scaling law:
  at fixed point:
  SOL width by vs balance:
linear drive
non-linear saturation
and for a TCV case from [Baschetti et al., NME 19 (2019)]

## Slide 12: Application to the TCV-X21 reference scenario
3

## Slide 13: The TCV-X21 experiment
  TCV-X21 = set of shots on TCV for edge turbulence codes confrontation
    Deuterium Ohmic L-mode, lower single-null
    Low magnetic field for lower
    Low density, targeting sheath-limited regime
Parameter | Value
Parameter | Value
  Main results in [D.S Oliveira, T. Body et al., Nucl. Fusion 62 (2022)]
    Public experimental dataset on https://github.com/SPCData/TCV-X21
TCV-X21 magnetic configuration and main edge diagnostics.

## Slide 14: The TCV-X21 benchmark
  Experimental dataset used to benchmark edge turbulence codes [D.S Oliveira, T. Body et al., Nucl. Fusion 62 (2022) & pre-print arXiv:2506.12180]
    GBS
    GRILLIX
    TOMAK3X
    HERMES-3
  Rather good agreement with mid-plane profile measurements – discrepancies in the divertor
  TCV-X21 plasmas simulated with SOLPS-ITER
  [Wang et al., Nucl. Fusion 64 (2024)]
Comparison between turbulence code simulations of a TCV-X21 shot – poloidal map of the density. On the left panel, the green and blue shaded areas display the particle and energy source respectively. Figure from [Oliveira et al, Nucl Fusion 62 (2022)].
 No Neutrals !
Comparison between RDPA density measurements and simulations

## Slide 15: SOLEDGE3X turbulence models vs TCV-X21
Simulation set-ups:
  Grids based on TCV #51333
    Coarse grid for mean-field simulation
    Fine grid for turbulent simulation
  EIRENE for neutrals
  Gas puff feedback to get
  Power source set to
 | Case 1 |  | Case 2 | Case 3
Type | 2D transport |  | 2D transport | 3D turbulent
Turbulent model | Empirical |  | -model | First-principle (ES)
Plasma composition | D | D+C | D | D
Grid points |  |  |  | 
CPU time | 1 day on 48 CPUs |  | 1 day on 48 CPUs | 2 month on 1024 CPUs
 | Case 1 |  | Case 2 | Case 3
Type | 2D transport |  | 2D transport | 3D turbulent
Turbulent model | Empirical |  |  | First-principle (ES)
Plasma composition | D | D+C | D | D
Grid points |  |  |  | 
CPU time | 1 day on 48 CPUs |  | 1 day on 48 CPUs | 2 month on 1024 CPUs
Coarse grid used for mean-field simulations. Left: quadrangles grid for SOLEDGE3X, right: triangles grid for EIRENE.

## Slide 16: Case1: Empirical mean-field modelling
Inputs: Thomson Scattering profiles (remapped at mid-plane)
Estimations from HRTS mid-plane data
Quantity | Experimental Value
Quantity | Experimental Value

## Slide 17: Case1: Empirical mean-field modelling
Estimations from HRTS mid-plane data
Inputs: Thomson Scattering profiles (remapped at mid-plane)
Outputs: Ad-hoc empirical diffusivities found by the automated procedure to fit experimental radial profiles 
  Quite complex radial variations with amplitude ranging over 1 order of magnitude, hard to guess a priori!
Quantity | Experimental Value
Quantity | Experimental Value

## Slide 18: Case1: Empirical mean-field modelling
Outputs: target profiles, divertor plasma properties
RDPA: Experiment vs SOLEDGE3X simulation
Electron density
Electron temperature
Fit:
Quantity | Experimental Value
Quantity | Experimental Value
Simulation results | 
Pure D | With Carbon
Simulation results | 
Pure D | With Carbon
Pure D

## Slide 19: Case1: Empirical mean-field modelling
Outputs: target profiles, divertor plasma properties
Quantity | Experimental Value
Quantity | Experimental Value
RDPA: Experiment vs SOLEDGE3X simulation
Electron density
Electron temperature
Simulation results | 
Pure D | With Carbon
Simulation results | 
Pure D | With Carbon
Fit:
With Carbon
Fit:

## Slide 20: Case1: Empirical mean-field modelling
Predictability
low – lot of free parameters
Experiment matching
multi-physics + fitting procedure
Numerical cost
cheap 1 day on 48CPUs
Numerical cost
cheap ∼ 1 day on 48CPUs
Predictability
low – lot of free parameters
Experiment matching
multi-physics + fitting procedure

## Slide 21: Case2: Semi-empirical mean-field modelling: k-model
Inputs:
  Heating power [ – 50/50 ion/electron channel]
  (used to tune gas puff rate)
Outputs: Map of turbulent kinetic energy computed with the k-model:
  Low field side ballooning
  Turbulence along LFS divertor leg
Profiles:
  profile OK but profile too flat
  overestimated  TCV-X21 not on the scaling law used to close the semi-empirical model!
 | TCV-X21 | Scaling () | Simulation
Value (mm) | 4.1 | 11 | 7.1
 | TCV-X21 |  | Simulation
Value (mm) | 4.1 | 11 | 7.1
Fit:
Fit:

## Slide 22: Case2: Semi-empirical mean-field modelling: k-model
Predictability
improved – less free parameters
Experiment matching
decent / rely on model hypothesis
Numerical cost
cheap 1 day on 48CPUs
Numerical cost
cheap ∼ 1 day on 48CPUs
Predictability
improved – less free parameters
Experiment matching
decent / rely on model hypothesis

## Slide 23: Case3: First principle simulations
  Enable direct comparison with turbulence measurements
   e.g.: Characterization of divertor localised filaments
Sketch of the gas puff imaging diagnostic on TCV. Figure from [Wütrich et al., Nucl. Fusion 62 (2022)]
Experimental data:
Normalized brightness Video from [Wütrich et al., Nucl. Fusion 62 (2022)]
Simulation data:
Deuterium atom radiation (W/m3)
[Bufferand et al., NME 41 (2024)]

## Slide 24: Case3: First principle simulations
Inputs:
  Heating power [ – 50/50 ion/electron channel]
  (used to tune gas puff rate)
Outputs:
  SOL profiles
  Turbulence pdf, filament size and velocity…
  prediction (OK w.r.t. experiment)
Experiment
Simulation
Density
Temperature

## Slide 25: Case3: First principle simulations
Inputs:
  Heating power [ – 50/50 ion/electron channel]
  (used to tune gas puff rate)
Outputs:
  SOL profiles
  Turbulence pdf, filament size and velocity…
  prediction (OK w.r.t. experiment)
Fit:
Good agreement on (midplane) – overestimation of at the divertor targets
Rather good agreement on in the SOL but too hot – good agreement at the divertor targets
Quantity | Experimental Value
Quantity | Experimental Value
Simulation results
122
Simulation results
122

## Slide 26: Case3: First principle simulations
Predictability
No free parameter
Experiment matching
OK if multi-physics (neutrals, impurities…)
Numerical cost
Heavy 2 months on 1024 CPUs
Numerical cost
Heavy ∼ 2 months on 1024 CPUs
Predictability
No free parameter
Experiment matching
OK if multi-physics (neutrals, impurities…)

## Slide 27: Conclusions and discussions
Hierarchy of turbulence models required to address wide range of edge-plasma modelling application
  Pros and cons of each approach
 | Empirical | K-model | 1st principles
Predictability |  |  | 
Accuracy |  |  | 
Cost |  |  | 
Cross-fertilization between the different approaches:
  1st principles simulations  data for developing reduced models
  Mean-field simulations  converge particle balance (long time scale): starting point for turbulent simulations / needed to address larger tokamaks
Multiphysics necessary for detailed comparison with experiments (neutrals, impurities…)
Push for increasing open database for benchmarking / code validation
  Same exercise in detached conditions (TCV-X23 [V. Quadri et al., Nucl. Mat. Energy 41 (2024)])
  H-mode plasmas

## Slide 28: Backup

## Slide 29: RDPA summary
Electron temperature
Electron density
Experiment | Case1 Empirical |  | Case2 k-model | Case3 1st principles
 | D | D+C | D | D

## Slide 30: Time scales of transport and turbulence simulations taking into account neutral physics
  Challenge: Time scale to reach Quasi-Steady-State with neutrals
  Time scales at play:
    = Turbulence time scale: time for turbulent structures to develop Interchange growth rate 
    = Transport time: time for a plasma quantity (particle/energy) to travel from the source to the sink (wall):
    = Particle and energy balance: time to equilibrate net sources with net sinks (e.g. energy injected = energy deposited / gas puff = pumped flow) 
 Recycling
Impurity content radiation balance
Turbulence
Transport
Energy balance
Particle balance
Turbulence
Transport
Energy balance
Particle balance
Time scales
23/09/2025
G. Ciraolo – 21st European Fusion Theory Conference – Aix en Provence