## Slide 1
Integrated Modelling Activities
in Support of the ITER Re-Baseline
15 October 2025
M. Schneider1, J. Artola1, X. Bonnin1, M. Dubrov1, Y. Gribov1, W. Helou1, O. Hoenen1,
S-H. Kim1, F. Köchl1, S. Korving1, E. Lerche2, A. Loarte1, S.D. Pinches1, R.A. Pitts1,
A.R. Polevoi1, M. Preynas1, A. Pshenov1, N. Schwarz1, J. Stober3, P. Vincenzi4,5, T. Wauters1
1 ITER Organization, St. Paul-lez-Durance Cedex, France
2 ERM/KMS, Brussels, Belgium
3 Max-Planck-Institut für Plasmaphysik, Garching, Germany
4 Consorzio RFX, Padova, Italy
5 Institute for Plasma Science and Technology, Padova, Italy
The views and opinions expressed herein do not necessarily reflect those of the ITER Organization
This work has been supported by the ITER Scientist Fellow Network
© 2025, ITER Organization

## Slide 2
The ITER new baseline
  Change of FW material Beryllium (Be)  Tungsten (W)
   New operational phases
      New staged approach
      New scenarios
   New plant (system) configuration
      First Wall (FW)
      Heating and Current Drive (H&CD) mix
      Boronization system
  How do we make these choices?
    Observations from current-day experiments
    Integrated Modelling (IM) activities  the topic of this talk!
  More details in this morning talks:
    Siwoo Yoon "2024 baseline" 15/10 10:40
    Alberto Loarte "BeW in new baseline" 15/10 11:00
SRO (Start of Research Operation)

## Slide 3
Modelling studies for the new baseline
  Disruption loads and mitigation
  Boronization system
  W source from the wall
  New heating mix
  EL
  EL
  The new baseline implies:
  Extra W source from the wall
   Modelling of W source & transport
  New Heating and Current Drive mix
   Modelling impact of H&CD on W
  Boronization system
   Modelling for optimal configuration
  Disruption mitigation strategy
   State-of-the-art 2D-3D modelling
  All possible through the IMAS Integrated Modelling & Analysis Suite!
1)
2)
3)
  Alberto Loarte "BeW in new baseline" 15/10 11:00

## Slide 4
Outline
  Developing the ITER Integrated Modelling platform IMAS
  Effect of extra W wall source on ITER plasma performance
  Characterization and mitigation of disruption
  Conclusion

## Slide 5
Outline
  Developing the ITER Integrated Modelling platform IMAS
  Effect of extra W wall source on ITER plasma performance
  Characterization and mitigation of disruption
  Conclusion

## Slide 6
How to best foster collaboration and teamwork?
Develop a standard to be used by the whole community
Provide the necessary support and training material
Share experience, methods, tools
Promote it and get the community to contribute to it
ITPAs,
conferences, workshops,
ISFN, IMEG, etc.
Encourage the community to do the same
Make the software open-source
https://github.com/iterorganization
2024 Baseline of the
ITER Research Plan
IMAS platform
New Baseline

## Slide 7
Towards self-consistent wall-SOL-edge-core modelling?
  JINTRAC = JETTO-SANCO+EDGE2D-Eirene
  DINA-JINTRAC: High Fidelity Plasma Simulator (HFPS)
   ITER workhorse for core-edge integrated modelling!
  S.H. Kim "HFPS" 17/10 14:00
 | Source / transport |  |  | 
Wall | WallDYN2D, WallDYN3D, DIVIMP ERO, ERO2 MEMOS-U, MEMENTO |  |  | 
 | Source / transport
Wall | WallDYN2D, WallDYN3D, DIVIMP ERO, ERO2 MEMOS-U, MEMENTO
SOL/divertor | SOLPS-ITER EMC3-Eirene EDGE2D-Eirene
 | Source / transport | 
Wall | WallDYN2D, WallDYN3D, DIVIMP ERO, ERO2 MEMOS-U, MEMENTO | 
SOL/divertor | SOLPS-ITER EMC3-Eirene EDGE2D-Eirene | JINTRAC
Core/Pedestal | JETTO-SANCO DINA ASTRA CORSICA METIS | 
 | Source / transport |  |  | 
Wall | WallDYN2D, WallDYN3D, DIVIMP ERO, ERO2 MEMOS-U, MEMENTO |  |  | 
SOL/divertor | SOLPS-ITER EMC3-Eirene EDGE2D-Eirene | JINTRAC | Transient transport | Runaway Electrons
Core/Pedestal | JETTO-SANCO DINA ASTRA CORSICA METIS |  | JOREK | DREAM
Goal: to predict full dynamics of temperature, density, rotation and current from the wall to the core

## Slide 8
Outline
  Developing the ITER Integrated Modelling platform IMAS
  Effect of extra W wall source on ITER plasma performance
  Characterization and mitigation of disruption
  Conclusion

## Slide 9
Tungsten transport
  Which mechanisms lead to W accumulation?
  W particle flux:
  Diffusion
= W density
  Neoclassical: induced by collisions
  Turbulent: induced by microscopic instabilities
  Neoclassical
D. Fajardo, PPCF 67 (2025) 015020
  Neoclassical
  Turbulent
  Turbulent
  H-mode 5MA / 2.65T
  H-mode 7.5MA / 2.65T
  Convection
  Pedestal
  Pedestal

## Slide 10
How does tungsten travel to the plasma core?
  Mechanisms leading to W transport:
 | SOL | Edge / Pedestal | Core
 | Transport assumed turbulent | Competition turbulent / neoclassical | 
Today's devices |  | : dominant inwards neoclassical pinch Efficient W exhaust with small ELMs | L-mode: low confinement, high core-edge transport (no barrier), low power  More Cw in H-mode
ITER (+ high Ti JET) |  | : outwards neoclassical pinch W screening in H-mode ELMs induce higher W core accumulation | L-mode: more neoclassical transport, locally high W radiative losses H-mode: dominant turbulent transport  More Cw in L-mode
 | SOL | Edge / Pedestal | Core
 | Transport assumed turbulent | Competition turbulent / neoclassical | 
Today's devices |  |  | L-mode: low confinement, high core-edge transport (no barrier), low power  More Cw in H-mode
ITER (+ high Ti JET) |  |  | L-mode: more neoclassical transport, locally high W radiative losses H-mode: dominant turbulent transport  More Cw in L-mode

## Slide 11
W source and transport in ITER L-mode plasmas
X-point at
t = 10 s
DINA
JINTRAC
prescribed to DINA
Realistic divertor source
Ad-hoc wall source
Diverted
phase
SOLPS-ITER
To DINA source model
Limiter
phase
High TSOL
W sputtering
Cw
Prad,core
Lower TSOL
Lower
sputtering
Lower
Prad,core
 Self-regulated mechanism
 Thermal stabilization
... But how do we avoid W radiative collapse in this early ramp-up phase?
SRO L-mode, 15 MA / 5.3 T H plasma
Highest risk of W radiative collapse in limiter phase
Lower
Cw
(No Ne seeding)
R. Pitts et al., NME 42 (2025) 101854
Core
Edge
Yanjie Zhang's NF 65 (2025) 056035
PLCFS
Lower PLCFS

## Slide 12
W source and transport in ITER L-mode plasmas
Prad
Prad
Radiative collapse!
JINTRAC using GRAY
  How do we avoid W radiative collapse in the early ramp-up phase?
    With central ECH
     Te rise  Increased heat turbulent transport  Outwards convective W flux
  With density tailoring
   Flattened or hollow density profile  Increased outwards W turbulent transport
  With Low-Z impurity injection (Neon)
   Cool down plasma edge  Reduced W sputtering
Central ECH
Off-axis ECH
Te
Ti
Te
Ti
R. Pitts et al., NME 42 (2025) 101854

## Slide 13
W source and transport in ITER ELM-free H-mode plasmas
  ELMs to be suppressed for to not melt W monoblocks  No ELM in simulations
  Restricted EDGE2D-Eirene grid in JINTRAC  Wall source to be provided externally
DIVIMP+WallDYN2D
DT baseline 15 MA / 5.3 T
High Ne seeding case
W wall influx and penetration to near-SOL region
   W dominated by Ne sputtering and W self-sputtering
  (low CXN-induced sputtering)
JINTRAC
  Confirmed by more self-consistent preliminary results with SOLPS-ITER + ERO2 + JINTRAC
  In the future to come: EMC3-Eirene|SOLEDGE3X + ERO2|WallDYN3D + JINTRAC

## Slide 14
W source and transport in ITER ELMy H-mode plasmas
  Integrated modelling of W source and ELM control for SRO H-mode conditions (40 MW ECH): SOLPS+JINTRAC
    W gross divertor source (+ prompt redep.): SOLPS
    W gross wall source: 10% of divertor source
SOLPS
0.95
0.80
0.90
0.95
0.90
0.85
PAUX = 30 MW
PAUX = 20 MW
JINTRAC
Electron density
W density
  ELM-averaged approach (continuous ELM model for pedestal)
   H-mode resilient to W influx due to W neoclassical screening
  and to high core Te0  Prad~ 25% even for
  Full-ELM resolved* approach: Prad ~ 18% but instantaneous Prad~15 MW  Robust ELM control needed!
  (*Simplified ELM model; for high fidelity: JOREK)
Divertor source
Wall source

## Slide 15
Outline
  Developing the ITER Integrated Modelling platform IMAS
  Effect of extra W wall source on ITER plasma performance
  Characterization and mitigation of disruption
  Conclusion

## Slide 16
Disruption loads and mitigation
  2D disruption modelling:
  DINA (scenario) + SMITER (power load on FW)
  + MEMOS-U (FW melt motion)
   Need to direct disruption upwards to preserve divertor
   JOREK: possible with VS coils a few 10ms before TQ
  3D non-linear MHD modelling:
  JOREK  Marginal W FW melting from unmitigated disruptions at 15 MA
  [J. Artola "Thermal loads during VDE" 18/10 8:30]
  RE damage assessment:
  DINA/JOREK (RE loading) + Geant4 (RE vol. depos.)
  + MEMENTO (heat transfer to FW)
   W tiles to be thickened to 12mm in localized areas
  RE mitigation:
  DREAM  SPI of H or Ne can lead to acceptable RE currents
  except in DT 15 MA plasmas (T β decay and Compton scattering from wall γ's)
DINA+SMITER+MEMOS-U
N. Schwarz et al, EPS 2025

## Slide 17
Outline
  Developing the ITER Integrated Modelling platform
  Effect of extra W wall source on ITER plasma performance
  Characterization and mitigation of disruption
  Conclusion

## Slide 18
Conclusion
  Substantial IM effort to support the new re-baseline
  IMAS tools continuously developed to achieve self-consistent modelling of
  physics processes from the wall to the plasma core
  Many models & assumptions successfully validated on present
  experiments to support the ITER new baseline
  Improvements required such as extending models to higher fidelity to
  refine ITER predictions
   Requires the involvement of the international fusion community through
  sharing of state-of-the-art models
   Facilitated when models publicly available for worldwide contributions
  by fusion experts
   Drive for new open-source software campaign launched by IO

## Slide 19
Backup slides

## Slide 20
  Users feedback
   Adapt the tools to the user needs!
  Intermediate results
   Already help defining the ITER new baseline!
 The agile approach is the one adopted to develop the ITER Integrating Modelling platform:
Developing the ITER Integrated Modelling platform
  Iterative process: fosters teamwork and flexibility
  Short planning cycles
  Appropriate when requirements evolve
Requirements
Design
Maintenance
Delivery
Development
Agile
approach!
Requirements
Design
Development
Delivery
Maintenance
  Linear: each phase to finish before next one starts
  Long-term planning cycles
  Appropriate with fixed requirements
Waterfall approach?

## Slide 21
Integrated Modelling
  What is Integrated Modelling?
  Integrated modelling combines multiple models into a single framework
  What is a framework?
  A framework is a structured environment (tools, methods, standards) to connect models together
  How do we connect models together?
   The two routes have been taken to produce the results shown in this presentation.
  Until workflows are ready: externally prescribe the result of a model into another one
  Ideally: by building self-consistent simulation workflows

## Slide 22
The ITER new baseline
SRO
Start of Research Operation
H, D plasmas
H-mode in D
(5-7.5MA / 2.65T)
L-mode in H
at full
(15 MA / 5.3T)
ECH 40 MW
ICH 10 MW
Inertially cooled FW
27 months
IC-I
(~18m)
DT1
Fusion Power Operation 1
H, D, DT plasmas
and
for 300-500s
Neutron budget:
ECH 60-67 MW
ICH 10-20 MW
NBI 33 MW
Water-cooled FW
IC-II
(~10m)
5 x 2 years
DT2
Fusion Power Operation 2
DT plasmas
Long pulse, steady-state
for 1000-3000s
Neutron budget:
ECH 60-67 MW
ICH 10-20 MW
NBI 49.5 MW
Water-cooled FW
IC-III
(TBD)
TBD

## Slide 23
Why is tungsten detrimental for fusion plasma performance?
  Tungsten (W) accumulated in the core significantly increases radiation losses
  Lawson criterion fulfilled when heating compensates for energy losses  Minimum for ignition
   The operational space to get plasma ignition is considerably reduced when the W concentration increases.
T. Pütterich et al, NF 50 (2010) 025012
  = Plasma density
  = Plasma temperature
  = Energy confinement time
  = Helium confinement time
  = W concentration

## Slide 24
ELM control strategies
  ELM pacing: 27 ELM coils + 4 pellet injectors
    If inwards W transport and peaked edge W profiles (today's devices)  Efficient W exhaust with ELMS
    If dominant W screening and hollow edge W profiles (ITER)  Inwards W flux from ELMs
  Higher wall clearance:
    Reduces ELMs but degrades plasma vertical stability
     Increase current in VS coils ( in SRO 5 MA/2.65 T)
     Adjust plasma shape and ne (to preserve pedestal)
  Caveat: 3D fields affect W edge neoclassical transport:
    With inwards pinch (today's devices)
     Enhanced outwards W transport
    With W edge screening (ITER)
     Reduced outwards W transport  W core accumulation
   Balance needed to preserve pedestal with 3D ELM control
ExB drift
Perturbed potential
S. Korving et al, submitted to NF (2025)
X. Bai et al, PPCF 66 055017 (2024)
large
outer wall gap
normal clearance
increased clearance
SRO H-mode
5 MA / 2.65T
MARS-F
JOREK