## Slide 1
MULTI-MACHINE VALIDATION OF PLASMA INITIATION MODELLING AND PROSPECTS FOR FUTURE DEVICES
Hyun-Tae Kim (MAST-U), Runze Chen (EAST), James Yang (DIII-D), Youngsun Lee (KSTAR), Jeongwon Lee (KSTAR), and Hongsik Yoon (VEST)
30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China

## Slide 2: contents
Motivation
Experiment database
DYON code and simulation setup
Multi-machine validation results
Prediction to ITER
Summary

## Slide 3: Inductive plasma initiation in tokamaks: Townsend breakdown and plasma burn-through
Gas
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China

## Slide 4: Inductive plasma initiation in tokamaks: Townsend breakdown and plasma burn-through
Gas
A few %
ionisation
Townsend breakdown phase
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
B. Lloyd PPCF 38 (1996) 1627
P. C. de Vries Nucl. Fusion 59 (2019) 096043

## Slide 5: Inductive plasma initiation in tokamaks: Townsend breakdown and plasma burn-through
# of ionisations while an electron traveling in 1 meter
Gas
A few %
ionisation
Townsend breakdown phase
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
B. Lloyd PPCF 38 (1996) 1627
P. C. de Vries Nucl. Fusion 59 (2019) 096043

## Slide 6: Inductive plasma initiation in tokamaks: Townsend breakdown and plasma burn-through
# of ionisations while an electron traveling in 1 meter
Gas
A few %
ionisation
Townsend breakdown phase
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
B. Lloyd PPCF 38 (1996) 1627
P. C. de Vries Nucl. Fusion 59 (2019) 096043

## Slide 7: Inductive plasma initiation in tokamaks: Townsend breakdown and plasma burn-through
# of ionisations while an electron traveling in 1 meter
Electrons and neutrals exist together in the burn-through phase
Ohmic heating VS Energy loss from radiation and charge exchange
Gas
A few %
ionisation
100%
ionisation
Townsend breakdown phase
Plasma burn-through phase
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
B. Lloyd PPCF 38 (1996) 1627
P. C. de Vries Nucl. Fusion 59 (2019) 096043

## Slide 8: Inductive plasma initiation in tokamaks: Townsend breakdown and plasma burn-through
# of ionisations while an electron traveling in 1 meter
Electrons and neutrals exist together in the burn-through phase
Ohmic heating VS Energy loss from radiation and charge exchange
Te[eV]
Degree of
Ionization[%]
100
0
~10
0
Gas
A few %
ionisation
100%
ionisation
Townsend breakdown phase
Plasma burn-through phase
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
B. Lloyd PPCF 38 (1996) 1627
P. C. de Vries Nucl. Fusion 59 (2019) 096043

## Slide 9: Inductive plasma initiation in tokamaks: Townsend breakdown and plasma burn-through
# of ionisations while an electron traveling in 1 meter
Electrons and neutrals exist together in the burn-through phase
Ohmic heating VS Energy loss from radiation and charge exchange
Te[eV]
Prad[W]
~105
0
Degree of
Ionization[%]
100
0
~10
D radiation barrier
0
Gas
A few %
ionisation
100%
ionisation
Townsend breakdown phase
Plasma burn-through phase
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
B. Lloyd PPCF 38 (1996) 1627
P. C. de Vries Nucl. Fusion 59 (2019) 096043

## Slide 10: Inductive plasma initiation in tokamaks: Townsend breakdown and plasma burn-through
# of ionisations while an electron traveling in 1 meter
Electrons and neutrals exist together in the burn-through phase
Ohmic heating VS Energy loss from radiation and charge exchange
Te[eV]
Prad[W]
~105
0
Degree of
Ionization[%]
100
0
~10
D radiation barrier
0
Gas
A few %
ionisation
100%
ionisation
Townsend breakdown phase
Plasma burn-through phase
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
B. Lloyd PPCF 38 (1996) 1627
P. C. de Vries Nucl. Fusion 59 (2019) 096043

## Slide 11: Tokamak operation for inductive plasma initiation
Magnetic field null configuration is required to maximise the connection length.

## Slide 12: Tokamak operation for inductive plasma initiation
Magnetic field null configuration is required to maximise the connection length.

## Slide 13: Tokamak operation for inductive plasma initiation
Magnetic field null configuration is required to maximise the connection length.

## Slide 14: Tokamak operation for inductive plasma initiation
Magnetic field null configuration is required to maximise the connection length.

## Slide 15: Tokamak operation for inductive plasma initiation
Magnetic field null configuration is required to maximise the connection length.

## Slide 16: Goal of plasma initiation modelling
p0 and
p0 and

## Slide 17: Goal of plasma initiation modelling
p0 and
p0 and
Vloop=5.3V
Vloop=4.9V

## Slide 18: Goal of plasma initiation modelling
p0 and
p0 and
Vloop=5.3V
Vloop=4.9V

## Slide 19: Goal of plasma initiation modelling
p0 and
p0 and
Vloop=5.3V
Vloop=4.9V

## Slide 20: Goal of plasma initiation modelling
DYON
p0 and
p0 and
Vloop=5.3V
Vloop=4.9V
DYON

## Slide 21: Goal of plasma initiation modelling
DYON
p0 and
p0 and
Vloop=5.3V
Vloop=4.9V
DYON
Plasma initiation phase is the most dynamic phase in the whole tokamak pulse.
Tokamak hardware determines the operational constraints:
  Coil design: Icoil limit
  Power supply design : dIcoil/dt limit
  Vessel conductivity: eddy currents
  Vacuum volume: required p0
For a new tokamak design, the feasibility of plasma initiation with the operational constraints should be ensured with predictive modelling.
This is particularly important for large superconducting devices such as ITER and STEP, as the plasma initiation will be challenging.

## Slide 22: contents
Motivation
Experiment database
DYON code and simulation setup
Multi-machine validation results
Prediction to ITER
Summary

## Slide 23: Devices for multimachine validation
Device | Aspect ratio | Coils | First wall material | Ferromagnetic material | Vv[m3] | Vp[m3] | Bt[T] | Lf[m]
MASTU | Spherical Torus (R=0.7m, a=0.5m) | Copper | Carbon | N/A | 55 | 6 | 0.6 | 75
EAST | Conventional Tokamak (R=1.85m, a=0.5m) | Super Conductor | Tungsten + Molybdenum | N/A | 38 | 7.5 | 2.5 | 311
DIIID | Conventional Tokamak (R=1.67m, a=0.65m) | Copper | Carbon | N/A | 35 | 16 | 1.8 | 292
KSTAR | Conventional Tokamak (R=1.8m, a=0.7m) | Super Conductor | Carbon | Incoloy 908 in the jacket of PF and TF coils | 55 | 5 | 1.8 | 315
VEST | Spherical Torus (R=0.3m, a=0.2m) | Copper | Stainless steel | N/A | 3.7 | 0.6 | 0.23 | 12

## Slide 24: Parameter scan experiments to identify plasma initiation operation space
  Loop voltage
  Prefill gas pressure
O
O
O
O
O
O
O
O
O
O
O
O
O
Successful plasma initiation
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China

## Slide 25: Parameter scan experiments to identify plasma initiation operation space
  Loop voltage
  Prefill gas pressure
O
O
O
X
O
O
O
X
O
X
X
X
X
O
O
O
O
O
Successful breakdown
but failed burn-through
(strong Dalpha but no Ip ramp-up)
O
Successful plasma initiation
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China

## Slide 26: Parameter scan experiments to identify plasma initiation operation space
  Loop voltage
  Prefill gas pressure
O
O
O
X
X
O
O
O
X
O
X
X
X
X
X
O
O
O
X
O
O
Paschen curve?
Successful breakdown
but failed burn-through
(strong Dalpha but no Ip ramp-up)
O
X
Failed breakdown
(no or very weak Dalpha)
Successful plasma initiation
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China

## Slide 27: Parameter scan experiments to identify plasma initiation operation space
  Loop voltage
  Prefill gas pressure
O
O
O
X
X
O
O
O
X
O
X
X
X
X
X
O
O
O
X
O
O
Paschen curve?
Successful breakdown
but failed burn-through
(strong Dalpha but no Ip ramp-up)
O
X
Failed breakdown
(no or very weak Dalpha)
Successful plasma initiation
MAST-U
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
Hyun-Taen Kim et al 2024 Nucl. Fusion 64 (2024) 126010

## Slide 28: Operation space in experiments
Hong-Sik Yun et al 2023 29th IAEA Fusion Energy Conference p [TH-C/1906]
Runze Chen et al, Nucl. Fusion 65 (2025) 076043
James Yang et al, Nucl. Fusion, submitted
Jeongwon Lee, et al 2025 4th iFPC
Hyun-Taen Kim et al Nucl. Fusion 64 (2024) 126010

## Slide 29: Operation space in experiments
The hypothesis is valid for all devices.
Failed burn-through at high p0
Failed burn-through at low Vloop
Hong-Sik Yun et al 2023 29th IAEA Fusion Energy Conference p [TH-C/1906]
Runze Chen et al, Nucl. Fusion 65 (2025) 076043
James Yang et al, Nucl. Fusion, submitted
Jeongwon Lee, et al 2025 4th iFPC
Hyun-Taen Kim et al Nucl. Fusion 64 (2024) 126010

## Slide 30: Operation space in experiments
The hypothesis is valid for all devices.
Failed burn-through at high p0
Failed burn-through at low Vloop
Failed breakdown at low p0
Hong-Sik Yun et al 2023 29th IAEA Fusion Energy Conference p [TH-C/1906]
Runze Chen et al, Nucl. Fusion 65 (2025) 076043
James Yang et al, Nucl. Fusion, submitted
Jeongwon Lee, et al 2025 4th iFPC
Hyun-Taen Kim et al Nucl. Fusion 64 (2024) 126010

## Slide 31: Operation space in experiments
The hypothesis is valid for all devices.
Failed burn-through at high p0
Failed burn-through at low Vloop
Failed breakdown at low p0
The conventional Townsend assessment with Lf (i.e. αLf > 1) over-predicts the lower limit of p0 for plasma breakdown.
Hong-Sik Yun et al 2023 29th IAEA Fusion Energy Conference p [TH-C/1906]
Runze Chen et al, Nucl. Fusion 65 (2025) 076043
James Yang et al, Nucl. Fusion, submitted
Jeongwon Lee, et al 2025 4th iFPC
Hyun-Taen Kim et al Nucl. Fusion 64 (2024) 126010

## Slide 32: contents
Motivation
Experiment database
DYON code and simulation setup
Multi-machine validation results
Prediction to ITER
Summary

## Slide 33: Effective prefill gas pressure
Prefill gas pressure p0 is an essential input for predictive plasma initiation modelling.
Sufficiently high p0 is required for Townsend breakdown.
Sufficiently low Vv*p0 is required for plasma burn-through.

## Slide 34: Effective prefill gas pressure
Prefill gas pressure p0 is an essential input for predictive plasma initiation modelling.
Sufficiently high p0 is required for Townsend breakdown.
Sufficiently low Vv*p0 is required for plasma burn-through.
However, raw data requires calibration.
Fast ion gauge calibration is often inaccurate.

## Slide 35: Effective prefill gas pressure
Prefill gas pressure p0 is an essential input for predictive plasma initiation modelling.
Sufficiently high p0 is required for Townsend breakdown.
Sufficiently low Vv*p0 is required for plasma burn-through.
However, raw data requires calibration.
Fast ion gauge calibration is often inaccurate.
Measured values vary at different locations of the fast ion gauges.
James Yang et al, submitted to Nucl. Fusion (2025)

## Slide 36: Effective prefill gas pressure
Prefill gas pressure p0 is an essential input for predictive plasma initiation modelling.
Sufficiently high p0 is required for Townsend breakdown.
Sufficiently low Vv*p0 is required for plasma burn-through.
However, raw data requires calibration.
Fast ion gauge calibration is often inaccurate.
Measured values vary at different locations of the fast ion gauges.
Effective prefill gas pressure = p0 coefficient x fast ion gauge data.
James Yang et al, submitted to Nucl. Fusion (2025)

## Slide 37: Effective prefill gas pressure
Prefill gas pressure p0 is an essential input for predictive plasma initiation modelling.
Sufficiently high p0 is required for Townsend breakdown.
Sufficiently low Vv*p0 is required for plasma burn-through.
However, raw data requires calibration.
Fast ion gauge calibration is often inaccurate.
Measured values vary at different locations of the fast ion gauges.
Effective prefill gas pressure = p0 coefficient x fast ion gauge data.
The strategy to validate the operating space prediction capability in DYON:
Determine the p0 coefficient that reproduces a representative discharge in each device
Use the same p0 coefficient for all other discharges
James Yang et al, submitted to Nucl. Fusion (2025)

## Slide 38: Effective prefill gas pressure
Prefill gas pressure p0 is an essential input for predictive plasma initiation modelling.
Sufficiently high p0 is required for Townsend breakdown.
Sufficiently low Vv*p0 is required for plasma burn-through.
However, raw data requires calibration.
Fast ion gauge calibration is often inaccurate.
Measured values vary at different locations of the fast ion gauges.
Effective prefill gas pressure = p0 coefficient x fast ion gauge data.
The strategy to validate the operating space prediction capability in DYON:
Determine the p0 coefficient that reproduces a representative discharge in each device
Use the same p0 coefficient for all other discharges
Note that p0 is easily adjustable in experiments. When predicting plasma initiation in future devices, it is important to ensure that there is a wide enough p0 range for successful initiation.
James Yang et al, submitted to Nucl. Fusion (2025)

## Slide 39: Machine description
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
The machine description data of each device was constructed using the engineering design data.
Mutual inductance matrices of coils (gray), passive structures (black and cyon), and the vacuum space
Resistivity matrices of passive structures (black and cyon),

## Slide 40: Synthetic flux loop data calculation in DYON
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
Calculated the measured Vloop at the inboard mid-plane using the coil current time traces.

## Slide 41: Synthetic flux loop data calculation in DYON
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
Calculated the measured Vloop at the inboard mid-plane using the coil current time traces.
This good reproduction confirms the validity of the machine description data.

## Slide 42: Synthetic flux loop data calculation in DYON
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
Calculated the measured Vloop at the inboard mid-plane using the coil current time traces.
This good reproduction confirms the validity of the machine description data.
Ready for full electromagnetic plasma initiation modelling  DYON modelling

## Slide 43: DYON: full electromagnetic plasma initiation simulator
Townsend breakdown assessment of each open field lines, and calculates Vp:
Open field lines with E║ > ETownsend
Volume enclosed with closed field lines
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China

## Slide 44: DYON: full electromagnetic plasma initiation simulator
Townsend breakdown assessment of each open field lines, and calculates Vp:
Open field lines with E║ > ETownsend
Volume enclosed with closed field lines
Plasma burn-through and early Ip ramp-up simulated by solving the ODE system of
full circuit equations of plasma, coils, and eddy currents +
global energy and particle balances of main fuel gas, ions, and impurities.
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China

## Slide 45: DYON: full electromagnetic plasma initiation simulator
Townsend breakdown assessment of each open field lines, and calculates Vp:
Open field lines with E║ > ETownsend
Volume enclosed with closed field lines
Plasma burn-through and early Ip ramp-up simulated by solving the ODE system of
full circuit equations of plasma, coils, and eddy currents +
global energy and particle balances of main fuel gas, ions, and impurities.
DYON requires only :
Machine description
control room input data i.e. Icoil and p0
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China

## Slide 46: DYON: full electromagnetic plasma initiation simulator
Townsend breakdown assessment of each open field lines, and calculates Vp:
Open field lines with E║ > ETownsend
Volume enclosed with closed field lines
Plasma burn-through and early Ip ramp-up simulated by solving the ODE system of
full circuit equations of plasma, coils, and eddy currents +
global energy and particle balances of main fuel gas, ions, and impurities.
DYON requires only :
Machine description
control room input data i.e. Icoil and p0
DYON predicts:
Successful plasma initiation
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
Hyun-Tae Kim et al 2022 Nucl. Fusion 62 (2022) 126012
Hyun-Taen Kim et al 2024 Nucl. Fusion 64 (2024) 126010

## Slide 47: DYON: full electromagnetic plasma initiation simulator
Townsend breakdown assessment of each open field lines, and calculates Vp:
Open field lines with E║ > ETownsend
Volume enclosed with closed field lines
Plasma burn-through and early Ip ramp-up simulated by solving the ODE system of
full circuit equations of plasma, coils, and eddy currents +
global energy and particle balances of main fuel gas, ions, and impurities.
DYON requires only :
Machine description
control room input data i.e. Icoil and p0
DYON predicts:
Successful plasma initiation
Failed plasma burn-through
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
Hyun-Tae Kim et al 2022 Nucl. Fusion 62 (2022) 126012
Hyun-Taen Kim et al 2024 Nucl. Fusion 64 (2024) 126010

## Slide 48: DYON: full electromagnetic plasma initiation simulator
Townsend breakdown assessment of each open field lines, and calculates Vp:
Open field lines with E║ > ETownsend
Volume enclosed with closed field lines
Plasma burn-through and early Ip ramp-up simulated by solving the ODE system of
full circuit equations of plasma, coils, and eddy currents +
global energy and particle balances of main fuel gas, ions, and impurities.
DYON requires only :
Machine description
control room input data i.e. Icoil and p0
DYON predicts:
Successful plasma initiation
Failed plasma burn-through
Failed Townsend breakdown
Hyun-Tae Kim et al 2022 Nucl. Fusion 62 (2022) 126012
Hyun-Taen Kim et al 2024 Nucl. Fusion 64 (2024) 126010
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China

## Slide 49: Simulation setup
Device | Sputtering yield | Ferromagnetic modelling | p0 coeffcient
MASTU | 0.1% initial O + Carbon sputtering by D ions = 0.03 | N/A | 0.1
EAST | 0.1% initial O | N/A | 1.35
DIIID | 0.1% initial O + Carbon sputtering by D ions = 0.03 | N/A | 0.25
KSTAR | 0.1% initial O + Carbon sputtering by D ions = 0.03 | Done | 0.2
VEST | 0.1% initial O | N/A | 0.5

## Slide 50: Simulation setup
Device | Sputtering yield | Ferromagnetic modelling | p0 coeffcient
MASTU | 0.1% initial O + Carbon sputtering by D ions = 0.03 | N/A | 0.1
EAST | 0.1% initial O | N/A | 1.35
DIIID | 0.1% initial O + Carbon sputtering by D ions = 0.03 | N/A | 0.25
KSTAR | 0.1% initial O + Carbon sputtering by D ions = 0.03 | Done | 0.2
VEST | 0.1% initial O | N/A | 0.5
Apart from the table above, the simulation setup used in all DYON modelling is identical, i.e. no tuning in individual discharges.
Only using the control room input data i.e. coil currents waveform and effective prefill gas pressure,
the plasma initiation in each discharge were predicted.

## Slide 51: contents
Motivation
Experiment database
DYON code and simulation setup
Multi-machine validation results
Prediction to ITER
Summary

## Slide 52: Operation space experiments

## Slide 53: Operation space prediction
The inductive operation spaces were reproduced in the full electromagnetic DYON modelling in all devices.
Strong confirmation of the validity of predictive modelling.

## Slide 54: Impact of initial impurities and wall treatment in metal wall
The operation space prediction does not change upto 1% of initial impurity (e.g. Oxygen) in the prefill gas.

## Slide 55: Impact of initial impurities and wall treatment in metal wall
The operation space prediction does not change upto 1% of initial impurity (e.g. Oxygen) in the prefill gas.

## Slide 56: Impact of initial impurities and wall treatment in metal wall
The operation space prediction does not change upto 1% of initial impurity (e.g. Oxygen) in the prefill gas.
If higher than 1%, the operation space prediction shrinks from the boundary.

## Slide 57: Impact of initial impurities and wall treatment in metal wall
The operation space prediction does not change upto 1% of initial impurity (e.g. Oxygen) in the prefill gas.
If higher than 1%, the operation space prediction shrinks from the boundary.
Physical sputtering model of Lithium and Boron implemented in DYON. Both do not change the operation space.
0.1% initial oxygen + boron physical sputtering for ITER prediction.

## Slide 58: contents
Motivation
Experiment database
DYON code and simulation setup
Multi-machine validation results
Prediction to ITER
Summary

## Slide 59: Prediction to the inductive plasma initiation in ITER
Machine description and coil current time traces are from IMAS (#105052).
DYON predicts with 0.1% initial oxygen + physical sputtering of Boron
Inductive plasma initiation is successful at 1mPa.

## Slide 60: Prediction to the inductive plasma initiation in ITER
Machine description and coil current time traces are from IMAS (#105052).
DYON predicts with 0.1% initial oxygen + physical sputtering of Boron
Inductive plasma initiation is successful at 1mPa.

## Slide 61: Prediction to the inductive plasma initiation in ITER
Machine description and coil current time traces are from IMAS (#105052).
DYON predicts with 0.1% initial oxygen + physical sputtering of Boron
Inductive plasma initiation is successful at 1mPa.
The upper limit of p0 for plasma burn-through is 1.5mPa.
The lower limit of p0 for Townsend breakdown is lower than 0.1mPa, because of the long connection length.

## Slide 62: Summary
Predictive modelling of operation space for inductive plasma initiation has been validated with multi-machine experiment data. This suggests that
Full electromagnetic DYON captures the essential physics of inductive plasma initiation, and
DYON is a useful tool for assessing the feasibility of inductive plasma initiation with the given hardware design and operating scenario in future devices such as ITER and STEP.
ITER predictive modelling was performed
with the simulation setup validated in EAST (Boron physical sputtering + 0.1% initial oxygen), and
with the machine description and coil current time traces (#105052) in IMAS.
DYON predicts
the inductive plasma initiation in ITER is successful at 1mPa.
the lower limit of p0 for Townsend breakdown is lower than 0.1mPa, because of the long connection length (10x longer than the present devices). The prediction of the lower limit of p0 should be confirmed with a more complete breakdown simulation, such as Particle-In-Cell modelling (e.g. BREAK).
the upper limit of p0 for plasma burn-through is 1.5mPa.
More DYON modelling will also be presented at this conference:
Validation of runaway electrons modelling by Youngsun Lee 17 Oct 2025, 14:40
ECH-assisted plasma initiation modelling in JT-60SA by Takuma Wakatsuki 17 Oct 2025, 10:40

## Slide 63: Back-up slides

## Slide 64
Full circuit equations
Energy balance of electrons and ions
Particle balance of D ions
Particle balance of impurities
Full circuit equation integrated in the ordinary differential equation system of global 0D energy and particle balance
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China

## Slide 65: Namelist
names.Lf_Option = 2;
names.Poh = 'dyon'
names.Rp = 'spitzer'
names.li_burnthrough ='inputdata'
names.li_rampup = 'inputdata';
names.Lp_burnthrough = 'dyon'
names.Lp_burnthrough_option = 2;
names.Lp_rampup = 'dyon';
names.Lp_rampup_option = 2;
names.Lp_Hirshman_optimize = '';
names.interp.dVpdt = 2;
names.dVpdt_heating = 1;
names.interp.dLpdt= 2;
names.interp.dRdt= 2;
names.interp.dZdt = 2;
names.interp.Vp =1;
names.t_start_EM = -0.02
names.t_townsend = 0.0 in MU, 0.03 in EAST,
0.0 in DIIID, 0.025 in KSTAR, 0 in VEST (=0.305)
names.t_start_plasma = names.t_townsend+0.0001
names.t_start_Ip = names.t_townsend+0.0002;
names.t_end= 0.1 in MU, 0.2 in EAST, 0.1 in DIIID, 0.1 in KSTAR, 0.01 in VEST (=0.315)
names.t_townsend_res0 = 1e-3;
names.t_townsend_res=1e-3;
names.t_step_max = names.t_townsend_res*0.01;
names.psi_calculation_burnthrough = 'Point';
names.psi_calculation_rampup = 'Point';
names.perpendicular_confinement_model = 'Bohm’;
names.field_line_following_streamslice = 1;
names.field_line_following_method = 'ode’;
names.interp_imp = 'c';
names.ferromagnetic_ON = 0 in MU, 0 in EAST, 0 in DIIID, 1 in KSTAR, 0 in VEST
names.R_calculation_Townsend = 0;
names.R_calculation_FBE = 0;
names.p0_townsend_option = 2;
names.N_div =50;
names.Lf_length_typical = 10000; (obsolete)
names.dLength = 0.01; (obsolete)
names.tau_p_coef=1.0;
names.tau_E_coef = 1.0
names.L_connection_coef=1.0
names.Townsend_Lf_coef=0.5
names.impurity.C =1 in MU; 0 in EAST, 1 in DIIID, 1 in KSTAR, 0 in VEST
names.impurity.O = 1;
names.W_coef1=1.0;
names.W_coef2=0.0;
names.t_Hrecycling = 0.1
names.cT = 1 in MU; 0 in EAST, 1 in DIIID, 2 in KSTAR, 1 in VEST
names.Sputtering_ObyO = 1.0 ;
names.Sputtering_CbyO = 1.0 in MU; 0 in EAST, 1.0 in DIIID, 1.0 in KSTAR, 0.0 in VEST
names.Sputtering_CbyH = 0.03 in MU; 0 in EAST, 0.03 in DIIID, 0.03 in KSTAR; 0 in VEST
names.fuelgas= 1;
names.Hmass= 2 in MU; 2 in EAST, 2 in DIIID, 2 in KSTAR, 1 in VEST

## Slide 66: Ip at 100ms in MASTU, 100ms in EAST, 100ms in KSTAR, 15ms in VEST, and 50ms in DIIID

## Slide 67: Ferromagnetic effects
Incoloy 908 used in the jacket of the PF1–5 coils and all the toroidal field (TF) Coils in KSTAR
Ferromagnetic effect of Incoloy 908 distorts the magnetic field, degrading the null configuration.
The 2D psi data from the ferromagnetic Incoloy 908 effects was calculated by Finite Element Method modelling of the nonlinear B–H curve of Incoloy 908, and used in DYON modelling of KSTAR discharges.
[J. Kim et al Nucl. Fusion 51 (2011) 083034]
The ferromagnetic psi data were necessary for DYON to reproduce a successful plasma initiation of KSTAR 37621.
However, ITER does not have Incoloy908 so the ferromagnetic effects were not modelled in the DYON prediction of ITER.
With modelling of ferromagnetic effects
Without modelling of ferromagnetic effects
Jeongwon Lee, et al 2025 4th iFPC