## Slide 1
MULTI-MACHINE VALIDATION OF PLASMA INITIATION MODELLING AND PROSPECTS FOR FUTURE DEVICES
Hyun-Tae Kim (MAST-U), Runze Chen (EAST), James Yang (DIII-D), Youngsun Lee (KSTAR), Jeongwon Lee (KSTAR), and Hongsik Yoon (VEST), and ITPA-IOS contributors
30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China

## Slide 2: contents
Background and motivation
Experiment database
DYON code and simulation setup
Multi-machine validation results
Prediction to ITER
Summary

## Slide 3: Inductive plasma initiation in tokamaks: Townsend breakdown and plasma burn-through
Gas
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China

## Slide 4: Inductive plasma initiation in tokamaks: Townsend breakdown and plasma burn-through
Gas
A few %
ionisation
Townsend breakdown phase
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
B. Lloyd PPCF 38 (1996) 1627
P. C. de Vries Nucl. Fusion 59 (2019) 096043

## Slide 5: Inductive plasma initiation in tokamaks: Townsend breakdown and plasma burn-through
Gas
A few %
ionisation
Townsend breakdown phase
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
B. Lloyd PPCF 38 (1996) 1627
P. C. de Vries Nucl. Fusion 59 (2019) 096043
# of ionisations while an electron traveling in 1 meter
()

## Slide 6: Inductive plasma initiation in tokamaks: Townsend breakdown and plasma burn-through
Gas
A few %
ionisation
Townsend breakdown phase
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
B. Lloyd PPCF 38 (1996) 1627
P. C. de Vries Nucl. Fusion 59 (2019) 096043
# of ionisations while an electron traveling in 1 meter
()

## Slide 7: Inductive plasma initiation in tokamaks: Townsend breakdown and plasma burn-through
# of ionisations while an electron traveling in 1 meter
()
Gas
A few %
ionisation
Townsend breakdown phase
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
B. Lloyd PPCF 38 (1996) 1627
P. C. de Vries Nucl. Fusion 59 (2019) 096043

## Slide 8: Inductive plasma initiation in tokamaks: Townsend breakdown and plasma burn-through
Electrons and neutrals exist together in the burn-through phase
Ohmic heating VS Energy loss from radiation and charge exchange
Gas
A few %
ionisation
100%
ionisation
Townsend breakdown phase
Plasma burn-through phase
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
B. Lloyd PPCF 38 (1996) 1627
P. C. de Vries Nucl. Fusion 59 (2019) 096043
# of ionisations while an electron traveling in 1 meter
()

## Slide 9: Inductive plasma initiation in tokamaks: Townsend breakdown and plasma burn-through
Electrons and neutrals exist together in the burn-through phase
Ohmic heating VS Energy loss from radiation and charge exchange
Te[eV]
Degree of
Ionization[%]
100
0
~10
0
Gas
A few %
ionisation
100%
ionisation
Townsend breakdown phase
Plasma burn-through phase
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
B. Lloyd PPCF 38 (1996) 1627
P. C. de Vries Nucl. Fusion 59 (2019) 096043
# of ionisations while an electron traveling in 1 meter
()

## Slide 10: Inductive plasma initiation in tokamaks: Townsend breakdown and plasma burn-through
Electrons and neutrals exist together in the burn-through phase
Ohmic heating VS Energy loss from radiation and charge exchange
Te[eV]
Prad[W]
~105
0
Degree of
Ionization[%]
100
0
~10
D radiation barrier
0
Gas
A few %
ionisation
100%
ionisation
Townsend breakdown phase
Plasma burn-through phase
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
B. Lloyd PPCF 38 (1996) 1627
P. C. de Vries Nucl. Fusion 59 (2019) 096043
# of ionisations while an electron traveling in 1 meter
()

## Slide 11: Inductive plasma initiation in tokamaks: Townsend breakdown and plasma burn-through
Electrons and neutrals exist together in the burn-through phase
Ohmic heating VS Energy loss from radiation and charge exchange
Te[eV]
Prad[W]
~105
0
Degree of
Ionization[%]
100
0
~10
D radiation barrier
0
Gas
A few %
ionisation
100%
ionisation
Townsend breakdown phase
Plasma burn-through phase
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
B. Lloyd PPCF 38 (1996) 1627
P. C. de Vries Nucl. Fusion 59 (2019) 096043
# of ionisations while an electron traveling in 1 meter
()

## Slide 12: Tokamak operation for inductive plasma initiation
Magnetic field null configuration is required to maximise the connection length.

## Slide 13: Tokamak operation for inductive plasma initiation
Magnetic field null configuration is required to maximise the connection length.

## Slide 14: Tokamak operation for inductive plasma initiation
Magnetic field null configuration is required to maximise the connection length.

## Slide 15: Tokamak operation for inductive plasma initiation
Magnetic field null configuration is required to maximise the connection length.

## Slide 16: Tokamak operation for inductive plasma initiation
Magnetic field null configuration is required to maximise the connection length.

## Slide 17: Goal of plasma initiation modelling
p0 and
p0 and

## Slide 18: Goal of plasma initiation modelling
p0 and
p0 and
Vloop=5.3V
Vloop=4.9V

## Slide 19: Goal of plasma initiation modelling
p0 and
p0 and
Vloop=5.3V
Vloop=4.9V

## Slide 20: Goal of plasma initiation modelling
p0 and
p0 and
Vloop=5.3V
Vloop=4.9V

## Slide 21: Goal of plasma initiation modelling
DYON
p0 and
p0 and
Vloop=5.3V
Vloop=4.9V
DYON

## Slide 22: Goal of plasma initiation modelling
DYON
p0 and
p0 and
Vloop=5.3V
Vloop=4.9V
DYON
Plasma initiation phase is the most dynamic phase in the whole tokamak pulse.
Tokamak hardware determines the operational constraints:
  Coil design: Icoil limit
  Power supply design : dIcoil/dt limit
  Vessel conductivity: eddy currents
  Vacuum volume: required p0
For a new tokamak design, the feasibility of plasma initiation with the operational constraints should be ensured with predictive modelling.
This is particularly important for large superconducting devices such as ITER and STEP, as the plasma initiation will be challenging.

## Slide 23: contents
Background and motivation
Experiment database
DYON code and simulation setup
Multi-machine validation results
Prediction to ITER
Summary

## Slide 24: Devices for multimachine validation
Device | Aspect ratio | Coils | First wall material | Ferromagnetic material | Vv[m3] | Vp[m3] | Bt[T] | Lf[m]
MASTU | Spherical Torus (R=0.7m, a=0.5m) | Copper | Carbon | N/A | 55 | 6 | 0.6 | 75
EAST | Conventional Tokamak (R=1.85m, a=0.5m) | Super Conductor | Tungsten + Molybdenum | N/A | 38 | 7.5 | 2.5 | 311
DIIID | Conventional Tokamak (R=1.67m, a=0.65m) | Copper | Carbon | N/A | 35 | 16 | 1.8 | 292
KSTAR | Conventional Tokamak (R=1.8m, a=0.7m) | Super Conductor | Carbon | Incoloy 908 in the jacket of PF and TF coils | 55 | 5 | 1.8 | 315
VEST | Spherical Torus (R=0.3m, a=0.2m) | Copper | Stainless steel | N/A | 3.7 | 0.6 | 0.23 | 12

## Slide 25: Parameter scan experiments to identify plasma initiation operation space
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
  Loop voltage
  Prefill gas pressure
O
O
O
O
O
O
O
O
O
O
O
O
O
Successful plasma initiation

## Slide 26: Parameter scan experiments to identify plasma initiation operation space
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
  Loop voltage
  Prefill gas pressure
O
O
O
X
O
O
O
X
O
X
X
X
X
O
O
O
O
O
Successful breakdown
but failed burn-through
(strong Dalpha but no Ip ramp-up)
O
Successful plasma initiation

## Slide 27: Parameter scan experiments to identify plasma initiation operation space
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
  Loop voltage
  Prefill gas pressure
O
O
O
X
X
O
O
O
X
O
X
X
X
X
X
O
O
O
X
O
O
Successful breakdown
but failed burn-through
(strong Dalpha but no Ip ramp-up)
O
X
Failed breakdown
(no or very weak Dalpha)
Successful plasma initiation

## Slide 28: Parameter scan experiments to identify plasma initiation operation space
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
  Loop voltage
  Prefill gas pressure
O
O
O
X
X
O
O
O
X
O
X
X
X
X
X
O
O
O
X
O
O
Paschen curve?
Successful breakdown
but failed burn-through
(strong Dalpha but no Ip ramp-up)
O
X
Failed breakdown
(no or very weak Dalpha)
Successful plasma initiation

## Slide 29: Parameter scan experiments to identify plasma initiation operation space
  Loop voltage
  Prefill gas pressure
O
O
O
X
X
O
O
O
X
O
X
X
X
X
X
O
O
O
X
O
O
Paschen curve?
Successful breakdown
but failed burn-through
(strong Dalpha but no Ip ramp-up)
O
X
Failed breakdown
(no or very weak Dalpha)
Successful plasma initiation
MAST-U
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
Hyun-Taen Kim et al 2024 Nucl. Fusion 64 (2024) 126010

## Slide 30: Operation space in experiments
Hong-Sik Yun et al 2023 29th IAEA Fusion Energy Conference p [TH-C/1906]
Runze Chen et al, Nucl. Fusion 65 (2025) 076043
James Yang et al, Nucl. Fusion, submitted
Jeongwon Lee, et al 2025 4th iFPC
Hyun-Taen Kim et al Nucl. Fusion 64 (2024) 126010
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Effective prefill gas pressure [mPa]

## Slide 31: Operation space in experiments
Hong-Sik Yun et al 2023 29th IAEA Fusion Energy Conference p [TH-C/1906]
Runze Chen et al, Nucl. Fusion 65 (2025) 076043
James Yang et al, Nucl. Fusion, submitted
Jeongwon Lee, et al 2025 4th iFPC
Hyun-Taen Kim et al Nucl. Fusion 64 (2024) 126010
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Effective prefill gas pressure [mPa]
Failed burn-through at high p0
Failed burn-through at low Vloop

## Slide 32: Operation space in experiments
Hong-Sik Yun et al 2023 29th IAEA Fusion Energy Conference p [TH-C/1906]
Runze Chen et al, Nucl. Fusion 65 (2025) 076043
James Yang et al, Nucl. Fusion, submitted
Jeongwon Lee, et al 2025 4th iFPC
Hyun-Taen Kim et al Nucl. Fusion 64 (2024) 126010
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Effective prefill gas pressure [mPa]
Failed burn-through at high p0
Failed burn-through at low Vloop
Failed breakdown at low p0

## Slide 33: Operation space in experiments
Hong-Sik Yun et al 2023 29th IAEA Fusion Energy Conference p [TH-C/1906]
Runze Chen et al, Nucl. Fusion 65 (2025) 076043
James Yang et al, Nucl. Fusion, submitted
Jeongwon Lee, et al 2025 4th iFPC
Hyun-Taen Kim et al Nucl. Fusion 64 (2024) 126010
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Effective prefill gas pressure [mPa]
Failed burn-through at high p0
Failed burn-through at low Vloop
Failed breakdown at low p0
The hypothesis is valid for all devices.

## Slide 34: Operation space in experiments
Failed burn-through at high p0
Failed burn-through at low Vloop
Failed breakdown at low p0
The hypothesis is valid for all devices.
The conventional Townsend assessment with Lf (i.e. αLf > 1) over-predicts the lower limit of p0 for plasma breakdown.
Hong-Sik Yun et al 2023 29th IAEA Fusion Energy Conference p [TH-C/1906]
Runze Chen et al, Nucl. Fusion 65 (2025) 076043
James Yang et al, Nucl. Fusion, submitted
Jeongwon Lee, et al 2025 4th iFPC
Hyun-Taen Kim et al Nucl. Fusion 64 (2024) 126010
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Effective prefill gas pressure [mPa]

## Slide 35: contents
Background and motivation
Experiment database
DYON code and simulation setup
Multi-machine validation results
Prediction to ITER
Summary

## Slide 36: Effective prefill gas pressure
Prefill gas pressure p0 is an essential input for predictive plasma initiation modelling.
Sufficiently high p0 is required for Townsend breakdown.
Sufficiently low Vv*p0 is required for plasma burn-through.

## Slide 37: Effective prefill gas pressure
Prefill gas pressure p0 is an essential input for predictive plasma initiation modelling.
Sufficiently high p0 is required for Townsend breakdown.
Sufficiently low Vv*p0 is required for plasma burn-through.
However, raw data requires calibration.
Fast ion gauge calibration is often inaccurate.

## Slide 38: Effective prefill gas pressure
Prefill gas pressure p0 is an essential input for predictive plasma initiation modelling.
Sufficiently high p0 is required for Townsend breakdown.
Sufficiently low Vv*p0 is required for plasma burn-through.
However, raw data requires calibration.
Fast ion gauge calibration is often inaccurate.
Measured values vary at different locations of the fast ion gauges.
James Yang et al, submitted to Nucl. Fusion (2025)

## Slide 39: Effective prefill gas pressure
Prefill gas pressure p0 is an essential input for predictive plasma initiation modelling.
Sufficiently high p0 is required for Townsend breakdown.
Sufficiently low Vv*p0 is required for plasma burn-through.
However, raw data requires calibration.
Fast ion gauge calibration is often inaccurate.
Measured values vary at different locations of the fast ion gauges.
Effective prefill gas pressure = p0 coefficient x fast ion gauge data.
James Yang et al, submitted to Nucl. Fusion (2025)

## Slide 40: Effective prefill gas pressure
Prefill gas pressure p0 is an essential input for predictive plasma initiation modelling.
Sufficiently high p0 is required for Townsend breakdown.
Sufficiently low Vv*p0 is required for plasma burn-through.
However, raw data requires calibration.
Fast ion gauge calibration is often inaccurate.
Measured values vary at different locations of the fast ion gauges.
Effective prefill gas pressure = p0 coefficient x fast ion gauge data.
The strategy to validate the operating space prediction capability in DYON:
Determine the p0 coefficient that reproduces a representative discharge in each device
Use the same p0 coefficient for all other discharges
James Yang et al, submitted to Nucl. Fusion (2025)

## Slide 41: Effective prefill gas pressure
Prefill gas pressure p0 is an essential input for predictive plasma initiation modelling.
Sufficiently high p0 is required for Townsend breakdown.
Sufficiently low Vv*p0 is required for plasma burn-through.
However, raw data requires calibration.
Fast ion gauge calibration is often inaccurate.
Measured values vary at different locations of the fast ion gauges.
Effective prefill gas pressure = p0 coefficient x fast ion gauge data.
The strategy to validate the operating space prediction capability in DYON:
Determine the p0 coefficient that reproduces a representative discharge in each device
Use the same p0 coefficient for all other discharges
Note that p0 is easily adjustable in experiments. When predicting plasma initiation in future devices, it is important to ensure that there is a wide enough p0 range for successful initiation.
James Yang et al, submitted to Nucl. Fusion (2025)

## Slide 42: Machine description
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
The machine description data of each device was constructed using the engineering design data.
Mutual inductance matrices of coils (gray), passive structures (black and cyon), and the vacuum space
Resistivity matrices of passive structures (black and cyon)
VEST
MAST-U
EAST
DIII-D
KSTAR

## Slide 43: Synthetic flux loop data calculation in DYON
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
Calculated the measured Vloop at the inboard mid-plane using the coil current time traces.
VEST
MAST-U
EAST
DIII-D
KSTAR
Icircuit [MA*turns]
Time [sec]

## Slide 44: Synthetic flux loop data calculation in DYON
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
Calculated the measured Vloop at the inboard mid-plane using the coil current time traces.
This good reproduction confirms the validity of the machine description data.
Icircuit [MA*turns]
Vloop[V]
VEST
MAST-U
EAST
DIII-D
KSTAR
Time [sec]
Time [sec]
Calculated
Measured

## Slide 45: Synthetic flux loop data calculation in DYON
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
Calculated the measured Vloop at the inboard mid-plane using the coil current time traces.
This good reproduction confirms the validity of the machine description data.
Ready for full electromagnetic plasma initiation modelling  DYON
Icircuit [MA*turns]
Vloop[V]
VEST
MAST-U
EAST
DIII-D
KSTAR
Time [sec]
Time [sec]
Calculated
Measured

## Slide 46: DYON: full electromagnetic plasma initiation simulator
Townsend breakdown assessment of individual open field lines, and calculates Vp:
Open field lines with E║ > ETownsend
Volume enclosed with closed field lines
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China

## Slide 47: DYON: full electromagnetic plasma initiation simulator
Townsend breakdown assessment of individual open field lines, and calculates Vp:
Open field lines with E║ > ETownsend
Volume enclosed with closed field lines
Plasma burn-through and early Ip ramp-up simulated by solving the ODE system of
full circuit equations of plasma, coils, and eddy currents +
global energy and particle balances of main fuel gas, ions, and impurities.
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China

## Slide 48: DYON: full electromagnetic plasma initiation simulator
Townsend breakdown assessment of individual open field lines, and calculates Vp:
Open field lines with E║ > ETownsend
Volume enclosed with closed field lines
Plasma burn-through and early Ip ramp-up simulated by solving the ODE system of
full circuit equations of plasma, coils, and eddy currents +
global energy and particle balances of main fuel gas, ions, and impurities.
DYON requires only :
Machine description
control room input data i.e. Icoil and p0
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China

## Slide 49: DYON: full electromagnetic plasma initiation simulator
Townsend breakdown assessment of individual open field lines, and calculates Vp:
Open field lines with E║ > ETownsend
Volume enclosed with closed field lines
Plasma burn-through and early Ip ramp-up simulated by solving the ODE system of
full circuit equations of plasma, coils, and eddy currents +
global energy and particle balances of main fuel gas, ions, and impurities.
DYON requires only :
Machine description
control room input data i.e. Icoil and p0
DYON predicts:
Successful plasma initiation
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
Hyun-Tae Kim et al 2022 Nucl. Fusion 62 (2022) 126012
Hyun-Taen Kim et al 2024 Nucl. Fusion 64 (2024) 126010

## Slide 50: DYON: full electromagnetic plasma initiation simulator
Townsend breakdown assessment of individual open field lines, and calculates Vp:
Open field lines with E║ > ETownsend
Volume enclosed with closed field lines
Plasma burn-through and early Ip ramp-up simulated by solving the ODE system of
full circuit equations of plasma, coils, and eddy currents +
global energy and particle balances of main fuel gas, ions, and impurities.
DYON requires only :
Machine description
control room input data i.e. Icoil and p0
DYON predicts:
Successful plasma initiation
Failed plasma burn-through
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China
Hyun-Tae Kim et al 2022 Nucl. Fusion 62 (2022) 126012
Hyun-Taen Kim et al 2024 Nucl. Fusion 64 (2024) 126010

## Slide 51: DYON: full electromagnetic plasma initiation simulator
Townsend breakdown assessment of individual open field lines, and calculates Vp:
Open field lines with E║ > ETownsend
Volume enclosed with closed field lines
Plasma burn-through and early Ip ramp-up simulated by solving the ODE system of
full circuit equations of plasma, coils, and eddy currents +
global energy and particle balances of main fuel gas, ions, and impurities.
DYON requires only :
Machine description
control room input data i.e. Icoil and p0
DYON predicts:
Successful plasma initiation
Failed plasma burn-through
Failed Townsend breakdown
Hyun-Tae Kim et al 2022 Nucl. Fusion 62 (2022) 126012
Hyun-Taen Kim et al 2024 Nucl. Fusion 64 (2024) 126010
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China

## Slide 52: Simulation setup
Device | Sputtering yield | Ferromagnetic modelling | p0 coeffcient
MASTU | Assumption of 0.1% initial O in D prefill gas + Carbon sputtering by D ions = 0.03 | N/A | 0.1
EAST | Assumption of 0.1% initial O in D prefill gas | N/A | 1.35
DIIID | Assumption of 0.1% initial O in D prefill gas + Carbon sputtering by D ions = 0.03 | N/A | 0.25
KSTAR | Assumption of 0.1% initial O in D prefill gas + Carbon sputtering by D ions = 0.03 | Done | 0.2
VEST | Assumption of 0.1% initial O in D prefill gas | N/A | 0.5

## Slide 53: Simulation setup
Device | Sputtering yield | Ferromagnetic modelling | p0 coeffcient
MASTU | Assumption of 0.1% initial O in D prefill gas + Carbon sputtering by D ions = 0.03 | N/A | 0.1
EAST | Assumption of 0.1% initial O in D prefill gas | N/A | 1.35
DIIID | Assumption of 0.1% initial O in D prefill gas + Carbon sputtering by D ions = 0.03 | N/A | 0.25
KSTAR | Assumption of 0.1% initial O in D prefill gas + Carbon sputtering by D ions = 0.03 | Done | 0.2
VEST | Assumption of 0.1% initial O in D prefill gas | N/A | 0.5
Apart from the table above, the simulation setup used in all DYON modelling is identical, i.e. no tuning in individual discharges.
Only using the control room input data i.e. coil currents waveform and effective prefill gas pressure,
the plasma initiation in each discharge were predicted.

## Slide 54: contents
Background and motivation
Experiment database
DYON code and simulation setup
Multi-machine validation results
Prediction to ITER
Summary

## Slide 55: Operation space experiments
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Effective prefill gas pressure [mPa]

## Slide 56: Operation space simulation
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Effective prefill gas pressure [mPa]

## Slide 57: Operation space simulation
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Effective prefill gas pressure [mPa]

## Slide 58: Operation space simulation
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Effective prefill gas pressure [mPa]

## Slide 59: Operation space simulation
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Effective prefill gas pressure [mPa]

## Slide 60: Operation space simulation
The inductive operation spaces were reproduced in the full electromagnetic DYON modelling in all devices.
Strong confirmation of the validity of predictive modelling for inductive plasma initiation.
Ready to add EC models for preionisation, heating, and current drive.
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Vloop[V]
Effective prefill gas pressure [mPa]

## Slide 61: contents
Background and motivation
Experiment database
DYON code and simulation setup
Multi-machine validation results
Prediction to ITER
Summary

## Slide 62: Prediction to the inductive plasma initiation in ITER
Machine description and coil current time traces are from IMAS (#105052).
DYON predicts with 0.1% initial oxygen + physical sputtering of Boron
Inductive plasma initiation is successful at 1mPa.

## Slide 63: Prediction to the inductive plasma initiation in ITER
Machine description and coil current time traces are from IMAS (#105052).
DYON predicts with 0.1% initial oxygen + physical sputtering of Boron
Inductive plasma initiation is successful at 1mPa.
Townsend breakdown possible at a low Vloop for long connection length (10x longer than the present devices).
Slower burn-through (D burn-through at 700ms) for a large vacuum volume

## Slide 64: Prediction to the inductive plasma initiation in ITER
Machine description and coil current time traces are from IMAS (#105052).
DYON predicts with 0.1% initial oxygen + physical sputtering of Boron
Inductive plasma initiation is successful at 1mPa.
Townsend breakdown possible at a low Vloop for long connection length (10x longer than the present devices).
Slower burn-through (D burn-through at 700ms) for a large vacuum volume
Upper p0 limit for burn-through =1.5mPa and lower p0 limit for breakdown = 0.1mPa (Caveat: risk of runaway electrons).

## Slide 65: Summary
Validated the predictive modelling of operation space for inductive plasma initiation with multi-machine experiment data. Full electromagnetic DYON
can capture the essential physics in the inductive plasma initiation
can assess the feasibility of inductive plasma initiation with the given hardware design and operating scenario.
is ready to add EC models for preionisation, heating, and current drive for future work.

## Slide 66: Summary
Validated the predictive modelling of operation space for inductive plasma initiation with multi-machine experiment data. Full electromagnetic DYON
can capture the essential physics in the inductive plasma initiation
can assess the feasibility of inductive plasma initiation with the given hardware design and operating scenario.
is ready to add EC models for preionisation, heating, and current drive for future work.
Predicted ITER with
the validated simulation setup
the machine description and coil current time traces (#105052) in IMAS.

## Slide 67: Summary
Validated the predictive modelling of operation space for inductive plasma initiation with multi-machine experiment data. Full electromagnetic DYON
can capture the essential physics in the inductive plasma initiation
can assess the feasibility of inductive plasma initiation with the given hardware design and operating scenario.
is ready to add EC models for preionisation, heating, and current drive for future work.
Predicted ITER with
the validated simulation setup
the machine description and coil current time traces (#105052) in IMAS.
In ITER,
Townsend breakdown possible at a low Vloop for long connection length (10x longer than the present devices).)
Slower burn-through (D burn-through at 700ms) for a large vacuum volume
Upper p0 limit for burn-through =1.5mPa and lower p0 limit for breakdown = 0.1mPa (Caveat: risk of runaway electrons).

## Slide 68: Summary
Validated the predictive modelling of operation space for inductive plasma initiation with multi-machine experiment data. Full electromagnetic DYON
can capture the essential physics in the inductive plasma initiation
can assess the feasibility of inductive plasma initiation with the given hardware design and operating scenario.
is ready to add EC models for preionisation, heating, and current drive for future work.
Predicted ITER with
the validated simulation setup
the machine description and coil current time traces (#105052) in IMAS.
In ITER,
Townsend breakdown possible at a low Vloop for long connection length (10x longer than the present devices).)
Slower burn-through (D burn-through at 700ms) for a large vacuum volume
Upper p0 limit for burn-through =1.5mPa and lower p0 limit for breakdown = 0.1mPa (Caveat: risk of runaway electrons).
More DYON modelling to be presented at this conference:
JT-60SA modelling by Takuma Wakatsuki 17 Oct 2025, 10:40
Runaway electron model development by Youngsun Lee 17 Oct 2025, 14:40

## Slide 69: Back-up slides

## Slide 70
Full circuit equations
Energy balance of electrons and ions
Particle balance of D ions
Particle balance of impurities
Full circuit equation integrated in the ordinary differential equation system of global 0D energy and particle balance
Hyun-Tae Kim | 30th IAEA Fusion Energy Conference | 13–18 October 2025, Chengdu, China

## Slide 71: Namelist
names.Lf_Option = 2;
names.Poh = 'dyon'
names.Rp = 'spitzer'
names.li_burnthrough ='inputdata'
names.li_rampup = 'inputdata';
names.Lp_burnthrough = 'dyon'
names.Lp_burnthrough_option = 2;
names.Lp_rampup = 'dyon';
names.Lp_rampup_option = 2;
names.Lp_Hirshman_optimize = '';
names.interp.dVpdt = 2;
names.dVpdt_heating = 1;
names.interp.dLpdt= 2;
names.interp.dRdt= 2;
names.interp.dZdt = 2;
names.interp.Vp =1;
names.t_start_EM = -0.02
names.t_townsend = 0.0 in MU, 0.03 in EAST,
0.0 in DIIID, 0.025 in KSTAR, 0 in VEST (=0.305)
names.t_start_plasma = names.t_townsend+0.0001
names.t_start_Ip = names.t_townsend+0.0002;
names.t_end= 0.1 in MU, 0.2 in EAST, 0.1 in DIIID, 0.1 in KSTAR, 0.01 in VEST (=0.315)
names.t_townsend_res0 = 1e-3;
names.t_townsend_res=1e-3;
names.t_step_max = names.t_townsend_res*0.01;
names.psi_calculation_burnthrough = 'Point';
names.psi_calculation_rampup = 'Point';
names.perpendicular_confinement_model = 'Bohm’;
names.field_line_following_streamslice = 1;
names.field_line_following_method = 'ode’;
names.interp_imp = 'c';
names.ferromagnetic_ON = 0 in MU, 0 in EAST, 0 in DIIID, 1 in KSTAR, 0 in VEST
names.R_calculation_Townsend = 0;
names.R_calculation_FBE = 0;
names.p0_townsend_option = 2;
names.N_div =50;
names.Lf_length_typical = 10000; (obsolete)
names.dLength = 0.01; (obsolete)
names.tau_p_coef=1.0;
names.tau_E_coef = 1.0
names.L_connection_coef=1.0
names.Townsend_Lf_coef=0.5
names.impurity.C =1 in MU; 0 in EAST, 1 in DIIID, 1 in KSTAR, 0 in VEST
names.impurity.O = 1;
names.W_coef1=1.0;
names.W_coef2=0.0;
names.t_Hrecycling = 0.1
names.cT = 1 in MU; 0 in EAST, 1 in DIIID, 2 in KSTAR, 1 in VEST
names.Sputtering_ObyO = 1.0 ;
names.Sputtering_CbyO = 1.0 in MU; 0 in EAST, 1.0 in DIIID, 1.0 in KSTAR, 0.0 in VEST
names.Sputtering_CbyH = 0.03 in MU; 0 in EAST, 0.03 in DIIID, 0.03 in KSTAR; 0 in VEST
names.fuelgas= 1;
names.Hmass= 2 in MU; 2 in EAST, 2 in DIIID, 2 in KSTAR, 1 in VEST

## Slide 72: Impact of initial impurities and wall treatment in metal wall
The operation space prediction does not change upto 1% of initial impurity (e.g. Oxygen) in the prefill gas.
If higher than 1%, the operation space prediction shrinks from the boundary.
Physical sputtering model of Lithium and Boron implemented in DYON. Both do not change the operation space.
0.1% initial oxygen + boron physical sputtering for ITER prediction.

## Slide 73: Ip at 100ms in MASTU, 100ms in EAST, 100ms in KSTAR, 15ms in VEST, and 50ms in DIIID

## Slide 74: Ferromagnetic effects
Incoloy 908 used in the jacket of the PF1–5 coils and all the toroidal field (TF) Coils in KSTAR
Ferromagnetic effect of Incoloy 908 distorts the magnetic field, degrading the null configuration.
The 2D psi data from the ferromagnetic Incoloy 908 effects was calculated by Finite Element Method modelling of the nonlinear B–H curve of Incoloy 908, and used in DYON modelling of KSTAR discharges.
[J. Kim et al Nucl. Fusion 51 (2011) 083034]
The ferromagnetic psi data were necessary for DYON to reproduce a successful plasma initiation of KSTAR 37621.
However, ITER does not have Incoloy908 so the ferromagnetic effects were not modelled in the DYON prediction of ITER.
With modelling of ferromagnetic effects
Without modelling of ferromagnetic effects
Jeongwon Lee, et al 2025 4th iFPC