## Slide 1
Advancing Fueling for Future D-T Fusion: Innovations in SMBI Technology and Physics-Based Fueling Strategies for Tritium
G.L. Xiao1, Y.R. Zhu1, Y.Q. Shen1, C.Y. Wang1, K. Xu1, J. Yin1, Y. Zhou1, A.S. Liang1,D.M. Fan1, H.L. Du1,
G.Q. Xue1, C.Y. Chen1, X.L. Zou2, W.L. Zhong1
Email: xiaogl@swip.ac.cn
1 Southwestern institute of physics, Chengdu, China
2 CEA, IRFM, St Paul-lez-Durance, France
EX-P #3117

## Slide 2: Outline
Background
Improvements of SMBI techniques
Strategy for fueling via SMBI
Heat load control with SMBI
Summary

## Slide 3
Background
SMBI stands as the leading candidate for T₂ fueling at present
Supersonic molecular beam injection (SMBI) was first introduced into the fusion field as a fueling technology on HL-1 and has been applied in more than a dozen fusion devices [G.L.Xiao RMPP 2023]
SMBI | Gas puffing
higher speed, higher fueling efficiency | slower speed, lower fueling efficiency
directivity | low directivity
lower recycling, supports long-pulse operation | higher recycling
……
Pégourié JNM 2003
[Zheng PPCF 2013]

## Slide 4
SMBI offers a significant benefit for heat load control
Background
ELM control with SMBI
ELM mitigation by fueling SMBI first demonstrated in HL-2 [Xiao NF 2012], then applied in EAST and KSTAR[Zou IAEA 2012, Xiao NF 2014, Lee PoP 2015]
ELM suppression with impurity (or mixture) SMBI on HL-2/3 [Zhong NF 2019] and EAST [Cao PST 2025]
Divertor detachment with SMBI
Similar to GP, SMBI at midplane is applied to reduce the divertor heat on HL-2[Yan NF 2010, Gao JNM 2017] and detachment experiment on EAST [Yuan FED 2020].
SMBI directly installed in divertor can has good capacity, implemented on HL-2/3 and EAST [Xiao, AAPPS-DPP 2021, Cao FED 2022]

## Slide 5
Challenges and solutions
Challenges
Solutions
techique improvements
AI based distribution prediction
injector optimization
Multi-phase SMBI
Vector SMBI
experimental fueling strategy
divertor SMBI for heat control
SMBI
application

?
low pressure for T2 fueling
SMB distribution control
convergent fuel
targeted plasma fueling
fueling efficiency
high heat load control
time response
enhanced capacity
Fuel supply
SMBI system design
Nozzle and injector
SMB characteristics
Plasma interaction

?

## Slide 6: Outline
Background
Improvements of SMBI techniques
Strategy for fueling via SMBI
Heat load control with SMBI
Summary

## Slide 7
SMBI testing platform and diagnostic systems
Diagnostics | Parameters | Measurements
Schlieren system | Beam structure, density | 
Glow discharge scanning LPs | Beam structure, velocity | 
Laser Rayleigh scattering | Scale of cluster | 
Laser induced fluorescence | Atom density, velocity | 
Offline SMBI testing platform
>5×10-5 Pa, dmax = 0.5 m, L =2.2 m
A offline SMBI testing platform with comprehensive diagnostic systems was estabished

## Slide 8
Obtain velocity distribution from density [ρ(x,y) → v(x,y)] via U-net deep learning model
Simulation data: ρ(x,y) & v(x,y) ;
Experimental testing data: ρ(x,y) (schlieren system) & v(x,y) (GD & langmiur probes)
[Xu K. et al, China Sci: Tech. sci, 2025]
AI-based SMBI velocity distribution
U-net model
High Generalization Capability ✔： Accurately predicts unseen data.
Optimal Architecture ✅ ：U-net + attention @ boundary → superior beam analysis

## Slide 9
AI-based SMBI distribution prediction
Realized > 1000× faster prediction of SMB distribution aiming for real-time control of plasma profiles
Key Assumption: Beam distribution is governed only by gas source pressure PSMBI
Fixed: Injector geometry (d, L, θ) & background pressure. Sole variable: PSMBI or P₀
Baseline: Surpasses traditional fluid simulation and beam image measurement
Speed: Millisecond-level beam distribution prediction for real-time control

## Slide 10: SMB parameter dependance
Parametric dependance of SMB characteristics on injector and working condition
Simulation
α
α : divergence angle
X M : effective distance
Injector structure design
Beam characteristic parameters:
XM: Length of silent zone; effective distance
α: Half of the divergence angle
L: Length of the expansion section
θ: cone angle
d: diameter of nozzle
P0: source pressure of SMBI
Pb: pressure of the background at oulet
offline experiment
α scaling ∝ d 0.15×L-0.82×θ -0.83×P0 0.21×Pb -0.12
Optimized injectors obtained for effective fueling

## Slide 11: Multi-phase SMB injection technology
Precise control of injected components via gas source temperature
Approches: Adjusting gas source temperature (also the pressure)
Regulates component injection from gas, cluster, to liquid phases and their mixing.
An illustrative measurement of the beam composition by the Schlieren system

## Slide 12: Vector injection technology
Vector injection SMB system: flexible beam steering before reaching plasma edge
Capabilities: precise control of injection position and angle
Adjustment Ranges:
Radial Position:
0 - 0.66 m
Poloidal/Toroidal Angle: ±20°

## Slide 13: Outline
Background
Improvements of SMBI techniques
Strategy for fueling via SMBI
Heat load control with SMBI
Summary

## Slide 14
In fluent simulation:
Xeff (0.9 bar) > Lworking
when: Lworking = 1.5 m
⇒ vH2 = 2100 m/s
⇒ vD2 = 1500 m/s
Simulation and experiments: the beam velocity is independent of pressure, which primarily affects density
Ideal design SMB nozzle allows adiabatic expansion → vmax∝ (γ, M constant)
Fueling analysis prioritize how SMB density distribution shapes edge plasma profiles
Maximized SMB velocity
In tokamak expriements:
Lworking = d(plasma, injector)
Δt = tDα,onset - tSMBI,start
⇒ v = slope (Lworking, Δt)

## Slide 15
Fueling efficiency analysis method
MR: Δne = ne,after(r) - ne,before(r)
Local Deposition (Transport Neglected)
Δne → Gaussian Fit → Ndeposited
Ninjected(PSMBI, tSMBI) : offline calibrated, linear relation for SMBI valve)
Localized analysis of short-time density distributions from microwave reflectometers
Fueling efficiency:

## Slide 16
Effect of gas pressure on fueling efficiency
η: ~53% @ 1 bar → ~ 47% @ 5 bar → ~35% @ 10 bar
Fueling experiments with SMBI pressure scan at fixed parameters:
ne = 2.4×1019 m-3, bt = 1.65 T , Ip = 0.5 MA, PSMBI ~ (1 - 10bar)
Fueling efficiency η decreases with increasing pulse pressure:
The use of low-pressure SMB is recommended, as it enables higher fueling efficiency while complying with tritium safety protocols.

## Slide 17
Effect of pulse width on fueling efficiency
Fueling efficiency η decreases with increasing pulse width
Analysis via single-pulse temporal evolution and multi-pulse width comparison
5bar
1 bar
The use of short-pulsed, high-frequency SMBI is advised over long-pulsed SMBI for higher fueling efficiency.

## Slide 18
Turbulence behavior
Correlation: PSMBI ↑ ⇒ ΔIturb ↑ (confirmed at fixed channel)
Spectral Analysis: PSMBI ↑ ⇒ fdominant : High frequency zone → Low frequency zone (large scale)
Higher turbulence intensity and scale for larger SMBI gas pressure
turbulence intensity
turbulence spectrum

## Slide 19
BOUT++ simulation:
Key Assumptions:
Constant beam velocity across all PSMBI cases
All deposited neutral particles are retained in the plasma
Low PSMBI → high PSMBI: local ∇ne steep ↑ ⇒ Γconv ↑ ⇒ η ↓
η: 89.2% @ 0.9 bar → 73.1% @ 5 bar → 60.8% @10 bar
Plausible physical process
Plausible physical process: PSMBI ↑ ⇒ nSMB ↑ (tSMBI) →
→ ∇ne (edge) ↑ → ↓ → turbulence↑ → Γtransport ↑ → ηfuel ↓

## Slide 20
Timing for HD ratio control
SMBI enables efficient H-D ratio control, with pre-injection providing further enhancement.
The pre-injection of T₂ is recommended, with the option to follow with a combined D/T feedback
For injection timing
Feedback SMBI:
Higher H₂ consumption
Pre-injection SMBI:
Requires only 25% of the H₂

## Slide 21: Outline
Background
Improvements of SMBI techniques
Strategy for fueling via SMBI
Heat load control with SMBI
Summary

## Slide 22
Divertor SMBI is more effective than GP: faster time response, stronger heat mitigation effects
 | SMBI | GP
Gas types | D2 | 60% N2+ 40% D2
injection ratio | 2e22 /s | 4e21 /s
response time （ velocity ） | 9 ms | 112 ms
Te OST | 9 eV | 25eV
Plasma experiments indicate particle injection rate and velocity as critical factors for heat load control
Comparison of heat load control with SMB and GP
Offline testing experiments show SMBI particles reach the divertor plasma in 2.7ms — 20 times faster than GP (50ms) over a 3-meter distance.

## Slide 23
SOLPS results: a higher injection rate significantly enhances and accelerates heat load mitigation
HL-2A SOLPS grid
gas injection
Simulation results indicate that with increasing injection rate:
strong target plate temperature drops.
control effect decay time shortens.
Both trends are in agreement with experimental data.
Particle injection rate effect simulation
Sufficient instantaneous particle flux control is adviced for enhanced, rapid heat load control

## Slide 24
#1 (GP)
#2
#3 (SMBI)
Gas source location
z [cm]
The different neutral particle deposition depths caused by different particle velocity in EMC3-EIRENE based on experimental data
Superior SMBI divertor heat load control via deeper, velocity-driven penetration
Particle velocity (deposit location) effect
Mid-plane results suggests: Higher velocity → Deeper deposition

## Slide 25: Outline
Background
Improvements of SMBI techniques
Strategy for fueling via SMBI
Heat load control with SMBI
Summary

## Slide 26
Summary
Technology Development
Integrated Test Platform: Established a comprehensive SMBI test platform, integrating diagnostics including Schlieren, glow discharge, scanning probe, and laser Rayleigh scattering/induced fluorescence systems.
AI-Powered Analysis: AI models enable integrated analysis of SMBI velocity distribution and rapid prediction of SMBI beam distribution including density and velocity.
Advanced Injection Systems: The vector and multiphase molecular beam injection systems provide enhanced support for improving supersonic beam directivity.
Strategy for experiments
Fueling Strategy: Experimental and simulation results confirm that low-pressure, short-pulse SMBI is advantageous for higher fueling efficiency, and pre-injection is better for DT ratio control.
Superior Heat Load Control: The higher injection rate and particle velocity of SMB offers better heat load control compared to conventional gas puffing, presenting a new approach for optimizing radiative divertor performance.