## Slide 1
This original Work was created by Howard Wilson, Director Science and Technology, on 9 October, 2025.
Copyright © UK Industrial Fusion Solutions Ltd. 2025. All rights reserved.
No part of this publication may be reproduced, stored in a retrieval system of any nature, or transmitted, in any form or by any means including photocopying and recording, without the prior written permission of the copyright owner.
Licences issued by the Copyright Licensing Agency or any other reproduction rights organisation do not apply. If any unauthorised acts are carried out in relation to this copyright work, a civil claim for damages may be made and/or a criminal prosecution may result.
COPYRIGHT NOTICE

## Slide 2: STEP: Driving a pathway to accelerated fusion delivery
Howard Wilson for the STEP Team
30th IAEA Fusion energy conference
13-18 October, 2025

## Slide 3: STEP: Accelerating fusion delivery
Climate change and energy security drive urgency in the delivery of a sustainable, reliable, independent means to power our industry and society
Raises a key and fundamentally important question:

## Slide 4: STEP: Accelerating fusion delivery
Climate change and energy security drive urgency in the delivery of sustainable, reliable, independent means to power our industry and society
Raises a key and fundamentally important question:
Can we accelerate the delivery of fusion energy?
The STEP programme is designed to provide an answer

## Slide 5: Commercially viable pathway to fusion delivery contains three key elements
Requirements
Near term benefits for stakeholders and investors
National skills and industrial capability to deliver fusion
Demonstration of technical and commercial viability
Commercial Fusion Power

## Slide 6: STEP: An Integrated Multi-pronged pathway to commercial fusion delivery
Commercial Fusion Power
Drive near term economic and societal benefits
Grow a skilled and capable fusion industry
Demonstrate commercial viability through prototype
STEP
STEP: Spherical Tokamak for Energy Production
  STEP Prototype Plant (SPP) is the key vehicle to drive delivery
    Net electrical power to the grid at the 100MW level
    Demonstrate fuel self-sufficiency
    Targeting operation in the 2040’s

## Slide 7: STEP: more than just a pilot plant

## Slide 8: STEP Prototype Plant (SPP) Timeline
2020
2025
2030
2035
2040
Concept
Concept/reference design
Site Selection
Operating model

## Slide 9: STEP Prototype Plant (SPP) Timeline
2020
2025
2030
2035
2040
Concept
Concept/reference design
Site Selection
Operating model

## Slide 10: STEP Prototype Plant (SPP) Timeline
Detailed Design and Mobilisation
2020
2025
2030
2035
2040
Main Constructuction
Commission and operate
Build partnerships
Engineering design
Test rigs
Early manufacture
Site Development
Full plant manufacture & assembly
Full site development
System testing
Commissioning
Prototype operations
Commercial plant design
Concept
Concept/reference design
Site Selection
Operating model

## Slide 11: STEP operating model: Achieves its objectives through partnerships

## Slide 12: STEP Prototype Plant: Why a spherical tokamak?
Compact radial build
High current-carrying capacity
Pathway to steady state operation
Novel, simplified maintenance options
  No requirement for inboard breeding

## Slide 13: Spherical tokamak offers advantages: 1) Compact radial build
Conventional Tokamak
Spherical Tokamak

## Slide 14: Spherical tokamak offers advantages: 1) Compact radial build
Radial build of SPP is below that of ITER
High SPP elongation means plasma volumes are similar
SPP has ~3 times the fusion power of ITER

## Slide 15: Spherical tokamak offers advantages: 1) Compact radial build
MAST-U
Harrison et al, PPCF 66 (2024) 065019
(H. Meyer, TH/6-2 ; J. Harrison OV/4-5; S Wang Poster 2813;
E. Tholerus, Poster 2899; D. Moulton Poster 3044; M.J. Kryjak)
Managing the exhaust in compact geometry requires a novel approach
MAST-U has demonstrated beneficial properties of Super-X, which SPP exploits
Acceptable power loads predicted for SPP with:
  Double null; balanced X-points
  Super-X outboard leg
  Extended inner leg
  Ar divertor gas seeding to drive detachment
  ~70% core radiation through Xe pellets
Further modelling/optimisation seeks to:
  Reduce core radiation requirement to access lower Pfus solutions
  Manage transients
  Quantify/reduce uncertainty in SOL width

## Slide 16: Spherical tokamak offers advantages: 2) High normalised current
ST geometry has high q for given IN=Ip/aB
  Provides access to high plasma current, Ip
High normalised current gives:
  High confinement time
  High b<bNIN
Puts STEP plasma in new regimes
  Turbulence and transport, for example
High ratio of toroidal to poloidal magnetic field on inboard side creates high q
(D. Kennedy, TH/6-3; L. Zanesi, Poster 2936)

## Slide 17: Spherical tokamak offers advantages: 3) Steady state with ~90% bootstrap
00
hollow current profile
Enabled by high edge magnetic shear
High Bootstrap
High q0
Monotonic q(r)
High bN
Second ballooning stability, and aids kink and neoclassical tearing mode stability
Low internal inductance
High elongation
Enabled by low A, and low li
∝ k→k2
Total
Bootstrap
EBW
ECCD
Large edge current density can be accommodated, keeping q(r) monotonic
Remaining current can be provided by microwaves
(E. Pennington, Poster 3068)

## Slide 18: Spherical tokamak offers advantages: 3) Steady state with ~90% bootstrap
Two significant challenges with non-inductive
Microwaves planned for remaining 10% current is inefficient
  Over 100MW required, driving up recirculating power
  Electron Bernstein wave (EBW) predicted to be more efficient: validation on MAST-U planned
  Drives R&D into higher efficiency gyrotrons
  Improved efficiency will reduce recirculating power, opening pathways to lower Pfus
Non-inductive ramp-up is feasible, but uncertain:
  Compact radial build leaves little room for solenoid
  Seeking innovative ways to maximise solenoid flux swing available for initiating plasma
(H.T Kim, Poster 2754; P. Jacquet Poster 2867)

## Slide 19: Spherical tokamak offers advantages: 4) Novel simplified maintenance options
Removable centre stack opens up novel vertical maintenance options
A challenge is remountable HTS joints
  We have an encouraging solution in an advanced state of testing
(R. Skilton, TEC/5-1; S. Kirk, Poster 2928)

## Slide 20: Managing Uncertainty: Science and technology advances inform design & operations
2020’s
2030’s
2040’s

## Slide 21: Managing Uncertainty: Science and technology advances inform design & operations

## Slide 22: Managing Uncertainty: Science and technology advances inform design & operations

## Slide 23: Managing Uncertainty: Science and technology advances inform design & operations
(R. Lawless, OV/5-1)

## Slide 24: Conclusions
STEP adopts an holistic approach to fusion delivery
  Delivering early benefits for stakeholders
  Building a skilled fusion industry capability
  Addressing technical challenges for fusion commercialisation
The STEP Prototype Plant is the key vehicle to deliver all three
  Exploits the advantages of the spherical tokamak
  Will deliver 100MW net electrical power and demonstrate fuel self-sufficiency
Meeting the 2040 timeline requires close integration between science & technology and design, engineering & testing to reduce technical risk

## Slide 25
DELIVER A UK PROTOTYPE FUSION ENERGY PLANT,
TARGETING 2040, AND A PATH TO
COMMERCIAL VIABILITY OF FUSION.
STEP MISSION