## Slide 1
ACCESSING STABLE OPERATIONAL WINDOWS IN K-DEMO:
A STABILITY ASSESSMENT WORKFLOW FOR CONCEPTUAL PILOT PLANT DESIGN
J.M. LEE, J.B. CHO, M.S. CHA, S.J. HAHN1, C. HANSEN2
Seoul National Univesity, Korea1, Columbia University, USA.2
jmlmir@snu.ac.kr
Developed an integrated workflow for K-DEMO operational-window exploration.
Optimized coil design and MHD stability using 5 analysis codes (TOKAMAKER, CHEASE, DCON[3], RDCON[4], STRIDE[5] etc.).
Successfully pinpointed a numerically consistent region that is the least unstable and most predictable, despite residual instabilities.
Coil Design and VDE Stability
A VDE-stable coil set ()[9] is designed using TOKAMAKER (Fig.6).
  Ideal/Resistive MHD-Optimized H-mode Profile
  A final H-mode candidate profile is identified from robust L-mode clusters via a pedestal scan (Fig. 4).
  Target is achieved by relaxing the tearing criterion to , as no profile was strictly stable to all modes.
METHODS
Coil design (TOKAMAKER) and fixed boundary scan (CHEASE) based on prior 0D design are executed (Fig. 2).
Identified robust candidates via clustering analysis on a stable data set (δW>0, ballooning stable, Δ′<offset).
  clusters with stable/total point ratio > 0.5 over a broad radius are selected (Fig. 5).
final operating point () via subsequent pedestal scan is pinpointed.
RESULTS
Successfully developed an integrated workflow to identify robust operating regions by overcoming Δ′ sensitivity through a comprehensive MHD stability assessment.
FUTURE WORK / IMPROVEMENTS
Find profiles strictly stable to both ballooning and tearing modes.
Integrate the workflow with transport simulations for a fully self-consistent analysis.
[1] C. Hansen et al., Comput. Phys. Commun. 298, 109111 (2024). [2] H. Lütjens et al., Comput. Phys. Commun. 97, 219 (1996).
[3] A. H. Glasser, Phys. Plasmas 23, 072505 (2016). [4] A. H. Glasser et al., Phys. Plasmas 23, 112506 (2016).
[5] A. S. Glasser et al., Phys. Plasmas 25, 082502 (2018). [6] J.S. Kang et al., Fusion Eng. Des. 211, 114741 (2025).
[7] J.S. Kang et al., Nucl. Fusion 57, 126034 (2017). [8] K. Kim et al., Nucl. Fusion 55, 053027 (2015).
[9] J. P. Freidberg et al., J. Plasma Phys. 83, 905830107 (2017).
Fig.2 Profile distribution of the initial L-mode database
(a)
R²=0.9004
(b)
R²=-0.0176
Fig.3 Prediction results of stability indices using a neural network
Fig.5 Pedestal scan result of H-mode scenario
Established workflow for 0D system scan(Table 1)[6] and ideal MHD[7], but did not yet include systematic tearing mode analysis.
Inherent sensitivity of Δ′ calculation, failing NN model training (Fig. 3) while a model for 𝛿W succeeded.
1. ABSTRACT
2. BACKGROUND & CHALLENGES
3. CHALLENGES / METHODS
4. KEY RESULTS
5. CONCLUSION
REFERENCES
Parameter | Reference
Major radius, (m) | 6.8
Aspect ratio, | 3.1
Magnetic field, (T) | 7.25
Plasma current, (MA) | 13
Normalized beta, | 2.77
Fusion gain, | 20.6
Confinement factor, | 1.28
Edge safety factor, | 5.85
Parameter | Reference
 | 6.8
 | 3.1
 | 7.25
 | 13
 | 2.77
 | 20.6
 | 1.28
 | 5.85
Fig.1 K-DEMO device design features.[8]
Table 1. System parameters of
K-DEMO design points.[6]
Fig.4 Results of the robust stable region search
Fig.6 Designed L-mode, H-mode scenario and coil