## Slide 1
First campaign with Alternative Divertor Configurations in ASDEX Upgrade
T.Lunt1 on behalf of the ASDEX Upgrade and EUROfusion teams 1Max Planck Institute for Plasma Physics, Boltzmannstr. 2, 85748 Garching, Germany
Outline: - Introduction - New upper divertor of ASDEX Upgrade - Overview experimental campaign 2025 - First results - Summary

## Slide 2
2
Introduction: Power and He exhaust challenge
Pa=400 MW
FHe= 7x1020 1/s
High neutral He densities (pressures) in subdivertor volume mandatory for reactor to remove He ‚ash‘
FHe = Spump nHe,pump
[Eich PRL 2011]
[Brunner NF 2018]
+Paux
Awet=2 p R fx lq
T.Lunt, IAEA-FEC 2025 Chengdu, China

## Slide 3: New Upper Divertor of ASDEX Upgrade: Configurations
Overview alternative divertor configurations
[Lunt et al. PRL 2023]
3
T.Lunt, IAEA-FEC 2025 Chengdu, China

## Slide 4
Overview experimental campaign 2025
lq
decreasing
increasing
Database of >100 discharges in stable ADC
fx=flux expansion
Position of the 2nd X-point
Operational space
Result 1:
Hardware installation completed
New upper divertor of AUG operational, but cryo-pump not yet at full performance
All alternative divertor configurations (ADC) successfully established, stable for seconds and during ELMs (except SF+)
Heating power up to 20 MW and plasma current up to 1 MA in ADC
4
T.Lunt, IAEA-FEC 2025 Chengdu, China

## Slide 5
Small field line incidence angles q^<2o can be handled
[Lunt NME 2019]
Alignment tolerance <300µm
AUG 43638 NIR camera
Result 2:
Small field line incidence angles q^<2o can be handled ..
with a tile aligment accuracy better than 300 µm
and optimized error fields of the current feeds
5
T.Lunt, IAEA-FEC 2025 Chengdu, China

## Slide 6
X-point radiator w/o impurity seeding in 800kA H-mode
Result 3:
Even without impurity seeding an X-point radiator can be established in a LFS SF- configuration …
accompanied by detachment of the primary strike line,
but far-SOL heat-fluxes beyond secondary strike line remain high
6
T.Lunt, IAEA-FEC 2025 Chengdu, China
[Bernert NF 2021], [Stroth NF 2022]

## Slide 7
Small-ELM regime (QCE?)
[Brunner NF 2018]
[Faitsch NME 2021]
Fmc,USN/Fmc,LSN ~ 7
7
T.Lunt, IAEA-FEC 2025 Chengdu, China

## Slide 8
Strike point splitting in 1MA H-mode
Result 4:
A splitting of the strike point is observed ..
accompanied by a reduction of a factor of 2 in the heat flux measured by Langmuir probes
8
T.Lunt, IAEA-FEC 2025 Chengdu, China
[Lunt NME 2017], [Pan PPCF 2018]

## Slide 9
Summary
First results:
Hardware installation of a pair of in-vessel coils, a charcoal coated cryo-pump and new divertor targets completed All alternative divertor configurations (ADC) successfully established, stable for seconds and during ELMs (except SF+) Heating power up to 20 MW and plasma current up to 1 MA in ADC
Even at high heating powers field line incidence angles can be made arbitrarily small – or even negative – due to outstanding target alignment accuracy and small magnetic error fields
X-point radiator forms in a LFS SF- configuration even without impurity seeding, where the primary strike point is fully detached, but far-SOL heat fluxes still high  far-SOL fluxes irrelevant at a reactor-like power fall-off lengths lq?
Splitting of the outer strike point observed, accompanied by reduction of the peak heat flux of a factor of ~2 in 1 MA LFS SF- discharges measured by Langmuir probes
9
T.Lunt, IAEA-FEC 2025 Chengdu, China

## Slide 10
10
Backup slides
T.Lunt, IAEA-FEC 2025 Chengdu, China

## Slide 11
Energy Balance