## Slide 1
In-pulse analysis at ITER: workflow managers and 3D visualization tools
P Abreu (ITER Organization) S. Rajesh (IO intership, Kalasalingam Academy of Research and Education, India) S. Blockhuizen, M. Sebregts, D. V. Vougt (Ignition Computing, Netherlands)
Disclaimer: The views and opinions expressed herein do not necessarily reflect those of the ITER Organization

## Slide 2
Orchestrator(s)
Orchestrator(s)
Workflow(s)
Workflow(s)
Trigger
Orchestrator
Workflow(s)
Airflow
new pulse or reprocessing
partial if reprocessing
Orchestrator(s)
Workflow(s)
Workflow(s)
Workflow(s)
Live display
Progress monitor
Motivation
What is in-pulse data processing?
A set of interdependent programs/actors that calculate plasma parameters from measurements.
They use as input both the raw data from the diagnostics and processed data by other programs (hence the interdependence).
The complete workflow(s) can be represented by a directed acyclic graph (DAG).
The wider goal is to provide a consistent interpretation of the plasma state (with uncertainties) from the measurements during each pulse to guide the current experimental session.
More specifically to provide accurate measurement parameters (MP) in time to prepare the next pulse in the control room.

## Slide 3
Orchestrator(s)
Orchestrator(s)
Workflow(s)
Workflow(s)
Trigger
Orchestrator
Workflow(s)
Airflow
new pulse or reprocessing
partial if reprocessing
Orchestrator(s)
Workflow(s)
Workflow(s)
Workflow(s)
Live display
Progress monitor
What is in-pulse data processing?
A set of interdependent programs/actors that calculate plasma parameters from measurements.
They use as input both the raw data from the diagnostics and processed data by other programs (hence the interdependence).
The complete workflow(s) can be represented by a directed acyclic graph (DAG).
The wider goal is to provide a consistent interpretation of the plasma state (with uncertainties) from the measurements during each pulse to guide the current experimental session.
More specifically to provide accurate measurement parameters (MP) in time to prepare the next pulse in the control room.
Motivation
Today

## Slide 4
Overview
Motivation
Workflow manager
  Airflow
  First application: equilibrium reconstruction
  Workflow framework
3D visualization
Conclusions & future work

## Slide 5
Motivation
In-pulse analysis workflows: from diagnostics to physics

## Slide 6
Motivation
In-pulse analysis workflows: from diagnostics to physics

## Slide 7
Motivation
In-pulse analysis workflows: from diagnostics to physics

## Slide 8
Apache Airflow as the workflow manager
    Open source
    Python
    DAG
    Web and CL interfaces
    Scalable (built-in task parallelism)
    Operators can have introspection into actors:
      Fault detection
      Restart
      Replace
Workflow manager: Airflow

## Slide 9
Airflow features at a glance
Retry Mechanism:
  Automatically retries failed tasks to enhance reliability.
Configuring Task Scheduling:
  Inbuild scheduling with Airflow.
  External scheduling.
Parallel Execution:
  Parallelism: Maximum number of tasks running across all DAGs.
  Concurrency: Maximum tasks allowed for a single DAG.
Task Dependencies:
  Specify execution order explicitly.
Workflow manager: Airflow

## Slide 10
  Or per workflow:
Simple parallelization per time slice
Most in-pulse actors process single time slices.
We can process time slcies in batches / ranges with simple parallelism
  Per actor / task:
Workflow manager: Airflow

## Slide 11
First application: equilibrium reconstruction with synthetic magnetics constraints
Workflow manager: equilibrium reconstruction
Magnetics Actor
  Magnetics_prep – Reads machine/diagnostic specific data.
  Magnetics – Synthetic diagnostic modelling for magnetics measurements.
Equilibrium Actor
  Equilibrium_prep – Reads machine/diagnostic specific data for the equilibrium reconstruction.
  Equilibrium –Actor used to reconstruct plasma equilibrium.
Machine agnostic: diagnostic/machine specificities are parameters to the actors.
Code agnostic: actors exchange data in IDS format, easily replaceable by other actors with the same inputs and outputs.
In this particular exercise:
  predictMagnetics (from the Minerva framework, L. Appel, UKAEA)
  EFIT++ (L. Appel, UKAEA)

## Slide 12
  55.A* magnetic diagnostics
  PredictMagnetics by L. Appel within the Minerva framework
  EFIT++ actor
First application: equilibrium reconstruction with synthetic magnetics constraints
Scenario
Machine Description
pf_active
equilibrium
PredictMagnetics
equilibrium
EFIT++
magnetics
pf_passive
tf
wall
Machine Description
pf_active
magnetics
pf_active
magnetics
M. Schneider @ ITPA TG Diag 2022
Workflow manager: equilibrium reconstruction

## Slide 13
Workflow info: the Magnetics Actor for IMAS Pulse 105027, consisting of 614 timeslices.
Serial Execution:
  Total execution time: 7.8 minutes.
  Tasks were executed sequentially without concurrency.
Parallel Execution + Merge:
  Average execution time of 5 parallel runs : 1.5 minutes.
  Merge operation of the runs : 0.5 minutes.
  Total execution time reduced to 2.0 minutes (1.5 + 0.5 minutes).
Conclusion:
  Even with the overhead of the merge step, the average execution time of the parallel runs combined is significantly faster than the serial/direct run.
First application: simple parallelism
Workflow manager: equilibrium reconstruction

## Slide 14
In-pulse Workflow Framework
  Developed a mock in-pulse processing workflow to simulate a complete plasma analysis workflow during a pulse.
  The workflow serves as a blueprint for future integration of real physics-based codes in ITER's real-time processing pipeline.
  All computational steps currently use placeholder actors, designed to be replaced with validated physics modules in future iterations.
  This framework establishes a baseline architecture for modular, scalable in-pulse workflows spanning multiple diagnostics and control loops.
Workflow manager: framework

## Slide 15
In-pulse Workflow Simulation
Workflow manager: framework

## Slide 16
In-pulse Workflow Simulation in Airflow
:
Workflow manager: framework

## Slide 17
In-pulse Workflow Simulation in Airflow
:
Failure detection: detects failures and supports resolution through retry logic, fallback paths, and execution monitoring.
Failure resolution: includes alternative placeholder codes that can be triggered dynamically if a primary actor fails enabling fault tolerance.
The architecture supports horizontal scaling, where multiple timeslices can be processed concurrently as they arrive.
It also enables vertical scaling, allowing additional dependent tasks (e.g., diagnostics, post-processing) to be added without disrupting existing workflows.
The orchestration setup is modular and extensible, allowing increased complexity and integration over time without changing the core design.
Workflow manager: framework

## Slide 18
Workflow Simulation: in-pulse and reprocessing
  1. In-Pulse Workflow (Simulated):
    Mimics online timeslice-by-timeslice processing during an active pulse. Tasks triggered sequentially as new timeslices arrive.
  2. Reprocessing Workflow (Simulated):
  Executes after pulse completion using full data availability. Represents a traditional, serial processing pipeline.
  Both workflows use identical placeholder actors and input conditions, isolating orchestration behaviour for easier comparison.
  Each actor had randomized processing times, generated deterministically using the component's name as a seed.
Workflow manager: framework

## Slide 19
Workflow Simulation: in-pulse and reprocessing
Reprocessing:
In-pulse:
Workflow manager: framework
Airflow execution time
∆t1
∆tn
parallel processing

## Slide 20
The Integrated Modelling and Analysis Suite (IMAS)
3D Visualization
Integrated Modelling & Analysis Suite is the collection of physics software that will be used to support ITER operations and research as defined in the ITER Integrated Modelling Programme.
Data Dictionary
Implements the IMAS data model Interface Data Structures (IDS).
Abstracts the storage format
Both for simulation and experimental data.
Access Layer API
Visualization

## Slide 21
Data visualization and exploration
Data is useless without insight.
There is an ongoing development of ITER plotting library (L. Abadie):
  iplot ecosystem and MINT
  DAN, SDN, IMAS, …
  1D and 2D
  control room display and user desktop
3D scientific data exploration tool was missing:
    Kitware Paraview
    +
    IMAS plugin
3D Visualization
SOLPS + Limiter + ECE LOS

## Slide 22
Data visualization and exploration
See IMAS-Paraview manual and example.
Open source on github
GUI and CLI (export to VTK)
GGD data (2D and 3D)
JOREK
1D profile data:
  Integrate 1D core with 2D edge
Machine/diagnostic description data:
  Divertor
  Wall
  LoS
  Magnetic sensors
  …
3D Visualization

## Slide 23
Example:
JOREK data (psi)
Divertor
Limiter
3D Visualization

## Slide 24
3D Visualization
Example:
JOREK data
Animation of the electron temperature and wall currents.
Data provided by J. Artola.

## Slide 25
Future work
Future work
Workflows:
  Realistic input data:
    Use synthetic diagnostic models as input to the workflows (see presentation from S. Pinches).
    Use mapped experimental data from other devices.
  Integrate with MUSCLE3 (persistent actor framework):
    Work by F. Poli based on the ETS-PAF
    H&CD workflow by M. Schneider
3D visualization: further improvements based on user request

## Slide 26
Thank you!
Paulo Abreu, ITER Organization Sixth IAEA Technical Meeting on Fusion Data Processing, Validation and Analysis
September 2025, Shanghai, China
In-pulse analysis at ITER: workflow managers and 3D visualization tools