## Slide 1
First high power experiments of Alternative Divertor Experiments in ASDEX Upgrade
Overview ADC and XPR experiments and gaps in extrapolating to future devices
Overview ADC and XPR experiments and gaps in extrapolating to future devices
T.Lunt1 on behalf of the ASDEX Upgrade and EUROfusion teams 1Max Planck Institute for Plasma Physics, Boltzmannstr. 2, 85748 Garching, Germany
Outline: - Introduction - New upper divertor of ASDEX Upgrade - Overview experimental campaign 2025 - First experimental observations - Gaps in extrapolating to future devices - Summary

## Slide 2
2
Introduction: Power and He exhaust challenge
Pa=400 MW
FHe= 7x1020 1/s
High neutral He densities (pressures) in subdivertor volume mandatory for reactor to remove He ‚ash‘
FHe = Spump nHe,pump
[Eich PRL 2011]
[Brunner NF 2018]
+Paux
Awet=2 p R fx lq
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 3
3
Introduction: Power and He exhaust challenge
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria
[Bernert NF 2021]
[Lunt/Bernert PRL 2023]
[Faitsch NME 2021]
[Ryutov IAEA-FEC 2012]
Alternative Divertor Configurations
Radiative scenarios
Small-ELM / QCE / EDA

## Slide 4: New Upper Divertor of ASDEX Upgrade: Configurations
[Lunt et al. PRL 2023]
4
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 5
Overview experimental campaign 2025
lq
decreasing
increasing
Database of >100 discharges in stable ADC
fx=flux expansion
Position of the 2nd X-point
Operational space
Hardware installation completed
New upper divertor of AUG operational, but cryo-pump not yet at full performance
All alternative divertor configurations (ADC) successfully established, stable for seconds and during ELMs (except SF+)
Heating power up to 20 MW and plasma current up to 1 MA in ADC
5
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 6
6
First experimental observations
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 7
Small field line incidence angles q^<2o can be handled
[Lunt NME 2019]
Alignment tolerance <300µm
7
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 8
Small field line incidence angles q^<2o can be handled
AUG 43638 NIR camera
Observation 1:
Small field line incidence angles q^<2o can be handled ..
with a tile aligment accuracy better than 300 µm
and optimized error fields of the current feeds
8
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 9
X-point radiator w/o impurity seeding in 800kA H-mode
Observation 2:
Even without impurity seeding an X-point radiator can be established in a LFS SF- configuration …
accompanied by detachment of the primary strike line,
but far-SOL heat-fluxes beyond secondary strike line remain high
9
[Bernert NF 2021], [Stroth NF 2022]
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria
t [s]

## Slide 10
[Dunne NF 2024]
[shots by G. Birkenmeier]
Small-ELM regime (QCE?)
10
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria
[Faitsch NME 2021]
Fmc,USN/Fmc,LSN ~ 7
Observation 3:
Most (all?) of the ADC discharges are in a small-ELM (QCE?) regime
The different shape …
…or the high main chamber neutral density might be the reason

## Slide 11
X-point radiator in sCRD configuration 600 kA H-mode
11
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria
[shots by B.Sieglin]
t [s]

## Slide 12
X-point radiator in sCRD configuration 600 kA H-mode
12
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria
Observation 4:
Despite the very large volume of large fx and Lc an XPR is not established/excited if lq>> DrXPR

## Slide 13
X-point radiator in sCRD configuration at 800 kA
13
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria
Observation 5:
A stable XPR is observed in sCRD configuration with N2 seeding
ELM size and far-SOL heat fluxes strongly reduced
t [s]

## Slide 14
Strike point splitting in 1MA H-mode
Observation 6:
A splitting of the strike point is observed ..
accompanied by a reduction of a factor of 2 in the heat flux measured by Langmuir probes
14
[Lunt NME 2017], [Pan PPCF 2018]
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria
t [s]

## Slide 15
15
Gaps in extrapolating to future devices
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 16
DEMO (9m/1.65m=5.45 times larger)
CRD experiments at AUG and their consequences for a reactor
16
[Lunt, Bernert et al.
PRL 2023]
XPR
[Eich, PRL 2011]
[Brunner NF 2018]
Gaps: stability of XPR at short lq
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria
Radial extension Dru,xpr of XPR increases compared to lq in ITER & DEMO
Is it stable?
Dru,XPR

## Slide 17
17
Gaps: Near/Far-SOL fall-off length
[Eich PRL 2011] / [Brunner NF 2018]
[Lunt PPCF 2020]
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria
Near-SOL power fall-off length scaling
Far-SOL power fall-off length scaling ?
Access to QCE ?
[Dunne NF 2024]

## Slide 18
Summary
Hardware installation of a pair of in-vessel coils, a charcoal coated cryo-pump and new divertor targets completed All alternative divertor configurations (ADC) successfully established, stable for seconds and during ELMs (except SF+) Heating power up to 20 MW and plasma current up to 1 MA in ADC
Observations:
Even at high heating powers field line incidence angles can be made arbitrarily small – or even negative – due to outstanding target alignment accuracy and small magnetic error fields
X-point radiator forms in a LFS SF- configuration even without impurity seeding, where the primary strike point is fully detached, but far-SOL heat fluxes still high
Most (all?) of the ADC discharges are in a small-ELM (QCE?) regime
Large XPR volume no guarantee for XPR formation
Stable XPR observed in sCRD configuration
Splitting of the outer strike point observed, accompanied by reduction of the peak heat flux of a factor of ~2 in 1 MA LFS SF- discharges measured by Langmuir probes
18
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 19
Outlook
Upcoming campaign
Install protection plates on cryo-pump
Carry out 1 MA discharges in (s)CRD configuration
Try other seeding gases to reduce far-SOL heat fluxes
Long term
Install baffles
19
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 20
20
Backup slides
T.Lunt, IAEA-FEC 2025 Chengdu, China

## Slide 21
21
Access to QCE
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria
[Dunne et al., NF 2024]

## Slide 22
22
Filamentary transport
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria
[Krasheninnikov, Phys.Rev. A]

## Slide 23: Experiments – discharges
CRD experiments at AUG and their consequences for a reactor
MAX-PLANCK-INSTITUT FÜR PLASMAPHYSIK | Tilmann Lunt | 49th EPS Conference on Plasma Physics, Bordeaux July 3-7th 2023
23
CRD successfully established, even
without feed-back control
15 MW total heating
with X-point exactly on target

## Slide 24: Experiments – IR thermography
IR camera images superimposed to 3D-CAD drawings
DTsurf=Tsurf-Tsurf,0, Tsurf,0=373 ± 30 K
Large toroidal coverage: Df=70°
1.5xlq,Eich
separatrix
CRD experiments at AUG and their consequences for a reactor
MAX-PLANCK-INSTITUT FÜR PLASMAPHYSIK | Tilmann Lunt | 49th EPS Conference on Plasma Physics, Bordeaux July 3-7th 2023
24
[Lunt, Bernert et al. PRL 2023]
No hotspots observed in CRD & PXD

## Slide 25: Experiments – heat fluxes
[Lunt, Bernert et al. PRL 2023]
< >
CRD experiments at AUG and their consequences for a reactor
MAX-PLANCK-INSTITUT FÜR PLASMAPHYSIK | Tilmann Lunt | 49th EPS Conference on Plasma Physics, Bordeaux July 3-7th 2023
25
strong reduction of heat flux of charged particles in CRD compared to SN
heatflux dominated by radiation in CRD

## Slide 26: Experiments – Interpretation with EMC3-EIRENE
CRD experiments at AUG and their consequences for a reactor
MAX-PLANCK-INSTITUT FÜR PLASMAPHYSIK | Tilmann Lunt | 49th EPS Conference on Plasma Physics, Bordeaux July 3-7th 2023
26
modeling of CRD successful with EMC3-EIRENE
state of deep detachment
large flux expansion at target seems to be favorable for neutral particle trapping

## Slide 27: Experiments – target tile alignment accuracy
Visible true color camera 16Boc
superimposed to 3D CAD drawings
S15
S16
S15
S16
q^=0.2°
Leading edge as large as
1.7 mm!
S1
S14
Tile state since 2003 (!)
CRD experiments at AUG and their consequences for a reactor
MAX-PLANCK-INSTITUT FÜR PLASMAPHYSIK | Tilmann Lunt | 49th EPS Conference on Plasma Physics, Bordeaux July 3-7th 2023
27
substantial (1.7 mm) tile misalignment compatible with CRD operation

## Slide 28: Core impurity pollution & dilution
CRD experiments at AUG and their consequences for a reactor
MAX-PLANCK-INSTITUT FÜR PLASMAPHYSIK | Tilmann Lunt | 49th EPS Conference on Plasma Physics, Bordeaux July 3-7th 2023
28
cN,max=3.5%
cW,max=2x10-4
[Pütterich et al. NF 2019]
Spectroscopy 40700:
cN<~2.5%
cW=2x10-5
individual impurity concentrations below limit
what about all impuritites together?
how does this scale to a reactor?

## Slide 29: Extrapolation to (EU-)DEMO – SOLPS-ITER modelling
[Pan et al, upcoming IAEA 2023]
CRD experiments at AUG and their consequences for a reactor
MAX-PLANCK-INSTITUT FÜR PLASMAPHYSIK | Tilmann Lunt | 49th EPS Conference on Plasma Physics, Bordeaux July 3-7th 2023
29
Modeling of AUG geometry scaled to DEMO
divertor neutral pressures up to 15 Pa (beneficial for He pumping)
impurity concentration far below tolerable limits
heat flux <=2 MW/m2 dominated by radiation

## Slide 30
30
SOL splitting
[Lunt NME 2017]
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 31
31
SOL splitting
[Pan PPCF 2018]
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 32
Small field line incidence angles q^<2o can be handled
[Lunt NME 2019]
Alignment tolerance <300µm
AUG 43638 NIR camera
Result 2:
Small field line incidence angles q^<2o can be handled ..
with a tile aligment accuracy better than 300 µm
and optimized error fields of the current feeds
32
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 33
Energy Balance
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 34
34
Effect on Lc
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 35
35
Gaps: importance of the XPR volume in large device
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria
DEMO (9m/1.65m=5.45 times larger)

## Slide 36
36
New upper divertor hardware
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 37
37
New upper divertor hardware
[Zammuto IEEE 2024]
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 38
38
AUG mechanical twin
[Zammuto IEEE 2024]
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 39
39
New upper divertor hardware
[Zammuto IEEE 2024]
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 40
40
New upper divertor hardware
Unspooler and straightening machine
AUG VV
Bending
machine
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 41
41
New upper divertor hardware
Eccentric bolt
Tungsten coated
graphite tile
Papyex pad
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 42
42
New upper divertor hardware
Cryo-pump installed in AUG
(coconut) charcoal coated cryo-pump for He-removal
cryo-pump installation finished
charcoal coating allows He-pumping
challenges for 3D in-vessel conductor bending and installation solved
completion of installation expected after summer 2024
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 43
43
New upper divertor hardware
New charcoal coated cryo pump
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 44
44
New upper divertor hardware
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 45
45
New upper divertor hardware
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 46
46
Cryopanel Temperature on stainless steel surface
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 47
47
Backup: 3D asymmetries (detachment?)

## Slide 48
48
Near/Far-SOL fall-off length
[Brunner NF 2018]
[Lunt PPCF 2020]
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 49
49
1 MA H-mode
lq,Eich/Brunner=1.9 mm
Dru,x2=10.8 mm
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria

## Slide 50
50
800 kA H-mode strong gas puff
lq,Eich/Brunner=2.1 mm
Dru,x2=1.2 mm
Dru,x2=11.8 mm
T.Lunt, 5th TM on divertor concepts 2025, IAEA Headquarters, Vienna, Austria