## Slide 1: Status of Divertor Operation in Stellarators
V. R. Winters1,2, F. Reimold2, D. Boeyaert3, R. Davies2, Y. Feng2, K. Garcia1,2,3, A. Kharwandikar2, D.M. Kriete4,N. Maaziz2, V. Perseo2, T. Tork2, D.Zhang2 and the W7-X Team
1Universität Greifswald, Institut für Physik, 17489 Greifswald, DE
2Max-Planck-Institut für Plasma Physik, 17491 Greifswald, DE
3University of Wisconsin – Madison, Madison, WI USA
4Auburn University, Auburn, AL USA

## Slide 2: Geometry as a basis for understanding differences in stellarator performance
[2]
A main difference between tokamak and stellarator divertors: the field line pitch, , in the SOL
  relative -displacement of a field line towards the divertor per arc length1
  determines projection of in radial/poloidal plane
  in tokamaks, , making 3D effects negligible
  in stellarators, , with  strong impact on energy/momentum transport in SOL
Ratio of - to -transport (predicted)3 very sensitive to :
Adapted from [3]
-transport much more important in stellarators than tokamaks!
1Y. Feng et al, Plasma Phys. Control. Fusion 64 (2022) 125012
2R. König et al, Plasma Phys. Control. Fusion 44 (2002) 2365-2422
3Y. Feng et al, Plasma Phys. Control. Fusion 53 (2011) 024009

## Slide 3: Momentum losses in stellarator SOLS: Not just plasma-neutral friction
  Tokamaks: generally, negligible momentum losses along fieldline until detachment  plasma-neutral friction4
  In stellarators, due to geometrical differences, more mechanisms of momentum loss
  Stellarator momentum loss is not limited to the region directly in front of the target
      increasing momentum losses limit divertor performance (density buildup)
  How do the different stellarator divertors compare in this respect?
4P. C. Stangeby, Plasma Phys. Control. Fusion 60 (2018) 044022
3Y. Feng et al, Plasma Phys. Control. Fusion 53 (2011) 024009
increasing mom losses
[3]

## Slide 4: Three Types of Stellarator Divertors
Island Divertor
1
1
2
2
[V. Perseo]
Machine Examples
W7-AS, W7-X
Helical Divertor
Machine Examples
LHD
Nonresonant Divertor
Machine Examples
HSX, CTH

## Slide 5: Three main types of stellarator divertors
Island Divertor
1
1
2
2
large island chain designed at the plasma edge, intersected by divertor target plates
  islands precess poloidally around the LCFS as they move toroidally
[V. Perseo]
island
separatrix
Shadowed by other targets
Machine Examples
W7-AS, W7-X

## Slide 6: The Target Shadow Region
Tokamak
Island Divertor
9R. Pitts et al, Nuclear Materials and Energy 12 (2017) 60-74
„target shadow“ corresponds to extremely small areas (constructed to avoid leading edges)
0.46
angle of incidence so small that targets must be tilted to ensure engineering feasibility
  large areas of target shadow
Areas can still be wetted from -transport![10]
„wetted area“
full toroidal extent!
0
2π
1Y. Feng et al, Plasma Phys. Control Fusion 64 (2022) 125012
5Y. Gao et al, Nucl. Fusion 60 (2020) 096012
„target shadow“
„target shadow“
„wetted area“
Baffle plates in target shadow were modified in W7-X after heatflux overload observed in first divertor experimental phase!5
  indicates importance of understanding heatflux decay length into this region*
*More details in talk by A. Kharwandikar
Simulations show significant momentum deposition inTSR in W7-X6
6Y. Feng et al, Nucl. Fusion 61 (2021) 086012

## Slide 7: Momentum losses to TSR  Suspected (as part) of density build-up difficulties in W7-X island divertor
nd (Stark Broadening) [1019 m-3]
Line Int. Density [1019 m-2]
[F. Henke PhD Thesis]
moderate increase until frad~50%
strong nd decrease
@
increased momentum losses (ex: into target shadow region) reduces density build-up capability
   issue for particle/heat exhaust!
significant degradation of nd at frad~50%  power starvation detachment
EMC3-Eirene
(approx)
*More Details in F. Henke‘s talk
Difficulties in density build-up  poor particle exhaust7 in W7-X island divertor
Not yet clear if a „closed“ divertor is the full solution, though there are promising results8
7T. Kremeyer et al, Nucl. Fusion 62 (2022) 036023
8N. Maaziz et al, Nuclear Materials and Energy (2025) 42 101886

## Slide 8: Three main types of stellarator divertors
Helical Divertor
utilizes inherent helical geometry of magnetic coils9,10
  X-points follow helical pattern  looks a bit familiar to tokamak geometry
  higher shear near the plasma edge leads to „edge stochastic layer“10
Machine Examples
LHD
9N. Ohyabu et al, Nucl. Fusion 34 (1994) 387
10M. Kobayashi et al, Nuclear Materials and Energy 12 (2017) 1043-1048
3Y. Feng et al, Plasma Phys. Control. Fusion 53 (2011) 024009
[9]
[3]

## Slide 9: Density Build-up in LHD
Historically, no high recycling regime observed in LHD11
Hypothesis11:
  momentum losses between counter-streaming flows
  Enhanced momentum losses from viscous losses between high and low Lc regions (chaos)
Recently: Record neutral pressures observed for a stellarator in LHD12 see talk G. Motojima (Fri)
  Physics mechanism not exactly clear yet?
[11]
[11]
11M. Kobayashi et al, Nucl. Fusion 55 (2015) 104021
12U. Wenzel et al, Nucl. Fusion 64 (2024) 034002

## Slide 10: Three main types of stellarator divertors
Nonresonant Divertor
Utilizes the fact that heat and particles preferentially leave LCFS near regions of high curvature
In a practical sense: „resilient“ divertors whose strikelines are unaffected by changes in the edge rotational transform14
  Necessary for stellarators that exhibit large bootstrap currents
Machine Examples
HSX, CTH
13R. Davies et al, Nucl. Fusion 65 (2025) 076018
14K. Garcia et al, Plasma Phys. Control. Fusion 67 (2025) 035011
15A. Bader et al, Phys. Plasmas 24 (2017) 032506
[13]
strikelines remain localized to same locations with 20kA current evolution15
Example: HSX

## Slide 11: Three main types of stellarator divertors
Nonresonant Divertor
Utilizes the fact that heat and particles preferentially leave LCFS near regions of high curvature
In a practical sense: „resilient“ divertors whose strikelines are unaffected by changes in the edge rotational transform12
  Necessary for stellarators that exhibit large bootstrap currents
Machine Examples
HSX, CTH
[13]
strikelines remain localized to same locations with 20kA current evolution15
Example: HSX
13R. Davies et al, Nucl. Fusion 65 (2025) 076018
14K. Garcia et al, Plasma Phys. Control. Fusion 67 (2025) 035011
15A. Bader et al, Phys. Plasmas 24 (2017) 032506
16A´. Bader et al, Nucl. Fusion 53 (2013) 113036
Relatively unexplored concept, but
  simulation results show poor density build-up16
  Both counter-streaming flows and perpendicular mixing of flux tubes likely responsible
Test show that NRD configurations can be tested on W7-X
  strike lines away from most edge diagnostic locations
HSX, doubled HSX
large island
std island
small island
2 x HSX
HSX
exhibit resiliency

## Slide 12: Three types of stellarator divertors
Island Divertor
1
1
2
2
[V. Perseo]
Machine Examples
W7-AS, W7-X
Helical Divertor
Machine Examples
LHD
[3]
Nonresonant Divertor
Machine Examples
HSX, CTH
[5]
Thus far, the island divertor has shown the most promising results in density build-up at the target.
  Large islands like W7-X minimize momentum losses, but more work needs to be done to improve
Our goal: To advance its maturity such that we have reactor-required performance in heat/particle exhaust

## Slide 13: Preview at the scale of the work ahead of us: First simulation results of reactor-size W7-X17
First observations at W7-X scaled up by factor 417:
  Densities too low, temperatures too high for recombination to take place
    Still (likely) power starvation detachment
    Saturation of nd  -transport effects
  Separation of heat and particle fluxes observed
    Possibly beneficial for pumping
    Could be serious issue for heat exhaust!
  New push for reactor-scale simulations with improvements in computing power!
17Y. Feng et al, J. Nuc. Mat. 438(2013) S497-S500

## Slide 14: Outlook and Conclusions: Stellarator Divertor Operation
Open Questions:
How can we improve density build-up (particle exhaust)/detachment in stellarator divertors?
  Transport
    How to further minimize momentum losses in stellarator devices?
      Access to improved detachment regimes (not just power starvation)
  Hardware
  Is better baffling or target shaping enough to overcome the particle exhaust challenge?
Completely untreated thus far:
  Drift effects/SOL current effects on heat/particle transport (some experimental observations, deep physical understanding missing)
    upcoming code suites  e.g. BOUT++
  Understanding edge turbulence in stellarator devices
    upcoming code suites  e.g. BOUT++, GRILLIX, GBS
How to extrapolate to reactor scale (higher power, larger scale size)?  Talk by V. Perseo
Not presented here but ongoing work: radiation stability, impurity retention Talk by F. Henke

## Slide 15: Back-up Slides

## Slide 16: density buildup
nd (Stark Broadening) [1019 m-3]
Line Int. Density [1019 m-2]
[F. Henke PhD Thesis]
moderate increase until frad~50%
strong nd collapse to detachment
increased momentum losses (ex: into target shadow region) reduces density build-up capability
   issue for particle/heat exhaust!
significant degradation of nd at frad~50%  power starvation detachment
EMC3-Eirene
(approx)
*More Details in F. Henke‘s talk

## Slide 17: Geometrical properties of the stellarator divertor compared to tokamaks
The field line pitch, Θ of the SOL defines the relative -displacement of a field line towards the divertor per arc length15
  determines projection of in radial/poloidal plane
  in tokamaks, , making 3D effects negligible
  in stellarators, , with  strong impact on energy/momentum transport in SOL
Ratio of - to - transport (predicted to be) highly sensitive to the magnetic field line pitch, , within the island[1]:
Adapted from [4]
-transport much more important in stellarators than tokamaks!
2R. König et al, Plasma Phys. Control. Fusion 44 (2002) 2365-2422
4Y. Feng et al, Plasma Phys. Control. Fusion 53 (2011) 024009
8Y. Feng et al, Plasma Phys. Control. Fusion 64 (2022) 125012

## Slide 18: Different areas of the SOL with similar geometric properties
      Main island SOL:
          , i.e. multiple toroidal turns around the core
          Direct and broad contact with the core
      Private flux region (PFR):
          , i.e. 1 or few toroidal turns around the core
          Only contact with the core through X-points
      Target shadow region:
          , i.e. less than one toroidal turn around the core
          No direct contact with the core
          Consequence of discrete targets
      Remnant islands:
          Confined part of the island not intersected by targets
In main island SOL:
Notes: Note: Lc integrated quantity (defined as integral over a flux surface) while local quantity! (the proportionality is not direct)
Note: Lc integrated quantity (defined as integral over a flux surface) while Θ_𝑖 local quantity! (the proportionality is not direct)

## Slide 19: The Target Shadow Region
Tokamak
Island Divertor
9R. Pitts et al, Nuclear Materials and Energy 12 (2017) 60-74
„target shadow“ corresponds to extremely small areas (constructed to avoid leading edges)
0.46
angle of incidence so small that targets must be tilted to ensure engineering feasibility
  large areas of target shadow
Areas can still be wetted from -transport![10]
„wetted area“
full toroidal extent!
0
2π
8Y. Feng et al, Plasma Phys. Control Fusion 64 (2022) 125012
10Y. Gao et al, Nucl. Fusion 60 (2020) 096012
„target shadow“
„target shadow“
„wetted area“
Baffle plates in target shadow were modified after heatflux overload observed in first divertor experimental phase!
  indicates importance of understanding heatflux decay length into this region*
*More details in talk by A. Kharwandikar
in simulations, most momentum flux deposited on target shadow region!11
11Y. Feng et al, Nucl. Fusion 61 (2021) 086012

## Slide 20: Geometrical properties of the stellarator divertor compared to tokamaks
[2]
Ti,e , Θi large enough to poloidally bring heat to X-point
large , smaller Θi  significant radial transport
The field line pitch, Θ of the SOL defines the relative -displacement of a field line towards the divertor per arc length15
  determines projection of in radial/poloidal plane
  in tokamaks, , making 3D effects negligible
  in stellarators, , with  strong impact on energy/momentum transport in SOL
shear at resonant surface
radial resonant field component
poloidal mode number of islands
Ratio of - to - transport (predicted to be) highly sensitive to the magnetic field line pitch, , within the island[1]:
2R. König et al, Plasma Phys. Control. Fusion 44 (2002) 2365-2422
4Y. Feng et al, Plasma Phys. Control. Fusion 53 (2011) 024009
8Y. Feng et al, Plasma Phys. Control. Fusion 64 (2022) 125012

## Slide 21: Momentum losses in stellarator SOLS: Not just plasma-neutral friction
Stellarators have additional sources of momentum losses compared to tokamaks
  Tokamaks: generally, small momentum losses along fieldline until detachment  plasma neutral friction??
In stellarators:
  friction between counter-streaming flows (small islands)
  -exchange between field lines of long, short Lc
    viscous losses
  momentum transport into target shadow region
??P. C. Stangeby, Plasma Phys. Control. Fusion 60 (2018) 044022
well-separated flow bundles reduce momentum exchange
„small“ island
large island
[14]
[15]
*Particularly prevalent in SOLs with significant chaos  helical/NRD divertors!
increasing mom losses
The island divertor likely has the lowest momentum losses compared to other stellarator divertor concepts  best performance
Counterstreaming flows well-separated
low-shear (required for large islands) means enhanced viscous losses from distorted flux tubes are minimal
Still, transport in the island divertor differs significantly from the tokamak
ex: significant -transport into target shadow region