## Slide 1
The “Chimney” divertor: A closed divertor with mid-leg pumping for core-edge integration in DIII-D
Presented by
Bob Wilcox1*
with
J.H. Yu2, A. Holm3, M.W. Shafer1, T. Elsey2, S.L. Allen3, W. Choi2, M.E. Fenstermacher3, F. Glass2, M. Groth4, J. Hicok2, C.T. Holcomb3, R. Hood5, C.J. Lasnier3, A.W. Leonard2, J.D. Lore1, R. Maurizio2, A.G. McLean3, W. Meyer3, A. Moser2, C. Murphy2, J. Ren6, T. Rognlien3, G. Ronchi1, F. Scotti3, C. Tsui5
1Oak Ridge National Laboratory
2General Atomics
3Lawrence Livermore National Laboratory
4Aalto University
5Sandia National Laboratories
6University of Tennessee – Knoxville
*contact: wilcoxrs@ornl.gov
IAEA Divertor Concepts Meeting
October 30, 2025
1
10
100

## Slide 2: A novel divertor design has been developed with the goal of improving both access to detachment and detachment control via mid-leg pumping
Pumping part way along the baffled divertor leg keeps neutral gas particles localized where they are useful for power dissipation
  SOLPS and UEDGE simulations find that this design robustly maintains a detached target (Te,targ < ~1 eV) with a hot fusion core (Te,Xpt > ~60 eV)
  Te,targ and q⟂ are predicted to be reduced for a given ne,sep
A “chimney” divertor has been designed to test this concept of mid-leg pumping in DIII-D
  Experiments will test simulation predictions, establish parametric dependencies
  Planning now to add reactor-relevant material(s)
Simulated Te (eV)
1
10
100

## Slide 3: Outline: DIII-D Chimney Divertor
Neutral particle control as a tool for detachment access and stabilization
Chimney divertor design and experimental goals

## Slide 4: Outline: DIII-D Chimney Divertor
Neutral particle control as a tool for detachment access and stabilization
Chimney divertor design and experimental goals

## Slide 5: Te-dependent dissipation processes require volume (L∥) for the target plasma to be detached without core confinement degradation
Goal
Colder, denser core, can be unstable
1D cartoon
Hot core

## Slide 6: Without careful control, detachment front often migrates to the X-point, negating benefit of the longer divertor leg
Hot core
1D cartoon

## Slide 7: Magnetic geometry can improve access and stability of detachment, but this can be constraining for reactor design
(Fraction of the exhaust flux tube in the divertor)
B. Lipschultz et al., Nucl. Fusion 56 (2016) 056007
K. Verhaegh et al., Nucl. Fusion 63 (2023) 016014
Decreasing field strength, long divertor legs are found to be stabilizing for detachment
  MAST-U is a good example of a magnetic geometry with stable detachment front
  Unstable example: short, vertical leg
    High triangularity is desirable for pedestal stability
  Modifications to basic DLS model find L∥, flux expansion more important
    C. Cowley et al., Nucl. Fusion 62 (2022) 086046

## Slide 8: Magnetic geometry can improve access and stability of detachment, but this can be constraining for reactor design
(Fraction of the exhaust flux tube in the divertor)
B. Lipschultz et al., Nucl. Fusion 56 (2016) 056007
K. Verhaegh et al., Nucl. Fusion 63 (2023) 016014
Decreasing field strength, long divertor legs are found to be stabilizing for detachment
  MAST-U is a good example of a magnetic geometry with stable detachment front
  Unstable example: short, vertical leg
    High triangularity is desirable for pedestal stability
  Modifications to basic DLS model find L∥, flux expansion more important
    C. Cowley et al., Nucl. Fusion 62 (2022) 086046
Internal PF coils can be an engineering challenge and experience high neutron flux, so it would be helpful to have other tools

## Slide 9: Pumping particles from a reactor divertor is necessary for He ash removal and core density control, but deprives neutral dissipation processes
Modified from R. Maingi et al., Nucl. Fusion 39 (1999) 1187
Historically, positioning pump near the strike point provides efficient particle removal
  Capture neutral particles sourced by recombination at the divertor target
  Core density can be minimized
  Efficient pumping for density control has been a primary goal of most experimental divertors
Pump duct
Pump

## Slide 10: Pumping particles from a reactor divertor is necessary for He ash removal and core density control, but deprives neutral dissipation processes
Modified from R. Maingi et al., Nucl. Fusion 39 (1999) 1187
Historically, positioning pump near the strike point provides efficient particle removal
  Capture neutral particles sourced by recombination at the divertor target
  Core density can be minimized
  Efficient pumping for density control has been a primary goal of most experimental divertors
Pump duct
Pump
But absolute minimization of particle inventory is not necessarily the primary goal of a divertor in a reactor
  Particles are a key element required for thermal dissipation in the divertor

## Slide 11: Can pumping part way up a “closed” divertor leg stabilize the detachment front before it migrates to the X-point and degrades the core?
Neutrals are desirable in the divertor
Neutral friction and CX ∝ nn
D0 ionization ∝ nD0
ions
neutrals
1D cartoon
Neutrals can be undesirable in the main chamber

## Slide 12: Can pumping part way up a “closed” divertor leg stabilize the detachment front before it migrates to the X-point and degrades the core?
Neutrals are desirable in the divertor
Ideally remove neutrals here
Neutral friction and CX ∝ nn
D0 ionization ∝ nD0
ions
neutrals
1D cartoon
Neutrals can be undesirable in the main chamber

## Slide 13: Coupled fluid-kinetic boundary modeling with SOLPS-ITER finds that pumping upstream from the divertor target increases neutral density and lowers Te at target
Pumping locations
Upstream pumping in simulations:
Higher neutral density at divertor target relative to main chamber
J. Yu et al., Nucl. Mat. Energy 41 (2024) 101826
SOLPS-ITER
Previous related work: C. Sang et al., Nucl. Fusion 61 (2021) 016022

## Slide 14: Coupled fluid-kinetic boundary modeling with SOLPS-ITER finds that pumping upstream from the divertor target increases neutral density and lowers Te at target
Pumping locations
Upstream pumping in simulations:
Higher neutral density at divertor target relative to main chamber
Lower Te and peak heat flux at the outer divertor target for a given core density
J. Yu et al., Nucl. Mat. Energy 41 (2024) 101826
SOLPS-ITER
Previous related work: C. Sang et al., Nucl. Fusion 61 (2021) 016022

## Slide 15: Coupled fluid-kinetic boundary modeling with SOLPS-ITER finds that pumping upstream from the divertor target increases neutral density and lowers Te at target
Pumping locations
Upstream pumping in simulations:
Higher neutral density at divertor target relative to main chamber
Lower Te and peak heat flux at the outer divertor target for a given core density
J. Yu et al., Nucl. Mat. Energy 41 (2024) 101826
SOLPS-ITER
Previous related work: C. Sang et al., Nucl. Fusion 61 (2021) 016022

## Slide 16: Coupled fluid-kinetic boundary modeling with SOLPS-ITER finds that pumping upstream from the divertor target increases neutral density and lowers Te at target
Pumping locations
Upstream pumping in simulations:
Higher neutral density at divertor target relative to main chamber
Lower Te and peak heat flux at the outer divertor target for a given core density
Minimum achievable core density is higher for given particle injection and pumping rate
  Likely acceptable as long as core density remains below stability limits for operational particle throughput
J. Yu et al., Nucl. Mat. Energy 41 (2024) 101826
SOLPS-ITER
Previous related work: C. Sang et al., Nucl. Fusion 61 (2021) 016022

## Slide 17: Outline: DIII-D Chimney Divertor
Neutral particle control as a tool for detachment access and stabilization
Chimney divertor design and experimental goals

## Slide 18: “Chimney” divertor is designed to pump part way up the divertor leg in attempt to stabilize the detachment front, reduce Te,targ and q⟂ for a given core plasma
9 𝜆q
4 𝜆q
IP = 1.8 MA
BT = 2.1 T
q95 = 3.3
𝛌q,Eich = ~1.6 mm @ OMP
16.8 cm
44 cm
Maintain high neutral density near the divertor target surfaces

## Slide 19: “Chimney” divertor is designed to pump part way up the divertor leg in attempt to stabilize the detachment front, reduce Te,targ and q⟂ for a given core plasma
9 𝜆q
4 𝜆q
Maintain high neutral density near the divertor target surfaces
Minimize neutral particles escaping to the main chamber
  Plasma exhaust influx helps to “plug” the slot by ionizing outgoing neutrals
  Minimize charge exchange fluxes to main chamber surfaces
IP = 1.8 MA
BT = 2.1 T
q95 = 3.3
𝛌q,Eich = ~1.6 mm @ OMP

## Slide 20: “Chimney” divertor is designed to pump part way up the divertor leg in attempt to stabilize the detachment front, reduce Te,targ and q⟂ for a given core plasma
Maintain high neutral density near the divertor target surfaces
Minimize neutral particles escaping to the main chamber
  Plasma exhaust influx helps to “plug” the slot by ionizing outgoing neutrals
  Minimize charge exchange fluxes to main chamber surfaces
Experimental flexibility enables variation of X-point position
  Scan outer leg length, flux acceptance into slot
9 𝜆q
4 𝜆q
IP = 1.8 MA
BT = 2.1 T
q95 = 3.3
𝛌q,Eich = ~1.6 mm @ OMP
X-point scans

## Slide 21: Despite strongly vertical leg, both UEDGE and SOLPS-ITER simulations predict a stable detachment front across wide range of power and particle injection
SOLPS-ITER
1
10
100
Te
J. Yu et al., Nucl. Mat. Energy 41 (2024) 101826
UEDGE: A. Holm et al., Nucl. Mat. Energy 41 (2024) 101782

## Slide 22: Despite strongly vertical leg, both UEDGE and SOLPS-ITER simulations predict a stable detachment front across wide range of power and particle injection
SOLPS-ITER
1
10
100
Te
J. Yu et al., Nucl. Mat. Energy 41 (2024) 101826
UEDGE: A. Holm et al., Nucl. Mat. Energy 41 (2024) 101782

## Slide 23: Modeling finds inner leg detachment front does not reach X-point for any experimental inputs using the range of inner leg lengths explored (> ~14.5 cm)
How long should inner leg be to minimize interference with study of outer leg detachment?
  We don’t expect inner leg detachment front to reach the X-point for any inner leg length studied (> 14.5 cm)
UEDGE
10 eV contours
Inner leg = 15 cm
Inner leg = 22 cm

## Slide 24: Modeling finds inner leg detachment front does not reach X-point for any experimental inputs using the range of inner leg lengths explored (> ~14.5 cm)
How long should inner leg be to minimize interference with study of outer leg detachment?
  We don’t expect inner leg detachment front to reach the X-point for any inner leg length studied (> 14.5 cm)
Inner leg length has some small impact on outer leg detachment front position when it is <~17 cm, depending on particle throughput
  LIL = 16.8 cm design point should be ok
  Particle throughput supersedes importance of inner leg length
X-point
Outer Target
–– LFS Leg
- - HFS Leg
Pumping x6
Pumping x0.1
UEDGE

## Slide 25: Relatively rapid, inexpensive iteration of divertor designs is made possible by custom-designed copper pedestals, mica baffling

## Slide 26: Relatively rapid, inexpensive iteration of divertor designs is made possible by custom-designed copper pedestals, mica baffling
Tiles designed to maintain neutral gas pressure in key volumes

## Slide 27: Extensive planned diagnostic suite would enable research to extrapolate physics to next-step devices
Thomson Scattering (Te, ne)
Langmuir probes, surface eroding thermocouples
Neutral gas pressure gauges
In-tile spectroscopy (impurity radiation)

## Slide 28: Summary and future work
A novel divertor design has been developed for DIII-D with the goal of achieving a robustly detached divertor target while maintaining a hot plasma core
  Extensive boundary modeling informs the divertor design, suggests detachment access at lower ne,sep and stability across a broad range of experimental inputs
  Pumping part way up the divertor leg could be applied to a range of plasma shapes, potentially reducing the required volume allocated to the divertor
  Model validation is critical for projecting results to future divertor designs
Installation scheduled for summer & fall 2026 for experiments in 2027
  Experiments would measure divertor conditions and core confinement as magnetic geometry, power and particle inputs are all scanned
  Planning now for future installation of reactor-relevant divertor material(s)
    Likely (but not necessarily) W-coated graphite

## Slide 29: Backup slides

## Slide 30: Fluid boundary plasma and neutral modeling with UEDGE finds a stable detachment front without active control using upstream pumping
contours
UEDGE
X-point
Outer Target
A. Holm (PSI 2024)
A. Holm et al., Nucl. Mat. Energy 41 (2024) 101782

## Slide 31: Adding cross-field drift effects to a subset of SOLPS simulations did not significantly modify the qualitative relationships
SOLPS-ITER

## Slide 32: Tiles designed to minimize line-of-sight between targets and copper, eliminate leading edges from bolt holes near strike points
Shiplapping tiles minimizes line-of-sight between plasma and copper, particularly near targets
  Energetic neutrals can sputter copper, contaminate plasma
Bolt holes avoided near priority strike point positions
  Leading edges from large incident field line angles cause hot spots, excessive material erosion
No bolt holes near strike points

## Slide 33: Tile design incorporates thin, pliable mica sheets to maintain gas pressure and prevent undesirable leakage in key areas
Maintaining high neutral pressure in the slot is critical to the design
  Budget and time constraints preclude new steel structures
Mica sheets will be inserted between tiles to minimize gas pressure loss
  Tile-to-tile gaps are calculated to result in unacceptable leakage rates
  Vacuum “caulk” would be ideal, but pliable ceramic sheets should sufficiently reduce leakage at each tile interface
Minimize gas pressure loss between tiles in divertor slot
Mica (red)

## Slide 34: Mica baffling has been demonstrated to be sufficient to hold gas pressure in presently-installed DIII-D SVR divertor
Mica Gas Baffle
Nose Tile
CFC

## Slide 35: This long-legged, conventional divertor would complement other approaches to detachment in the international tokamak community
Can we achieve a stable detachment front between the target and the X-point using a conventional magnetic geometry?
  Ideally fully detached (Te < ~1 eV at the wall) with a “hot” core (Te,sep >= ~60 eV)
  “Conventional”: no secondary X-points and no poloidal field coils inside the blanket envelope
Mid-leg pumping geometry would be a unique capability
K. Verhaegh et al., Nucl. Fusion 63 (2023) 016014
TCV
(Switzerland)
MAST-U
(UK)
DIII-D Chimney
AUG CRD/XPR
(Germany)
T. Lunt et al., Phys. Rev. Lett. 130 (2023) 145102
S. Gorno et al., Phys. Plasmas 31 (2024) 072504

## Slide 36: Divertor is designed for experimental flexibility to perform strike point sweeps and X-point height scans up to IP=1.8 MA with DIII-D coil set (𝛌q = ~1.6 mm)
IP = 1.8 MA
BT = 2.1 T
q95 = 3.3
𝛌q = ~1.6 mm at OMP
Shape flexibility
16.8 cm
44 cm
9 𝜆q
4 𝜆q

## Slide 37: Changing the target material from graphite may modify integrated divertor physics in critical ways
DIII-D first wall is all made of graphite, including proposed divertor tiles
  Carbon retains D fuel particles, modifies recycling dynamics
Carbon self-regulates by eroding at high Te, cooling the plasma to prevent further erosion
  Control of detachment front with metal target may be less stable without self-regulating C
    Should be less important if target is consistently detached
Carbon radiation increases
up to detachment, then saturates
CII
CIII
CIV
Ly-⍺
Normalized density
A.G. McLean PSI 2021

## Slide 38: Next step: Incorporate reactor-relevant materials
What material(s) should we test? Where?
  Baseline concept is W-coated graphite at the outer target, but we want more ideas
If experiments confirm predictions from modeling, this divertor geometry could ease material requirements
  Reduced material sputtering, peak heat flux for a given plasma core
  Easier detachment control
Goal: demonstrate good core confinement with a reactor-relevant plasma-facing material
???

## Slide 39: UEDGE X-point height scan shows position of radiation front on outer leg is tied to physical structures and pump more than X-point
Total radiated power (D+C, W/m3)

## Slide 40: Magnetic geometry can improve access and stability of detachment, but this can be constraining for reactor design
(Fraction of the exhaust flux tube in the divertor)
B. Lipschultz et al., Nucl. Fusion 56 (2016) 056007
C. Cowley et al., Nucl. Fusion 62 (2022) 086046
Normalized Detachment Threshold

## Slide 41: Installation will test whether some core-edge integration challenges for a reactor can be addressed with advanced divertor design
Can pumping part way up the divertor leg prevent the cold detachment front from migrating to the core plasma?
  Are q⟂ and Te,targ reduced for a given plasma core?
  Does this enable a divertor design that requires less volume / fewer coils in a reactor?
  Does it reduce the quantity of radiating impurities that need to be injected to prevent damage or high-Z impurity influx from divertor materials?
How does chimney divertor performance change with geometric parameters?
  How long does the divertor leg need to be (scan ZXpt)?
  How wide does the slot need to be to keep neutrals contained (scan RXpt)?
Where do computational models need improvement?
  Many details that may become important in dissipative conditions
    Lyman opacity, atomic physics, time-dependent dynamics, cross-field transport, …

## Slide 42: Even for very resilient materials, for stationary pulses, a large fraction of plasma exhaust energy must be radiated away to prevent damage
courtesy of A.G. McLean
ITER1
~SPARC2
~ARC3
1K. Krieger et al., Nucl. Fusion 65 (2025) 043001
2A.J. Creely et al., J. Plasma Phys. 86 (2020) 865860502
3B.N. Sorbom et al., Fusion Eng. & Design 100 (2015) 378
Present assumptions

## Slide 43: Comprehensive set of Langmuir probes and SETCs are planned

## Slide 44: Necessary outer leg length (40-50 cm) determined based on poloidal Te gradient measured with divertor Thomson scattering in open divertor configuration
[A.G. McLean]
Stable detachment front for 9 MW plasma with N seeding
  This is a challenge to keep stable
  ∇pol(Te) ≈ 200 eV / m
If we want ~1 eV at the target and ~80-100 eV at the separatrix
   ~40-50 cm divertor leg
Measurement was with an open, unbaffled divertor
  Might expect neutral baffling to be able to increase this gradient, but we want to make sure the long leg is achievable

## Slide 45: New upper divertor structures should not be a significant constraint on standard LSN plasma shapes, even those approaching DN
Super-H
IBS
ISS
AT

## Slide 46: Tangential cameras have view access to most of the divertor volume for monitoring heat flux and impurity line radiation
TangTV (R+1)
Impurity radiation
IR Periscope (R0)
Heat flux
Bill Meyer, LLNL
Diagnostic camera views with proposed divertor tile structures

## Slide 47: Divertor diagnostic needs are based on 2D evaluation of radiative dissipation
Essential
Langmuir probes
Single TS laser path with multiple vertical positions
SETCs
ASDEX gauges^
Magnetics ^
2D Bolometry
Infrared*
TanTV*
CIS/flows*
In-tile spectroscopy
  MDS, FS, broadband UV/VIS/NIR
Gas lines^
Desired
Ion temperature
EUV/VUV spectroscopy
Important
In-slot views of the single TS laser path
Penning gauges
In-tile thermocouples
Volumetric neutral density
Additional gas lines
Focus on particle AND radiative fluxes
In 2D for spatial identification of radiation
* = Acceptable as-is
^ = Move existing
The rest require significant development

## Slide 48: If model predictions are validated experimentally, “upstream pumping” concept could be beneficial to other magnetic confinement designs
W7-X
Realta Fusion YouTube channel
Add baffling to maximize neutral density near target?
Y. Feng et al., Nucl. Fusion 61 (2021) 086012
Mirror (Realta)
SPARC (CFS)
J.D. Lore et al., Nucl. Fusion 64 (2024) 126054
?
?
A. Kuang et al., J. Plasma Phys. 86 (2020) 865860505

## Slide 49: Having PFR baffling too close to the inner leg can allow neutrals to go through the plasma to get to the pump
Reducing inner wall baffling provides a more-direct path for particles to flow from inner target to the pump without going through the core
=1019 contours (dashed)
=1020 contours (solid)
B⨯∇B
UEDGE
=3 contours (dashed)
=10 contours (solid)

## Slide 50: Sufficient clearance of upstream plasma to walls ensures that most recombination and plasma-wall interaction will happen in the divertor
To minimize ELM particle fluxes that intercepted upstream, request clearance for ~2.5 cm of outboard midplane flux
  Good to have some outer gap to accommodate fast particle orbits as well
  Somewhat conservatively accounts for worst case scenario
[R. Perillo et al., NF 2023]
[W. Choi (Toksys)]

## Slide 51: 12.5 MW, Dpuff = 1.0 E22 s-1, Cpuff = 0.15 E22 s-1
SOLPS-ITER

## Slide 52: 12.5 MW, Dpuff = 2.0 E22 s-1, Cpuff = 0
SOLPS-ITER

## Slide 53: 20 MW, Dpuff = 1.0 E22 s-1, Cpuff = 0
SOLPS-ITER

## Slide 54: 20 MW, Dpuff = 1.0 E22 s-1, Cpuff = 0.15 E22 s-1
SOLPS-ITER

## Slide 55: 20 MW, Dpuff = 2.0 E22 s-1, Cpuff = 0
SOLPS-ITER