## Slide 1: XPR access and stability for different impurities in AUG, JET and DEMO
U. Stroth, M. Bernert, G. Birkenmeier, R. Dux, T. Lunt, O. Pan, V. Rohde, B. Sieglin, and the ASDEX Upgrade Team

## Slide 2: Outline & Objectives
Recap of the reduced XPR model and its extension
Effect of different impurities on XPR height in AUG, JET and DEMO
A word on the stability of XPRs
XPR operation and L-H Power threshold

## Slide 3: Recap of the reduced XPR model and its extension

## Slide 4: Power balance analysis in the XPR volume
XPR power source
    heat conduction
XPR power losses
    impurity line radiation
    neutral deuterium ionization
    charge exchange
Realistic geometry
    flux expansion fexp
    connection length Lc
AUG cross-section
High flux
expansion
[U. Stroth et al., NF 2022]

## Slide 5: XPR power balance and access condition
An increase in neutral density cools the plasma until a radiative collapse occurs
XPR access parameter
n0
Geometry:
flux expansion
connection length
Deuterium fueling
Heating power
[U. Stroth et al., NF 2022]

## Slide 6: Model extension to estimate XPR height and XPR-edge coupling
      Apply the model to more inner volumes
      XPR grows until the local XA value becomes too small
      Upstream Te and Ti profiles are continuously recalculated, taking into account losses in the XPR
Parameters
[U. Stroth et al., PPCF 2025]
n0

## Slide 7: Evolution of XPR and edge temperature profiles AUG, 10 MW heating power, split 70/30 to electrons/ions
XPR profiles Upstream profiles
      XPR reaches a height of 12 cm and dissipates up to 70 % of the heating power

## Slide 8: Comparison with an AUG experiment with 10 MW heating power
      Model reproduced edge temperature drop
Experimental upstream Te profiles
[L. Hofstadler, Master thesis, TU Wien; E. Wolfrum et al. EPS 2025]
The pressure gradient drop near the separatrix may lead to ELM suppression

## Slide 9: The XPR height is directly related to the dissipated power, regardless of impurity species and neutral density

## Slide 10: Study effect of different impurities on XPR height in AUG, JET and EU-DEMO
Reduced divertor compression
sputtering

## Slide 11: Loss curves for the main impurities
      Ar radiates most strongly
      Ne radiates at high temperature
      B radiates at lowest temperature

## Slide 12: Parameters of tokamaks investigated
Reference values taken from SOLPS-ITER runs (Ou Pan). P refers to power crossing the pedestal (in AUG, 1 cm from separatrix). AUG geometry scaled up  a0
Conclusions refer to these parameters

## Slide 13: XPR development for various impurities in AUG
      With Ar or N, heights of 810 cm are reached
      Ne produces only small XPRs
      Both observations are consistent with experiment
[M. Bernert et al., NME 2025]

## Slide 14: XPR development for various impurities in JET
Similar observations as in AUG
        XPR achieved at lower n0, due to low power
        Ar produces XPRs up to a height of 2025 cm at low cAr before the height saturates
        Ne doesn’t produce large XPRs
        This is consistent with JET experiments, where XPR control is only possible with Ar and not with Ne
[T. Bosman et al., NF 2025]

## Slide 15: XPR development for various impurities in JET
      With cAr = 0.3 %, up to 70 % of the power entering the pedestal can be dissipated

## Slide 16: Mixed impurities in JET varying the Ne concentration on a fixed Ar background
The XPR height is mainly determined by the Ar concentration
Adding Ne has only little influence on the XPR height
Core and edge radiation losses are not considered here
   See also the next presentation by Ou Pan

## Slide 17: XPR development for various impurities on DEMO
      Due to the higher edge temperature, large XPRs demand high neutral densities
      Small changes in cAr have a strong effect on XPR height
      With N or Ar, up to 80 % of the pedestal power can be dissipated
      With Ne, the XPR remains small in DEMO either

## Slide 18: Neutral density effect on the XPR for DEMO with Ar
In DEMO, Ar at low concentration can be used to create a strongly dissipative XPR

## Slide 19: A word on XPR stability  see also presentation by Filippo Scotti on DIIID

## Slide 20: XPR instability stability at low XPR temperatures
          Radiation curves at low temperature
      Particle balance in the XPR volume
  At TX < TM a pressure hole develops and a MARFE may be triggered
[U. Stroth et al., NF 2022]

## Slide 21: Effect of boron on an XPR controlled by nitrogen seeding
      A small admixture of B significantly reduces TX; this may affect the XPR stability
      Initial AUG experiments where B was added to an XPR discharge were not conclusive

## Slide 22: On a possible link between XPR physics and the LH power threshold

## Slide 23: CX-losses in X-point region may affect the L-H power threshold density scan without impurities in AUG
      At high neutral pressure, CX losses can reach up to 40 % of the heating power
      This can cause a density dependence of the L-H power threshold as found in scalings  PLH = Psep,crit + Pcx
      …and could introduce a dependence of PLH on divertor closeness, as observed on JET
[H. Meyer et al., Report EFDA–JET–CP(14)03/20]

## Slide 24: L-H power threshold in JET depends on divertor configuration
    The effect of power losses in the XPR region on the L-H transition my be important
[H. Meyer et al., EPS Berlin, 2014]

## Slide 25: Summary & Conclusion
The extended XPR model qualitatively reproduces experimental findings on XPR height and dissipated power
It indicates that neon cannot produce large XPRs in AUG, JET and DEMO
For DEMO, it is indicated that high neutral compression is required for high power dissipation rates at low Argon concentrations
CX losses in the X-point region may influence the L-H power threshold
XPR stability needs to be further investigated (experiments, MHD and turbulence codes)