## Slide 1: First Principles Based Divertor Optimization A Unified MCF Divertor Framework applied to W7-X
Thierry Kremeyer1, A. Menzel1, J. Fellinger1, R. Davies1, D. Boeyaert2, C.P. Dhard1, A. Kharwandikar1, A. Pandey1, M. Jakubowski1, and M. Endler1
1 Max Planck Inst. for Plasma Physics, 17491 Greifswald, Germany
2University of Wisconsin – Madison, Madison, WI, USA

## Slide 2: Mission: Build a fleet of fusion reactors that provide primary energy heat source at market competitive price
Notes: Boil water

## Slide 3: Divertor Reactor performance requirements – He/H exhaust & retention
W7-X
Fusion Triple Product nTτE [1020 m-3 keV s]
Plasma Temperature [keV]
[adapted Reiter FSAT 2010]
FPP
[adapted Reiter NF 1990]
  ΓHe,exh = Γα,1 ΓH,exh = Γp,1
  Function 1: Function 2:
  Exhausted particles do not have to be retained
Function 2:
Function 1:
Γedge,out
Γcore,in
Γexh
[adapted Reiter NF 1990]

## Slide 4: Divertor Reactor performance requirements – He/H exhaust & retention
  ΓHe,exh = Γα,1 ΓH,exh = Γp,1
  Function 1: Function 2:
  Exhausted particles do not have to be retained
6σ – 99.99966%
5σ – 99.977%
4σ – 99.38%
3σ – 93.3 %
2σ – 69%
1σ – 31%
0σ < 31%
Functions
HELIAS He4 Birth rate from [S. Lazerson PPCF 2021]
6σFS
1σFS
2σFS
3σFS
4σFS
5σFS
Separatrix
1
0
Core – burning region Edge P-SOL
Γedge,out
Γcore,in
Γexh
Function 2:
Function 1:
W7-X
Notes: ATTENTION: He exhaust and retention for Stellarators unsolved

## Slide 5
MCF – Toroidal coordinate system
z
R
r
a
3
2
1
ι/2
1
2
3
O-Loop / Magnetic axis
RP
Adapted [Stroht Springer 2018]
Notes: Assumption 1: MCF is commercially more viable than ICF Assumption 2: Gauss‘s law for magnetism = 0 Assumption 3: Poincaré-Brouwer / Hairy Ball theorem Toroid only closed flux surface for = 0 Assumption 4: Magnetic toroid needs a rotational transform ι to compensate for drifts Assumption 5: Toroid is composed of nested flux surfaces, with continuous ι -profile
ι= 5/6 in the low iota, ι= 5/5 in the standard, and at ι= 5/4 in high iota.
n is set by my field periods and is fixed to 5 for W7-X, or is it Tamara? 1/1 island
Joachim -> Jean Boscary -> Kisslinger
No iota limit, but iota is necessary and determined by core optimization
Low iota does 6 toroidal transits, high iota only 4
Poloidal magnetic flux over toroidal magnetic flux
q = m/n > 2 More toroidal turns on good curvature per poloidal turn
Iota limit, practical coil Limit, Joachim, Tamara, Per 2014
Theta = Arctan@B R(z)/Bw(z)
Theta ist in Flux coordinate independent approach (FCI), iota in field-line aligned (FA)
Achieve rotational transform
Stellarator: through external field 𝜾 limits?
Tokamak: through plasma current 𝜾<𝟏/𝟐 necessary for MHD

## Slide 6: 1.1 Divert Plasma Particles – Critical Volumina with one X-Loop
X-Loop(s) described by
0/1
1/1
Magnetic metrics:
Flux expansion X-Loop -> Target
Toroidal
Poloidal
Chaotification: Lyapunov exponent / Greene‘s residue

## Slide 7: 1.1 Divert Plasma Particles – Critical Volumina with one X-Loop
Introduce core source
0/1
1/1
Magnetic metrics:
Flux expansion X-Loop -> Target
Toroidal
Poloidal
Chaotification: Lyapunov exponent / Greene‘s residue

## Slide 8: 1.1 Divert Plasma Particles – Critical Volumina with one X-Loop
Introduce plasma SOL – P-SOL
0/1
1/1
Magnetic metrics:
Flux expansion X-Loop -> Target
Toroidal
Poloidal
Chaotification: Lyapunov exponent / Greene‘s residue

## Slide 9: 1.1 Divert Plasma Particles – Critical Volumina with one X-Loop
Introduce divertor SOL – D-SOL
0/1
1/1
Magnetic metrics:
Flux expansion X-Loop -> Target
Toroidal
Poloidal
Chaotification: Lyapunov exponent / Greene‘s residue

## Slide 10: 1.1 Divert Plasma Particles – Critical Volumina with one X-Loop
Introduce private flux region - PFR
0/1
1/1
Magnetic metrics:
Flux expansion X-Loop -> Target
Toroidal
Poloidal
Chaotification: Lyapunov exponent / Greene‘s residue

## Slide 11: 1.1 Divert Plasma Particles – Critical Volumina with one X-Loop
Consequences without a sink
0/1
1/1
Magnetic metrics:
Flux expansion X-Loop -> Target
Toroidal
Poloidal
Chaotification: Lyapunov exponent / Greene‘s residue

## Slide 12: 1.1 Divert Plasma Particles – Critical Volumina with one X-Loop
0/1
1/1
Magnetic metrics:
Flux expansion X-Loop -> Target
Toroidal
Poloidal
Chaotification: Lyapunov exponent / Greene‘s residue
Will be decoupled from now on
Core
Edge
P-SOL
D-SOL
PFR
Separatrix
Plasma stagnation
Divertor stagnation
5/5

## Slide 13
1.1 Divert Plasma Particles – Critical Volumina with one X-Loop
Core
Edge
P-O-loop
PFR
a6σ
Plasma Stagnation
aP
Γedge,out
ΓD-SOL,out
ΓP-SOL,out
Γcore,out
Γ
P-SOL
D-SOL
Separatrix
Divertor Stagnation
nP-SOL
aP
rP
Γedge,out
nP-SOL
rP
Γedge,out
nP-SOL
rP
Γedge,out
nD-SOL
aD
rD
nD-SOL
rD
nD-SOL
rD
nP-SOL(X-loop) = nD-SOL(X-loop)
ΓD-SOL, out
ΓD-SOL, out
ΓD-SOL, out
nPFR
nPFR
nPFR= 0
X-loop
Separatrix
X-Loop
ηdiversion = Γdiv,in / Γedge,out
Γdiv,in
Notes: Perspective! X-Loop!
Parallel, perpendicular, bi-normal transport

## Slide 14: 1.2 Neutralize Plasma Particles
η0 = Γ0 / Γdiv,in
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
ΓP-SOL,out
Γdiv,in
Target
A Target is defined through it‘s function of intercepting and neutralizing plasma
Notes: Target – shadow modul
shadow auseinander gezogen
shadow nach hinten
Build up each principle

## Slide 15: 1.2 Neutralize Plasma Particles
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
ΓP-SOL,out
Γdiv,in
Γ0
Target
TSR
η0 = Γ0 / Γdiv,in
A Target is defined through it‘s function of intercepting and neutralizing plasma
Notes: Target – shadow modul
shadow auseinander gezogen
shadow nach hinten
Build up each principle

## Slide 16: 1.2 Neutralize Plasma Particles
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
ΓP-SOL,out
Γdiv,in
Γ0
Γ0
Target
TSR
η0 = Γ0 / Γdiv,in
A Target is defined through it‘s function of intercepting and neutralizing plasma
Notes: Target – shadow modul
shadow auseinander gezogen
shadow nach hinten
Build up each principle

## Slide 17: 1.2 Neutralize Plasma Particles
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
ΓP-SOL,out
Γdiv,in
Γ0
Γ0
Γ0
Target
TSR
η0 = Γ0 / Γdiv,in
A Target is defined through it‘s function of intercepting and neutralizing plasma
Notes: Target – shadow modul
shadow auseinander gezogen
shadow nach hinten
Build up each principle

## Slide 18: 1.2 Neutralize Plasma Particles
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
ΓP-SOL,out
Γdiv,in
TSR
Γ0
Γ0
Target
η0 = Γ0 / Γdiv,in
A Target is defined through it‘s function of intercepting and neutralizing plasma
Notes: Target – shadow modul
shadow auseinander gezogen
shadow nach hinten
Build up each principle

## Slide 19: 1.2 Neutralize Plasma Particles
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
ΓP-SOL,out
Γdiv,in
Γ0
Γ0
TSR
Target
Γ0
η0 = Γ0 / Γdiv,in
A Target is defined through it‘s function of intercepting and neutralizing plasma
Notes: Target – shadow modul
shadow auseinander gezogen
shadow nach hinten
Build up each principle

## Slide 20: 1.2 Neutralize Plasma Particles
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
ΓP-SOL,out
Γdiv,in
TSR
Γ0
Γ0
Target
Γ0
Target
TSR
η0 = Γ0 / Γdiv,in
A Target is defined through it‘s function of intercepting and neutralizing plasma
Notes: Target – shadow modul
shadow auseinander gezogen
shadow nach hinten
Build up each principle

## Slide 21: 1.2 Neutralize Plasma Particles
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
ΓP-SOL,out
Γdiv,in
Target
TSR
η0 = Γ0 / Γdiv,in
A Target intercepts and neutralizes plasma
at a connection length Lc,X-T with an incidence angle α and a separatrix angle ζ
Mandatory Requirement | Heatload | Sputtering | Mechanics | Neutrons
Metric |  |  |  | DPA
Mandatory Requirement | Heatload | Sputtering | Mechanics | Neutrons
Metric |  |  |  | DPA
Γ0
Γ0
α
Lc,X-T
View down Separatrix
ζ = 0°(PFR) - 45° - 90° - 135° - 180°(SOL)
ζ
Notes: Target – shadow modul
shadow auseinander gezogen
shadow nach hinten
Build up each principle

## Slide 22: 1.3 Collect Neutral Particles
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
ΓP-SOL,out
Γdiv,in
Target
TSR
ηcoll = Γcoll / Γ0
Γ0
Γ0
Γ0
Pumpopening
Pumping plenum
Γcoll
Notes: Target – shadow modul
shadow auseinander gezogen
shadow nach hinten
Build up each principle

## Slide 23: 1.4 Remove Neutral Particles
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
ΓP-SOL,out
Γdiv,in
Target
TSR
ηremoval = Γexh / Γcoll
Γ0
Γ0
Γ0
Pumpopening
Γcoll
Pumping plenum
Γexh
Notes: Target – shadow modul
shadow auseinander gezogen
shadow nach hinten
Build up each principle

## Slide 24: 1. Performance Function: Particle exhaust
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
ΓP-SOL,out
Γdiv,in
Target
TSR
ηexh = Γexh / Γedge,out
= ηdiversion η0 ηcoll ηremoval
Γ0
Γ0
Γ0
Pumpopening
Γcoll
Pumping plenum
Γexh
Notes: Target – shadow modul
shadow auseinander gezogen
shadow nach hinten
Build up each principle

## Slide 25: 2.1 Pumping plenum containment
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
ΓP-SOL,out
Γdiv,in
Target
TSR
ηplenum-con = 1 - (Γplenum-loss / Γcoll)
Γ0
Γ0
Γ0
Pumpopening
Γcoll
Pumping plenum
Γexh
Γplenum,loss
Notes: Target – shadow modul
shadow auseinander gezogen
shadow nach hinten
Build up each principle

## Slide 26: 2.2 Divertor re-ionization
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
ΓP-SOL,out
Γdiv,in
Target
TSR
ηdiv-re-ion = Γ div-re-ion / (Γ0 – Γexh)
Γ0
Γ0
Γ0
Pumpopening
Γcoll
Pumping plenum
Γexh
Γplenum,loss
Γdiv-re-ion
Notes: Target – shadow modul
shadow auseinander gezogen
shadow nach hinten
Build up each principle

## Slide 27: 2.3 Divertor plugging through a closed divertor
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
ΓP-SOL,out
Γdiv,in
Target
TSR
ηplg = 1 – (Γdiv,loss / Γdiv,in) = ηplg,0 + ηplg,ion
Γ0
Γ0
Γ0
Pumpopening
Γcoll
Pumping plenum
Γexh
Γplenum,loss
Γdiv-re-ion
Γdiv,loss
Divertor Closure – Closed divertor chamber through baffles.
A baffles function is to confine neutral particles in the divertor chamber. They can be placed in the SOL or in the PFR, forming a divertor throat
∧
Notes: Target – shadow modul
shadow auseinander gezogen
shadow nach hinten
Build up each principle

## Slide 28: 2.4 Particle screening
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
ΓP-SOL,out
Γdiv,in
Target
TSR
ηscr = 1 - v 1-
Γ0
Γ0
Γ0
Pumpopening
Γcoll
Pumping plenum
Γexh
Γplenum,loss
Γdiv-re-ion
Γdiv,loss
Divertor Closure – Closed divertor chamber through baffles.
A baffles function is to confine neutral particles in the divertor chamber. They can be placed in the SOL or in the PFR, forming a divertor throat
∧
Γcore,in
Notes: Target – shadow modul
shadow auseinander gezogen
shadow nach hinten
Build up each principle

## Slide 29: A-priori first principle Design Metrics
Performance Function 1: Particle exhaust
ηexh = Γexh / Γedge,out
= ηdiversion η0 ηcoll ηremoval
1.1 Particle diversion
ηdiversion = Γdiv,in / Γedge,out
1.2 Particle neutralization
η0 = Γ0 / Γdiv,in = η0,surf + η0,vol
η0,surf = Γ0,surf / Γdiv,in
1.3 Particle collection
ηcoll = Γcoll / Γ0
1.4 Particle removal
ηremoval = Γexh / Γcoll
1σ – 31%
2σ – 69%
3σ – 93.3 %
Performance Function 2: Particle retention
ηretention = ηsub-con ηdiv-re-inztn ηplg ηscr
2.1 Pumping plenum containment
ηplenum-con = 1 - (Γplenum-loss / Γcoll)
2.2. Divertor re-ionization
ηdiv-re-ion = Γ div-re-ion / (Γ0 – Γexh)
2.3. Divertor plugging
ηplg = 1 – (Γdiv,loss / Γdiv,in) = ηplg,0 + ηplg,ion
2.4. Particle screening
ηscr = 1 - = 1-
1.1
1.2
1.3
1.4
2.1
2.2
2.3
2.4
Exhaust
Retention
4σ – 99.38%
5σ – 99.977%
6σ – 99.99966 %
Mandatory Requirement | Heatload | Sputtering | Mechanics | Neutrons
Metric |  |  |  | DPA
W7-X | 1.67 | ? | > 1 | ?
Mandatory Requirement | Heatload | Sputtering | Mechanics | Neutrons
Metric |  |  |  | DPA
W7-X | 1.67 | ? | > 1 | ?
W7-X
Attractive requirements
Recycling
Radiation
Volume Recombination
T-Core Recycling
W7-X
Winters et al. PPCF 2021
Wenzel et al. NF 2024
Boeyaert et al. PPCF 2024
Varoutis et al. NF 2024
Winters et al. NF 2024
Kremeyer et al. NF 2022
Kremeyer et al. PSI 2022
Haak et al. PPCF 2023
Partesooti et al. NME 2024
Zhang et al. NF 2021
Feng et al. NF 2025
Jakubowski et al. NF 2021
Notes: ACTION: Define one statistical metric for each a-priori function.
Quantify entire divertor function on one slide
As precicse as necessary, as imprecise as possible!
Product: Don‘t need to optimize one function from 4 to 5 sigma, if other processes are below 1
Assume no f_rad, what is f_H_rad that can‘t be avoided?

## Slide 30: A-priori first principle Design Metrics
Performance Function 1: Particle exhaust
ηexh = Γexh / Γedge,out
= ηdiversion η0 ηcoll ηremoval
1.1 Particle diversion
ηdiversion = Γdiv,in / Γedge,out
1.2 Particle neutralization
η0 = Γ0 / Γdiv,in = η0,surf + η0,vol
η0,surf = Γ0,surf / Γdiv,in
1.3 Particle collection
ηcoll = Γcoll / Γ0
1.4 Particle removal
ηremoval = Γexh / Γcoll
1σ – 31%
2σ – 69%
3σ – 93.3 %
Performance Function 2: Particle retention
ηretention = ηsub-con ηdiv-re-inztn ηplg ηscr
2.1 Sub-divertor containment
ηsub-con = 1 - (Γsub-loss / Γcoll)
6. Divertor re-ionization
ηdiv-re-inzn = Γ div-re-inzn / (Γ0 – Γexh)
7. Divertor plugging
ηplg = 1 – (Γdiv,loss / Γdiv,in) = ηplg,0 + ηplg,ion
8. Particle screening
ηscr = 1 - = 1-
Exhaust
Retention
4σ – 99.38%
5σ – 99.977%
6σ – 99.99966 %
Mandatory Requirement | Heatload | Sputtering | Mechanics | Neutrons | Cost/Time
Metric |  |  |  |  | 
W7-X | 1.67 |  |  |  | 
Mandatory Requirement | Heatload | Sputtering | Mechanics | Neutrons | Cost/Time
Metric |  |  |  |  | 
W7-X | 1.67 |  |  |  | 
W7-X
1.1
1.2
1.3
1.4
2.1
Notes: ACTION: Define one statistical metric for each a-priori function.
Quantify entire divertor function on one slide
As precicse as necessary, as imprecise as possible!
Product: Don‘t need to optimize one function from 4 to 5 sigma, if other processes are below 1
Assume no f_rad, what is f_H_rad that can‘t be avoided?

## Slide 31: Distinct Divertor Geometry Concepts
Attached concepts
Reflection into PFR Systematic deviations Reflection into D-SOL
Detached concepts
Re-ionisation on incoming field line Neutrals pointed to Separatrix/Density peak
A
A
A-A
0°(PFR) - 45° - 90° - 135° - 180°(SOL)

## Slide 32: Control Models and Benchmark
VMEC
HINT
Core and Edge field up to LCFS
Diverted field lines / islands
Divertor chamber
Python
Parametric, field aligned Kisslinger
EMC3lite
Plasma code
Neutral code
EMC3
EIRENE
Comsol
Performance result
Analyze
Improve
4/8
8/8
Low fidelity
cyle time
(L-CT)
High fidelity
cyle time
(H-CT)
CATIA/ .stp
Extender
Mercury
Parametric Design
Target maker
  ~ Hours – by hand
  5-30 min – parametric on field line tracer
  300 ms – parametric on gordon
Baffle maker – in development
EMC3Lite
30 s
COMSOL
2 h setup – newbie
20 min setup – experienced
15-30 min ηcollection
4-5 h ηremoval
Mercury
2 min setup
Parallelisation:
Now 15-45 min ηcollection
from 90 min ηcollection
Further reduction through coarsening of grids
Notes: BMW (Kelly hat ihn für CTH genutzt)

## Slide 33: Risk 1 – Drift effects
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Core
ΓP-SOL,out
Γdiv,in
PFR
D-SOL
PFR
D-SOL
Drift effects can move strike line peak by 3 cm
[Hammond et al, PPCF, 2019]
Notes: Target – shadow modul
shadow auseinander gezogen
shadow nach hinten
Build up each principle

## Slide 34: Risk 2 – Perpendicular diffusion coefficient for a FPP
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
ΓP-SOL,out
Γdiv,in
Γ0
Γ0
Γ0
Target
TSR
[Dräger et al, DPG, 2025]
Notes: Target – shadow modul
shadow auseinander gezogen
shadow nach hinten
Build up each principle

## Slide 35
Risks: Drift effects and D┴ prediction

## Slide 36: Establish a traditional optimization method in our community
Notes: Last TG long discussion, I‘d like to use this 2nd chance with a different introduction to the method

## Slide 37: 6σ – Traditional optimization method based on statistical analysis
Plasma physics and nuclear fusion is full of stochastic processes!
How do we quantify them?
Design of landing rockets & safety of human rated spacecraft
Performance, reliability, & safety of nuclear power plants
Continuous quality & process optimization
Stabilize human/nuclear rated unstable systems 16x B83 (5E+15 J) = 12.5E+9 x ITER (6.4E+6 J)
Probability density
Velocity [m/s]
Maxwellian Probability Density Function (PDF)
Notes: Maxwellian PDF
Use standard deviations to quantify and optimize stochastic processes
Common practice applied in:
ARRI Hollywood Colloquium in December

## Slide 38: 6σ – Traditional optimization method based on statistical analysis
Probability density
Velocity [m/s]
Accuracy
Relation of most probable outcome on target
Precision
Scatter within or around Lower Specification Limit (LSL) & Upper Specifiation Limit (USL)
How close are outomes together
σ-level | DPMO (defects per million opportunities) | Yield %
0 | > 691 462 | < 31 %
1 | 691 462 | 31 %
2 | 308 537 | 69 %
3 | 66 807 | 93.3 %
4 | 6 210 | 99.38 %
5 | 233 | 99.977%
6 | 3.4 | 99.99966 %
Maxwellian Probability Density Function (PDF)
Notes: Accuracy Dart board

## Slide 39: 6σ – Often only an upper or lower limit – Example: Sputtering
Probability density
Energy E [eV]
Integrated Maxwellian PDF
Upper Specification Limit – USL
Sputtering Thrershold Eth [eV]
σ-level | DPMO (defects per million opportunities) | Yield %
0 | > 691 462 | < 31 %
1 | 691 462 | 31 %
2 | 308 537 | 69 %
3 | 66 807 | 93.3 %
4 | 6 210 | 99.38 %
5 | 233 | 99.977%
6 | 3.4 | 99.99966 %

## Slide 40: 6σ – Three possible solution strategies
Move USL
Avoid – No solution
Aim low
Solve – Effective solution
Change PDF
Optimize - Efficient solution

## Slide 41: 6σ – DMAIC design cycle to optimize W7-X divertor
Define
Measure
Analyze
Improve
Control
Efficient process
Define
Measure
Analyze
Improve
Control
Today (Part I)
Outlook: W7-X
(Part II)
σ-level | DPMO (defects per million opportunities) | Yield %
0 | > 691 462 | < 31 %
1 | 691 462 | 31 %
2 | 308 537 | 69 %
3 | 66 807 | 93.3 %
4 | 6 210 | 99.38 %
5 | 233 | 99.977%
6 | 3.4 | 99.99966 %
Quality or performance steps one standard deviation apart
Ensures efficient step size
  Too small of step has fixed overhead without gain
  Too large step might stretch system and bring overwhelming complexity to meet excessive requirements
  Enables precise definition of boundaries in distributions
Notes: 80/20 rule
Any physics where the effect is too small for step size can be ignored.
Coarse to fine
Hartmut Zohm – Disruptionmitigation 100% reliable

## Slide 42: 6σ – Often only an upper or lower limit – Example: Sputtering
Probability density
Energy E [eV]
Integrated Maxwellian PDF
σ-level | DPMO (defects per million opportunities) | Yield %
0 | > 691 462 | < 31 %
1 | 691 462 | 31 %
2 | 308 537 | 69 %
3 | 66 807 | 93.3 %
4 | 6 210 | 99.38 %
5 | 233 | 99.977%
6 | 3.4 | 99.99966 %
Quality or performance steps one standard deviation apart
Ensures efficient step size
  Too small of step has fixed overhead without gain
  Too large step might stretch system and bring overwhelming complexity to meet excessive requirements
  Enables precise definition of boundaries in distributions

## Slide 43: 6σ – Often only an upper or lower limit – Example: Sputtering
Quality or performance steps one standard deviation apart
Ensures efficient step size
  Too small of step has fixed overhead without gain
  Too large step might stretch system and bring overwhelming complexity to meet excessive requirements
  Enables precise definition of boundaries in distributions
Probability density
Energy E [eV]
σ-level | DPMO (defects per million opportunities) | Yield %
0 | > 691 462 | < 31 %
1 | 691 462 | 31 %
2 | 308 537 | 69 %
3 | 66 807 | 93.3 %
4 | 6 210 | 99.38 %
5 | 233 | 99.977%
6 | 3.4 | 99.99966 %
Integrated Maxwellian PDF

## Slide 44: 6σ – Often only an upper or lower limit – Example: Sputtering
Quality or performance steps one standard deviation apart
Ensures efficient step size
  Too small of step has fixed overhead without gain
  Too large step might stretch system and bring overwhelming complexity to meet excessive requirements
  Enables precise definition of boundaries in distributions
Probability density
Energy E [eV]
σ-level | DPMO (defects per million opportunities) | Yield %
0 | > 691 462 | < 31 %
1 | 691 462 | 31 %
2 | 308 537 | 69 %
3 | 66 807 | 93.3 %
4 | 6 210 | 99.38 %
5 | 233 | 99.977%
6 | 3.4 | 99.99966 %
Integrated Maxwellian PDF

## Slide 45: 6σ – Often only an upper or lower limit – Example: Sputtering
Quality or performance steps one standard deviation apart
Ensures efficient step size
  Too small of step has fixed overhead without gain
  Too large step might stretch system and bring overwhelming complexity to meet excessive requirements
  Enables precise definition of boundaries in distributions
Probability density
Energy E [eV]
σ-level | DPMO (defects per million opportunities) | Yield %
0 | > 691 462 | < 31 %
1 | 691 462 | 31 %
2 | 308 537 | 69 %
3 | 66 807 | 93.3 %
4 | 6 210 | 99.38 %
5 | 233 | 99.977%
6 | 3.4 | 99.99966 %
Integrated Maxwellian PDF
Notes: In 6 succesful steps to an efficient process or a physical limit

## Slide 46: 6σ – Johari Window
Known Knowns
Things we are aware of and understand
Unknown Unknowns
Things we are neither aware of nor understand
Unknown Knowns
Things we understand but are not aware of
Known Unknowns
Things we are aware of but don‘t understand
Notes: Describe the process by it‘s a priori functions and define a statistical metric for each.
Optimize each individually

## Slide 47: 6σ – Johari Window
Known Knowns
Things we are aware of and understand
Unknown Unknowns
Things we are neither aware of nor understand
Unknown Knowns
Things we understand but are not aware of
Known Unknowns
Things we are aware of but don‘t understand
A posteriori
(Experimental Physics)
Measurement

## Slide 48: 6σ – Johari Window
Known Knowns
Things we are aware of and understand
Unknown Knowns
Things we understand but are not aware of
Known Unknowns
Things we are aware of but don‘t understand
A posteriori
(Experimental Physics)
A priori
(Theory & Engineering)
Unknown Unknowns
Things we are neither aware of nor understand
Measurement
Reasoning
Notes: As and engineer I need to understand principles to apply them

## Slide 49: Why a poloidal tokamak and LHD helical are not resonant
Single Null Double Null
x
o
o
o
o
r
0
π
2π
o
x
X-Loop(s) described by
0/1
1/1
o
o
x
x
o
o
x
o
0/2
0/2
o
x
Homoclinic X-Loops
x
x
o
x
o
o
0/1
0/1
x
x
o
o
o
10/5
0/2
Heteroclinic X-Loops
o
x
Notes: SN: island no 2 pointy ends. Force an X-loopthrough external coil, q95
DN: homoclinic X-loops on one or two surfaces
Heteroclinic: Field lines don‘t have to close on themselves
Kobayashi JNM 2015 different n/m

## Slide 50: Resonance forms separatrix for resonant divertor configurations
Resonant divertor – On rational 𝜾 = 𝒏/𝒎 surfaces, magnetic field lines close on themselves.
A matching spatial magnetic perturbation causes a resonance
Resonant X-Points are homoclinic X-points
In 3D, resonant X-Points form X-Loops with the same 𝜾 as the original rational surface
n = 1
n = 2
n = 3
n = 4
o
𝜾 = 1
x
o
o
o
o
o
x
x
o
o
o
x
x
x
x
o
o
o
o
o
x
x
x
o
r
0
π
2π
r
0
π
2π
r
0
π
2π
r
0
π
2π
r
0
π
2π
o
x
x
x
x
x
x
x
x
x
x
x
x
x
x
o
o
o
o
o
o
o
o
o
Notes: Apoge and Peroge have same distance

## Slide 51: Four possibilities to divert field lines away from a toroid in a divergence free vector field – Whats the best n/m?
Homoclinic X-point/line/loop (connection) Heteroclinic X-point/line/loop (connection)
Homoclinic Tangle (intersection) Heteroclinic Tangle (intersection)
x
x
o
o
x
o
o
x
x
o
o
resonant
non-resonant
x
x
o
o
o
resonant
non-resonant
o
x
Notes: Closed vs open field lines

## Slide 52: Plasma regions and divertor chamber for one leg
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
Sub-divertor
Divertor chamber
ΓP-SOL,out
Γdiv,in
Γdiv,loss
Γcoll
Γexh
D-SOL
PFR

## Slide 53: Hypothetical fv-rec increase
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
Sub-divertor
Divertor chamber
ΓP-SOL,out
Γdiv,in
Γdiv,loss
Γcoll
Γexh
fv-rec
D-SOL
PFR

## Slide 54: Hypothetical fv-rec increase
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
Sub-divertor
Divertor chamber
ΓP-SOL,out
Γdiv,in
Γdiv,loss
Γcoll
Γexh
fv-rec
D-SOL
PFR

## Slide 55: Hypothetical fv-rec increase
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
Sub-divertor
Divertor chamber
ΓP-SOL,out
Γdiv,in
Γdiv,loss
Γcoll
Γexh
fv-rec
D-SOL
PFR

## Slide 56: Hypothetical fv-rec increase
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
Sub-divertor
Divertor chamber
ΓP-SOL,out
Γdiv,in
Γdiv,loss
Γcoll
Γexh
High fv-rec
Aids in fullfilling mandatory heat and sputtering requirements
Maintains divertor performance
fv-rec
56
fs-rec fv-rec
Lamberts cos law isotropic
D-SOL
PFR

## Slide 57: Hypothetical frad increase
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
Sub-divertor
Divertor chamber
ΓP-SOL,out
Γdiv,in
Γdiv,loss
Γcoll
Γexh
D-SOL
PFR

## Slide 58: Hypothetical frad increase
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
Sub-divertor
Divertor chamber
ΓP-SOL,out
Γdiv,in
Γdiv,loss
Γcoll
Γexh
frad
D-SOL
PFR

## Slide 59: Hypothetical frad increase
X-Loop
Edge
P-O-loop
a6σ
aP
Γedge,out
Γcore,out
Γ
P-SOL
Separatrix
Divertor Stagnation
Core
Sub-divertor
Divertor chamber
ΓP-SOL,out
Γdiv,in
Γdiv,loss
Γcoll
Γexh
frad
D-SOL
PFR

## Slide 60: Hypothetical frad increase
X-Loop
Edge
P-O-loop
a6σ
aP
Γcore,out
Γ
Core
Sub-divertor
Divertor chamber
Γcoll
Γexh
frad
High frad
Aids in fullfilling mandatory heat and sputtering requirements
Compromises divertor performance
D-SOL
PFR

## Slide 61: Benchmark
Performance metric | Standard 5/5 | High-Mirror 5/5 | High-Iota 5/4 | Low-Iota 5/6
Particle diversion | 99.86 % | 99.94 % | 99.71 % | 99.93%
Particle collection | 2.94 % | 3.32 % | 3.83 % | 1.01 %
Particle removal | 2.99 % | 3.45 % | 2.84 % | 3.14 %
Particle exhaust | 0.084 % | 0.113 % | 0.108 % | 0.032 %
×
×
=

## Slide 62: Particle collection: Comparison to high-fidelity model
 | AC method | EMC3-Eirene | (Wenzel et al., NF 2024)
Particle collection (Standard configuration) | 2.83 % | 4.0 % - 10.4 % | 0.69 % ± 0.28 %
[D. Boeyaert, PPCFET 2024]

## Slide 63: Particle removal: Comparison to high-fidelity model
AEH port
AEP port
 | AC method |  | DIVGAS |  | EMC3-Eirene
Divertor section | Low-Iota | High-Iota | Low-Iota | High-Iota | Low-Iota
Particle removal | 2.99 % | 2.84 % | 1.9 % - 2.7 % | 3.0 % - 4.0 % | 4.75 % - 5.88 %
[S. Varoutis, NF 2024]

## Slide 64: Divertor Operational performance requirements – Density control
  Stable density in equilibrium
  Γexh = Γsource
  Wall independent density control
  Γexh > Γwall
  Exhaust limited density control
  Γexh < Γwall + ΓNBI + Γpellet (+ΓGas)
  Fueling limited density control
  Γexh > Γwall + ΓNBI + Γpellet (+ΓGas) Combine divertor with throttle
Functions also apply to D/T fuel
Function 1: Exhaust
Function 2: Retention
Notes: INTEREST: Effective but in-efficient exhaust leads to
Wall dependent density control
Limits fueling

## Slide 65: A priori first principle divertor functions
Divert plasma particles
Neutralize plasma particles
Collect neutral particles
Remove neutral particles
Contain particles in sub-divertor
Recycle neutrals in divertor
Plug particles in divertor
Screen impurity particles from core
Survive – Heat, Sputtering, Forces,…
Cost/Time function
Exhaust
Retention
Performance
Mandatory
Out of scope
Notes: ACTION: Break down into a-priori functions

## Slide 66: Complex multi function metrics unsuited for optimization
Neutral pressure scaling
Icc has large impact on 2. and small impact on 3.
[Reimold PSI invited 2024]
[Reimold PSI invited 2024]
[Barbui NF 2020]
Divertor functions
Divert plasma particles
Neutralize plasma particles
Collect neutral particles
Remove neutral particles
Contain particles in sub-divertor
Recycle neutrals in divertor
Plug particles in divertor
Screen impurity particles from core
Notes: Measure it
Understand it: Parallel/Perpendicular transport ratio, Function 2 and 3
Why quantify a priori functions?
Multi-function metric highly non-linear, don‘t know when which function dominates metric
A priori metrics depend on 1 function by definition. Reduces non-linearity

## Slide 67
particle transport through:
Diffusive transport:
Fick’s law ∝ n, Lc, …
Neo-classical transport:
MHD ∝ n, Lc, …
Turbulent transport:
Reynolds ∝ n, Lc, …
Assume all combined as one
random walk process with one D⊥,P
[Stroht Springer 2018]
1. Divert Plasma Particles - SOL width definition
[Stangeby IOP 2000]
Cumulative Gaussian probability distribution function
Normalized poloidal radius [rp/ap]
1 1.01 1.02 1.03 1.04
Γedge,out
nP-SOL
Separatrix
0
Lc
< <
Wall
Notes: Higher n – higher collisionality, particles go to low cosinality

## Slide 68
particle transport through:
Diffusive transport:
Fick’s law ∝ n, Lc
Neo-classical transport:
MHD ∝ n, Lc
Turbulent transport:
Reynolds ∝ n, Lc
Assume all combined as one
random walk process with one D⊥,P
[Stroht Springer 2018]
1. Divert Plasma Particles - SOL width definition
[Stangeby IOP 2000]
[A. Venaille arXiv: Fluid Dynamics 2024]
Turbulent density widths
Notes: Higher n – higher collisionality, particles go to low cosinality

## Slide 69: 2. Neutralize Plasma Particles
      Surface recombination
        Directional neutral particle release: Lambert‘s cosine law
        Particle energy deposited on Awetted: Prec,surf = Γion,tar ((γTi)+(½mionvion²)+εi)
        = sin(α)
      Volume recombination (Detachment)
        Isotropic neutral particle release
        Isotropic energy radiation
        Te decrease through
          Ionization, Dissociation, MAD
T [eV]
<σv> [m3s-1]
[ADAS209,c-r 1996 ADF11 & Verhaegh NF63, 2023]
0
EIR
MAR
Ionization
n0
ne = 1E+21 m-3
ne = 1E+18 m-3
MAD
Dissociation
η0 = Γ0/Γdiv,in = η0,surf + η0,vol
η0,surf = Γ0,surf/Γdiv,in
η0,vol = Γ0,vol/Γdiv,in
Notes: Heat flux to PFM is always conductive, convection only within plasma

## Slide 70: 3. Collect Neutral Particles
      Molecular flow
        Direct collection Only if dSL-PG <
        Optimize
        Indirect collection Build up neutral pressure
        Optimize
        Keep neutrals neutral
        No recycling if not necessary
        Small divertor volume p = n/V
      Continous flow Molecular flow needs to be optimized to achieve it
      Driven by pressure gradient
Target
Lamberts Cosine Law
ηcoll = Γcoll / Γ0

## Slide 71: 4. Remove Neutral Particles
Seff through pump technology
Steady state Turbo Molecular Pumps
Cycled Cryo (activated C coated), Adsorption (Getter, Wall)
Selective He Membrane (molecular sieve), Direct Internal Recycling (DIR), Mass-spectr.
5. Sub-divertor containment
      Molecular flow Directed reflections: pump gap pannel, funnel, chevrons, maze
      Tesla Valve
      Continuos flow at pumpgap Turns pumpgap into one-way
      Minimize
ηremoval = Γexh / Γcoll
ηsub-con = 1 - (Γsub-loss / Γcoll)

## Slide 72: 6. Divertor recycling
[Stangeby IOP 2000]
ηdiv-recy = Γ div-recy / (Γ0 – Γexh)
Γdiv,in
Γ0
Γ recy
Neutralization
Re-ionization
Transport

## Slide 73: 7. Plug Particles
Block escaping neutrals ηplg,0 = 1 – (Γ0,div,loss / Γdiv,in)
      Hardware (Baffles): ∧
      Re-Ionization: minimize
      He is hardest to ionize
Block escaping ions ηplg,ion = 1 – (Γion,div,loss / Γdiv,in)
      Parallel ion transport driven by pressure gradient
ηplg = 1 – (Γdiv,loss / Γdiv,in) = ηplg,0 + ηplg,ion
Divertor
chamber
Plasma
(Main) chamber
[Stangeby IOP 2000]
Upstream
Downstream
Notes: First ionization level!
Plug escaping ions?

## Slide 74: 8. Screen Impurity Particles
Maximize neutral screening by minimizing
Parallel pressure profile in SOL, where do impurities ionize?
Minimize/Prevent ion inward impurity transport:
Electron Root – Te >> Ti
Screening possible in PFR, D-SOL, P-SOL, & Edge
ηscr = 1 - = 1-

## Slide 75: 6. Screen impurity Particles
Intrinsic: H, D, T, He
Seeded: Ne, Ar, N, Xe, Krypton
PFM: 74W, 74 W28Ni26Fe, 73Ta, 14Si6C, 3Li, 50Sn, 5B, 4Be, 8O, 6C (Tritium retention/high Z less sputtering)
EUROFER97: 89.14 % Fe
9% Cr 3σ
1.1% W
0.2 % V (no ADAS)
0.14 % Ta (no ADAS)
0.42 % Mn (no ADAS)
ITER Stahl: Cr, Ni, Mo, Mn, Si, N, P, C, S
http://www.metalcor.de/datenblatt/15/

## Slide 76: 7. Survive – Heat loads
  Material/Technology dependent
    Available PFM: 74W, 74 W28Ni26Fe, 73Ta, 14Si6C, 3Li, 50Sn, 8O, 6C
    Available target technologies:
Swirl tape
?
    W Monoblock W Tile 3D print Liquid
    Tungsten Cu-OFHC CuCrZr
Notes: Heat flux conductive/convective
Cross section type, 11.11. DCD Präsentation heat flux, solid temperature, pressure drop
Get powder out

## Slide 77: 7. Survive – Sputtering
  Energy and material dependant sputtering yield Y
  Reverse Requirement: Impurity release
[SDTrimSP 4.10]
1
1E-1
1E-2
1E-3
1E-4
1E-5
1E-6
Ar
Ne
N
He
T
D
H
Ytungsten
10 100 1000
Energy [eV]
6σ
5σ
4σ
3σ
+
Fuel ion (CX neutral)
Fuel atom
PFM atom
+
physical sputtering
Ep
E6σ
# of particles
Maxwellian PDF
Sputtering nullified if
E6σ < Eth
Chemical sputtering for C, Li, B excluded

## Slide 78: 7. Survive - Neutrons
  Atomic displacement
    ITER 0.14 - 2.5dpa
    DEMO 70 – 80 dpa
  Transmutation
    Rhenium major solid
    He/H formation
  Modifies material properties
    Thermal conductivity
    Brittleness
    Swelling
Lack of material studies with 14 MeV neutrons at high dpa
[Villari FE&D 2013]
[Moslang NF 2005]

## Slide 79: Fault tree analysis structures complexity systematically
ηexh
ηret
ηdiversion
η0
ηcoll
ηremoval
η0,surf
η0,vol
η0,MAR
η0,3-EIR
η0,2-EIR
ηsub-con
ηplg
ηscr
ηdiv-recy
ηpumpgap
ηleak
ηleak1
ηleak2
ηleak3
ηscr,edge
ηscr,PFR
ηscr,D-SOL
ηscr,P-SOL
ηexh,α
ηexh,D/T
ηret,PFM
ηret,seeded
ηret,α