## Slide 1
Experimental characterization and numerical investigation of
X-point radiator regime in WEST
E. Serre1, H. Yang1, Y. Kudashev1, H. Bufferand2, G. Ciraolo2, N. Fedorczak2, N. Rivals2, P. Tamain2 & WEST team2
1Aix Marseille Univ., CNRS, Ecole Centrale Marseille, M2P2 UMR 7340
2IRFM, CEA Cadarache, F-13108 St. Paul-lez-Durance
This work has been carried out within the framework of the EUROfusion Consortium, funded by the European Union via the Euratom Research and Training Programme (Grant Agreement No 101052200 — EUROfusion). Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the European Union or the European Commission. Neither the European Union nor the European Commission can be held responsible for them.
WEST EXP :
#57929
SOLEDGE3X-EIRENE SIMU
Fifth Technical Meeting on Divertor Concepts

## Slide 2
CONTEXT AND MOTIVATIONS
Focus on the rapid dynamics (~ms) observed from attached outer target to XPR [Rivals et al. NME 2024]
Provide new insights on the mechanisms underlying this transition using time-dependent transport simulations
Perform a cross-validation exercice between WEST and SOLEDGE3X-EIRENE [Bufferand et al. NF 2021]
Motivations : the rapid dynamics to XPR
Context: XPR regime in WEST
WEST: a tungsten environment tokamak with an actively cooled ITER-grade divertor operated at CEA Cadarache
Bifurcation into X-point radiator regime is obtained in L-mode discharges with 4MW LHCD
Improved L-mode XPR scenario was obtained lasting >20s [Fedorczak et al. ITPA DivSOL 23]
Notes: ITER successful operation : high performance in the core + controlling heat exhaust [Pitts et al. 2019] Pitts et al. Nucl. Material and Energy 2019

## Slide 3
OUTLINE
WEST EXPERIMENT & SOLEDGE3X-EIRENE SET-UP
TRANSITION FROM ATTACHED TO XPR: EXPE VS SIMU
NUMERICAL INSIGHTS ON XPR DEVELOPMENT
CONCLUDING REMARKS AND PERSPECTIVES

## Slide 4
OUTLINE
WEST EXPERIMENT & SOLEDGE3X-EIRENE SET-UP
TRANSITION FROM ATTACHED TO XPR: EXPE VS SIMU
NUMERICAL INSIGHTS ON XPR DEVELOPMENT
CONCLUDING REMARKS AND PERSPECTIVES

## Slide 5
WEST EXPERIMENT & SOLEDGE3X-EIRENE SET-UP
ne,int,core
ne,int,X
N2 seeding
D₂ puff
Pump
Dynamical set-up:
  (D₂) puff feedback used to control ne,int,core in WEST and global particle balance in SOLEDGE3X
  N seeding prescribed through a feed-forward ramp in WEST and SOLEDGE3X:
  in simu the N feed-forward ramp is accelerated to save running time
#57929 WEST pulse | SOLEDGE3X-EIRENE
Lower Single Null + 4.2 MW of Lower-hybrid resonance heating power injected Key diagnostic : interferometry with line-integrated density in the core (ne,int,core) and around X-point (ne,int,X) | 2D time-dependent transport mode with full drifts + kinetic neutrals with EIRENE Lower Single Null with 2 MW of injected power across core edge interface Exp. like diffusion profile + ballooning Recycling coefficients Rwall,N = 0.9 & Rwall,D = 1 Pump speed = 35 m3/s
Simu
Everything is done to match ne profiles at the outer midplane
Nitrogen-seeded from the Private Flux Region
Expe
Notes: In simu N seeding is X3 due to the interplay with the recycling R=0.9 Reduce R will increase the seeding rate
The jump in D feedback is to maintain particle balance because the pumping is X5 larger in simu than in experiment
2MW correspond to 4.2 – 2 supposed to be radiated. Since the core is not simulated it is the power enterinf the SOL

## Slide 6
OUTLINE
WEST EXPERIMENT & SOLEDGE3X-EIRENE SET-UP
TRANSITION FROM ATTACHED TO XPR: EXPE VS SIMU
NUMERICAL INSIGHTS ON XPR DEVELOPMENT
CONCLUDING REMARKS AND PERSPECTIVES

## Slide 7
Evolution of parameters as a function of time in experiment and simulation
Overall agreement between the two dynamics despite a global time scale reduction in simu :
  Continuous cooling of the inner target down to 5eV
  A sharp and rapid (<10ms) transition [around t∼11s (expe) and t ∼ 0.6 (simu)]
XPR transition markers :
  Initial rise of ne,int,X followed by a rapid drop
  At outer target : temperature cliff + a sharp increase of particle flux
  ∼ X 2 divertor radiation (∼ 80% of the input power radiated)
XPR transition markers
TRANSITION FROM ATTACHED TO XPR
Global time scale reduction in simulation due to a faster ramp-up + quicker wall recycling time
A sharp and rapid dynamics : expe vs simu
Remark: Such quick transition to XPR is only observed when drifts are included
Notes: in the line integrated density across the X point
Why Gamma_e behaves differently between expe and simu?The reason is that the HFS and LFS in the simulation are very ideally isolated from each other, the neutral particle transport is stopped by the hot plasma between two branches, but in the experiment, there is gaps between the Monoblock, which allow the neutral particle to move between the two branches. This makes the HFS deeper detached in the simulation compared with experiment, as more neutrals and impurities confined in the HFS. Thus we see the difference in particle flux.

## Slide 8
Simu (t=0.019s)
Radiation “filament” grows on the HFS divertor before bifurcation
Simu (t=0.869s)
1
2
3
4
Deep XPR Radiation center moves toward the LFS upstream inside the separatrix – consistent with expe
WEST visible synthetic camera model
Post-onset XPR Radiation front penetrates into the X-point region
Attached
Inner detached first
1
2
3
4
TRANSITION FROM ATTACHED TO XPR
A sharp and rapid dynamics : expe vs simu
Time evolution of 2D maps of total power radiation
Bifurcation (~1ms) : the radiation filament jumps from HFS to LFS region
Notes: a quick transition to XPR occurs only in the cases with drifts

## Slide 9
Target profiles: expe vs simu
EXP:
# 58089
: Detachment preliminary happens at inner side before XPR
: rapidly once the XPR transition begins to
profile become almost symmetric after entering XPR
1
2
3
2
1
3
Inner
Outer
1 2
2 3
Time evolutions
- -> After bifurcation both targets are cold (2∽3eV) and dense
TRANSITION FROM ATTACHED TO XPR
Notes: Temperature not so far but density much higher in simulation

## Slide 10
OUTLINE
WEST EXPERIMENT & SOLEDGE3X-EIRENE SET-UP
TRANSITION FROM ATTACHED TO XPR: EXPE VS SIMU
NUMERICAL INSIGHTS ON XPR DEVELOPMENT
CONCLUDING REMARKS AND PERSPECTIVES

## Slide 11
Formation of an electric potential well
2D map of the electric potential in the divertor region from the WEST simulation
During transition from about 80 V to a few volts or negative values ().
Progressively a potential well forms around the onset of XPR at t=0.595s
The deepest well is observed in the post-onset XPR state t=0.599s
It is largely reduced in deep XPR, t=0.869s
NUMERICAL INSIGHTS ON XPR DEVELOPMENT
The onset of the XPR data is obtained at t = 0.595 s
→ Related to plasma cooling around X-point…
(a) t = 0.019 s, attached
(b) t = 0.551 s, inner divertor
detached
(c) t = 0.599 s, post-onset
of XPR
(d) t = 0.869 s, deep XPR

## Slide 12
NUMERICAL INSIGHTS ON XPR DEVELOPMENT
Formation of an electric potential well
With detachment, T significantly at HFS & along the separatrix
Further HFS detachment →neutral and N2 penetration cool the PFR + LFS below the X-point
All regions beside X-point cool down progressively
2D maps of electron temperature in the WEST simulation, showing the transition process to XPR
(a) t = 0.019 s, attached
(b) t = 0.551 s, inner divertor
detached
(c) t = 0.599 s, post-onset
of XPR
(d) t = 0.869 s, deep XPR
Notes: the condition ∇ · ( ∇ ∥ϕ ) > 0 indicates that
ϕ attains a local minimum (“potential well”) along the field line relative to neighboring locations.

## Slide 13
NUMERICAL INSIGHTS ON XPR DEVELOPMENT
Formation of an electric potential well
With detachment, T significantly along the separatrix
Further detachment →neutral and impurity penetration cool the PFR + LFS below the X-point
All regions beside X-point cool down progressively
Time evolution of the terms in Eq. (1) at points beside the X-point.
Mainly driven by an increase of ) ( line) corresponding to the formation of a temperature well, which indicates that strong local cooling takes place.
In the quasi-neutral limit, the overall charge balance leads to
Occurrence at successive times of potential wells beside X-point characterized by ∇·(∇∥ f) > 0 lines
Sketch of the X-point region. Potential wells occur successively on time,
from 1 to 4
1
2
3
4
XPR transition
XPR transition
XPR transition
XPR transition
Notes: the condition ∇ · ( ∇ ∥ϕ ) > 0 indicates that
ϕ attains a local minimum (“potential well”) along the field line relative to neighboring locations.

## Slide 14
Formation of a “X-point vortex”
NUMERICAL INSIGHTS ON XPR DEVELOPMENT
Time evolution of integrated radial component of the total and EXB fluxes (sum of all ion fluxes)
Green arrows indicate the flow direction.
Reversing the sign of modifies the E × B flow pattern
Between t3 = 0.592s and t6 = 0.595s the E × B fluxes grow up to exceed the opposing diffusive fluxes
at t3
between t4 and t7
Together these steps form a closed counterclockwise flow
reversing the total flux at the LFS above the X-point ( ) and below X-point ( ), at the HFS below X-point ( )
Sketch of the fluxes crossing between the LFS sommon SOL and the closed flux region
< t3

## Slide 15
OUTLINE
WEST EXPERIMENT & SOLEDGE3X-EIRENE SET-UP
TRANSITION FROM ATTACHED TO XPR: EXPE VS SIMU
NUMERICAL INSIGHTS ON XPR DEVELOPMENT
CONCLUDING REMARKS AND PERSPECTIVES

## Slide 16
To our knowledge, first time-dependent simulations carried out about XPR transition:
  ☞ Good overall agreement between SOLEDGE3X and WEST
  ☞ Highlight of a E×B convective mechanism driven by the temperature collapse around X-point
  ☞ A « E×B X-point vortex » forms that enhances cross-field transport + impurity accumulation above the X-point
  ➩ a driving a self-reinforcing cycle that speeds up the transition.
CONCLUDING REMARKS AND PERSPECTIVES
Plasma cooling
Change in
Change in ∇_∥ 𝑇
Change in
Change in Φ_
E X B fluxes modification
Plasma cooling
E X B fluxes modification
The XPR regime in WEST (L-mode discharges with 4MW LHCD ) sustained by sufficient nitrogen seeding show a very sharp transition within milliseconds
Sketch of what could be the self-reinforcing mechanism leading to this rapid transition

## Slide 17
CONCLUDING REMARKS AND PERSPECTIVES
Work in progress : Extend the model proposed by Stroth et al. 22 and based upon a power balance with XA > 1
With respect to a fixed configuration:
- when XA>1 et FA>1 at the LFS ⇨ the net plasma flow enters the closed flux region upstream of the X-point
➩ ⤤ nu and ⤥ Tu,
➩ accelerating the transition towards XA> 1 in the closed flux surface
Mainly considers the change of nu and Tu from the upstream midplane, and the increase of n0 from the penetration process.
- ->The E × B driven flux presented here could provide an additional driving mechanism that modifies the evolution of XA , which has not been considered before.
As in Stroth et al. 22, considering a 1D strongly dissipative plasma volume leads
XA and FA evolutions. nu and Tu and n0 are obtained from simulations
XPR transition
(∽15ms)

## Slide 18
THANK YOU