## Slide 1: Nuclear level density from the Oslo method
1st RCM on Updating and Improving Nuclear Level Densities for Applications
24.03.2025
Vetle W. Ingeberg

## Slide 2: Outline
The Oslo Method
Normalization of NLDs
  Auxiliary normalization data
  Interpolation of NLD to Sn
  Systematics of normalization data
Data available from the Oslo group
Ongoing projects

## Slide 3: The Oslo method
Light ion scattering experiments
  p, d, 3He, ⍺ beam
  Typical energy 12-30 MeV
Measure particle-𝛾 coincidences
Gamma-ray energies up to neutron separation energy
≈ 135º
NaI(Tl) or LaBr3(Ce)
Si E-E
telescope
p
Target nucleus
p'

## Slide 4: Oslo Cyclotron Laboratory
Scanditronix MC-35 cyclotron
Built in 1978
First beam 1979
  Protons
  Deutrons
  3He
  4He
He-3 recovery system
CACTUS+SiRi
OSCAR+SiRi

## Slide 5: OSCAR Array
Commissioned in 2018
30 Large volume LaBr3:Ce (3.5x8-inch)
Largest LaBr3:Ce array in the world
Digital data acquisition (XIA Pixie-16)
Excellent energy resolution
  2-2.5% @ 1332 keV
Excellent time resolution
  < 1 ns @ 1332 keV
Excellent efficiency (FE)
  15% @ 1332 keV

## Slide 6: SiRi
Silicon Ring array
Eight trapezoidal particle telescopes
ΔE – E configuration
Front detector: 130 um
Back detector: 1550 um
Eight rings ± 1 degree
Angles:
  40-54 degrees (forward config.)
  126-140 degrees (back config.)

## Slide 7: Fission setup at OCL
Main goal: investigate prompt fission gamma
Secondary goal: NLDs and gSF of nuclei in nuclei heavier than Pb
Expected to be commissioned in fall of 2025

## Slide 8: Oslo method experiment
M. Guttormsen et al., Nucl. Instr. Methods A 648,168 (2011)
≈ 135º
NaI(Tl) or LaBr3(Ce)
Si E-E
telescope
p
Target nucleus
p'
V. W. Ingeberg et al., Phys. Rev. C 106, 054315 (2022)

## Slide 9: The Oslo method with inverse kinematics
≈ 135º
NaI(Tl) or LaBr3(Ce)
Si E-E
telescope
p
Target nucleus
p'
≈ 135º
NaI(Tl) or LaBr3(Ce)
Si E-E
telescope
d
Heavy ion
p'
Deuterated polyethylene targets

## Slide 10: β-Oslo method
Implant radioactive nucleus in a total absorption spectrometer
Initial excitation energy determined by sum-𝛾
Can work with low beam current (down to ≈ 1 particle/s)
Requires sufficient efficiency
Needs careful treatment of NLDs due to narrow spin window populated in β-decay
A. C. Larsen et al., Prog. in Part. and Nucl. Phys. 107, 69 (2019)

## Slide 11: Future experiments: (p, 2p) reaction
Proposal accepted at SAMURAI setup with STRASSE+CATANA
Reaction: 113In(p,2p)112Cd
Will be proof-of-principle experiment
Experiment lead by Takashi Nakamura & Yasuhiro Togano

## Slide 12: Oslo Method in 4 (simple) steps!
Obtain excitation energy tagged gamma spectra
  E.g. light ion scattering, inverse kinematics, etc.
Unfolding method
  Correct for detector response for 𝛾-rays
First generation method
  Obtain distribution of the first emitted 𝛾 in each cascade
Extract NLD and 𝛾SF
V. W. Ingeberg et al., Phys. Rev. C 106, 054315 (2022)

## Slide 13: Extraction of NLD and GSF
Each vector element in r and f is treated as a free parameter
56Fe(p,p’) example:
Data points (“pixels”): 2052
Free parameters: 184
Nfree << Ndata
Runs 50 iterations, but converges often at 10-20 iterations (depending on the case)
Higher order estimates through a least c2-minimization:
See: A. Schiller et al., NIM A 447, 498 (2000)

## Slide 14: Oslo Method: Normalization
V. W. Ingeberg et al., Phys. Rev. C 106, 054315 (2022)
First generation matrix
symmetric under transformation:
Only relative shape of NLD & GSF!
Need to normalize to auxiliary nuclear data to find physical solution!

## Slide 15: Normalization of NLD
Comparison to NLD from tabulated discrete levels
Comparison to NLD at neutron separation energy
  : Average s-wave resonance spacing
  : Parity asymmetry
  : Spin-cutoff parameter
Between Sn and data: Interpolation with some model (usually CT)
Gives the absolute value of the NLD, A, and the slope
V. W. Ingeberg et al., Phys Rev. C 106, 054315 (2022)
63Ni

## Slide 16: Normalization of NLD - discrete levels
Known tabulated discrete levels
NNDC, RIPL-3, ENSDF, XNSDF, etc.
RIPL-3: Evaluated highest excitation energy with complete level scheme
Possible error sources:
  Low energy Yrast states not populated due to high spin
  Difference in underlying structure
  Incomplete level scheme

## Slide 17: Normalization of NLD – NLD at particle threshold
Use resonance spacing at particle threshold to determine NLD:
Where:
  : s-wave resonance spacing, most often neutron resonances, sources such as RIPL-3 and Mughabghab
  : Ground state spin of the A-1 nucleus
  : Parity asymmetry
  : Spin-cutoff parameter

## Slide 18: NLD at particle threshold – neutron resonance parameter
Typically taken from Mughabghab or RIPL-1/2/3
Can be large discrepancies between RIPL and Mughabghab
References are typically hard to track down
  Example 132Xe(n,ɣ):
    RIPL-1/2/3: Ignatyuk, A.V. Contribution to the Second CRP Meeting on RIPL (Vienna, November 1996)
    Mughabghab: Unknown, probably Private Comm.

## Slide 19: When D0 doesn’t exist?
Estimation from neighboring nuclei
Model estimation
Uncertainties are estimated from best fit
Currently considering more appropriate uncertainty estimation
Bayesian approach
Frequentist: Predictive interval
A. C. Larsen et al., Phys. Rev. C 87, 014319 (2013)
M. Markova et al., Phys. Rev. C 106, 034322 (2022)

## Slide 20: NLD at particle threshold – spin distribution
Only model dependent parameter in OM
Typically models used
  Rigid moment of inertia (E&B06)
  Gilbert & Cameron
  Constant temperature (E&B09)
  Fermi-gas (E&B09)
  Tabulated microscopic NLDs
Typical shape (‘Alex’):

## Slide 21: Parity asymmetry
Equiparity often assumed
Seems to be fulfilled in heavier nuclei where more orbitals are accessible
Could have a larger influence on NLDs
GSF often more sensitive
Not much exp. data beyond discrete levels
A. C. Larsen et al., Phys. Rev. C 83, 034315 (2011)

## Slide 22: Interpolation function
Constant temperature model
Backshift fermi-gas
  /
Microscopical NLD models
  HFB+Comb.
Models can often be excluded from raw data
T. Renstrøm et al., Phys. Rev. C 93, 064302 (2016)

## Slide 23: Shape method
Decay to discrete levels
Can obtain the shape of the 𝛾SF
Constrains the slope of OM data
M. Wiedeking et al., Phys. Rev. C 104, 014311 (2021)
For more details see Mathis’ talk!

## Slide 24: Shape method
Possibility of model independent normalization of NLD
Requires reasonably good resolution in Ex and E𝛾 (100-300 keV)
D. Mücher et al., Phys. Rev. C 107, L011602 (2023)
For more details see Mathis’ talk!

## Slide 25: Reaction dependent systematic errors
(d, p) reaction
  Close to Coulomb barrier – reaction resembles a deuteron breakup + neutron absorption
  Limited spin window populated
Test with RAINIER (DICEBOX)
Theoretical spin-parity population
Green’s function transfer formalism
F. Zeiser et al., Phys. Rev. C 100, 024305 (2019)

## Slide 26: Reaction dependent systematic errors
Nd chain: (p,p) and (d,p)
Limited spin population
Shape method indicates that OM overestimates the slope significantly
For (d,p): 11% of full NLD observed
For (p,p): 22% of full NLD observed
Independently confirmed by measurements of ground state band feeding
M. Guttormsen et al., Phys. Rev. C 106, 034314 (2022)

## Slide 27: Reaction Spesific Errors
Initial population determined by side-feeding
M. Guttormsen et al., Phys Rev. C 106, 034314 (2022)

## Slide 28: Sources of errors – unfolding method
Assuming a efficiency reduction of ≈ 20%
A.C. Larsen et al., Phys. Rev. C 83, 034315 (2011)

## Slide 29: Resolution in inverse kinematics
V. W. Ingeberg et al., Eur. Phys. J A 56, 68 (2020)
V. W. Ingeberg et al., Phys. Rev C 106, 054315 (2022)
Direct kinematics, 64Ni(p,d)63Ni
V. W. Ingeberg et al., Phys. Rev. C 111, 015803 (2025)

## Slide 30: Normalization without D0
How in-accurate will the normalization be without D0?
63Ni: D0 and evaporation data does not agree
Could say that OM data favors D0
V. W. Ingeberg et al., Phys. Rev C 106, 054315 (2022)

## Slide 31: Nuclear Level Density: Role of deformation
Role of deformation?
  Mean-field: Breaks degeneracy – reduces NLD
  Vibration: Increases by ≈ 10x
  Rotation: Increases by ≈ 100x
  Overall increase expected to be ≈ 1000x
Investigated the NLD as a function of deformation in Nd isotopic chain
M. Guttormsen et al., Phys. Lett. B 816, 136206 (2021)

## Slide 32: Systematics of NLD in Sn
M. Markova et al., Phys. Rev. C 106, 034322 (2022)
M. Markova et al., Phys. Rev. C 109, 054311 (2022)

## Slide 33: KShell calculations
A large number of nuclei were considered in large-scale shell model calculations with KShell – J. Midtbø et al., Phys. Rev. C 98, 064321 (2018)
Most (all?) were all within the same major shell
From 17O to 80Ga
Will give NLD by Ex, J, π
(May be) limited validity due to truncations, limited model space, etc.

## Slide 34: Ni isotopes
67Ni

## Slide 35: Plan for CRP
Determine the relevant metadata required for user to understand the limitations of a dataset
  Challenge: No ”standard” way of reporting metadata – for some publications these are not reported
Relevant metadata for quality assessment of data sets
Collect tabulated NLD data and metadata
  Need to determine a suitable format
  Consider YAML – both human and machine readable
Tabulate theoretical NLD from KShell calculations
  Need to determine relevant metadata (input file?)
  Consider if these are relevant for the database
Quality assessment of experimental NLD data sets

## Slide 36: Oslo method data available (not complete)