## Slide 1
FNG Tungsten Benchmark Analysis using Pointwise and Multigroup FENDL-3.2 Data
I. Kodeli
FENDL Meeting, IAEA, 13-16 May 2025

## Slide 2: FNG Fusion benchmarks (14 MeV DT source) - FNG-SS Shield (1989) - FNG-ITER Blanket Bulk Shield (1995) - FNG-ITER Neutron Streaming (1997-1998) - FNG-ITER Dose Rate Experiment (2000-2001) - FNG Silicon Carbide (2001) - FNG Tungsten (2002) - FNG HCPB Tritium Breeder Module (2005) - FNG HCLL Tritium Breeder Module (2009) - FNG Cu (2013-2015) - FNG WCLL (2020) - FNG W (2023) - FNG Concrete (late 2025)
Objectives:
Validation of JEFF basic nuclear data of relevance for fusion and/or of fusion reactor components for ITER/DEMO. Pre- & post-analysis using S/U, stored in SINBAD for future use
EUROfusion experimental programme - Frascati Neutron Generator (FNG)
SINBAD Tungsten
- OKTAVIAN Tungsten Sphere
- FNS Tungsten
- FNG Tungsten (2002)
- FNG/TUD Tungsten (spectra)

## Slide 3: FNG-W 2002 FNG-W 2023
Densimet180/176:
42-47 x 46.85 x 49 cm3
W, SS and H2O:
48 x 42 x 39.4 cm3
DENSIMET-180: 7 cm, 3 cm, 3 cm
Perspex: 6 x 2 cm
SS-316: 6 x 2.4 cm

## Slide 4
Measured reaction rates
Ni-58(n,2n)
Zr90(n,2n)
Nb-93(n,2n)
Al-27(n,a)
Fe56(n,p)
Ni-58(n,p)
In115(n,n’)
Au-197(n,g)
Mn55(n,g)
Detector positions:
D1 - 5 cm
D2 - 15 cm
D3 - 25 cm
D4 - 35 cm
D ≈ ± 5 - 6%
Measured reaction rates
Ni-58(n,2n)
Nb-93(n,2n)
Al-27(n,a)
Ni-58(n,p)
In115(n,n’)
Au-197(n,g)
W.186(n,g)
Detector positions (inside SS-316 & W slabs):
D1 – 13.5 cm
D2 - 17.9 cm
D3 - 22.6 cm
D4 – 25.5 cm
D5 – 29.7 cm
D6 - 34.4 cm
D7 - 37.05cm
D8 - 41.5cm
D9 – 44.8 cm
FNG-W 2002 FNG-W 2023

## Slide 5: Calculational tools
Computer Codes (Discrete ordinates)
  MCNP using ENEA Frascati inputs
  DORT (DOORS package) & TWODANT
    P5, S16 approximations, R-Z geometry
    First collision source: GRTUNCL (DORT) and built-in analytic option (TWODANT)
    XSUN-2023/SUSD3D sensitivity & uncertainty package
  Nuclear Data
  W-2002: EFF-3.2, FENDL-2 & -2.1, JENDL-3.3, cross-section data (175 energy groups)
  W-2023: JEFF-3.3, ENDF/B-VIII.0, FENDL-3.2 (175 energy groups)
  Response functions from IRDF-90.2 (2002) & IRDFF (2023)

## Slide 6
XSUN2023 Nuclear Data
(NEA-1882)
- up to 440 nuclides
Transport cross sections in Vitamin-J 175- and ECCO 33- energy groups from JEFF-3.3, ENDF/B-VIII.0, FENDL-3.2 (211n/42g)
Covariance matrices processed by NJOY or ANGELO from:
  JEFF-3.3 in ECCO 33n & VITAMIN-J 175n structures
  ENDF/B-VIII.0 (ECCO 33 & VITAMIN-J 175n)
  FENDL-3.2 (211n/42g)
  Older nuclear data from ENDF/B-VII.1, JENDL-4.0u, COMMARA-2, SCALE-6.0 and IRDFF for limited number of isotopes
Ongoing:
  Extension to other transport codes (DENOVO, THOR)
  Nuclear data (JENDL-5.0, ENDF/B-VIII.1, CENDL-3.2, JEFF-4T)
NJOY Processing Flowchart for Multigroup XS Processing

## Slide 7
FNG-W 2002 vs. FNG-W 2023

## Slide 8
ND sensitivities & uncertainties for: 186W, 197Au, 55Mn, 93Nb, 27Al, 115In reaction rates at deep position (D8) in the block
Dosimetry reaction(D8) | Uncertainty JEFF-3.3 (%) | Top sensitivities | Top uncertainty
93Nb(n,2n) | 7.71 % | 56Fe(n,n’),184,182W(n,2n), 56Fe(n,2n),186W(n,2n),1H(n,n) | 93Nb(n,2n),C(n,n’),186W(n,2n), 56Fe(n,n’),182W(n,n’),56Fe(n,np)
27Al(n,a) | 12.02 | 56Fe(n,n’),184,182W(n,2n), 56Fe(n,2n),186W(n,2n),1H(n,n) | 27Al(n,2n),C(n,n’),56Fe(n,n’), 186W(n,2n),56Fe(n,np),182W(n,n’)
56Fe(n,p) | 3.86 | 56Fe(n,n’),184,182W(n,2n), 56Fe(n,2n),186W(n,2n),1H(n,n) | C(n,n’),56Fe(n,n’),186W(n,2n), 56Fe(n,np),56Fe(n,2n),182W(n,n’)
58Ni(n,p) | 3.50 | 56Fe(n,n’),184,182,186W(n,2n), 1H(n,n),56Fe(n,2n) | 58Ni(n,p),C(n,n’),56Fe(n,n’),186W(n,2n), 56Fe(n,np), 184W(n,2n)
115In(n,n’) | 2.53 | 1H(n,n),56Fe(n,n’),184,182,186W(n,2n), 184W(n,n’) | 184W(n,n’),56Fe(n,n’),C(n,n’), 1H(n,n),186W(n,2n), 56Fe(n,n)
197Au(n,g) | 2.21 | 1H(n,n),56Fe(n,g),56Fe(n,n), 56Fe(n,n’),C(n,n),184W(n,2n) | 184W(n,n’),54Fe(n,g),186,182W(n,n’),183W(n,n), 183W(n,n’)
186W(n,g) | 4.95 | 1H(n,n),56Fe(n,n),56Fe(n,g), 56Fe(n,n’),C(n,n),184W(n,2n) | 186W(n,g),184W(n,n’),54Fe(n,g), 186,182W(n,n’),183W(n,n)
55Mn(n,g) | 4.20 | 1H(n,n),56Fe(n,g),56Fe(n,n), 56Fe(n,n’),C(n,n),184W(n,2n) | 55Mn(n,g),54,57,56Fe(n,g),184,186,182W(n,n’),183W(n,n)
Notes: 8

## Slide 9
MCNP vs. DORT
MCNP input error – Nb instead of In

## Slide 10
MCNP vs. DORT: VERDI detectors not modelled, approx. W/Au self-shielding
Chart: 197Au(n,g)
| 8.3024999999999984 | 12.6525 | 18.052499999999998 | 20.852499999999999 | 25.452499999999997 | 29.6525 | 32.752499999999998 | 36.352500000000006
MCNP-ENEA | 0.89512 | 1.0517 | 0.91068 | 0.87423 | 0.91876 | 0.92592 | 0.87514 | 0.91418
MCNP-corrected | 0.848 | 0.97697 | 0.79129 | 0.8662 | 0.91953 | 0.81341 | 0.87097 | 0.90638
Foil density variations (W, Au)
0 =103 for Au and 1.3.104 for W instead of position dependent ~1.59.103 and 2.6.103

## Slide 11
MCNP vs. DORT
JEFF3.3
ENDF/B-VIII.1
JENDL-5.0
FENDL3.2
CENDL-3.2
JEFF4T4

## Slide 12
MCNP vs. DORT
JEFF3.3
ENDF/B-VIII.1
JENDL-5.0
FENDL3.2
CENDL-3.2
JEFF4T4

## Slide 13
Conclusion
FNG W benchmark studied neutron transport in a shielding composed of layers of tungsten, SS and water;
Activation foils are sensitive to many cross sections: W(n,2n), (n,g), (n,n(‘)), 56Fe(n,n’), (n,g), C(n,n’). Due to complex and multiple cross section dependency the benchmark is likely to validate the overall ND performance rather than resolving specific ND problems;
Good C/E agreement. Excellent agreement between MCNP and DORT. DORT/TORT codes & multigroup XS are still useful: S/U analyses, trend analysis, V&V.
Variations in Au and W foil masses observed, which could be due to variations in radii, thickness or/and density; assuming the radii are as certified the variations of density have 2 to ~5% impact on RR.

## Slide 14
Position | Measured foils masses (g) |  | Foil density (g/cm3) | 
 | Au | W | Au | W
1 | 0.2914 | 0.7285 | 22.90 | 19.09
2 | 0.3080 | 0.6325 | 24.21 | 16.57
3 | 0.3134 | 0.7269 | 24.63 | 19.04
4 | 0.2929 | 0.6231 | 23.02 | 16.32
5 | 0.3065 | 0.6298 | 24.09 | 16.50
6 | 0.3115 | 0.6136 | 24.48 | 16.08
7 | 0.3050 | 0.6491 | 23.97 | 17.01
8 | 0.2885 | 0.6070 | 22.67 | 15.90
Table 6: Foils masses (in grams), error on the last digit.
Foil dimensions (GOODFELLOW) | Foil dimensions | 
 | Au | W
D (mm) | 50 | 150
R (mm) | 9 | 9
r (g/cm3) | 19.3 | 17.5
Up to ~20 higher density for Au than GOODFELLOW values; +-10% for 186W
FNG-W 2023: Foil masses & sizes
Discrepant RR: 115In(n,n’) (-30%) 58Ni(n,p) (+15%) 60Ni(n,p) (0/-50%)
W/SS/H2O layers: 48 x 42 x 39.4cm3
DENSIMET-180: 7/3/3 cm
Perspex: 6 x 2 cm
SS-316: 6 x 2.4 cm

## Slide 15
Position | 197Au(n,g) |  | 186W(n,g) | 
 | Cm/C0 | DCm/C0 | Cm/C0 | DCm/C0
1 | 0.96 | 0.015 | 0.98 | 0.017
2 | 0.94 | 0.012 | 1.02 | 0.015
3 | 0.91 | 0.031 | 1.00 | 0.012
4 | 0.95 | 0.026 | 1.02 | 0.032
5 | 0.96 | 0.030 | 1.02 | 0.036
6 | 0.88 | 0.090 | 1.00 | 0.032
7 | 0.99 | 0.069 | 1.01 | 0.080
8 | 0.93 | 0.095 | 1.03 | 0.114
Table 6: Foils masses (in grams), error on the last digit.
Up to ~20 higher density for Au than GOODFELLOW values; +-10% for 186W
Impact on RR due to self-shielding difference: +-2 to 3% for W, around -5% for Au.
FNG-W 2023: Foil masses & sizes
MCNP-6.3 calculation using FENDL-3.2
ENEA results (MCNP)