## Slide 1: Overview of FENDL: Library, processing methods and tools Presented by: Daniel López Aldama email: dlopezaldama@gmail.com Contributing authors: Tim Bohm, Daniel L. Aldama, Georg Schnabel, Marco Fabbri, Saerom Kwon, Davide Laghi, Andrej Trkov, Alex Valentine, Víctor López, Patrick Sauvan Consultancy Meeting on the Preparation of a Major FENDL Release Vienna 13th – 16th May 2025

## Slide 2: Outline
Overview of FENDL
Nuclear data management tools developed at the NDS/IAEA within the framework of the FENDL project
Future work towards a major release of FENDL
Consultancy Meeting on the Preparation of a Major FENDL Release Vienna 13th – 16th May 2025

## Slide 3: Current status of FENDL
Nuclear Data Sheets 193 (2024) 1-78
(Big paper based on FENDL-3.2b)
Producing, processing, verifying, validating and documenting FENDL: Team effort
Coordinated by NDS/IAEA during decades
Fusion Science and Technology (ANS)
(Special issue on Nuclear Data for Fusion Applications)
Submitted, under review (FENDL-3.2c)

## Slide 4: FENDL Project: From evaluators to final user

## Slide 5: Main updates in evaluations from FENDL-3.2b to FENDL-3.2c
Incident neutrons
  Tungsten (W) isotopes were taken from ENDF/B-VIII.0 (with extended RRR)
  Correction of the reference frame in MF=6 from LAB (LCT=3) to center-of-mass (LCT=2) for the energy-angle distribution of the recoil nucleus of Mn-55, Th-232, and all tungsten (W) isotopes.
Incident protons
  Li-7 data have been replaced with the revised JENDL-5 evaluation from August 2023. (MT=51,601 => MT=5)
Incident deuterons
  Invalid values (NaN) were removed from sections MF3/MT2 and MF6/MT2 for Ti-50, Ba-132, Gd-157, Er-170, W-182
  Web page:
  https://www-nds.iaea.org/fendl/
  GitHub repository:
  https://github.com/IAEA-NDS/FENDL-ENDF

## Slide 6: Main updates in processing methods
Processing codes:
  FENDL-3.2b: incident neutrons - NJOY2016.60+IAEA patches
  incident protons - NJOY2016.49+JAEA patches for Japanese files,
  NJOY2016.60+IAEA patches for the rest of files
  incident deuterons - NJOY99.364+JAEA patches for Japanese files
  NJOY2016.60+IAEA patches for the rest of files
  FENDL-3.2c: NJOY2016.74+NDS/IAEA patches for all incident particles (n, p, d)
  https://github.com/IAEA-NDS/NJOY2016/tree/nds-iaea-njoy2016
  https://github.com/IAEA-NDS/NJOY2016/tree/nds-iaea-njoy2016-dev
Last commit contains:
NJOY2016.78+all NDS/IAEA patches

## Slide 7: Main processing updates
1. Heating and damage calculation (HEATR)
  Adopted upper kinematic limit for total and partial heating numbers [Kasuaki & Konno]
  Corrected heating calculation for MT=102=(n,γ) [yield issue, reported by Wen Yin et. al., 2021)
  Use of the available energy (Ea) for the damage calculation involving charged-particle emitting reactions [suggested by Chen and Bernand, 2022]
2. Probability tables in the Unresolved Resonance Range (PURR)
  Implemented a simple procedure to handle extremely small samples of the total cross section to avoid negative probability tables. Important for processing La-139, Cd-106, Re-185 and Re-187.
3. Correction of energy-angle distribution smoothing for MF6/LAW=1
(ACER and GROUPR)
4. Major updates for incident protons and deuterons (ACER, RECONR)
  Conversion of MF6/LAW=7(laboratory angle-energy distribution) to ACE/LAW=67 to avoid issues with Monte Carlo codes such as MCNP and PHITS.
  Correction of the reconstruction of the scattering cross section and the corresponding angular distribution for the nuclear+interference formalism
  Other “minor corrections”, such as using the correct values of AWI and AWP for charged particles
  Correction of double counting of redundant cross sections when using RECONR and ACER.
https://doi.org/10.61092/iaea.gd60-3d8h

## Slide 8: W-184 heating: HEATR + MF6/(LCT=2)

## Slide 9: W-184 damage: HEATR + MF6/LCT=2

## Slide 10: Cd-106: PURR/URR Ptables
FENDL-3.2b
FENDL-3.2c
Marco, Davide, et al.

## Slide 11: Fe-58: PURR/URR Ptables
Marco, Davide, et al.
FENDL-3.2c
FENDL-3.2b

## Slide 12: Hf-176: PURR/URR Ptables
Marco, Davide et. al
FENDL-3.2c
FENDL-3.2b

## Slide 13: FENDL-3.2c vs FENDL-3.2b for incident neutrons
FENDL-3.2c
FENDL-3.2b
Tim Bohm et. al.
Tim Bohm et. al.
FENDL-3.2c
FENDL-3.2b
Computational benchmarks: Sphere Leakage, FNSF 1-D , ITER-1D,
Experimental benchmarks: Oktavian, TIARA, FNG Bulk Blanket, TUD Fe Slab, ASPIS Iron 88, FNS W—BLKT –TOF
No significant differences were observed between the results of FENDL-3.2b and FENDL-3.2c.
The observed differences are consistent with the updates introduced in FENDL-3.2c.
FNSF 1-D: Flux ratio vs FENDL-2.1
FNSF 1-D: Heating ratio vs FENDL-2.1
Summary of V & V for incident neutrons:

## Slide 14: Charged particles: p + Li-7 : RECONR+ACER updates

## Slide 15: Charged particles: d+Be-9 : RECONR+ACER updates
Ratio=
Elastic scattering ratio max. diff. < 2 % at 20 MeV

## Slide 16: Charged particles: d+d from ENDF/B-VIII.1 (ACER update)
Identical charged-particles using nuclear+interference formalism for the elastic cross-sections

## Slide 17: p+Li-7 spherical shell (MCNP-6.2/6.3 issue MT=601,51)
D.L. Aldama & A. Trkov
Proton Flux/source
Shell sphere:
Ri=10cm
Thickness=2.5mm
Proton source: 10 MeV

## Slide 18: p + C: NJOY2016 updates (LAW61 vs LAW67 MCNP-6.x)
Saerom Kwon & C. Konno

## Slide 19: 5 MeV deuteron integral test : d + Cu
Victor López & Patrick Sauvan (UNED)
TENDL-UNED: P. Sauvan et. al. “Implementation of a new energy-angular distribution of particles emitted
by deuteron induced nuclear reaction in transport simulations”, EPJ Web of Conferences 146, 02010 (2017),
ND2016, https://doi.org/10.1051/epjconf/201714602010

## Slide 20: 5 MeV deuteron integral test: d + C
Victor López & Patrick Sauvan (UNED)
TENDL-UNED: P. Sauvan et. al. “Implementation of a new energy-angular distribution of particles emitted
by deuteron induced nuclear reaction in transport simulations”, EPJ Web of Conferences 146, 02010 (2017),
ND2016, https://doi.org/10.1051/epjconf/201714602010

## Slide 21: 32 MeV deuteron integral test: d + Li
Victor López & Patrick Sauvan (UNED)

## Slide 22: 40 MeV deuteron integral test: d + Li
Victor López & Patrick Sauvan (UNED)

## Slide 23: 9 & 53.8 MeV deuteron integral test: d + Nb
Victor López & Patrick Sauvan (UNED)
TENDL-UNED: P. Sauvan et. al. “Implementation of a new energy-angular distribution of particles emitted
by deuteron induced nuclear reaction in transport simulations”, EPJ Web of Conferences 146, 02010 (2017),
ND2016, https://doi.org/10.1051/epjconf/201714602010

## Slide 24: Tools developed at NDS/IAEA in the frame of FENDL
https://github.com/iaea-nds/fendl-processed
github + git-annex + Apptainer
Managed by G. Schnabel, NDS/IAEA

## Slide 25: endf-parserpy: Read, write, compare, check, convert ENDF-6 files
https://github.com/IAEA-NDS/endf-parserpy
PENDF
MF
https://arxiv.org/pdf/2312.08249

## Slide 26
NJOY
PENDF
PREPRO
PENDF
NJOY
PREPRO
COMPARISON &
EVALUATION TOOLS
EXFOR
DATA
MODEL CODE
DATA
ENDF
JSON
Under development
MF support:
MF1
MF2+MF3
MF4
MF5
MF6
MF12
MF13
MF14
MF15
Be-9(n,2n)
endf-userpy: Interpretation and processing data

## Slide 27: User-oriented multi-layered approach
Phyton
FORTRAN
Higher layer is user-oriented
Data can be obtained at any point of the phase space { E, E’, Ω(μ) }

## Slide 28: Endf-userpy: W-184(n,2n)
endf-userpy: ddxs=compute_dist2d_values(endf_dict, mt=16, zap=1, energies=14.1, energies_out, angle_cosines_out)
G. Schnabel, D. L. Aldama

## Slide 29: endf-userpy: Fe-56(n,p)
G. Schnabel, D. L. Aldama

## Slide 30: endf-userpy: U-235(n,nx)
Neutron production ddxs
delayed neutrons not included
G. Schnabel, D. L. Aldama

## Slide 31: Future work towards a major release of FENDL
Assessment of new evaluations
Review of evaluations in recently released and upcoming nuclear data libraries, including:
  INDEN
  ENDF/B-VIII.1
  JENDL-5
  TENDL-20xx
  JEFF-4
Coverage includes all incident particles (n,p,d) and applications in both Monte Carlo and deterministic codes.
2. Activation Data
Review of data relevant to activation applications and codes such as FISPACT-II, ACAB-2008, and others.
3. Uncertainty Quantification
Generation and assessment of covariance data to support uncertainty quantification.
Verification/Correction of NJOY for processing covariance files (e.g. MF40)
4. Thermal scattering laws inclusion (TSL) for moderator materials
5. Verification & Validation (V&V)
Enhancing and automating the V&V process (JADE, …).
Incorporation of new sets of numerical and experimental benchmarks.
6. Tools for Nuclear Data Management
Development and enhancement of software tools for comparison, manipulation, correction, processing,
visualization, and distribution of nuclear data (e.g., endf-parserpy, endf-userpy, etc.).

## Slide 32: Thank you for your attention
Overview of FENDL: Library, processing methods and tools
Presented by: Daniel López Aldama email: dlopezaldama@gmail.com
Contributing authors: Tim Bohm, Daniel L. Aldama, Georg Schnabel, Marco Fabbri, Saerom Kwon, Davide Laghi, Andrej Trkov, Alex Valentine, Víctor López, Patrick Sauvan
Consultancy Meeting on the Preparation of a Major FENDL Release Vienna 13th – 16th May 2025