## Slide 1: International Nuclear Data Evaluation Network (INDEN) Nuclear data evaluation of structural materials (INDEN-SM) Overview of INDEN structural material evaluations after JEFF-4.0 release
Roberto Capote
Deputy Section Head, NDDU head
On behalf of the whole INDEN collaboration
Andrej Trkov
Josef Stefan Institute, Ljubljana, Slovenia
INDEN-SM meeting, 15-19 December 2025, IAEA HQ, Vienna, Austria

## Slide 2: International Nuclear Data Evaluation Network (INDEN)
https://www-nds.iaea.org/INDEN

## Slide 3: INDEN evaluation strategy
Chart: 
INDEN collaboration is addressing data issues with the following strategy:
Identify data problems through integral validation and feedback
Identify underlying data issues in differential data evaluation (sensit)
Assess available experimental differential data to find alternative solutions to improve integral benchmarks (both shielding and criticality)
Update selected experimental data to the latest standards/references
A GLSQ fit of available comprehensive datasets is the preferred solution
If model is available, use model including correlations as prior
“It doesn't matter how beautiful your theory is,
it doesn't matter how smart you are.
If it doesn't agree with experiment, it's wrong.”
Richard Philips Feynman, Nobel Prize in Physics 1965

## Slide 4
https://www.nndc.bnl.gov/endf-releases/
INDEN fluorine, copper, iron, manganese,
silicon, chromium evaluations adopted
+ JEFF-4.0

## Slide 5
Outlook
Chromium (new data by Maroto et al, n_TOF)
Iron evaluations (new data by Gkatis, Kostal…)
F-19 evaluation (new data by Kostal, Viebach, Knijpstra,…)
Cu evaluations (new JRC exp, RRR evaluation needed)
Future evaluation needs from validation Zr, W, Pb (Ni,V,Bi)
“It doesn't matter how beautiful your theory is,
it doesn't matter how smart you are.
If it doesn't agree with experiment, it's wrong.”
Richard Philips Feynman, Nobel Prize in Physics 1965

## Slide 6: Chromium updates
INDEN evals adopted by JEFF-4.0 and ENDF/B-VIII.1
IAEA/BNL/ORNL/JSI

## Slide 8: Cr-50(n,g) MACS (NEA HPRL)
P. Maroto PhD, Univ. Sevilla, Spain, Sept 2024 (unpub)
MACS30(197Au)=601(23)mb
STD=620(11) mb
MACS30(50Cr)=37.1(20)mb
JEFF-3.3:
MACS30(50Cr)=37.8 mb
INDEN:
MACS30(50Cr)=44.3 mb

## Slide 9
MACS30(50Cr)=37.1(20)mb
JEFF-3.3:
MACS30(50Cr)=37.8 mb
INDEN:
MACS30(50Cr)=44.3 mb
50Cr(n,g) (NEA HPRL) ToF thin (n,g) yield
Cr-53, Cr-50 RRR eval needed using Maroto et al data

## Slide 10: 53Cr(n,g) (NEA HPRL) ToF thin (n,g) yield
INDEN too high
CENDL-3.2 closest
JEFF-3.3 too low
Cr-53, Cr-50 RRR eval needed using Maroto et al data

## Slide 11
T. Czakoj et al, NDST 2025, Madrid, unpublished
Cr-nat broomstick experiment
@ VR-1 reactor, Prague, CZ

## Slide 12: Iron updates INDEN evals adopted by JEFF-4.0 and ENDF/B-VIII.1

## Slide 13
INDEN Fe evaluation
Fe-56 from 850keV up to 4 MeV based on exp. data alone
20-30% leakage underestimation found in ENDF/B-VIII.0
* New INDEN evaluation updated in 2019-2023, inelastic reduced
leakage problem solved
New transmission experiment in Dresden (Junghans, Beyer et al)
Overestimation of transmission near 300 keV
mostly solved by updating the Fe-57 evaluation
See validation of the RRR from Kostal presentation
TO DO:
  New Fe-56 data appear in 2025, see Gkatis presentation, el+inl
  New Fe-54 evaluation undertaken at RPI, check inelastic
  Need of URR for Fe-54 and Fe-57 (see URR discussion later)
  Self-shielding for inelastic in Fe-56 ??

## Slide 14
Fe isotopes (IAEA/JSI), fe57e80m, fe56e80X29r41, fe54e80o
Cr isotopes, BNL/ORNL/IAEA/JSI/CEA, v2.3.2
INDEN updated “structural” evaluations:
see nds.iaea.org/INDEN/ - Validation
SS neutron leakage
(Rez, CZ, 11/2021)
M. Schulc et al, Ann. Nucl. En. 179 (2022) 109433
https://nds.iaea.org/INDEN/data/ALARM-CF-steel-SHIELD-001-final.pdf
This energy region
sensitive to Ni58(n,p)
B-VIII.0 iron:
-20% leakage

## Slide 15: Fe-54 elastic cross sections
G. Gkatis PhD, Aix-Marseille Université, 10 June 2024 (unpub)

## Slide 16: Fe-54 inelastic cross sections
Do we measure shielded INL XS?
See URR work & discussions

## Slide 17: F-19 updates INDEN eval adopted by JEFF-4.0 and ENDF/B-VIII.1

## Slide 18: Issues in 19F(n,el) AD below 1 MeV at forward angles (JENDL colleagues)
  ELISA (JRC) measurements of F-19 needed

## Slide 19: Morgan 76 data adopted << Broder data
By using Morgan derived INL data (nng x 4pi)
F-19(n,inl) reduced by ~40% from 300 keV
B8 & JENDL-5
followed Broder
with REF Fe !

## Slide 20
hmf007
/32-34
19F criticality impact (HEU)  -1000pcm
hmi011
(CURIE)

## Slide 21
CSWEG,
Nobre et al,
ENDF/B-VIII.1 paper
(to be published in 2026)
RPI quasidifferential data (Siemers et al)
45 deg

## Slide 22
CSWEG,
Nobre et al,
ENDF/B-VIII.1 paper
(to be published in 2026)
RPI quasidifferential data (Siemers et al)
150 deg

## Slide 23
Teflon transmis. (TUD) & leakage (Rez)
F-19 validation (post-release)
Data issues below 2 MeV in 2 exps!

## Slide 24
Teflon neutron transmission (TUD, Dresden)
Rez neutron leakage drop below 2 MeV confirmed
in transmission (TUD, Dresden) experiment
Chart: Energy [MeV]
Transmission very sensitive to tot

## Slide 25
Larson x 0.92
F-19: (n,tot) below 2 MeV
All evaluations based on Larson 76 data
Larson 76 x 0.92
consistent !!
with Foster Jr 71
& Abfalterer 2000
f19e80_zt9
to
f19f4t4_tot6

## Slide 26
Teflon neutron leakage (HPD)
f19f4t4_tot6 f19e80_zt9
JEFF-4.0

## Slide 27
Teflon neutron leakage (stilbene)
Neutron leakage drop below 2 MeV
confirmed in broomstick experiments
and JEFF-4.0

## Slide 28
hmf007
/32-34
New 19F criticality impact  -400pcm
hmi011
(CURIE)
-1200 pcm: angular distributions & inelastic (0.1-1 MeV)
-400pcm: total XS below 2 MeV

## Slide 29
INDEN 2024 Cu evaluation
Fast evaluation patched, a new RRR evaluation highly desirable
Corrected emission spectra above 10 MeV
Corrected angular distributions in the RRR
INDEN evals adopted by JEFF-4.0 and ENDF/B-VIII.1

## Slide 30: RPI quasi-differential experiment (2021)
Y. Danon, ENDF/B-VIII.1 paper (submitted)

## Slide 31
Cu isotopes, ORNL/IAEA/JSI (in progress)
INDEN updated “structural” evaluations:
see nds.iaea.org/INDEN/ - Validation
Cu cube, neutron leakage (Rez, CZ)
Schulc et al, Rad.Phys.Chem. 2021
n,
discr.
nds.iaea.org/INDEN/data/ALARM-CF-CU-SHIELD-001
INDEN-2024
ENDF/B-VIII.0

## Slide 32: Fast neutron benchmarks - Cu

## Slide 33: New LANL/NCERC Cu benchmark
JEFF-4.0
0.99983
0.99542
0.99335
AVER BIAS +862 pcm +34 pcm -580 pcm
P. Brain et al, INDEN 2024 meeting, hmf106

## Slide 34: Oktavian shielding 14 MeV benchmark
INDEN (B81 & JEFF-4)
shows excellent
fusion performance
adopted JENDL-4
DDXS above En=10 MeV

## Slide 35: W evaluation IAEA fast eval adopted by JEFF-4.0, and ENDF/B-VIII.0/VIII.1

## Slide 36
R. Han et al, EPJ Web of Conferences 239, 18009 (2020)
https://doi.org/10.1051/epjconf/202023918009
W DT testing @ CIAE, 60 deg

## Slide 37
R. Han et al, EPJ Web of Conferences 239, 18009 (2020)
https://doi.org/10.1051/epjconf/202023918009
W DT testing @ CIAE, 120 deg

## Slide 38
Y. Nie et al. Annals of Nuclear Energy 136 (2020) 107040
https://doi.org/10.1016/j.anucene.2019.107040
W-nat DT testing @ CIAE, 15 cm

## Slide 39
M. Kostal et al, CVR, Rez near Prague, CZ, unpublished
W-nat Cf(sf) testing @ Rez

## Slide 40
Future research @Rez is warranted !!
Teflon, Ti, V, Cr, Ni, Cu, Zr, Mo, W

## Slide 41
Future work
To redo with new data: Cr-53 and Cr-50 (n_TOF, USE)
To improve with new data: Fe (Gkatis), Fe-54 and Fe-57
Need of new total XS data for F-19, new inl data (Knijpstra)
To improve: Zr, W, Pb, Ni, Cu (in the RRR), V, Bi
see Simakov, Kostal presentations on validation
To help with chlorine (Cl) ?
“It doesn't matter how beautiful your theory is,
it doesn't matter how smart you are.
If it doesn't agree with experiment, it's wrong.”
Richard Philips Feynman, Nobel Prize in Physics 1965

## Slide 42: Thank you!
Notes: Thank you!