## Slide 1: Non-linear MHD simulations for ITER
G. Huijsmans1, F. Liu1, A. Loarte1, S. Futatani3, F. Koechl4, M. Hoelzl5, A. Garofalo6, W. Solomon6, P.B. Snyder6, E. Nardon2, F. Orain2, M. Bécoulet2 and JET contributors
Non-linear MHD modelling of ELMs and their interaction with RMPs in rotating plasmas
M. Bécoulet2, F. Orain2, J. Morales2, X. Garbet2, G. Dif-Pradalier2, C. Passeron2, G. Latu2, E. Nardon2, A. Fil2, V. Grandgirard2, G. Huijsmans1, S. Pamela7, A. Kirk7, P. Cahyna8, M. Hoelzl5, E. Franck5, E. Sonnendrücker5, B. Nkonga9
1ITER Organization,2CEA/IRFM, 3Ecole Centrale de Lyon, 4TU Wien, 5IPP/Garching, 6General Atomics, 7CCFE/Culham,
8IPP-ASCR/Prague, 9Universite de Nice

## Slide 2: ELM Control in ITER
Natural ELMs in ITER
  Exp. collisionality scaling: ∆W=20 MJ
  Mitigation to 0.7MJ required
ITER ELM control methods
  Magnetic perturbation coils (RMP)
  Pellet injection
Alternatives?
  Vertical kicks (Y. Gribov, PPC/P3-21)
  QH-mode
Physics basis for ITER
  Prediction natural ELM size requires simulations of multiple ELM cycles
  Physics of RMP ELM mitigation
  Minimum pellet size for ELM trigger, pellet triggered ELM size
  Conditions for QH-mode in ITER
ITER ELM coils

## Slide 3: Outline
Introduction
  ITER ELM control
Non-linear MHD code JOREK
  MHD model, flows
ELMs, multiple cycles
  Diamagnetic flow
ELM control:
  RMPs, ELM mitigation
  Pellet pacing in JET
  QH-mode in DIII-D
Narrow Scrape-off Layer MHD Stability in ITER
Conclusions
TH/6-1Rb
Becoulet et al.
TH/6-1Ra
Huijsmans et al.

## Slide 4: Non-Linear MHD code JOREK
3D toroidal geometry (reduced) MHD code
  full domain, open-closed field lines, resistive wall, vacuum, PF coils
  developed within (mostly) European collaboration
including flows: ion and electron diamagnetic flows, source of toroidal rotation, neoclassical poloidal viscosity
  divertor sheath boundary conditions
JET #77329
V//=Cs
Vneoclassic
Vpoloidal
Eradial
Stationary equilibrium flows

## Slide 5: ELM Simulation: Mode Rotation
Observations in MAST, AUG, KSTAR: ELM precursor rotating poloidally mainly in the electron diamagnetic (=ExB) direction
ELM simulations with consistent poloidal, diamagnetic and parallel flows show linear ballooning mode (~precursor) moving in electron diamagnetic direction (~0.5e*, in the lab frame, Vpol~20-40 km/s)
  mode rotation in ion diamagnetic direction in plasma frame (~0.5i*)
In the non-linear phase:
  Reduction of flows
  Filaments are sheared off in the opposite (ion) direction due to non-linear driven n=0 poloidal flow

## Slide 6: ELM Simulations with Diamagnetic Flows
Experimentally, ELM energy losses are predominantly (2:1) towards the inner divertor
Previously, ELM MHD simulations (not including diamagnetic flow) yielded larger heat load asymmetry towards the outer divertor
Including diamagnetic flows leads to a symmetric distribution (1:1) of ELM divertor heat loads
*=0 (no diamagnetic flows)
including *,Vneo, Vtor
Divertor Power

## Slide 7: MHD Simulation of Multiple ELM Cycles
Without diamagnetic flow:
  residual MHD after ELM crash prevents pedestal rebuild => single ELM
  ELM size depends on initial conditions (no reliable ELM size predictions)
Including diamagnetic flows: regular ELMy regime
  Stabilisation of residual MHD by diamagnetic flows allows pedestal rebuild
  Small high frequency ELMs (~500-2000 Hz)

## Slide 8: RMP ELM Mitigation
JET #77329, Error Field Correction Coils (EFCC), n=2
Large discrete ELMs are replaced by small bursty events- continuous MHD
  Due to non-linear coupling of toroidal harmonics by low-n RMP
  Threshold in RMP coil current
Divertor peak heat flux reduced up to factor ~10
[Becoulet, PRL2014]
RMP on
magnetic energy perturbation
RMP off
density perturbation

## Slide 9: ELM Mitigation by RMPs
Ballooning mode structure of natural ELM changes to modes with tearing parity
  Island chains form at q = m/n = 9/4, 14/6 and 15/6
  Modes non-linearly driven through coupling with n=2 RMP fields
no RMP, n=0-8
n=2 RMP
n=2 RMP, n=0-8

## Slide 10: RMP Mitigated ELM Divertor Foot Prints
The divertor footprints of the simulated mitigated ELMs mainly exhibit structures created by RMPs (here n=2), modulated by other toroidal harmonics of mitigated ELMs (n=4,6,8)
  Mitigated ELM perturbation not locked to RMP
[Cahyna, TH/P6-1]
RMP off: rotating footprints with main mode structure n=8 ELM
connection length
RMP n=2 only: static footprints
RMP(n=2)+ELMs: n=2,4,6,8
connection length

## Slide 11: Pellet Triggered ELMs in JET
Previous: pellet triggered ELM simulations in DIII-D
  ELMs (ballooning modes) are triggered by local 3D pressure perturbation created by the pellet
    Density perturbation moving with sound speed, faster parallel conduction
    Reasonable agreement on minimum pellet size required for ELM trigger
Here: complete cycle pellet triggered ELM in JET (#82885)
  Pellets simulated as adiabatic moving density source using NGS ablation model
    Pellet size 3.2x1020, speed 78 m/s , LFS-mid plane, Ip = 2.0 MA, B0 = 2.1T, W = 2.9 MJ
density at the wall

## Slide 12: Pedestal Dependence Pellet Triggered ELMs Size
“Predicted” ELM size 108kJ (∆W/W=4%) compares to 100-250kJ in JET #82885
Experimentally, pellet triggered ELM size increases with time since previous ELM
Non-linear MHD simulations show strong dependence of pellet triggered ELM energy loss on pedestal pressure gradient
  No sharp transition from stable to unstable
  This dependence (and imposed pellet frequency) determines the maximum sustainable pedestal gradient and possible performance penalty due to pellet pacing.
JET #82885
ballooning unstable

## Slide 13: MHD Simulations of DIII-D QH-mode Plasmas
Quiescent H-mode regime characterised by good confinement without ELMs
  discovered in DIII-D, reproduced in AUG, JET, JT60-U
Edge Harmonic Oscillation (EHO) induces density losses and allows a steady state H-mode
  EHO assumed to be a saturated kink-peeling MHD mode
DIII-D QH-modes approaching ITER-relevant conditions
Burrell, NF2013
DIII-D
Burrell, TTF2011
DIII-D
Can QH-mode be an option for ITER?
Towards validation of non-linear MHD simulations on DIII-D QH-mode plasmas
Extrapolation to ITER

## Slide 14: MHD Simulation of DIII-D QH-mode #145117
DIII-D #145117 pedestal close (below) to kink-peeling ideal MHD stability limit
JOREK simulations (ideal wall, no rotation) show saturated kink-peeling mode with dominant n=1 structure (3D stationary state)
  n=5 mode most unstable mode, n=1 strong growth due to non-linear coupling
  Bursting behavior found in some cases at high resistivity
magnetic energy perturbation
magnetic energy perturbation

## Slide 15: EHO: Saturated Low-n Kink-peeling Mode
Toroidal localisation, n=1-5 toroidal harmonics in phase
  Localised density perturbation at the separatrix
  Consistent with EHO observations
Ergodic region (~5cm width in mid-plane)
  Contributes to mode saturation?
perturbed
flux
Poincare
DIII-D #145117
density at separatrix

## Slide 16: QH-mode Density Perturbation
density (ψ=0.95) evolution
ExB flows from external kink/peeling mode leading to a significant outflow of density
  Reduction of pedestal density by ~25%
  Provides density/energy loss channel necessary for stationary ELM free H-mode
n=1
n=2
n=3
n=4
frequency spectrum density
density profiles

## Slide 17: MHD Stability of Narrow SOL in ITER
Scaling laws for the SOL width (in low-recycling regime) predict narrow SOL widths in ITER attached divertor conditions
  Is there an MHD limit to the narrow SOL widths in ITER?
MHD stability analysis shows ITER plasmas with a narrow 1.2mm SOL are MHD stable
  Pressure gradient is below infinite-n ballooning limit at separatrix
  Integrated pedestal/SOL MHD stability using JOREK code finds no local SOL MHD limit (n<50)
perturbed flux (n=40)
Ballooning mode (n=40)

## Slide 18: Conclusions
Nonlinear MHD simulations of ELMs
  Regular ELMy regime (diamagnetic effects)
  ELM precursor rotates in electron diamagnetic direction, filaments mostly in opposite direction
RMP ELM mitigation
  non-linearly driven by RMP modes with “tearing” like structure, providing reconnections with open field lines before large ELMs have time to develop
Pellet triggered ELMs
  reasonable agreement on ELM amplitude
  pellet triggered ELM amplitude depends on phase in ELM cycle
QH-mode
  Simulation of DIII-D QH-mode plasmas show low-n saturated kink-peeling mode, with EHO-like features (density loss, toroidal localisation)
SOL Stability
  No MHD stability limit found for SOL widths down to 1.2mm in ITER
  MHD not likely to limit ITER SOL width