## Slide 1: (FIP/2-5Ra) Development of DC ultra-high voltage insulation technology for ITER NBI H. Tobari et al., (JAEA) (FIP/2-5Rb) Progress in long pulse production of powerful negative ion beams for JT-60SA and ITER A. Kojima et al., (JAEA)
Recent progress on R&D toward Neutral Beam Injector
for ITER and JT-60SA
Rapporteur; Hiroyuki TOBARI
(Japan Atomic Energy Agency)
25th IAEA FEC
13-18 Oct. 2014, St. Petersburg, Russia

## Slide 2: Target and status on NBIs for ITER and JT-60SA
Negative ion beam | (ITER NB) 1 MeV, 40 A, 3600 s | (JT-60SA) 500 keV, 22 A, 100 s
 | on or before FEC 2012 | on FEC 2014
Items | High voltage insulation | 
Insulating transformer | DC 500 kV, 10 s | DC 1 MV, 3600 s
HV bushing | Part test | 1MV vacuum insulation design
 | Long pule beam production & acceleration | 
High current beam | 13 A, 30 s | 15 A, 100 S
High energy beam | 980 keV, 0.4 s | 680 keV, 60 s

## Slide 3
1 MV insulating transformer
【Function of the insulating transformer】
To feed AC power to the PS for negative ion source at DC 1 MV potential.
A bushing extracting output lead at 1 MV from the transformer to the air is needed.
(Issue) f=2 m, H=10 m insulator is required for 1 MV in ITER.
No existing manufacturing facility.
AC power
Extraction bushing
Insulating transformer for JT-60U (DC 500 kV, 10 s)
transformer
~2.5 m

## Slide 4: New 1 MV bushing
Combined with
Simple FRP tube
Small condenser bushing
Condenser bushing(porcelain + aluminum foil + oil-immersed paper)
The 1 MV bushing with manufacturable parts has been newly devised.
【New device】 Composite bushing
Not manufacturable
with manufacturable parts
Air insulation
outside
Oil insulation
inside
Air insulation
outside
SF6 gas insulation
inside
@0.4 MPa
Coax. of

## Slide 5: 1 MV insulating transformer mockup
The 1 MV insulating transformer mockup has demonstrated stable insulation of 1.2 MV for 1 hr (including 20 % margin of rated voltage).
The ITER requirement was achieved.
Transformer
Composite
bushing
The 1 MV insulating transformer has been successfully developed for ITER.

## Slide 6: HV bushing
Transmission line
SF6
Beam source
D0 beam
An insulating feedthrough to transmit 1 MV.
Tritium and vacuum boundary.
The world’s largest ceramic ring is utilized as five-stage insulator (FEC2010).
Vacuum
1MV
200kV
400kV
600kV
800kV
Cooling water pipes
f1.46 m
Conductors
All conductors and pipes at five different potentials (200 kV~1 MV), electrically shielded by five coaxial cylindrical screen (e.g. f=500 mm, H=3.6 m), in a single vacuum space in order to minimize the tritium boundary.
Even with the world’s largest ceramic ring (f1.46 m I.D.), insulation distance of each gap is no more than around 70 mm.
to Tokamak
HV bushing
D-
~70mm
Cross sectional view

## Slide 7
Vacuum insulation of the HV bushing for ITER has been ensured.
f2000 mm
Two-stage mockup
Stable insulation of 480 kV for 1 hr.
(including 20 % margin of rated voltage for ITER )
vacuum insulation design for 1 MV is validated.
Using this scaling, two-stage mockup was designed and and tested.
(Issue) Voltage holding in large coaxial electrodes is not clarified in the field of vacuum insulation.
VHC=31*S-0.13
The dependence of voltage holding capability on surface area was investigated in wide range of surface area.
The empirical scaling for large electrode has been obtained.
Inner structure
Range of

## Slide 8: NBIs on ITER and JT-60SA
ITER NBI
JT-60SA N-NBI
RF-driven negative ion source
Arc-driven negative ion source
Five-stage accelerator
Three-stage accelerator
D- beam
500 keV
22 A, 130 A/m2
100 s
D- beam
1 MeV
40A, 200 A/m2
3600 s
2.7 m
2 m
1.8 m
Cs-seeded negative ion source & Multi-Aperture Multi-Gap (MAMuG) accelerator
(Issue) Long pulse acceleration
(Issue) Long pulse production

## Slide 9
Long pulse production in Cs-seeded source
Plasma grid (PG) temperature control is issued for long pulse production.
A 120-130 A/m2 beams have successfully produced for 100 s (JT-60SA requirement).
Active control of PG temp.
Active temperature control of plasma grid has demonstrated the long-pulse beam production.
Low work function

## Slide 10: Achievement of long-pulse high-current production
  Long pulse production of 15 A negative ion beam, equivalent to 70 % of the beam current (22 A) for JT-60SA, has been achieved for 100 s.
The reduction of beam current on the pulse duration time will be recovered by the feedback control of arc discharge power to produce the higher-current beam.
Active PG temperature control has been applied to produce high current and long pulse negative ion beam in JT-60 negative ion source.
JT-60 negative ion source
IR camera
Beam target
Source plasma
1.8 m

## Slide 11: Long pulse acceleration in MAMuG accelerator
Negative ion source
FRP
MeV accelerator in JAEA
1 MeV
0.5 A, 200 A/m2
3600 s
2 m
Acceleration grids
extractor
Heat load on EXG
cooling channel close to heat receiving surface
310150℃ around magnet (<allowable temp. (200 ℃) )
Grid heat load by beam deflection
controlling the beam steering by aperture offset
Grid heat load: 10 % of input power
H- beam
【Issue and solution】
original
New
Cooling channel
magnet
Aperture
offset(0.7 mm)
The modification enabled the long pulse beam acceleration.
Low grid heat load enables steady state operation.
EXG
PG

## Slide 12: Achievement of long pulse acceleration
JT-60SA
0.5 MeV, 22 A, 100 s
Beam energy density has been increased two orders of magnitude in the last two years.
No degradations of voltage holding and beam optics during long pulse acceleration.
Increases of beam energy and pulse length are in progress with further conditionings for ITER and JT-60 SA.
980 keV, 185 A/m2, 0.4s
882 keV, 130 A/m2, 9 s
683 keV, 100 A/m2, 60 s
1 MeV, 200 A/m2, 60s
(facility limit)
Recovery from earth quake 3.11
ITER
1 MeV, 40 A, 3600 s

## Slide 13: Present status and schedule
1.3 MV testing PS (June 2014)
Brazing of ceramic (May 2014)
5 m
1.56 m
The procurement activities on ITER NBTF are in progress as scheduled in Japan.

## Slide 14: Summary
In order to realize NB system for ITER and JT-60SA, key technologies have been developed in the past two years.
DC high voltage technology;
The new composite bushing with manufacturable parts,
The 1 MV insulating transformer has been realized.
1MV vacuum insulation scaling of large electrodes to be scalable to ITER
The design of the HV busing has been ensured.
Beam production & acceleration;
Active temperature control technology of plasma grid in Cs-seeded negative ion source
A 100 s negative ion beam production at 15 A.
Beam steering and heat removal technology on MAMuG accelerator
A 60 s beam acceleration at 683 keV, 100 A/m2, that is two orders of magnitude longer than the previous achievement.

## Slide 15: Neutral Beam Injector (NBI) System
Power supply component
Beam source (negative ion source+ accelerator)
Beam line components
To tokamak
D0
D-
Transmission line
DC generator
200 kV x5
HV bushing
1 MV
Insulating transformer
~100 m
P/S for negative ion production
Two NBIs in ITER
NBTF identical to ITER in Padova

## Slide 16
Long pulse acceleration of high power density beam
Heat load on the extraction grid is issued for long pulse beam acceleration.
High-power and long-pulse beam acceleration of 70 MW/m2 for 60 s was achieved.
【issue】Limited less than 1 MW/m2.

## Slide 17: Insulation structure between windings for DC 1 MV
【New device】
Insulation structure with insulation oil and oil-immersed paper layer to realize a feasible transformer
and barrier
By applying existing insulation structure(DC 500 kV, 10 s) to DC long-pulse operation;
Five times higher electric field (Elong/Eshort = 5)
Ten times higher in ITER (1 MV)
Allowable electric field: 16 kV/mm
Insulation structure inside the transformer to sustain 1 MV for long pulse operation was established.
【Issue】
Dimension drastically increases.
Ten times larger transformer? Too large installation space!
Not acceptable in ITER.
Time constant >3000 s

## Slide 18
Improvement of spatial uniformity of
negative ion beam
Beam Uniformity : 69 % ⇒ 83 %
32 A negative ion beam from total extraction area
22 A from segment 2~4.
Requirement on JT-60 SA was satisfied.
Due to magnetic (B×▽B) drift, primary electron drifts in one direction. Non-uniform negative ion production occurs in the source.
B×∇B drift direction
Magnetic field line
Tent-shaped magnetic filter
Negative ion beam
Non uniform negative ion beams causes local grid heat load that prevents long pulse operation.