## Slide 1
G.Y. Park1, S.S. Kim1, T. Rhee1, H.G. Jhang1, P.H. Diamond1,2, I. Cziegler2, G. Tynan2, and X.Q. Xu3
1National Fusion Research Institute, Korea
2CMTFO and CASS, UCSD, USA
3Lawrence Livermore National Laboratory, USA
LH Transition Criterion:
A 3D Nonlinear Simulation Study
25th IAEA Fusion Energy Conference, 13-18 Oct. 2014, Saint Petersburg, Russia

## Slide 2
Introduction
L-H transition phenomenology
  Sudden bifurcation to high confinement (H-mode)
  Studied for ~32 years
  Theory perspective-based on transport bifurcation and
  profile self-organization via predator-prey dynamics
  Main paradigm: ExB flow shear(ExB) suppression of the turbulence
    ExB > lin  turbulence suppressed and H-mode sustained
  Unknown
    Trigger mechanism
    Transition criterion based on microphysics (need predictive capability)
Main questions
  What triggers the transition?
  How the transition evolves?
  How predict transition, and power threshold?
To be explained in the present talk

## Slide 3
H-mode and L-H transition
H-mode: enhanced plasma confinement with edge transport barrier (ETB)
H-mode history/phenomenology (1982-2014)
  Wagner (1982): first discovered at ASDEX-U
  Er shear layer at edge, fluctuation decrease, existence of power threshold (Pth)
  Predator-Prey paradigm [Diamond, PRL, 1994; Kim & Diamond, PRL 2003]
    Zonal flow (ZF): predator, turbulence: prey, mean flow: another predator
    ZF triggers the transition, while mean flow sustains the barrier
Why H-mode is important for fusion?
  Practical reason: can reduce reactor size
  H-mode driven high pedestal height
   high fusion performance

## Slide 4
Experimental evidence of a role of turbulence-driven (ZF) flow in triggering L-H transition
Tynan (2013) and Manz (2012)
  Normalized Reynolds power
  meaning a ratio of kinetic energy
  transfer from turbulence into ZF to
  the turbulence input power
  Turbulence collapse condition
RT > 1
  Experimental results show that L-H transition occurs when RT >1
Yan (2014) reported a similar finding at DIII-D
Tynan (2013)
Blue and Red:
~1cm inside LCFS
Green line: SOL
D drop

## Slide 5
Main results
3D flux-driven simulation of edge transport barrier (ETB) formation shows that
  ETB forms once input power exceeds a threshold value
    Steep pressure pedestal , deep Er well appear when Pin > Pth
    Q versus -P curve shows a feature of first-order phase transition
  ETB transition is triggered by turbulence-driven flow shear
    RT > 1: criterion for the trigger of the transition
    Burst of the turbulence-driven flow shear appears just prior to the transition point
  Time sequence of the transition is clear
    Peaking of the normalized Reynolds power (RT > 1):
    Turbulence suppressed and pressure gradients increased
    Mean flow shear (VE from P) rises: sustain H-mode
Microphysics (RT) may govern LH transition!

## Slide 6
3D model using BOUT++
Vorticity (U)
Pressure (P)
 Overall results are independent of the particular source and sink profiles
 For transport coefficients, we use ||=0.1, neo==3.010-6
Neoclassical poloidal flow damping
accounting for self-consistent flow
Heat source
Sink  models SOL loss
  Electrostatic model with resistive ballooning (RBM) turbulence
  Two field (vorticity, pressure) reduced MHD equations (constant density)
  Flux driven, self-consistently evolving pressure profile
: Lundquist number (=105)
: Neoclassical flow/friction coefficients
Since

## Slide 7
Edge transport barrier (ETB) forms when Pin > Pth
  ETB forms at x~0.95 for Pin > Pth [Park, H-mode Workshop, 2013]
   Steep pressure pedestal
   Deep Er well
   Discontinuity in slope of Q versus -P graph
    A feature of first-order phase transition
   Similar simulation result of ETB formation has been
  reported [Chone, PoP, 2014]
Pressure [B02/(20)]
Er [VAB]
Transition point
Q [a.u.]
-P [B02/(20R0)]

## Slide 8
Power ramp up simulation shows the turbulence collapse at t=tR via an intermediate phase
Limit-cycle oscillation (LCO) appears prior to the transition
Turbulence is continuously growing and peaks just before the transition
ExB flow shear changes abruptly near the transition (yellow shaded area)
: transition time
LCO
ExB flow shear
Turbulence intensity
Pin (power)  t

[A]
[A-1]
[a.u.]

## Slide 9
RT > 1 for the trigger of the transition at t=tR:
fluctuation energy  flow (m=n=0) energy
Turbulence collapse condition ( )  RT  1
RT > 1 means the conversion of fluctuation energy into flow energy faster than turbulence energy increase
Reynolds work (simulation)
Tynan (2013)
[A]
RT at edge
D drop

## Slide 10
Simulation shows a similar sequence of the transition to that observed on C-Mod (Cziegler, 2014)
  RT >1 at t=tR  an increase of pressure gradient.
    RT >1 at t=tR triggers the transition
    Turbulence collapse  an increase of ▽P
Cziegler (2014)
: transition time
[A]

## Slide 11
Microscopic time sequence of the transition: P, ExB flow shear (ExB), and linear growth rate (lin)
  RT > 1 causes the surge of the turbulence-driven flow shear at t=tR
  Increase of pressure gradient precedes mean flow shear development
  Positive feedback between ▽P and ExB begins at t=tP
  Mean shear criterion (ExB > lin) is satisfied later, at t=tC  H-mode sustained afterward
Mean flow shear
dominant (ExB  P)
Turbulence-driven flow
shear dominant
ExB > lin
[A]

## Slide 12
Preliminary electromagnetic three-field results
Simulation of ETB formation using three-field model
  Two-field model + Ohm’s law for perturbed vector potential ()
  Profiles of neo and kneo are fixed in time in this simulation
  ETB occurs for Pin = 2.0 as seen in right figures
  Suggests that the transition physics as found in electrostatic case may also apply for the electromagnetic case (Work is in progress)

## Slide 13
Conclusions and discussions
First 3D turbulence simulation to explicitly show
  ETB formation for Pin > Pth
  The criteria RT > 1 is the trigger of the LH transition
  Detailed time sequence of the L-H transition
    RT > 1  the surge of the turbulence-driven flow shear
    An increase of pressure gradient  mean flow shear development via positive feedback
    ExB > lin  steady H-mode sustained
Future works
  Microscopic parameter trends in RT and their relation to LH transition power threshold scaling
  Formation of sudden deep (in time) RT just prior to the transition
  HL back transition and hysteresis
  Electromagnetic case
Microphysics (RT) may govern LH transition process