## Slide 1: Summary of FNS/1-1: Configuration Studies for an ST-Based Fusion Nuclear Science Facility (FNSF)
Ex-vessel PF coil set identified to support range of equilibria with Super-X/snowflake divertor to mitigate divertor heat flux
0.5MeV NNBI optimal for heating & current drive for R=1.7m
Vertical maintenance approach and test-cell layout identified
Shielding adequate for MgO insulated inboard Cu PF coils
  Outboard PF coils (behind outboard blankets) can be superconducting
Calculated full 3D TBR, TBR reduction from TBM, MTM, NBI
Threshold major radius for TBR ~ 1 is R0 ≥ 1.7m
R=1m TBR = 0.88  0.4-0.55kg of T/FPY  $12-55M/FPY
R=1m device will have lower electricity and capital cost  future work could assess size/cost trade-offs in more detail