## Slide 1
Shinsuke Fujioka*
*Institute of Laser Engineering, Osaka University, Japan
IAEA Fusion Energy Conference 2014
Experimental Platform for Efficient Heating of Fusion Fuel with Fast-Ignition Scheme
1 mm
ILE, Osaka

## Slide 2
  Fast-Ignition Realization EXperiment (FIREX) was performed on GEKKO XII - LFEX laser facility.
  There are three difficulties of the fast-ignition scheme, namely “shut-in”, “diverging” and “ unstoppable” of REB.
  All physical parameters of the REB were measured to evaluate absolutely the heating efficiency.
The most critical problem is generation of too energetic REB (> 15 MeV) in a long-scale preformed plasma.
Plasma mirror will be installed to suppress generation of too energetic REB.
Guiding of REB was demonstrated with 0.6 kT of external B-field.
Slope temperature and divergence of relativistic electron beam (REB) must be controlled for efficient heating of fusion fuel.
Summary

## Slide 3
Three difficulties in fast-ignition scheme;
“shut-in”, “diverging”, and “unstoppable” of REB.
Shut-in
A few MeV electrons, which may heat efficiently a fuel core, are absorbed in the cone wall itself. Most of these absorbed electrons are not ejected from the cone.
Diverging
Electron beam has a large divergence angle (> 100 deg.). Energy flux of the e-beam decreases significantly during transport.
Unstoppable
Too energetic electrons are generated by laser-plasma interactions, those electrons do not deposit their energy within the fuel.
Heating laser
Heating laser
Fusion fuel
cone
ILE, Osaka
Fast Ignition Basic Experiment Platform

## Slide 4
E-beam cross section @fuel
Ta
GXII
LFEX
e-
e-
e-
X ray
X ray
X ray
PS shell
Fast ignition basic experiment
Absolute x-ray yield measurement
Heating
Efficiency
Laser- Electron
Conversion
Efficiency
Kα imaging
with a tracer layer
Fuel
cross section
=
X
X
X
Electron
Transmittance
Divergence, energy distribution and flux of REB
are measured by using x-ray convertor attached target.
2 x fuel areal density
Range of e-beam
Te measurement
with hard x-rays
X-ray shadowgraph
1 mm
ILE, Osaka
Fast Ignition Basic Experiment Platform

## Slide 5
ρRmax = 54 mg/cm2 and ρmax = 22 g/cm3 are obtained with
a plastic ball with asymmetric-spherical irradiation.
2D simulation
X-ray shadow
of compressed plastic ball
Density
Temperature
200 µm
@max. comp.
200 µm
ILE, Osaka
Fast Ignition Basic Experiment Platform

## Slide 6
Cu tracer layer
LFEX
e-
e-
e-
Kα x-ray
C/Cu/C block target
Cross section of REB is measured by imaging
Kα emission from a varied tracer layer.
Kα x-ray
Kα x-ray
Kα x-ray
100 µmφ
Monochromatic Kα image
ILE, Osaka
Fast Ignition Basic Experiment Platform

## Slide 7
Absolute energy sepectrum of REB was obtained
from hard x-ray spectrum with 2-T assumption.
Fast Ignition Basic Experiment Platform
Energy distribution of REB measured with ESM & HEXS
TREB2 = 15 MeV
determined from ESM
TREB1 = 1 MeV
determined from HEXS
ESM signal
TREB1 = 1 MeV
(7.9% of EREB)
TREB2 = 15 MeV
(92.1% of EREB)
Vacuum Electron Spectrum
ILE, Osaka
Effect of sheath field

## Slide 8
Fuel cross section
ILE, Osaka
Heating
Efficiency
Laser- Electron
Conversion
Efficiency
E-beam cross section @fuel
=
X
X
X
Electron
Transmittance
Heating efficiency is evaluated with measured divergence, energy distribution and flux of REB.
Summary of FI Basic Experiment
40 %*
=
Range of e-beam
2 x Fuel rho-R
π (50/2 µm)2
=
=
0.11 g/cm2
π (100/2 µm)2
=
=
4.4 g/cm2
(weighted for 1 & 15 MeV)
=
25 %
=
2.5 %
!!!
Heating efficiency estimation
X
X
0.3%
=
Reduction of Te is essential for efficient heating.
See details in the poster by Z. Zhang (IFE/P6-2, Thursday).

## Slide 9
Too energetic electrons are generated in a long-scale
plasma generated by foot of the heating laser pulse.
ILE, Osaka
Suppression of Too Energetic REB Generation
Preferable electrons decrease
Energetic electrons increase
Long-scale plasma generated by foot pulse
Laser filamentation
in a long scale plasma
Long-scale plasma generated by foot pulse

## Slide 10
Foot pulse can be removed by using plasma mirror.
It is a challenge to install plasma mirror to kJ lasers system.
ILE, Osaka
Suppression of Too Energetic REB Generation
Intensity (log scale)
Time (log scale)
1 ps
200 ps
1020 W/cm2
1010 W/cm2
Typical shape of laser pulse
Principle of plasma mirror
See details in the poster by A. Morace (IFE/P6-4, Thursday).

## Slide 11
Laser-generated relativistic electron beams can be
guide by a few kT of externally imposed B-field
ILE, Osaka
Guiding REB with external B-field
See details in a poster by T. Johzaki (IFE/P6-5, Thursday).
nb
(cm-3)
2.1ps
2.1ps
Bz,ext = 0
Bz,ext = 2 kT
Bz
Fuel
Divergence of REB is a critical issue for the fast-ignition ICF.
#Simulation by Prof. Honrubia.

## Slide 12
1 kT B-field* was generated
with a capacitor-coil target# and a ns-kJ laser.
*S. Fujioka et al., Sci. Rep. (2013).
#H. Daido et al., PRL (1985), C. Courtois et al., JAP (2005),
Photo of capacitor-coil target
1mm
B
Current ~ several MA
kJ-ns laser beams
2nd disk w/hole
1st disk
One-turn coil
ILE, Osaka
Suppression of Too Energetic REB Generation

## Slide 13
Laser-generated REB was pinched
by externally imposed 0.6-kT magnetic field.
ILE, Osaka
Spatial profile of transmitted REB
Suppression of Too Energetic REB Generation
Experimental setup
w/o B
w/ B
nb
(cm-3)
w/B
w/o B
Notes: Eint = 0.036kJ
Elimp = 2.5 kJ
⇒ himp = 1.44 %

## Slide 14
2D radiative-MHD code is under development
for full computation of B-assisted fast ignition scheme.
ILE, Osaka
Magnetic field [G]
Density profile [g/cm3]
β value
Pressure [dyn/cm2]
Suppression of Too Energetic REB Generation
See details in the poster by H. Nagatomo (IFE/P6-6, Thursday).
Computations by 2D-Rad-MHD code (PINOCO-MHD)
Notes: Eint = 0.036kJ
Elimp = 2.5 kJ
⇒ himp = 1.44 %

## Slide 15
S. Fujioka, Z. Zhang, Y. Arikawa, A. Morace, T. Nagai, Y. Abe, K. Ishihara, S. Kojima, S. Sakata, M. Taga, T. Ikenouchi, H. Inoue, T. Utsugi, S. Hattori, H. Lee, T. Hosoda, K. Matsuo, Y. Fujimoto, T. Jitsuno, Y. Hironaka, K. Mima, M. Murakami, N. Miyanaga, H. Nagatomo, M. Nakai,Y. Nakata, K. Nishihara, H. Nishimura, T. Norimatsu, T. Sano, Y. Sakawa, K. Shigemori, K. Tsubakimoto, A. Yogo, H. Shiraga, H. Azechi
Institute of Laser Engineering, Osaka University, Japan
A. Sunahara
Institute for Laser Technology, Japan
T. Johzaki
Hiroshima University, Japan
T. Morita, N. Yamamoto, H. Nakashima
Kyusyu University, Japan
K. Kondo
Tokyo Inst. Tech., Japan
T. Enoto
RIKEN, Japan
A. Iwamoto, T. Ozaki, T. Watanabe, H. Sakagami
National Institute for Fusion Science, Japan
H. Sawada, Y. Sentoku
University of Nevada, Reno, USA
Y-T. Li
Institute of Physics, China
G. Zhao, F-L. Wang, J. Zhong
National Astronomical Observatories , China
J. Santos, L. Giuffrida, M. Bailly-Grandvaux, D. Batani, R. Bouillaud,
P. Forestier-Colleoni, S. Hulin, Ph. Nicolaï, V. Tikhonchuk
CELIA, Univ. Bordeaux, France
J.L. Dubois, J. Gazave, D. Raffestin and J. Ribolzi.
CEA, France
M. Chevrot, S. Dorard, E. Loyez, J.R. Marques, F. Serres
LULI, Ecole Polytechnique, France
J. Honrubia
Universidad Politécnica de Madrid, Spain
D. Salzmann
Weizmann Institute of Science, Israel
Y. Kuramitsu
National Central University, Taiwan

## Slide 16
Acknowledgement
This research was supported by the Japanese Ministry of Education, Science, Sports, and Culture (MEXT), by a Grant-in-Aid for Young Scientists (A) for ’Extreme Magnetic Field Generation for Quantum Beam Control and Laboratory X-ray Astronomy (No. 24684044), ‘Bilateral Program for Supporting International Joint Research by JSPS’, ’ Collaboration Research program by NIFS (NIFS12KUGK057 and NIFS11KUGK054) and by the Institute of Laser Engineering at Osaka University (under contract ’Laboratory X-ray Astrophysics with Strong Magnetic Field’).

## Slide 17
  Fast-Ignition Realization EXperiment (FIREX) was performed on GEKKO XII - LFEX laser facility.
  There are three difficulties of the fast-ignition scheme, namely “shut-in”, “diverging” and “ unstoppable” of REB.
  All physical parameters of the REB were measured to evaluate absolutely the heating efficiency.
The most critical problem is generation of too energetic REB (> 15 MeV) in a long-scale preformed plasma.
Plasma mirror will be installed to suppress generation of too energetic REB.
Guiding of REB was demonstrated with 0.6 kT of external B-field.
Slope temperature and divergence of relativistic electron beam (REB) must be controlled for efficient heating of fusion fuel.
Summary

## Slide 18
The fast ignition consists of three stages; “compression
by ns-laser”, “heating by ps-laser”, and “ignition&burning”.
Compression
(x 1000 solid density)
Heating
(up to 5 keV)
Ignition
& Burn
10 kJ-PW laser – LFEX – is constructing for FIREX-I.
FIREX: Fast Ignition Realization EXperiment
ILE, Osaka

## Slide 19
Three beams of the LFEX laser are in operation.
The full four beams will be operational from this November.
Interaction chamber
SM1
SM2
M2
M7
M7
M6
M4
M3
M9
M-10
M1
Grating 2
Grating 1
Monitor 1
Monitor 3
Off axis
parabola mirror
M5
SiO2
HfO2
SiO2
HfO2
0.575 µm
Beam# 4 beam
Energy 700 J/beam, 2.8 kJ/total
Duration < 1 ps
Wavelength 1053 nm
ILE, Osaka
FIREX: Fast Ignition Realization EXperiment
Notes: Again, this shows the path from the amplifier output , gratings, focusing optics, and the target chamber.
Beam configuration is 2x2 here, and then 1x4 here, and finally it is 2x2 again, and goes into the target chamber.
The whole system after M2 is inside vacuum chambers.

## Slide 20
Cone
Coil
FIREX (Fast Ignition Realization Experiment) target design
is refined based on the recent studies.
Compression
(9 of 12)
B-generation
(3 of 12)
Laser-driven capacitor
Heating
(4 of 4)
ILE, Osaka
Magnetized Fast Ignition: MFI

## Slide 21
There are a lot of unexplored plasma physics
in magnetized fast ignition scheme.
Magnetized Fast Ignition: MFI
2.1ps
Bz
Hydrodynamic instability
e-beam guiding
EM wave propagation
Thermal insulation
ILE, Osaka

## Slide 22
There are a lot of unexplored plasma physics
in magnetized fast ignition scheme.
kilo Tesla
B-field
b) Fast electron guiding
Dense fuel generation
Efficient
Heating
Ignition
High Gain
d) Thermal
Insulation
a) hydrodynamic instability
c) Whistler wave propagation
Field compression
e) α particle
confinement
ILE, Osaka
Flow chart of magnetized fast igntion
Magnetized Fast Ignition: MFI

## Slide 23
with laser-driven capacitor-coil target
Strong Magnetic Field Generation

## Slide 24
We generate 1 kT B-field* with a capacitor-coil target#
and a ns-kJ laser (GEKKO [JAPAN] & LULI [FRANCE]) .
*S. Fujioka et al., Sci. Rep. (2013).
#H. Daido et al., PRL (1985), C. Courtois et al., JAP (2005),
Photo of capacitor-coil target
1mm
B
Current ~ several MA
kJ-ns laser beams
Strong-B Generation
2nd disk w/hole
1st disk
One-turn coil
ILE, Osaka

## Slide 25
Movement of non-thermal hot electrons between the disks
drives electric current in the wire.
Strong-B Generation
electron
Plasma
-
-
-
-
-
-
-
B
current
GEKKO XII
kJ-ns pulses
Non-thermal hot electron generation
Electrons accumulates on the disk
Current is driven in wire
ILE, Osaka

## Slide 26
600 T of the maximum strength and 2 ns of FWHM duration
of B-field generated with a capacitor-coil target.
Strong-B Generation
t = 0.6 ns
(Half-rise time)
Time (ns)
Strength of B-field (T)
at coil center
ILE, Osaka
Temporal history of B-field
600 T of the peak magnitude and 2 ns of the duration

## Slide 27
Electrons traveling with a plasma expansion front# are accumulated on the capacitor disk.
Strong-B Generation
ni (x)
ne (x)
Rarefaction
wave front
Ion expansion front
Total charge density (/cm2) at the front is -σ
LASER
#P. Mora, PRL (2003).
Position (normalized)
Charge density (/cm2)
0
-2σ
σ
σ
Drawing of C-C target
Plasma profile between disks
ILE, Osaka

## Slide 28
Electric potential difference of the capacitor
can be calculated with the isothermal expansion model#.
Strong-B Generation
Total charge density at the ion front (C/m2)
Q = σS
Charge accumulated on the disk.
S is the size of the disk (m2)
Electric field at the ion front.
Temperature of hot electrons generated by resonance absorption
Time duration for that the ion front arrives at the accumulation disk.
d
d is the distance between the disks.
V = 0.5 MV, I = 0.3 MA, and B = 750 T for 1 kJ with the model.
#P. Mora, PRL (2003).
ILE, Osaka

## Slide 29
Hydrodynamics of a magnetized HEDP

## Slide 30
Hydrodynamics of a HED plasma under strong B-field
is important in Magnetized Fast Igntion.
Hydrodynamics in strong B-field
2D hydrodynamic simulation of laser-driven implosion under strong B-field
ILE, Osaka

## Slide 31
B
Thermal conductivity becomes anisotropic
under strong B-field.
kperp
kpara
kpara = kw/o B
kperp = k w/o B/(1+(ωceτe)2)
kw/o B : conductivity (w/o B)
ωce : elec. gyrofrequency
τe : elec. collisional time
Te = 100 eV, ne = 9 x 1021 cm-3
ωceτe ~ 1
Thermal conductivity
in parallel B-field
Braginskii coefficient
ILE, Osaka
Hydrodynamics in strong B-field

## Slide 32
Uniform magnetic field was generated for this experiment
by using a Helmholtz-type coil-capacitor target.
1500 µm-diameter coil
900 µm gap
25 µm-thick PS foil
Parallel B-field
Geometry
Perpendicular B-field
Geometry
Each capacitor was driven by 1.5 kJ/1.2 ns laser.
ILE, Osaka
Hydrodynamics in strong B-field

## Slide 33
220 T of the magnetic field at the center was obtained
from Faraday rotation measurement and LADIA code.
Experiment set-up of
Faraday rotation measurement
TGG crystal as Faraday medium is located at (-3, -3, 0).
3 mm
3 mm
TGG crystal
B-field profile
along coil center axis
0.21 MA current in the Helmholtz coil corresponds to 220 T at the center.
ILE, Osaka
Hydrodynamics in strong B-field

## Slide 34
Corrugated CH target
Zn foil for face-on BL
(~ 1.5 keV)
Cu foil for side-on BL
(~ 1.2 keV)
Slit
X-ray CCD camera
X-ray streak camera
1.2-ns laser pulse
1.2-ns laser pulse
Flash x-ray
300 mm
1 ns
Side-on XBL
Face-on XBL
LASER
1 ns
Slit
Hydrodynamics of magnetized HED plasma will be studied with face-on and side-on x-ray backlighting.
ILE, Osaka
Hydrodynamics in strong B-field
Notes: In the RT experiment, we used both face-on and side-on x-ray backlighting technique.
In the face-on geometry, Slit imager was coupled with an x-ray streak camera.
We can obtain temporal evolution of areal-mass-density perturbation due to the RT instability.
In the side-on geometry, Fresnel phase zone-plate was used as a two-dimensional spatial resolved imager.
X-ray detector was an x-ray CCD camera, and flash x-ray backlighting technique was used to obtained 100 ps-single flame x-ray image with an x-ray CCD camera.
In the side-on geometry, perturbation amplitude of the target is directly measured.

## Slide 35
Laser-driven plastic foil is faster in parallel B-field
than that without B-field.
B
Side-on x-ray shadowgraph
w/o B-field
Side-on x-ray shadowgraph
w/ parallel B-field
Time (1 ns)
Space (100 µm)
LASER
LASER
ILE, Osaka
Hydrodynamics in strong B-field

## Slide 36
B-field changes shape of ablated plasmas by B-field.
Plasma expansion was flatten in parallel B-geometry.
B
B
LASER
LASER
after 5 ns
after 3 ns
Ablating plasma image
(parallel B-field)
Ablating plasma image
(perpendicular B-field)
ILE, Osaka
Hydrodynamics in strong B-field

## Slide 37
Two dimensional simulation of HEDP with external B-field
is on going to understand the experimental results.
Lorenz force effect (magnetic pressure) is not included in this simulation.
2D hydro simulation (parallel B)
1D profile
ILE, Osaka
Hydrodynamics in strong B-field

## Slide 38
Guiding of laser-produced REB by B

## Slide 39
1 ns of diffusion time
corresponds to 10 eV of preheat of a plastic target.
Diffusion time of magnetic field
μ0 : permeability
η : resistivity
L : diffusion length
Guiding REB with external B-field
Diffusion of magnetic field in metal target
After Prof. Honrubia.
ILE, Osaka
Notes: Eint = 0.036kJ
Elimp = 2.5 kJ
⇒ himp = 1.44 %

## Slide 40
B
ωc/ωpe = 0
ωc/ωpe = 0.7
Weibel instability, source of REB divergence,
can be suppressed by external magnetic field.
Guiding REB with external B-field
ILE, Osaka
Weibel instability in counter streaming electrons
Initial spatial non-uniformity of B-field makes local current density non-uniform. The non-uniform current density amplifies B-field non-uniformity.
Suppression of Weibel instabity with external B-field
External B-field guide return current and suppress instability growth.

## Slide 41
Alternative approaches for 5 keV
with truly isolated target and ion heating

## Slide 42
Truly isolated target is proposed to demonstrate
fast heating of material to several keV temperature.
Alternative approaches
H.-S. Park, PoP 13, 056309 (2006)
REB trapping
by self-generated E-field.
REB may be confined by strong self-generated E-field in a truly isolated target.
1 J laser
pulse
0 ns
+10 µs
Target isolation
by stalk cutting with a 1J laser pulse
Target stalk is the major route, through which electrons is supplied to a positively charged target.
Initial
position
ILE, Osaka
Notes: Eint = 0.036kJ
Elimp = 2.5 kJ
⇒ himp = 1.44 %

## Slide 43
Two teams are organized to conduct supportively
electron-based fast-ignition and ion-based fast-ignition.
Alternative approaches
ILE, Osaka
43

## Slide 44
Current status of “conventional” Fast-ignition researches in Osaka
    Basic experiment platform is developed for absolute measurement of all physics parameters those determine heating efficiency.
    Generation of too energetic electron (> 10 MeV) in a long-scale preformed plasma is the most crucial problem.
    “Cool REB” campaign will be conducted with a plasma mirror and the experiment platform in 2014.
Hydrodynamics of a HED plasma under strong B-field,
    Electron thermal conduction is anisotropic in strong B-field.
    Hydrodynamics of a laser-driven plastic foil was clearly changed by externally imposed B-field.
Guiding of relativistic electron beam (REB) by strong B-field,
    Guiding of REB is a key for the magnetized fast-ignition ICF .
    Pinching of the REB was clearly observed with sub-kT B-field.
    Suppression of the Weibel instability will be studied.
Alternative approaches for Fast Igntion
    Truly isolated target was developed to confine energetic electrons by self-generated E-field.
    Two teams are organized to conduct supportively both of electron-based and ion-based FI.
SUMMARY

## Slide 45
Acknowledgement
This research was supported by the Japanese Ministry of Education, Science, Sports, and Culture (MEXT), by Special Education and Research Expenses for ’Laboratory Astrophysics with High-Power Laser’ and a Grant-in-Aid for Young Scientists (A) for ’Extreme Magnetic Field Genera- tion for Quantum Beam Control and Laboratory X-ray Astronomy (No. 24684044), ‘Bilateral Program for Supporting International Joint Research by JSPS’, ’ Collaboration Research program by NIFS (NIFS12KUGK057 and NIFS11KUGK054) and by the Institute of Laser Engineering at Osaka University (under contract ’Laboratory X-ray Astrophysics with Strong Magnetic Field’).

## Slide 46
100 KeV
Ta cube: 1 mm
Slope temp.: 1 MeV
Divergence: 45 deg. (half)
Beam dia.: 60 μm
ILE, Osaka
Kα signal from a block was used to evaluate conversion efficiency. MonteCarlo code was used to compute Kα yield.
Fast Ignition basic experiment
Kα1
Kα2
Kβ
0th order
1st order
Detection image of LAUE spectrometer
1st order
Lineout of the LAUE spectrometer
Trajectory of electrons
computed by PHITS code
46

## Slide 47
During Ph. D (1999 ~ 2004) Rayleigh-Taylor instability in laser-driven plastic plasma (< 1015 W/cm2)
2004 ~ 2009 Extreme Ultraviolet Light Source Development for Industry (< 1012 W/cm2)
2009 ~ 2013 Photo-ionized plasma generation with high-power laser (< 1015 W/cm2)
2012 ~ Strong Magnetic Field Generation with High Power Laser & Fast-Ignition Laser Fusion (< 1020 W/cm2)

## Slide 48
REB was generated by ps-laser pulse. Cu-Kα and CTR emanated from REB were imaged from the rear side.
ILE, Osaka
CTR represents properties of REB.
CTR emission from the rear side was imaged with lens on an visible streak camera.
The slit of the streak camera is fully open (several mm).
The streak camera is operated with a slow sweep velocity.
The streak camera acts as a flaming camera in this condition, because duration of the CTR emission is a few ps.
Cu Kα imaging was relatively unstable because strong background was generated by the ns-pulse.
Guiding REB with external B-field
Notes: Eint = 0.036kJ
Elimp = 2.5 kJ
⇒ himp = 1.44 %

## Slide 49
Atomic physics in a magnetized HED plasma
is also important in ICF and astrophysics.
ILE, Osaka
Deceleration phase w/strong-B
Pressure by compressed magnetic field suppresses hydrodynamic instability.
L. J. Perkins et al., PoP 2013.
Alfven speed << RM growth rate
Alfven speed > RM growth rate
RM instability in strong-B
Vorticity of the Rechtmyer-Meshkov instability carried by the Alfven wave.
Strong-B Applications
T. Sano et al., PRL 2013.

## Slide 50
Diffusion of magnetic field in metal target
After Prof. Honrubia.
Diffusion time of magnetic field.
μ0 : permeability
η : resistivity
L : diffusion length
tdiff(Al@10 eV, 50 µm) = 0.7 ns
tdiff(CH@10 eV, 50 µm) = 1.5 ns
B-field duration tB=3ns

Smaller than
Target can be magnetized within duration of B-field pulse.
It takes finite time (a few ns)
that pulsed B-field diffuses into a plastic target.
ILE, Osaka
Guiding REB with external B-field

## Slide 51
An ablating plasma may be shaped by ambipolar diffusion initiated by electrons guided by B-field.
Hydrodynamics in strong magnetic field
ILE, Osaka
B
E
Electron
Ion

## Slide 52
B-flux density was measured
by using Faraday effect of a fused silica in B-field.
B
Probe beam
(YAG@532 nm)
λ/2 wave plate
Wollaston prism
(divergence angle 5 deg)
Fused silica
Band pass
filter
Image lens 1
Iris
Image lens 2
photocathode slit
GEKKO XII laser
HA filter
Visible streak camera
w
w
600 µm
500 or 100 µm
600 µmφ
500 µmφ
Fused silica
Coil
Probe
Rotation angle is determined from intensity ratio IH and IV.
Strong-B Generation
ILE, Osaka
#S. Fujioka et al., Sci. Rep. (2013).

## Slide 53
71 deg. of Faraday rotation (corresponding to 0.4 kT) was observed around 1.5 ns after the GEKKO laser irradiation.
w
w
Reference w/o B
0
1
2
3
4
−１
Time (ns)
w
w
Streak image w/B
Time (ns)
0
1
2
3
4
−１
Black out
laser fire
Fused silica becomes opaque for probe light soon after B-generation.
Strong-B Generation
ILE, Osaka
#S. Fujioka et al., Sci. Rep. (2013).

## Slide 54
1 kT B-field@850 µm from the coil
was obtained with the laser-driven capacitor-coil target.
Strong-B Generation
ILE, Osaka
Max. B flux density vs. Intensity
λL = 1.053 µm
Faraday rotation measurement
Pick-up probe measurement
λL = 0.53 µm
S. Fujioka et al., Sci. Rep. (2013).

## Slide 55
For efficient heating,
    Reduction of preformed plasma generation.
    Development of long & low-Z cone.
    Generation of > 1 kT B-field to guide e-beam.
For testing novel ideas,
    Development of FI-basic and heating exp platforms.
    Development of 0.1 – 30 MeV x-ray spectrometers.
    Development of x-ray insensitive neutron detectors.
    Estimation of heating efficiency with all measured values.
For 5 keV heating,
    Reduction of electron temperature is essential.
    Guiding of low-temperature electron by strong-B field will be studied.
The goal of the FIREX-I is to demonstrate efficient fuel heating up to 5 keV with the fast-ignition scheme.

## Slide 56
Heating experimental shows x17 enhancement of DD-neutron yield. This result is being analyzed with simulation.
ILE, Osaka
Υn = (1.1 +/- 0.6) x 106
1D simulation
GXII
CD ball
LFEX
GXII
CD ball
Υn = 6.4 x 104
Result of Fast Ignition Heating Experiment
x 17
5ps
Notes: この二つのグラフはMANDALAのヒストグラムのデータです。横軸は時間、縦軸はカウント数です。冒頭で述べたとおり、2010年までの高速点火実験では、追加熱エネルギー５００J程度でこのようにｇｎだらけになってしまい、DDの到着時刻にピークを確認することができませんでしたが、コリメーター導入の結果、2012年は追加熱が１ｋJ以上のショットでもこの程度のｇｎ量に抑えることができていて、DD中性子のピークを確認できるまでになりました。
またこの赤いラインは、チャンネルの生存率を表します。カウントモードのMANDALAは、一度信号がかかると、その信号が閾値以下に立ち下がるまでは次の信号を検出できません。したがってすべてのチャンネルが立ち下がった状態が１、すべてのチャンネルが立ち上がりのままである状態を０として、各時刻のアクティブなチャンネルの割合を示しています。2010年ではこのようにX線の到達後、生存率の回復が遅く、DD時刻においても生存率は６割程度でしたが、シンチの小型化により、生存率の回復が格段に速くなりました。
これにより、2012年の高速点火実験シリーズでは、すべてのショットにおいてイールド評価を行うことができました。

## Slide 57
based on FI basic and heating experiments.
Future direction

## Slide 58
DLC plate + Au coating
Coil
Low temperature (< 1 MeV) electron beam generated with “defocused” short laser pulse must be guided.
Future direction
Laser-driven capacitor
ILE, Osaka
“Defocused”
Heating Laser
Te < 1 MeV
e-beam
After Sunahara, Johzaki, Fujioka.
Focal spot dL = 360 µm (for 1 x 1018 W/cm2)
>> Fuel diameter (70 µm)

## Slide 59
< 3 x 1014 W/cm2
1.3ns
Target: Polystyrene 25 µmt
Laser: 1.3 ns Gaussian
SSD
w/ RPP
3w
Spot diameter 300 µm
Energy 230 J (total)
Intensity < 3 x 1014 W/cm2 （実際はこれよりもう少し小さい）
Trajectoryを1Dと合わせて評価
Notes: In the RT experiment, we used both face-on and side-on x-ray backlighting technique.
In the face-on geometry, Slit imager was coupled with an x-ray streak camera.
We can obtain temporal evolution of areal-mass-density perturbation due to the RT instability.
In the side-on geometry, Fresnel phase zone-plate was used as a two-dimensional spatial resolved imager.
X-ray detector was an x-ray CCD camera, and flash x-ray backlighting technique was used to obtained 100 ps-single flame x-ray image with an x-ray CCD camera.
In the side-on geometry, perturbation amplitude of the target is directly measured.

## Slide 60
Shell
Diameter 500 µm
Thickness 7 µm
Material CD plastic
Solid ball
Diameter 200 µm
Material CD plastic
Cone
Angle 45 deg.
Material Gold or DLC
Compression Laser:
GEKKO-XII
Fusion Fuel
Heating Laser:
LFEX
Beam# 12 beams
Energy 280 J/beams
(2.5 kJ total)
Duration 1.3 ns
(Flat top)
Wavelength 527 nm
Beam# 3 beam
Energy 500 J/beam
Duration < 2 ps
Wavelength 1053 nm
Cone-attached surrogate fuel is
compressed by GEKKO-XII laser and heated by LFEX laser
FIREX: Fast Ignition Realization EXperiment
ILE, Osaka
Notes: We have performed integrated experiments of Fast Ignition target by using Gekko-XII for implosion of the shell target, and LFEX for heating.
The target was a plastic shell with a gold cone.

## Slide 61
Oscillator System
Fiber Osc.
Fiber Amp.
Compressor
Grating Stretcher
1st OPCPA
Grating Stretcher
2nd OPCPA
3rd OPCPA
Saturable absorber
Pump laser
Pump laser
*AOPF
Quencher
Pump laser
*K. Kondo et al., J. Opt. Soc. Am. B, Vol. 23 (2006).
AOPF quencher* and saturable absorber
are introduced to reduce the pedestal intensity.
ILE, Osaka
Reduction of Preformed Plasma
Notes: According to these test results, we designed the rear-end sub-system which consists of beam transport optics, 1x4 vertical arrayed pulse compressor, final focusing optics and beam monitoring optics as shown here.