## Slide 1
Methodology on
Cyber Security for Digital I&C System in Research Reactors
Date 2015. 11. 16 ～ 2015. 11. 20
Jinsoo Shin1, Gyunyoung Heo1*,
Hanseong Son2
1: Kyung Hee University / 2: Joongbu University
+82-31-201-3835
* gheo@khu.ac.kr
ICRR 2015
Vienna, Austria
1

## Slide 2
Layout
Methodology on Cyber Security for Digital I&C System in Research Reactors
2015.11.18
Introduction
Methodology on Cyber Security
  Event Tree Analysis
  Cyber Security Evaluation Model using Bayesian Belief Network
Conclusions
2

## Slide 3
Methodology on Cyber Security
for Digital I&C System in Research Reactors
Research Goal
Proposing the methodology for cyber security risk evaluation
with Event Tree (ET) and Bayesian Belief Network (BBN) model
▶ ET model
Systematic analysis for hazard scenarios under cyber-attack
Deduction of critical digital asset (CDA) for research reactors
Goal
3
▶ BBN model
I&C architecture modeling (ex. Reactor Protection System) to be merged with ET models
Quantification from Qualitative values

## Slide 4
Cyber Security
Introduction
Methodology on Cyber Security
for Digital I&C System in Research Reactors
Introduction
Insufficiency of Activity-Quality
Attack to
vulnerability of
architecture
4

## Slide 5
Cyber Security
Issues
Methodology on Cyber Security
for Digital I&C System in Research Reactors
Insufficiency of Activity-Quality
Attack to
vulnerability of
architecture
  Cyber Security
5
Introduction

## Slide 6
Cyber Security
Cyber Security for Research Reactors
Methodology on Cyber Security
for Digital I&C System in Research Reactors
6
Introduction
  One Goal : Power Production
  Multi-Goals : Neutron Beam, Irradiation Test…
  Access
  Access
  User (Operator)
  Users
  I&C

## Slide 7
Cyber Security
Methodology on Cyber Security
for Digital I&C System in Research Reactors
6
Introduction
  One Goal : Power Production
  Multi-Goals : Neutron Beam, Irradiation Test…
  Access
  Access
  User (Operator)
  Users
  Threat
  Threat
  Threat
  I&C
Cyber Security for Research Reactors

## Slide 8
Methodology on Cyber Security
for Digital I&C System in Research Reactors
Definition of Cyber Threat for Digital I&C System in Research Reactors
7
Methodology on Cyber Security
Event Tree Analysis for Research Reactors
  Attack-Tree
  Test-Bed example

## Slide 9
Methodology on Cyber Security
for Digital I&C System in Research Reactors
Definition of Cyber Threat for Digital I&C System in Research Reactors
7
Methodology on Cyber Security
Event Tree Analysis for Research Reactors
  Attack-Tree
  Test-Bed example
  Systematic?
  Scope?

## Slide 10
Methodology on Cyber Security
for Digital I&C System in Research Reactors
Event Tree Analysis to identify Design Basis Accident (DBA) for cyber security
8
Methodology on Cyber Security
Event Tree Analysis for Research Reactors

## Slide 11
Methodology on Cyber Security
for Digital I&C System in Research Reactors
8
Methodology on Cyber Security
Event Tree Analysis for Research Reactors
Event Tree Analysis to identify Design Basis Accident (DBA) for cyber security

## Slide 12
Probabilistic Safety Assessment (PSA)
Methodology on Cyber Security
for Digital I&C System in Research Reactors
Event Tree
Fault Tree
Methodology on Cyber Security
9
Existing Safety Assessment Methodologies

## Slide 13
Probabilistic Safety Assessment (PSA)
Existing Safety Assessment Methodologies
Methodology on Cyber Security
for Digital I&C System in Research Reactors
Event Tree
Fault Tree
Methodology on Cyber Security
9

## Slide 14
Methodology on Cyber Security
Methodology on Cyber Security
for Digital I&C System in Research Reactors
Flowchart of BBN Model for Research Reactors
Check list
Mitigation Measure
Vulnerability
Vulnerability risk
Architecture
Final Risk
Qualitative Analysis
Quantitative Analysis
BBN Cyber Security Evaluation Model
  Reasons for using BBN
  → Modeling complex dependencies with ease
  → Use of prior & posterior information
  → Use of both quantitative
  & qualitative information
10
Activity-quality
Architecture

## Slide 15
Methodology on Cyber Security
for Digital I&C System in Research Reactors
Qualitative and Quantitative Analysis
Check list
Mitigation Measure
Qualitative Analysis
Quantitative Analysis
Evaluating the quantitative analysis of mitigation measure through the evaluation of the check list
Need to convert from qualitative analysis to quantitative analysis
  Words of estimative probability
  Assignment of node probability table value according to connection strength between node and node (using KAERI/TR-2668/2004 )
BBN Cyber Security Evaluation Model
Methodology on Cyber Security
11

## Slide 16
Methodology on Cyber Security
for Digital I&C System in Research Reactors
Activity-quality model
Cyber Security Evaluation Index (CSEI)
Where,
- s is a numeric value of each node
- E is a percentage ratio of evaluation for each node
How compliant with regulatory guides (From 10 to 90)
Goodness of cyber-attack occurrences or the completeness of mitigation measures
Numeric value of Stage | Mean (Compliance)
5 | Very Well
4 | Well
3 | So so
2 | Bad
1 | Very Bad
Architecture model
Numeric value of Stage | Mean (Attack Occurrence)
5 | Very Low
4 | Low
3 | Medium
2 | High
1 | Very High
12
BBN Cyber Security Evaluation Model
Methodology on Cyber Security

## Slide 17
Methodology on Cyber Security
for Digital I&C System in Research Reactors
BBN Model for Reactor Protection System in Research Reactors
13
BBN Cyber Security Evaluation Model
Methodology on Cyber Security

## Slide 18
Methodology on Cyber Security
for Digital I&C System in Research Reactors
BBN Model for Reactor Protection System in Research Reactors
13
BBN Cyber Security Evaluation Model
Methodology on Cyber Security

## Slide 19
Methodology on Cyber Security
for Digital I&C System in Research Reactors
14
BBN Cyber Security Evaluation Model
Methodology on Cyber Security
Analysis Process with the BBN Model
Model Buildup
Model Applications

## Slide 20
Cyber Security Evaluation with ET and BBN model
Methodology on Cyber Security
for Digital I&C System in Research Reactors
Methodology on Cyber Security
Methodology on Cyber Security for Research Reactors
15

## Slide 21
Methodology on Cyber Security
for Digital I&C System in Research Reactors
Conclusions
▶▶ Cyber Security Risk Evaluation for Research Reactors
 It is difficult to quantify and standardize all potential situations
 We proposed the methodology with ET and BBN models
 ET model can help to identify the issues (point of interests) for cyber security
 BBN model can facilitate to develop activity-quality as well as architecture of RPS from the viewpoint of cyber security
16
Conclusions