## Slide 1: International Conference for Research Reactors: Safe Management and Effective utilization, 16-20 November 2015 Vienna, Austria,
By
M. K. Shaat
Former Director of ETRR-2, PSC for RAF1005, Prof. Nuclear Eng. Consultant for EAEA for Nuclear Affairs.
Management of Ageing and Modifications for Research Reactors

## Slide 2: Outline
Objectives
Introduction
Considerations in planning ageing management program,
Elements of ageing management program
Management of obsolescence
Case study ( Egypt ), based on IAEA, SSG-10. 6.1. Modifications for ETRR-1 Reactor.
6.2. Ageing Management Program for ETRR-2 Reactor
7. Concluding remarks

## Slide 3: 1. Objectives
To ensure the long term safety and reliable operation of SSCs of research reactors,
To establish an ageing management program for SSCs of the research reactor ,which should meet the requirements for safety as derived from:
The SAR,
The OLCs,
The Regulatory Body,
The manufactures recommendations.
To monitor and minimize the expected ageing degradation,

## Slide 4: 2. Introduction
Nuclear installations, experience two kinds of aging effects:
Physical ageing,( deterioration in physical characteristic)
Obsolescence , ( becoming out-of-date)
During the last decade, reactor technology have been developed on worldwide. So, it was necessary to upgrade,
modernize the aged SSCs in RRs to achieve the safe operation and reliable utilization.
The following sections discuss the ageing management program for RRs in general and specifically for Egyptian RRs - as a case study.

## Slide 5: 3. Considerations in Planning Ageing Management Program
Design specifications, not violated specially during modifications and refurbishment,
Fabrication and construction, according to design and service conditions,
Operation, optimum operation in accordance with OLCs ,
Regulatory requirements, and feedback from operating experience ( specific & generic ).

## Slide 6: 4. Elements of Ageing Management Program (as mentioned in IAEA, SSG- 10)
Screening of SSCs;
Minimization of expected ageing degradation;
Detection, monitoring and trending of ageing degradation;
Mitigation of ageing degradation;
Continuous improvement of the ageing management program;
Record keeping.

## Slide 7: 5. Management of Obsolescence (as mentioned in IAEA, SSG- 10)
Condition | Action
Change in technology | Ensure systematic identification Of useful service life and anticipated obsolescence prepare modification projects; provide spare parts for the planned Service lifetime.
Change in safety requirements, Regulations and advances in knowledge. | Ensure compliance with Current safety standards Regulations; Consider modifications of SSCs important to safety as required.
Documentation becoming Out of date | Ensure establishment of an effective/ integrated Management system

## Slide 8: 6. Case Study
Egypt operates two research reactors, ETRR-1 and ETRR-2.
ETRR-1 is a WWR-C Russian type, which was commissioned in 1960, its power is 2 MW, uses EK-10 fuel with 10% enrichment, and uses light water as coolant, moderator and reflector.
ETRR-2 is an open pool type, 22MW power, uses plate type fuel elements of 19.75% enrichment, cooled and moderated by light water and with beryllium reflectors. The reactor was commissioned in 1997 with utilization purpose for R&D, radioisotope production, Mo-99 production, iodine production, NAA, and silicon doping.

## Slide 9: 6.1. Modification of ETRR-1
Based on the development in nuclear technology, and for enhancing the performance and safety of the reactor, the following items were installed or modernized:
I&C System:
Control rods drive mechanisms
Instrumentation (nuclear and process parameters)
Signaling and safety logic systems
Fission chamber assembly
Operator console
Data acquisition system
Horizontal beam ports control circuits
Automatic water level compensation system
Radiation monitoring system

## Slide 10: 6.2. Ageing Management Program for ETRR-2
The program includes the following sections:
Maintenance group:
i) Organization, ii) Management and function
Start-up of the maintenance program
The ageing management covers all the reactor systems including safety systems and safety-related systems.

## Slide 11
Periodic Testing:
Maintain and improve the availability of equipments
Ensure compliance with OLCs
Detect and correct abnormal conditions
Inspection:
Asses the physical status of equipment, component important to reactor safety
On-line or Off-line monitoring
Sampling
Measurement of response time for safety systems
Preventive Maintenance Activities:
Walk- through inspection;
Measurement of operational parameters;
Calibration/alignment/checks/lubrication
Chemistry control
Surface treatment and paining

## Slide 12
Predictive Maintenance Program:
Based on the surveillance program
Includes detection, analysis and correction
To eliminate catastrophic equipment failures
Maintenance Procedure:
Title
Purpose
Prerequisites
Special precautions
Special tools and equipment
References
Procedure (step by step instructions)
Return to service

## Slide 13
Corrective Maintenance:
Repair/replacement
Needs adequate resources (spare parts, fund)
Not occurring on regular schedule
Preventive maintenance will reduce the need for corrective maintenance.
Reports and Record Keeping:
Weekly performance report
Monthly performance report
Equipment historical data records
Schedule preventive maintenance
Inventory& spare parts control
Training program

## Slide 14
Surveillance and Review Program:
To insure that the maintenance program meets its purpose;
To check the control of radiation doses;
To check the quality insurance requirements;
To check the adequacy of procedures & instructions.
Reactor Safety Committee:
Review and assess the maintenance and management program and its impact on the reactor safety.

## Slide 15
  7. Concluding Remarks
Ageing management of SSCs should be implemented proactively throughout the lifetime of a RR project;
Ageing management program is accomplished by ;
Integrating and coordinating existing programs, including maintenance, periodic testing and inspection and periodic safety review;
Applying good operational practices;
Incorporating lessons learned from operating experience;
Guidance with IAEA Safety Standards
Modifications of major safety significance should be subjected to review and assessment by safety authorities, and to procedures for ; design, fabrication, construction, commissioning and safety analysis as applied to the reactor itself;
Refurbishment and modernization should be limited to replacement of SSCs; but based on safety improvements to comply with the up-to-date safety requirements and criteria

## Slide 16: THANKS
Maintenance is Life Extension