## Slide 1
Jae-Min Kwona in collaboration with
S. Kub, C.S. Changb, M.J. Choia, R. Hagerb,
E.S. Yoonc, H.H. Leea, and H.S. Kima
aNational Fusion Research Institute, Korea
bPrinceton Plasma Physics Laboratory, USA
cUlsan National Institute of Science and Technology, Korea
27th IAEA Fusion Energy Conference
Oct. 22~27. 2018, Gandhinagar, India
Gyrokinetic XGC1 Simulation of Magnetic Island Effects on Neoclassical and Turbulence Physics in a KSTAR Plasma

## Slide 2: Motivation - KSTAR Experiment
Dedicated experiments employing RMP and fluctuation diagnostics(ECEI) on KSTAR (M.J. Choi et al, NF 57, 126058 (2017))  Impact of 3D magnetic island on plasma flow and fluctuation
profile flattening by m/n=2/1 island, little change in central due to steep gradient region  physics of sustained confinement?
M.J. Choi, EX/11-2

## Slide 3: Motivation - KSTAR Experiment
Anisotropic distribution of electron temperature fluctuations around magnetic island
  fluctuation is strong near the X-point (slightly shifted).
  Very weak (or no) fluctuation is observed around the O-point and inside of magnetic island.
20
10
0
-10
-20
z [cm]
O-point
R [cm]
200 205
X-point
10
8
6
4
2
0
Summed
coherence
M.J. Choi, EX/11-2

## Slide 4: Motivation - KSTAR Experiment
Poloidal flow distribution shows an opposite trend from fluctuation
  Weaker flow is observed near the X-point
  Stronger flow is observed near the O-point
0 20 40 60 80 100
Cross phase
Frequency [kHz]
0
[km/s]
15
10
0
-5
-15
Z [cm]
5
-10
6
4
2
0
-2
-2
-6
0 20 40 60 80 100
Frequency [kHz]
Cross phase
0
205
210
R [cm]
Electron
direction
Ion
direction
Physical mechanisms behind the observed flow and turbulence patterns?
Sustained electron thermal confinement in the inner region?
M.J. Choi, EX/11-2

## Slide 5: Contents
Perturbed neoclassical equilibrium by magnetic island
  Modified equilibrium profiles, equilibrium potential, and flow by magnetic island
  Global XGC1* total-f electrostatic neoclassical simulation with magnetic island and KSTAR data
Global linear instabilities of perturbed profiles by magnetic island
  Detailed properties of micro-instabilities such as growth rate, frequency
  Global gKPSP** linear stability analysis using perturbed profiles from XGC1 simulation
Global nonlinear turbulence simulation with self-consistent neoclassical physics and magnetic island
  Nonlinear evolution of turbulence and zonal flow around magnetic island
  Global XGC1* total-f electrostatic turbulence simulation with magnetic island
* S. Ku et al, JCP 315, 467(2016); S. Ku et al, PoP 25, 056107(2018)
** L. Qi et al, PoP 23, 062513(2016); J.-M. Kwon et al, CPC 215, 81(2017)

## Slide 6
Perturbed 3D neoclassical equilibrium by magnetic island

## Slide 7: Profile Change by Magnetic Island
(2,1) magnetic island is modelled by
profile immediately responds to magnetic island, and enters into quasi-steady state after .
Across O-point, magnetic island width is with steepened- in inner region.
Across X-point, profile shows little change with finite .
(eV) across O-point
W/O Island
W/ Island
Magnetic Island
W/O Island
W/ Island
Magnetic Island
(eV) across X-point
Poincare plot of field lines

## Slide 8: Perturbed Potential Structure
Magnetic island induces non-axisymmetric electrostatic potential perturbation , which has (2,1) structure with tearing parity.
Finite phase difference in poloidal angle between magnetic island and ()  is not flux function (non-ideal effects)
flow and shear are maximum and minimum across potential O, X-point, respectively  Stronger suppression of micro-instability is expected in the region neighboring O-point of magnetic island with the phase shift .
Magnetic Island
Across X-point of
Across O-point of
Electron
Direction
Ion
Direction

## Slide 9
Global linear instabilities
of perturbed profiles
by magnetic island

## Slide 10: Global Linear Analysis
TEM
Perturbed equilibrium profiles from XGC1 neoclassical simulation are used for global linear stability analysis.
driven TEM is dominant in the inner region neighboring magnetic island.
TEMITG in outer region as and collisionality increase.
TEM/ITG

## Slide 11: Flow Shearing vs
Around the O-point, flow shear is strong enough to suppress a significant portion of micro-instabilities.
Around the X-point, TEM with can still exist.
Due to the phase difference between magnetic island and potential, the region with maximum and minimum fluctuation will appear poloidally shifted regions from magnetic X, O-point  consistent with ECEI observation
Across X-point of
Across O-point of
Magnetic Island
TEM
ITG

## Slide 12
Global nonlinear turbulence simulation with magnetic island and self-consistent neoclassical physics

## Slide 13: Turbulence Evolution near O-point
Nonlinear turbulence simulation starts from the established 3D neoclassical equilibrium with magnetic island
Instabilities are found to be excited outside of magnetic island.
Turbulence spreads into the island. But the island blocks turbulence spreading across the separatrix.
time

## Slide 14: Turbulence Evolution near X-point
Very different turbulence evolution patterns are found in the X-point region.
Instabilities are excited both inside and outside of magnetic island (finite near X-point).
Turbulences spread into the island and pass through to the other side.
time

## Slide 15: profiles across O, X-point
Around the O-point, shearing structure is similar with the neoclassical equilibrium
 turbulence generated zonal flow is relatively weak.
Around the X-point, shearing is dominated by time varying zonal flow driven by turbulence
profile across O-point
before turbulence onset
after turbulence onset (time averaged)
profile across X-point
before turbulence onset
after turbulence onset (time averaged)
Magnetic
Island
R [m]
R [m]
Magnetic
Island

## Slide 16: profiles across O, X-point
“Leakage” of electron thermal energy in both cases: stronger penetration into the X-point  consistent with the turbulence evolution patterns.
“Leakage” is not enough to degrade the central confinement inside the island radii.
Island size estimated by flat- is smaller than the real island size.
profile across O-point
profile across X-point
before turbulence onset
after turbulence onset
before turbulence onset
after turbulence onset
R [m]
R [m]
Magnetic
Island
Magnetic
Island

## Slide 17: Conclusion (1/2)
Magnetic island induces perturbed equilibrium flow
  In O-point region, flow shear is strong enough to suppress ambient TEMs and good electron thermal confinement is sustained.
  In X-point region, flow shear becomes weaker and stronger instabilities are excited.
  However, magnetic O,X-point do not coincide with maximum/minimum shearing region due to phase difference between and  separate fluctuation measurement
Magnetic
Island
Potential
Perturbation
Phase difference
in poloidal angle
Weak
Turb
Strong
Flow
Strong
Turb
Weak
Flow
Jae-Min Kwon et al, Phys. Plasmas 25, 052506 (2018)

## Slide 18: Conclusion (2/2)
Nonlinear turbulence evolution pattern is different in O- and X-point. (L. Bardoczi et al, PoP 24, 122503(2017); K. Ida et al, PRL 120, 245001(2018))
Due to turbulence spreading, fluctuation penetrates into magnetic island, and flat- region becomes smaller than island region  separate measurement of magnetic perturbation
“Shallow penetration
by turbulence spreading”
“Shallow penetration
by turbulence spreading”
“Transport through X-point”

## Slide 19
Thanks for your attention!