## Slide 1: Advances in predictive thermo-mechanical modelling for the JET divertor experimental interpretation, improved protection, and reliable operation
D. Iglesias, W. Arter, I. Balboa, P. Bunting, C. Challis, J.W. Coenen, Y. Corre, S. Esquembri, S. Jachmich, K. Krieger, G. F. Matthews, R. A. Pitts, V. Riccardo, M. L. Richiusa, M. Porton, F. Rimini, S. Silburn, V. Thompson, R. Otin, D. Valcarcel, L. Vitton-mea, Z. Vizvary, J. Williams

## Slide 2: Overview
Motivation
Modelling advances
  Parallel heat flux (amplitude)
  Engineering footprint (width)
Divertor integrity predictive analysis
  Validation activities
  Application to engineering assessments
Conclusions
Bulk-W
W-coated CFC
W-coated CFC
ITER-like (Be) wall and (W) divertor

## Slide 3: Motivation
Operational risks:
  JET divertor is protected by a set of operating instructions, limiting maximum tile temperature and energy
  Several tiles where found damaged with cracks and broken tie-rods during the last two shutdowns
  Last high-power campaign has exposed weaknesses in divertor design requiring additional protection measures
In support to ITER, experiments at JET studied the impact of melting an exposed tungsten edge
Modelling needs

## Slide 4: Motivation
Reconstruction of parallel heat flux for 2013 melting experiments was only possible reducing the IR derived q// by a factor of 5 for L-mode and 2.5 for H-mode [1]
Assuming that λq from the inter-ELM scaling laws [2] applies for the heat flux on all components leads to:
  An overestimation of the peak temperature, and
  An underestimation of the maximum stress
JPN 84779 [1]
[1] ARNOUX G. et al, Thermal analysis of an exposed tungsten edge in the JET divertor, J. Nucl. Mat. 463 (2015) 415–419.
[2] EICH T. et al, Scaling of the tokamak near the scrape-off layer H-mode power width and implications for ITER, Nucl. Fusion 53 (2013) 093031.
Operational
limit
Simulation issues

## Slide 5: Modelling advances
Characterized using results from 2013 and 2015-16 melting experiments
Three geometries compared, with 2˚, 15˚, and 90˚ angles
New inverse code ALICIA [3] for increased IR derived heat flux calculation
Geometrical and surface loading effects considered
Power measured at shadowed region used as cross-check
Parallel heat flux
[3] IGLESIAS D. et al, Digital twin applications for the JET divertor, Fusion Eng. Des. 145 (2017) 71–76.
2013 Experiment
2015-16 Experiment

## Slide 6: Modelling advances
Background measured with strike point away
Mismatch between q// measured by typical approach:
Measurements at three different angles match when adding an additional term [4]:
Parallel heat flux
[4] IGLESIAS D. et al, An improved model for the accurate calculation of parallel heat fluxes at the JET bulk tungsten outer divertor, Nucl. Fusion 58 (2018) 106034

## Slide 7: Modelling advances
Fit averaging ELM and inter-ELM contributions
Includes natural movements of the strike point due to EM and control system transients
Tile 5 analysed for C and ILW-wall with no major differences between materials
Engineering footprint [5]
[5] RICCARDO V. et al, “Power footprint definition for JET divertor protection”, 22nd PSI, Roma, Italy (2016).

## Slide 8: Modelling advances
Tile 6 has different equilibrium, with longer connection length
Footprint fit found is broader than tile 5
Compared to inter-ELM scaling, engineering footprint for tile 6 is 5-10 times larger
Engineering footprint
shot | λq inter-ELM (mm) | λfootprint T5 (mm) | λfootprint T6 (mm)
90271 | 2.1 | 2.2-3.5 | 9-17
92025 | 2.1 | 2.1-3.0 | 11-19
92436 | 2.1 | 2.1-2.5 | 10-19
92398 | 2.5 | 2.0-3.2 | 13-16

## Slide 9: Divertor integrity predictive analysis
Tile surface heat flux density calculated at equatorial plane using the engineering footprint
Projected using Flush (2D) or SMARDDA/PFC (3D), and
Taking into account the corrected optical projection
Forward model

## Slide 10: Divertor integrity predictive analysis
Temperature evolution captured during flat-top and ramp-down
Energy consistent predictive model with 15% error in temperatures and energy
Validation

## Slide 11: Divertor integrity predictive analysis
Preparation: JET Operating Instructions checks running synthetic shots in the integrated modelling tool VITA
Workflows

## Slide 12: Divertor integrity predictive analysis
Protection: Real-time protection using WALLS with the engineering footprint and fast FE 2D RT models
Workflows

## Slide 13: Divertor integrity predictive analysis
Post-pulse integrity assessment: possible even if camera signals are not available for the shot. The surface load is calculated at the equatorial plane, projected to the divertor and then linked to 3D FE codes, such as ANSYS
Workflows

## Slide 14: Divertor integrity predictive analysis
Damage prediction:
Melting experiments simulation with IR derived heat flux and corrected optical projection [4]
Integrity assessments
Melting onset
changes emissivity
[4] IGLESIAS D. et al, An improved model for the accurate calculation of parallel heat fluxes at the JET bulk tungsten outer divertor, Nucl. Fusion 58 (2018) 106034

## Slide 15: Divertor integrity predictive analysis
Failure mode investigation:
Tile radial cracks due to poloidal temperature gradient
Tie-rod failure due to fatigue produced by repeated tile extension and bending
Integrity assessments
Cracks
Tie-rod fatigue
[6] RICHIUSA M. L. et al, Maximizing JET divertor mechanical performance for the upcoming Deuterium-Tritium experiments, Fusion Eng. Des. (2018) Submitted.
Risk assessment:
Cracks risk is high [6] for toroidal stress > 6 Mpa
Fatigue failure avoided by managing energy accumulated through life

## Slide 16: Conclusions (I)
The corrected optical projection for the parallel heat flux is 40% of that inferred when geometrical and loading corrections are not taken into account
The non-parallel heat flux component is characterized by direct measurements and needed in JET for consistency, although its origin is uncertain and more analysis is required to separate any diagnostic error from understood physics
Future experiments and dedicated modelling should assess what the implications of the corrected projection are for the steady loads on ITER
The engineering footprint averages ELM and inter-ELM contributions leading up to 5-10 times broader profiles when compared to the inter-ELM scaling laws

## Slide 17: Conclusions (II)
Modelling improvements have been integrated in predictive analysis tools, with a maximum 15% error in temperatures and energy estimations
Melting, cracks and tie-rod failures at the divertor tiles can now be reproduced and prevented in the upcoming high power D-T campaign
The thermal behaviour is calculated in a matter of seconds while a 3D thermo-mechanical assessment can be automatically performed in less than 10 minutes.
This development extends the operational envelope for JET high power and high energy shots and is also transferable to ITER

## Slide 18: Advances in predictive thermo-mechanical modelling for the JET divertor experimental interpretation, improved protection, and reliable operation
D. Iglesias, W. Arter, I. Balboa, P. Bunting, C. Challis, J.W. Coenen, Y. Corre, S. Esquembri, S. Jachmich, K. Krieger, G. F. Matthews, R. A. Pitts, V. Riccardo, M. L. Richiusa, M. Porton, F. Rimini, S. Silburn, V. Thompson, R. Otin, D. Valcarcel, L. Vitton-mea, Z. Vizvary, J. Williams
Thank you for your attention!