## Slide 1: Increasing the density in Wendelstein 7-X: Benefits and limitations
G. Fuchert1, K.J. Brunner1, K. Rahbarnia1, T. Stange1, D. Zhang1, J. Baldzuhn1, M.N.A. Beurskens1, S.A. Bozhenkov1, C.D. Beidler1, S. Brezinsek2, R. Burhenn1, H. Damm1, A. Dinklage1, M. Hirsch1, Y. Kazakov3, J. Knauer1, Y. Feng1, A. Langenberg1, H.P. Laqua1, S. Lazerson4, N. Pablant4, E. Pasch1, T. Sunn Pedersen1, E.R. Scott1, F. Warmer1, V. Winters5, R.C. Wolf1,6 and W7-X team
1Max Planck Institute for Plasma Physics, Greifswald, Germany, 2Forschungszentrum Jülich, Jülich, Germany, 3Royal Military Academy, Brussels, Belgium, 4Princeton Plasma Physics Laboratory, Princeton NJ, USA, 5University of Wisconsin-Madison, Madison WI, USA, 6Technische Universität Berlin, Berlin, Germany

## Slide 2: Motivation: Density scaling of the energy confinement
[Dinklage, NF 47, (2007)]
Empirical scaling ISS04
Positive density scaling and negative power scaling („power degradation“).
Triple product benefits from increasing the density.
Power and density scaling agree with neoclassical plateau regime. [Dinklage , NF 47, (2007)]
ISS04 close to a gyro-Bohm scaling: turbulent transport?

## Slide 3: Motivation: Density scaling of the energy confinement
  Neoclassical prediction for W7-X
  Neoclassical transport modeling suggests a negative power scaling close to ISS04 and a stronger positive density scaling. [Turkin, PoP 18, (2011)]
  Increase the density!
  Limitations? Empirical τE scaling?
[Turkin 2007 (EPS)]

## Slide 4: Outline
Energy confinement time before boronization
Scaling close to ISS04
Density limited by radiative collapses
Critical density
Comparison of analytical models with experimental observations
Critical density before and after boronizatoin
Energy confinement time after boronization
Scaling after boronization
Energy confinement time at higher densities
Summary and conclusion

## Slide 5: Energy confinement before boronization
Spread of experimental data, not error
Before boronization, τE showed a scaling close to ISS04 in hydrogen.
Densities above ~ 4∙1019 /m3 were only accessible transiently with pellet fuelling due to radiative collapses.
Scenario | a0 | α | β
Standard divertor | 0.16 | 0.56 | -0.78
Limiter (OP1.1) | 0.13 | 0.75 | -0.64
ISS04 | - | 0.54 | -0.61
tE ~ a0naPb

## Slide 6: Density scaling of the energy confinement

## Slide 7: Density scaling of the energy confinement

## Slide 8: Density scaling of the energy confinement
Common phenomenon in stellarators, e.g. in
LHD: [J. Miyazawa et al., Fusion Sci. Technol. 58 (2010)]
TJ-II: [M.A. Ochando, 41st EPS Conference on Plasma Physics (2014)]
W7-AS: [L. Giannone et al., Plasma Phys. Control. Fusion 45 (2003)]
W7-A: [G. Cannici et al., Proc. 7th Int. Conf. on Plasma Phys. And Control. Nucl. Fusion (1978)]

## Slide 9: Predicting the critical density for strong edge radiation
Critical density from the detachment model by Itoh [K. Itoh and S. Itoh, J. Phs. Soc. Jpn. 57 (1988)]
Sudo density limit [S. Sudo et al., Nucl. Fusion 30 (1990)]
Limits with different transport and radiation models [H. Wobig, Plasma Phys. Control. Fusion 42 (2000)]
Modified Itoh model for W7-AS [L. Giannone et al., Plasma Phys. Control. Fusion 45 (2003)]
Implicit dependences on transport and edge impurities (low Z) have to be made explicit [Zanca et al., Nucl. Fusion 57 (2017)]

## Slide 10: Predicting the critical density for strong edge radiation
Critical density from the detachment model by Itoh [K. Itoh and S. Itoh, J. Phs. Soc. Jpn. 57 (1988)]
Sudo density limit [S. Sudo et al., Nucl. Fusion 30 (1990)]
Limits with different transport and radiation models [H. Wobig, Plasma Phys. Control. Fusion 42 (2000)]
Modified Itoh model for W7-AS [L. Giannone et al., Plasma Phys. Control. Fusion 45 (2003)]
Implicit dependences on transport and edge impurities (low Z) have to be made explicit [Zanca et al., Nucl. Fusion 57 (2017)]
Image courtesy by T. Pütterich

## Slide 11: Predicting the critical density for strong edge radiation
Critical density from the detachment model by Itoh [K. Itoh and S. Itoh, J. Phs. Soc. Jpn. 57 (1988)]
Sudo density limit [S. Sudo et al., Nucl. Fusion 30 (1990)]
Limits with different transport and radiation models [H. Wobig, Plasma Phys. Control. Fusion 42 (2000)]
Modified Itoh model for W7-AS [L. Giannone et al., Plasma Phys. Control. Fusion 45 (2003)]
Implicit dependences on transport and edge impurities (low Z) have to be made explicit [Zanca et al., Nucl. Fusion 57 (2017)]
Configuration | c
Standard | 0.56
High-iota | 0.59
High-mirror | 0.57
Details on the magnetic configurations:
[J. Geiger et al., Plasma Phys. Control. Fusion 57 (2015)]
W7-X

## Slide 12: Critical density before boronization
Large scatter in nc
Weaker power scaling than predicted (if any…)
Possible reasons:
  Changing impurity content (depending on heating power?)
  Profile effects, importance of edge density (δ)
  Model not applicable (local effects, changing main radiator,…)
Hydrogen plasmas with central X2-heating

## Slide 13: Critical density before boronization
Large scatter in nc
Weaker power scaling than predicted (if any…)
Possible reasons:
  Changing impurity content  under investigation
  Profile effects, importance of edge density (δ)
  Model not applicable  local effects exist (e.g. Marfe [U. Wenzel, NF 58 (2018)]), but their importance is unclear
Common mitigation strategies:
  Pellet fueling (decouple core and edge density)
  Wall conditioning by e.g. boronization [->R. Brakel, EX/P8-17]
[G. Kocsis, T. Szepesi]

## Slide 14: Critical density after boronization
After boronization, radiation from oxygen and carbon lines went down significantly
  Reduced by a factor of 5 to 10
  Only moderate additional boron lines
  [-> Pedersen et al., EX/9-1]
At the same time, nc increased by a factor of ~3
  In the scaling law this would correspond to a reduction of fimp by a factor of 5 to 10
Configurational effects are either absent or subtle
fimp=5%
fimp=1%
fimp=0.5%

## Slide 15: Profile effects
Estimate edge density by δ=n0/n0.85ρ
Significantly improved agreement with scaling for ne/δ
 Profile effects are a major source for the scatter in nc

## Slide 16: Profile effects
Estimate edge density by δ=n0/n0.85ρ
Significantly improved agreement with scaling for ne/δ
 Profile effects are a major source for the scatter in nc
tE?

## Slide 17: Energy confinement at higher densities
Scenario | a0 | α | β
After boronization | 0.16 | 0.38 | -0.59
ISS04 | - | 0.54 | -0.61
Energy confinement after boronization
For simplicity, only X2-heated plasmas are shown
  In O2 similar observations, but Pabsorbed < Pheat.
Also in these experiments a positive density scaling of τE is found.
This trend can be observed even in single experiments.
Density scaling gets weaker at high frad=Prad/PECRH or densities close to nc.

## Slide 18: Energy confinement at higher densities
Scenario | a0 | α | β
After boronization | 0.16 | 0.38 | -0.59
ISS04 | - | 0.54 | -0.61
Only accessible after boronization
Energy confinement after boronization
For simplicity, only X2-heated plasmas are shown
  In O2 similar observations, but Pabsorbed < Pheat.
Also in these experiments a positive density scaling of τE is found.
This trend can be observed even in single experiments.
Density scaling gets weaker at high frad=Prad/PECRH or densities close to nc.

## Slide 19: Energy confinement at higher densities
Energy confinement after boronization
For simplicity, only X2-heated plasmas are shown
  In O2 similar observations, but Pabsorbed < Pheat.
Also in these experiments a positive density scaling of τE is found.
This trend can be observed even in single experiments.
Density scaling gets weaker at high frad=Prad/PECRH or densities close to nc.
Scenario | a0 | α | β
After boronization | 0.16 | 0.38 | -0.59
… ne > 4∙1019 /m3 | 0.11 | 0.62 | -0.64
ISS04 | - | 0.54 | -0.61

## Slide 20: Energy confinement at higher densities
Energy confinement after boronization
For simplicity, only X2-heated plasmas are shown
  In O2 similar observations, but Pabsorbed < Pheat.
Also in these experiments a positive density scaling of τE is found.
This trend can be observed even in single experiments.
Density scaling gets weaker at high frad=Prad/PECRH or densities close to nc.
Scenario | a0 | α | β
After boronization | 0.16 | 0.38 | -0.59
… ne > 4∙1019 /m3 | 0.11 | 0.62 | -0.64
ISS04 | - | 0.54 | -0.61
?

## Slide 21: Energy confinement close to nc
Before boronization, the density scaling becomes weaker above ~0.5·nc,5%
After boronization, the density scaling becomes weaker above ~1.0·nc,5%
frad increases with ne/nc
As it was shown before, high densities as such are not an issue

## Slide 22: Summary and conclusion
  Energy confinement time in W7-X
  Improves with density, roughly in-line with ISS04 (tE~n0.54).
  Improvement obviously limited by radiative collapses.
    Critical density can be estimated from analytical models.
    Boronization crucial to achieve relevant densities.

## Slide 23: Summary and conclusion
  Energy confinement time in W7-X
  Not one single scaling law for the entire parameter range.
    Unravelling the main transport/loss channels has only started.
  Plasmas with pellet-fueling [-> Bozhenkov et al., EX/P8-8] or O2 and NBI-heating are not even included in the analysis yet.
  tE–scalings need to take different regimes and operational limits into account. This is well established for tokamaks, but not yet for stellarators.