## Slide 1: Super H-Mode Experiments on Alcator C-Mod and DIII-D Achieve High Fusion Performance, Record Pedestal Pressure
Super H-mode (SH) predicted in strongly shaped plasmas: high pped, increases with ne [Snyder NF15]
Record pedestal pressures (~81 kPa) achieved in C-Mod SH experiments [Hughes NF18]
  Successful tests of EPED model up to ~90% of predicted ITER pped
Record DIII-D fusion gain (QDT,eq~ 0.5). QDT,eq/IaB and QDT,eq/(RB)2 highest reported on any tokamak
High performance sustained w/ 3D magnetic perturbations to control ne and impurity accumulation
High pped and τE sustained with high rates of D2 and N2 puffing, strong reduction of divertor Te
Super H-mode compatible with both high fusion performance and high separatrix density for divertor solutions
P.B. Snyder EX/2-4
C-Mod SH expts pped= 40-81 kPa