## Slide 1: Min Xu on behalf of HL-2A team & collaborators Southwestern Institute of Physics, Chengdu , China
Overview of HL-2A Recent Experiments
27th IAEA FEC, October 22-27, 2018, Ahmedabad, India
In collaboration with
IRFM/CEA, Cadarache, France
University of California, San Diego, USA
University of Wisconsin – Madison, Wisconsin, USA
CCFE, Culham Science Centre, UK
NIFS, Japan
PPPL, USA
MIT, USA
Kyushu University, Kyoto University, Japan
ASIPP, China
USTC, HUST, Dalian UT, Beijing U, Tsinghua U, HIT, Sichuan U, China

## Slide 2
Outline
Present status of the HL-2A Tokamak
Progress of physics study in H-mode plasma
  Techniques and physics of ELM control
  Pedestal dynamics & L-H transitions
  ITB in H-mode plasma
Energetic particle physics and modulation of turbulence by MHD
  Control of fishbone by ECRH
  Fishbone-like mode destabilized by fast ions
  Interaction between TM and turbulence
Summary & Outlook

## Slide 3
Outline
Present status of the HL-2A Tokamak
Progress of physics study in H-mode plasma
  Techniques and physics of ELM control
  Pedestal dynamics & L-H transitions
  ITB in H-mode plasma
Energetic particle physics and modulation of turbulence by MHD
  Control of fishbone by ECRH
  Fishbone-like mode destabilized by fast ions
  Interaction between TM and turbulence
Summary & Outlook

## Slide 4
R: 1.65 m
a: 0.40 m
Bt: 1.2~2.7 T
Ip: 150 ~ 480 kA
ne: 1.0 ~ 6.0 x 1019 m-3
Te: 1.5 ~ 5.0 keV
Ti: 0.5 ~ 3.5 keV
NBI1
NBI2
SOUTH
NORTH
Newly developed diagnostics
Beam Emission Spectroscopy (BES)
Phase Contrast Imaging (PCI)
He Gas-Puss-Imaging (He-GPI)
Coherence Imaging Spectroscopy (CIS)
CO2 laser collective Thomson scattering system
Plan view
Heating systems:
ECRH/ECCD: 5 MW
NBI (tangential): 3 MW
LHCD: 2 MW (PAM, 2 s)
Present Status of HL-2A Tokamak

## Slide 5
Mission: key physics for advanced tokamaks (e.g. ITER)
  Present stage:
    H-mode physics: L-H transition, edge turbulence & transport
    MHD control: ELM, EPM, Disruption control
  Next plan:
    real time control of MHD (NTM, Disruption,…)
    development of advanced ELM control techniques
    multi-scale physics
Current operation regime
  High beta：
  Good confinement: H98 ~ 1.2
  Bootstrap current fraction: >30%
  Full non-inductive operation: Vloop ~ 0
Mission of the HL-2A
Notes: Beta_N, Beta_p：shot34340@908ms；beta_p from MARS-F estimation.
Bootstrap cuttent: shot34185, based on Aiping’s modelling result
H98： Wulv’s extimation

## Slide 6: Fuelling and MHD Control Systems
Supersonic molecular beam injection (SMBI):
  new skimmer, 1kHz,Max throughput :1022
  H2,D2, He,Ar…,with pressure: 0.1-5 MPa
Laser blow-off (LBO):
  Al, Fe, Ti, W,…
  multi-pulses frequency: 30 Hz
Shattered pellet injection(SPI)：
  diameter: 3.5 mm, length: ~4.5 mm
  Velocity: 0.2 to 0.5 km/s
Pellet injection:
  diameter: 1-1.2 mm; 0.1-0.5 km/s
Gas Puffing: ~0.18 MPa
Massive gas injection (MGI): max throughput :1023
SMBI injector with higher fueling efficiency
SPI system
LBO system
Notes: (a) Schematic diagram of the LBO system in HL-2A; (b) LBO target with footprints of laser ablation

## Slide 7
Main diagnostics on the HL-2A
Diagnostics for transport study
  Te profile: Thomson Scattering, ECE
  Ti profile: CXRS, CP-NPA
  ne profile: Thomson Scattering, Interferometer, Reflectometer
  rotation : CXRS, Doppler reflectometer, Probe array
  q profile: MSE, Polarimeter
Diagnostics for plasma fluctuations
  : Interferometers, Doppler reflectometers, Reflectometer, BES
  : ECE, ECEI, Soft-x-array, Electrostatic probe
  : Mirnov coils
Diagnostics for fast ions
  Fast ion distribution: FIDA, CP-NPA ,CXRS
  Fast ion loss: Fast ion loss probe, Fission chamber, neutron rate

## Slide 8
Outline
Present status of the HL-2A Tokamak
Progress of physics study in H-mode plasma
  Techniques and physics of ELM control
  Pedestal dynamics & L-H transitions
  ITB in H-mode plasma
Energetic particle physics and modulation of turbulence by MHD
  Control of fishbone by ECRH
  Fishbone-like mode destabilized by fast ions
  Interaction between TM and turbulence
Summary & Outlook

## Slide 9
ELM Mitigation by LHCD
ELM mitigation with LHCD and significantly reduction of the divertor heat load.
A plausible mechanism : LHCD → Edge velocity shear decrease → Turbulence radial spectral shift → Turbulence amplitude → ELM mitigation
Xiao(SWIP), Zou(CEA), et al., EX/7-4
Mechanism: LHCD → ExB shear decrease → shift → increase → ELM mitigation
Pedestal turbulence intensity
Notes: Some theory results shown below will support the conclusion about the mechanism of ELM mitigation
LHCD – change the E -- change ExB
我们的猜测是LHCD影响电流电厂

## Slide 10
Velocity shear: severe reduction after LBO.
Pedestal turbulence: Intensity enhanced.
radial wavenumber spectral shift.
ELM Mitigation
Xiao(SWIP), Zou(CEA), et al., EX/7-4
ELM Mitigation by LBO Fe impurity seeding
Notes: 而impurity seeding主要是导致局部温度下降，碰撞增加
形成剪切阻尼
所以二者都导致shear变化

## Slide 11
Mechanism of ELM Mitigation by LHCD/LBO
Theoretical results confirm enhancement of turbulence by shift of radial wavenumber
Theoretical results
Q: heat source
U: reduction value of ExB shear
Averaged radial wavenumber
Turbulence intensity
Theory model predicts the turbulence enhancement by shift of radial wavenumber
LHCD/LBO ExB shear decrease shift increase ELM mitigation
Xiao(SWIP), Zou(CEA), et al., EX/7-4
Notes: 这个case 我之前初步算了下，没看到。附近的炮都没看到，也不知道是物理不一样了，还是那段时间测量有问题。目前还在分析更多的数据。但是纯D2 发现了。

## Slide 12
  Mixture SMBI mitigates ELMs & significantly reduce divertor heat flux
  Impurity ions and change of pedestal profiles lead to ELMs mitigation
Divertor heat flux near the striking point
Zhong et al., EX/P5-3
  D2 +Ne(30% ) SMBI strongly mitigates ELMs
ELM mitigation with D2+Ne SMBI
Mitigate ELMs
ELM frequency ratio
Improve confinement

## Slide 13
ELM suppressed by LBO-seeded impurity
LBO-seeded impurity measured by camera and bolometer
ELM suppressed by LBO seeded impurity (W)
In suppression phase, a new mode (Harmonic Coherent Mode, HCM) was found.
Zhang, Mazon, et al., NF (2018)
A new ELM suppression technique: LBO-seeded impurity
ELM control by LBO W impurity seeding
Notes: HCM: EM mode, too weak to identify the mode number and structure

## Slide 14
Interaction between plasma flows and turbulence
GAM facilitates the L-I transition with energy transfer from GAM to LCO.
Increased mean E×B flow shear promotes the L-I and I-H transitions .
The increment of comes from the ion diamagnetic component
Liang et al., PoP 2017
Pressure gradient  E×B flow shear increase  L-I&I-H transition

## Slide 15
Nonlinear coupling in pedestal turbulence
CM: f=30-70 kHz, m=20-24,localized in pedestal (2~3cm)
Inward particle flux induced by the coherent mode
CM generation mechanism: nonlinear coupling of small scale turbulence
Cheng et al., AAPPS-DPP, 2017
CM
Coherent mode (f=30-70 kHz, EM) plays a key role in inward particle flux
Notes: h中的红线和蓝线分别代表的是悬浮电位扰动和密度梯度扰动; 采用条件平均方法计算; 表明了电位扰动超前密度梯度; 局部梯度扰动是因为模发展而引起;
CM基本特性: 电磁结构, 模数m=20-24, Localized 台基区域 (通常宽度2-3cm); 但在接近ELM的过程中, 模结构会发生变化.

## Slide 16
16
Nonlinear coupling of turbulence  localized mode  streamer
Streamer: life time 10 ~ 20 us, size: ~10 cm * 5 cm
Streamer provides a fast transport channel connected the edge to core plasmas
First observation of streamer in H mode
Cheng, EX/P5-6
Time increases
t= 0 us
t=+26 us
Transition to streamer
Time increases
In ELM phase: streamer induces a transport channel from core to edge within a few microsecond
ECEI
(ECEI)
Notes: The first observation of radially elongated streamer in pedestal during inter-ELM phase, which provides a transport channel connected the edge to core plasmas within a few microsecond. 形成机制: 湍流通过非线性耦合而形成; Streamer 径向空间尺度10-15 cm (占装置小半径尺寸的20-30%),

## Slide 17
(1/1) fishbone plays an important role in the formation and sustainment of ITB at low central shear;
Formation of ITB in H mode plasma
Turbulence suppressed during ITB sustainment
ITB in H-mode plasma
ITB
Liu et al., EX/P5-28
HL-2A # 29710
ELMy
Fishbone  fast ion redistribution change of q shear  affect transport  ITB formation

## Slide 18
RS and Turbulent Generation of Edge Poloidal Flows
T. Long, P.H. Diamond et al. EX/P5-5
Reynold stress and particle flux PDF at 1cm inside LCFS show elevated kurtosis, which indicates fat tails;
Deviation from Gaussian suggests the consideration of:
1. Validity of quasilinear models of edge turbulence transport
2. Phase correlations and dynamics
Significant deviation of mean poloidal flow from neoclassical due to turbulent stresses. Shift ↑ with power.

## Slide 19
Outline
Present status of the HL-2A Tokamak
Progress of physics study in H-mode plasma
  Techniques and physics of ELM control
  Pedestal dynamics & L-H transitions
  ITB in H-mode plasma
Energetic particle physics and modulation of turbulence by MHD
  Control of fishbone by ECRH
  Fishbone-like mode destabilized by fast ions
  Interaction between TM and turbulence
Summary & Outlook

## Slide 20
Stabilization of m/n=1/1 fishbone by ECRH
Chen et al., EX/P5-20&NF, 2018
Mode stability depends on both the PECRH and deposition location ()
Fishbone suppressed when PECRH exceeds a threshold.
Mechanism: ECRH  Te increase  resistivity decrease  resistive fishbone stabilized
ECRH
growth rate
Mode frequency
Reynolds number
Theoretical result
Scan , fixed PECRH=1 MW
Scan PECRH , = 0.42
PECRH = 0.37 MW
PECRH = 0.55 MW
PECRH = 0.60 MW
= 0.02
= 0.42
= 0.66
fishbone

## Slide 21
Wave-particle resonance converts unstable TM to fishbone-like mode with frequency chirping and amplitude bursting
Excitation of m/n=2/1 fishbone by fast ions
Chen et al., EX/P5-20
ECEI
Resonant interactions between fast ions and m/n=2/1 TM were observed

## Slide 22
Co-passing energetic-ions drive the m/n=2/1 fishbone-like mode
Simulated mode structure and mode frequency chirping consistent with the measurements
Resonance condition: ωφ−2ωθ−ω = 0, and co-passing energetic-ions are responsible for the mode drive
with EP
without EP
Mode structure
Resonance condition
M3D-K modelling collaborates with Zhu (DLUT)
Co-passing energetic-ions play a key role in the fishbone-like mode drive

## Slide 23
Mode propagates in electron diamagnetic drift directions
TAE locates in the core(ρ=0.35), with n=4, m=4 and 5
fTAE=224 kHz by theory close to experimental results (235 kHz);
Yu et al., PoP, 2018
TAEs driven by energetic electrons
Theory predicted
mode structure
High-frequency TAE driven by energetic electrons was observed

## Slide 24
turbulence
flow
Interaction among island, flow and turbulence
Turbulence reduced inside island while elevated at island boundary, consistent with gradient-driven turbulence
Perpendicular flow, flow fluctuation and density fluctuation were modulated by island rotation.
Jiang et al., NF, 2018
Pressure gradient plays a key role in modulation of turbulence by TM
(@ outer bdry of island)
Island width
Notes: Shear increase at outer bdry of island
While turbulence increase, which implies that that pressure have a key role on affecting turbulence

## Slide 25
Localized modulation of by large island
An island-width threshold (6.6 cm) was found in the turbulence modulation.
Jiang et al., EX/P5-4
Modulation of by island only appears in the inner half island (marked by green dots in (a) )
Large difference between X- and O-point in inner half island

## Slide 26
Outline
Present status of the HL-2A Tokamak
Progress of physics study in H-mode plasma
  Techniques and physics of ELM control
  Pedestal dynamics & L-H transitions
  ITB in H-mode plasma
Energetic particle physics and modulation of turbulence by MHD
  Control of fishbone by ECRH
  Fishbone-like mode destabilized by fast ions
  Interaction between TM and turbulence
Summary & Outlook

## Slide 27
Summary of research highlights
ELM control techniques were developed:
  LHCD were achieved
  LBO seeded impurity,
  impurity mixture SMBI
In ELM phase: streamer induces a transport channel from core to edge within a few microsecond
Control of resistive fishbone by ECRH realized on the HL-2A. Wave-particle resonance converts unstable TM to fishbone-like mode.
Found island-width threshold for turbulence modulation. Modulation of by island only appears in inner half island.

## Slide 28
Outlook
HL-2M
  Mission: In support of ITER & CFETR: high performance, high beta, and high bootstrap current plasma; advanced divertor configuration (snowflake, tripod), PWI at high heat flux, etc.
  Parameters: R=1.78 m, a=0.65 m, Bt=2.2 T, Ip=2.5 MA, Heating~ 25 MW, triangularity=0.5, elongation=1.8-2.0
  Status: Start the assembling before the end of this year.
HL-2M tokamak

## Slide 29
OV/5-1 Xu: Overview of HL-2A recent experiment
EX/P5-20 Chen: Suppression and destabilization of ion fishbone activities on HL-2A
EX/P5-28 Liu: Development of the q=1 Advanced tokamak Scenarios in HL-2A
EX/P5-6 Cheng: Pedestal dynamics in inter-ELM phase on HL-2A tokamak
EX/P5-4 Jiang: Localized modulation of turbulence by magnetic islands on HL-2A tokamak
EX/P5-19 Shi: Energetic-ion Driven Toroidal and Global Alfvén Eigenmodes on HL-2A
EX/P5-3 Zhong: Plasma confinement and pedestal dynamics responses to impurity seeding in HL-2A H-mode plasmas
EX/P5-8 Zhang: Effect of LBO-seeded Impurity on ELMs in the HL-2A tokamak
EX/P5-12 Xu: Experimental evaluation of electron energy probility function and sheath potential coefficient of HL-2A
EX/7-4 Xiao: ELM Control Physics with Impurity Seeding and LHCD in the HL-2A Tokamak
Welcome to the poster session for further discussions!
List of HL-2A Contributions

## Slide 30
List of SWIP Contributions
OV/5-1 M.Xu : Overview of HL-2A recent experiments
FIP/2-1 J. Chen:Progress in Developing ITER and DEMO First Wall Technologies at SWIP
FIP/1-6 X. Wang: Current Design and R&D Progress of CN HCCB TBS
EX/7-4 G. L. Xiao: ELM Control Physics with Impurity Seeding and LHCD in the HL-2A Tokamak
EX/P5-20 W. Chen: Suppression and destabilization of ion fishbone activities on HL-2A
EX/P5-28 Y. Liu: Development of the q=1 Advanced tokamak Scenarios in HL-2A
EX/P5-6 J. Cheng: Pedestal dynamics in inter-ELM phase on HL-2A tokamak
EX/P5-4 M. Jiang: Localized modulation of turbulence by magnetic islands on HL-2A tokamak
EX/P5-19 P. W. Shi: Energetic-ion Driven Toroidal and Global Alfvén Eigenmodes on HL-2A
EX/P5-3 W. Z. Zhong: Plasma confinement and pedestal dynamics responses to impurity seeding in HL-2A H-mode plasmas
EX/P5-8 Y. P. Zhang: Effect of LBO-seeded Impurity on ELMs in the HL-2A tokamak
EX/P5-12 M. Xu: Experimental evaluation of electron energy probility function and sheath potential coefficient of HL-2A
FIP/P1-38 L. Cai: Preliminary development on a conceptual first wall for DEMO
TH/P2-3 H. He: Simulation of Toroidicity-Induced Alfven Eignenmode Excited by Energetic Ions in HL-2A Tokamak Plasmas
FIP/P3-22 H. Liao: Recent progress of R&D activities on Chinese reduced activation ferritic/martensitic steel (CLF-1)
FIP/P3-11 Z. Xu: Splashing Effect of Liquid Metal Divertor Due to ELMs Crashing
EX/P5-15 X. Q. Ji: Nonlinear evolution of multi-helicity neoclassical tearing modes in HL-2A low rotation plasmas
EX/P5-29 Y. B. Dong: Study of disruption and runaway electrons mitigation using multipulse supersonic molecular beam injection on HL-2A
EX/P5-30 X. M. Song: First Plasma Scenario Development for HL-2M
EX/P5-27 L. W. Yan: Real-time control system of neoclassical tearing modes in the HL-2A tokamak
TH/P5-13 G. Z. Hao: Centrifugal force driven low frequency modes in spherical tokamak
TH/P6-22 Z. H. Wang: Physics of fast component of deuterium gas jet injection in magnetized plasmas
TH/P8-13 Y. Li: Nonlinear turbulent parallel momentum transport due to blobs
FIP/P8-13 P. Y. Li: Recent Progress of ITER Magnet Supports Package in SWIP

## Slide 31
Thanks for your attentions!
HL-2M (under construction)
HL-2A

## Slide 32
Back-up slides
Highlights of recently upgraded/developed diagnostics on the HL-2A
Introduction of HL-2M

## Slide 33
Laser source: HCOOH laser (λ=432.5um)
Composition: 4-chord Polarimeter + 4-chord Interferometer
Time resolution: 1.0us, spatial resolution: 7.0cm
1). Y.G. Li, et al., RSI. 88, 083508 (2017)
2). Y.G. Li, et al., JINST. 12, C11004 (2017)
3). Y.G. Li, et al., FED 137, 137 (2018)
Figure:
Schematic layout of HL-2A Polarimeter and Interferometer.
HCOOH laser
Multi-channel FIR laser Polarimeter-Interferometer has been commissioned on HL-2A for electron density and Faraday rotation angle measurements.
FIR laser Interferometer and Polarimter on the HL-2A

## Slide 34
M. Jiang, NF 2018; PoP 2017; RSI 2013&2015;
Z. B. Shi, RSI 2014; PST2018
P.W. Shi, POP2017&2018. W. Chen, NF2018;
Double e-fishbone images
Tearing mode images
Optics of ECEI system
24(vertical)× 16(radial)=384 channel, with a coverage of 53 cm (vertical) × 30 cm (radial).
Tempo-spatial resolution: 2μs, 1-3 cm.
Abundant physics have been captured, such as TM, fishbone, ELM crash and multi-scale physics.
24×16 Electron Cyclotron Emission Imaging (ECEI) on the HL-2A

## Slide 35: Recent process of BES on the HL-2A
32-channel BES array has been installed on the outer mid-plane of HL-2A tokamak, focusing on the edge and SOL region.
Spatial resolution: Δr  0.8 cm； ΔZ  1.2 cm, covering r = 34.5 ~ 40.5 cm.
  High SNR has been achieved in the experiments last year.
shot # 33103, 640 ms

## Slide 36: BES applied on turbulence studies
Turbulence density spectrum is broadened when ECRH is applied.
Poloidal velocity and shear increased with ECRH.
Density spectrum
Poloidal velocity profiles
HL-2A # 33103

## Slide 37
Preliminary results from Phase Contrast Imaging:
System design
Expanding platform
Imaging platform
Systematic Parameters
Time resolution: 1 us
Spatial resolution: ~1mm
Detector array: 32 channels
Wavenumber: 2~15cm-1
The consistent experimental results obtained from magnetic probe and PCI data confirm the reliability of this diagnostic.
Experimental Setup
Calibration by Sound Wave
Observation of MHD instabilities

## Slide 38
Plasma current Ip = 2.5 (3) MA
Major radius R = 1.78 m
Minor radius a = 0.65 m
Aspect ratio R/a = 2.8
Elongation Κ = 1.8-2
Triangularity δ > 0.5
Toroidal field BT = 2.2 (3) T
Flux swing ΔΦ= 14Vs
Heating power 25 MW
Main parameters
Mission: In support of ITER & CFETR: high performance, high beta, and high bootstrap current plasma; advanced divertor configuration (snowflake, tripod), PWI at high heat flux,etc.
Introduction of HL-2M