## Slide 1: Overview of the JET preparation for Deuterium-Tritium Operation with the ITER Like-Wall
E. Joffrin, on behalf of EUROfusion JET contributors
Acknowledgments: to the JET Task Force and Project Leaders, JET secondees, EUROfusion Programme Management Unit, JET Exploitation Unit and JET operator

## Slide 2: JET is designed for fusion power studies in support of ITER
1975 JET design proposal: “…describes a large Tokamak experiment, which aims to study plasma behaviour in conditions and dimensions approaching those required in a fusion reactor”.
JET is capable of confining 90% of alpha particle for Ip above 2.5MA

## Slide 3: Objectives and outline
Develop D-T scenario and fusion power prediction
Understand isotope physics
Prepare the operation in D-T
DTE1 in 1997-98: M. Keilhacker Nuc Fus 39 (1999) 209 & J. Jacquinot Nuc Fus 39 (1999) 235
EUROfusion research roadmap: Secure the success of future ITER operation via specific preparation and experiments, including D-T operation of JET.
DTE1
JET-C
(1997)
92436: PFUS-EQ
JET-ILW (2016)
15MW/5s target
0 1 2 3 4 5 6 7 8
Time (s)
15
10
5
0
Fusion power (MW)
EUROfusion MST1 task Force: H. Meyer, OV2-1
https://www.euro-fusion.org/eurofusion/roadmap

## Slide 4: Stationary Scenarios for the DT phase achieved ~7-8MW of equivalent PFUS
PNBI (MW)
PICRH (MW)
bN
Line integrated density (1019m-2)
PNBI (MW)
PICRH (MW)
bN
Line integrated density (1019m-2)
“Hybrid” scenario 2.2MA/2.8T
q95~4, H98(y,2)=1.3
“Baseline” scenario 3.0MA/2.8T
q95~3, H98(y,2)=1.1
Time (s)
Time (s)
L. Garzotti, EX/3-6
E. De la Luna, EX/2-1
PEQ-FUS (MW)
30-35% thermo-nuclear
Fusion equivalent power for a 50/50 D/T mix: 7-8MW of fusion power for both scenarios
PEQ-FUS (MW)
~60% thermo-nuclear
50/50 D/T mix for identical plasma parameters
No credit for isotope effects
No credit for a-power
D-T equivalent fusion power

## Slide 5
“After-glow” ITB scenario shows promising route for alpha-driven mode studies
50/50 D-T
Prediction
n=4
Stability calculation
R. Dumont, Nuc. Fus. 2018
S. Sharapov, EX/P1-28
TAEs
After-glow

## Slide 6
D-T equivalent fusion power
for 2014-2016 discharges
Equivalent fusion power at 40MW reaching similar level than in the 1998 D-T campaign (DTE1) with two stationary scenarios: baseline and hybrid.
Transient ITB scenario for a-particle driven mode studies
Prospects for 10 to 15MW of fusion power in stationary scenarios in JET-ILW
0
2
4
6
8
10
12
14
16
0
5
10
15
20
25
Baseline
Hybrid
ITB
DTE1
Actual PFUS
PFUS [MW]
W [MJ]
D-T Equivalent fusion power with 40MW
Hot-ion H-modes
(transient)

## Slide 7: 10-16MW of fusion power also predicted in D-T by first principle based modelling
Isotope effect from ExB shear stabilisation or energy exchange.
Alpha power contribution
Self-consistent modelling with core (BGB)-pedestal (EUROped) with no isotope effects.
Uncertainty in PFUS accounts for different plasma current and bootstrap models
19
15
11
7
3
PFUS (MW)
20 30 40 50
PIN (MW)
CRONOS-TGFL & JINTRAC-QUALIKIZ: filled symbols
JINTRAC-BGB-EUROped: open symbols
CRONOS-CDBM: Stars
Hybrid
Baseline
ITB
J. Garcia, TH/3-1
F. Casson, TH/3-2
S. Saarelma, PPCF 2017
Taking into account additional effect:

## Slide 8: ICRH power can efficiently control W accumulation in D-T scenario
  Fundamental H minority
  electron heating
  Fundamental He3 minority
  ion heating
  Combination of both
PRAD inside r=0.2 (MW)
Central Te (keV)
Central Ti (keV)
P. Jacquet, Nucl. Fus. 2016
D. van Eester, IAEA 2016
F. Casson, TH/3-2
4
3
2
1
0
7 8 9 10 11
Time (s)
Tio=10.7 [keV]
Tio=12.7 [keV]
Tio=14.2 [keV]
ICRH schemes developed for D-T scenarios
First principle prediction of D-T scenario with 40MW & Ti>Te
Ion heating predicted to provide resilience to high-Z accumulation
Demonstrated experimentally
PICRH (MW)
E. Lerche, Nucl. Fus. 2016
M. Goniche, PPCF 2017

## Slide 9: 3 ion schemes: a new development in support of D-T
Y. Kazakov, EX/8-1 & Nat. Phys. 2017
J. Ongena, RF Conf. 2017
D-T plasmas: optimize Q-fusion using NBI+ICRH synergies:
ET-NBI = 118keV,  <ET> ≈ 200keV (off-axis n = 1 ICRH)
T-NBI + n=1 ICRH
T-NBI
 Efficient acceleration of small minorities fractions to higher energies with n = 1 ICRH in mixed plasmas.
H-D plasmas: increase in neutron rate due to accelerating D-NBI ions to ED ≈ 1-2MeV,
Confirmed with TOFOR, γ-ray measurements and ICRH modeling

## Slide 10
Understand isotope physics

## Slide 11: L-mode: weak positive isotope dependence on thermal confinement & transport
Small positive isotope dependence of tth
Consistent with the H97L scaling t ~ A0.2
L-mode confinement scaling with mass
(PIN scan at ne=cst, Ti~Te; BT=2.9 T, Ip=2.5 MA)
Match of r*, b, n* H/D pair satisfies scale invariance (same wcitEth )
No additional isotope dependence needed
Agreement achieved with QL modelling (ETS/TGLF) for the H/D identity pair but not in general.
C. Maggi, PPCF 2018
tth ~ A0.15±0.02
Hydrogen
Deuterium
H. Weisen, EX/P1-4 & P. Strand, TH/P6-14
R (m)
R (m)
3.0 3.2 3.4 3.6 3.8
3.0 3.2 3.4 3.6 3.8

## Slide 12: L-H power threshold likely to be lower in Tritium for D-T scenarios
C. Maggi, PPCF 2017
J. Hillesheim, EX/4-1
PL-H threshold likely to be reduced by 2/3 in tritium and 1/3 in D-T.
Consistent with past DTE1 results (Righi et al. 1999).
Prediction with non-linear fluid turbulence code (HESEL) reproduces strong dependence: ~ 1/A1.4
H
x2
x2/3
PL-H threshold ~ 1/A
(2008 scaling)
D-T
T
D
For divertor corner configuration

## Slide 13: Type I ELMy H-mode: strong positive isotope dependence on thermal confinement
Stronger isotope dependence than in JET-C and IPB98(y,2) (~A0.2)
Global momentum ~ A0.5±0.15
Particle confinement ~ A0.5±0.06
All scaling in A are robust against the set of variables chosen for the regression.
Note: Density systematically lower in H at same external fuelling
Hydrogen
Deuterium
The pedestal is an important player in the observed isotope dependence
tth ~ A0.4±0.1
H-mode confinement scaling with mass
H: 1.0MA/1.0T and 1.4MA/1.7T
D: 1.0MA/1.0T, 1.4MA/1.7T, 1.7MA/1.7T
H. Weisen, EX/P1-4
C. Maggi, PPCF 2018

## Slide 14: Larger pedestal pressure in D than H at same power and gas fuelling rate
IP=1.4MA; BT=1.7T; PIN=10MW ELMs; same fuelling rate: 19Hz in D and 31Hz in H
Isotope effect on peeling-ballooning is weak for same separatrix Te.
Different separatrix temperature in H and D could change pedestal stability.
Different Inter-ELM particle loss observed in H and D.
H. Weisen, EX/P1-4
L. Horwarth, Nuc. Fusion in preparation
Lower density observed in H for equivalent external gas injection rate

## Slide 15: Isotope mixing: key particle transport effect for D-T scenarios
In typical JET scenario:
 Di/De>1 and Vi/Ve>1
R/LT
Important for isotope fuelling & control in JET and ITER.
nD and nH R/Ln similar and independent of the source.
Multiple ion plasma: more freedom on ambipolarity constraint.
 ion flux not tied to electron flux
Di/De
C. Bourdelle Nuc Fus 2018
M. Maslov Nuc Fusion 2018
C. Angioni, Phys. Plasmas 2018
91232 (1.4MA/1.7T), H/D=0.9

## Slide 16
L-mode Inter-ELM
Intra-ELM
Detachment
Be  W
T  Be
D  Be
H  Be
T  W
D  W
H  W
Physical sputtering yields
Be and W physical sputtering will increase with Tritium
From binary collision approximation (SDTtrimSP code)
The increase of Be physical sputtering by tritium can lead to an increase of W sputtering by Be
Increase of W sputtering yields and threshold energy by tritium in intra-ELM phase.
Increase of Be sputtering by tritium in inter-ELM phase
D. Borodin, EX/P1-14
S. Brezinsek, EX/9-4

## Slide 17: Intra-ELM sputtering will dominate W sputtering in tritium
A. Kirschner PPCF 2018
Synthetic image ERO2.0
Be erosion modelled for scenarios
T
D
H
(Analytical model)
  Intra-ELM: ~70% of the gross-erosion
J. Romazanov, PSI 2018
I. Borodkina, Nuc. Mater. Energy 2017
From post-mortem analysis in D:
  W gross erosion: 40-60 g
  W net erosion: 2.4-4.8 g
  90% of prompt redeposition
(Deuterium)

## Slide 18: Decrease of material deposition rate by x4-9 compared to JET-C
M. Mayer, EX/P1/15
A. Widdowson, Phys. Script. 2018
Since 2011, operation with JET-ILW: 60h of plasma and 600MJ of input energy
Dominant strike point position
5
4
6
Cryo-pump
Be: 7 1019 atoms/cm2
D: 4 1018 atoms/cm2
C: 3 1018 atoms/cm2
O: 1019 atoms/cm2
N: 5 1018 atoms/cm2
Be: 2 1019 atoms/cm2
D: 2 1018 atoms/cm2
C: 2 1018 atoms/cm2
O: 1019 atoms/cm2
Be: 4 1019 atoms/cm2
D: 2 1018 atoms/cm2
C: 5 1018 atoms/cm2
O: 5 1018 atoms/cm2
N: 5 1018 atoms/cm2
Deuterium retention decreased by a factor of 10 to 20 wrt to JET-C.
The retention of tritium in deposits is not expected to be significantly different than deuterium.

## Slide 19: Prepare the operation in D-T

## Slide 20: Upgrades for D-T: NBI and T injection
5 new tritium gas injection modules, (Only one existing in DTE1)
I. Carvalho, 29th SOFT 2016
New plates with optimised cooling removing the limits to beam voltage and pulse length  34MW in D-T (21MW in DTE1)
A. Shepherd, 29th SOFT 2016
Beam injectors
Maximum NBI power so far limited by one of ion dumps component cooling capabilities.

## Slide 21: Unique set of new diagnostics in place for alpha physics and burning plasma studies in DTE2
J. Figueiredo, EX/P7-42
S. Sharapov, EX/P1-28
Visualization of fast particle orbits with g-ray tomography
Several burning plasma diagnostics ready for the D-T phase.
Charge Exchange (Ti)
TAE antenna
Neutron Camera
Vertical Neutron Spectrometer
g-Ray Camera
Horizontal g-Ray Spectrometer for alpha-Particle Diagnostic
Upgrade of the scintillator based Fast-Ion Loss Detector (FILD)
Most diagnostics included synthetically in modelling suites for code validation

## Slide 22
40m
New mirrors
New tools developed for burning plasma
V. Huber, EX/P1-31
Isotope ratio controlled at 50% in H-mode
Infra-red protection camera moved outside the biological shield
M. Lennholm & D. Valcarcel, FED 2017
Both techniques will be essential for ITER D-T operations
Camera
Pulse 91234 (1.4MA, 1.7T)
PNBI (MW)
Isotopic ratio (vis. Spec.)
D
H
Time (s)

## Slide 23: 14MeV neutron detector for the D-T phase calibrated with an accuracy of ±6%.
14MeV neutron generator deployed inside JET vessel by remote handling
  76h of irradiation in 73 different poloidal and toroidal positions
  Calibration within ±6%
Neutronic modelling carried out and codes validated for ITER.
 Procedure transferable to ITER.
3 Fission (235U) chambers and 1 Activation system
P. Batistoni, Nuc Fus 2018,
E. Laszynska, SOFT 2018 ,
T. Vasilopoulou, SOFT 2018,
S. R. Villari, SOFT 2018
Notes: Check 3 Fission (235U) chambers and 1 Activation system

## Slide 24: Tritium operation with JET-ILW: x5 more neutron budget than in DTE1
E. Belonohy, SOFT 2016
 | DTE1 | TT
Neutron | 3. 1020 | 0.1 1021
Tritium injected | 35g | ~300g
Strict accounting of tritium used <11g in cryo panels regenerated every day
Restricted access to area where neutron activation and g radiation can be high.
Plasma operation rehearsal planned during the D campaign
T: 60g
for DTE2
DTE2
1.55 1021
~150g

## Slide 25: Highlights of the preparation for D-T
Existing D-T scenarios have reached 7-8MW/2.5s equivalent fusion power and can attain 10 to 16MW of fusion power with 40MW of input power in the JET ITER-like wall
After-glow ITB scenario is a credible route for alpha particle driven instabilities study and code validation for ITER
Confinement and particle transport show strong positive isotope dependences and is also investigated for ITER conditions
Tritium will modify the SOL conditions and plasma surface interactions significantly but retention is expected to stay low
JET has developed a comprehensive set of diagnostics, tools and procedures in support of ITER burning plasma operation

## Slide 26: Next JET timeline and Prospects
D-T campaign
15 MW of fusion power for 5s in stationary conditions
Study of alpha physics
H & T
Isotope campaigns
Shattered Pellet Injector
D campaign
Disruption/RE studies
D-T scenario preparation

## Slide 27: Thank you for your attention on behalf of the EUROfusion JET contributors

## Slide 28: JET papers at this Fusion Energy Conference
OV2-1: H. Meyer, Overview of Physics Studies on ASDEX-Upgrade
EX/3-6: L. Garzotti, Scenario Development for DT Operation at JET
TH/3-1: J. Garcia, First Principles and Integrated Modelling Achievements Towards Trustful Fusion Power Predictions for JET and ITER
EX/P1-5: H.-T. Kim, High Fusion Performance at High Ti/Te in JET-ILW Baseline Plasmas with High NBI Heating Power and Low Gas Puffing
EX/2-1: E. de la Luna, Impact of ELM Control in JET Experiments on H-Mode Terminations with/without Current Ramp-Down and Implications for ITER
EX/P1-22: C. Sozzi, Early Identification of Disruption Paths for Prevention and Avoidance
EX/P8-1: A. Kappatou, Energy Confinement and Performance of Pure Helium Plasmas and Helium Seeded Deuterium Plasmas
EX/P7-1: G. Verdoolaege, First Analysis of the Updated ITPA Global H-Mode Confinement Database.
EX/P1-4; H. Weisen, Isotope Dependence of Confinement in JET Deuterium and Hydrogen Plasmas
EX/P8-22; L. Frassinetti, Role of the Pressure Position on the Pedestal Stability in AUG, JET-ILW and TCV in Deuterium and Hydrogen Plasmas and Implications for ITER
EX/4-1: J. C. Hillesheim, Implications of JET-ILW L-H Transition Studies for ITER
TH/2-2: M. T. Kotschenreuther, Gyrokinetic Analysis and Simulations of Pedestals
EX/3-4: C. Giroud, Optimization of JET-DT and ITER Operation by Developing an Understanding of the Role of Low-Z Impurity on the H-Mode Pedestal
TH/4-4: H. Strauss, Asymmetric Wall Force Reduction in ITER and JET Disruptions
EX/P1-23: S. Jachmich, Minimizing Power Load Asymmetries During Disruption Mitigation at JET
EX/P1-24: S. N. Gerasimov, Overview of Disruptions with JET-ILW
TH/P6-26: S. Nowak, Analysis and Modelling of NTMs Dynamics in JET Discharges Using the European Transport Simulator (ETS) and Integrated Modelling Tools
EX/9-4 S. Brezinsek, Erosion, Screening, and Migration of Tungsten in JET Equipped with Tungsten Divertor
EX/P1-29 C. C. Klepper, Sub-divertor Fuel Isotopic Content Detection Limit for JET and Impact on the Control of ICRH for JET-ILW and JET-DT Operation

## Slide 29: JET papers at this Fusion Energy Conference
TH/3-2: F. J. Casson, Predictive Multichannel Flux-Driven Modelling to Optimize ICRH Tungsten Control in JET
EX/P1-3: D. Frigione, Impact of Neon Injection on Electron Density Peaking in JET Hybrid Plasmas
EX/4-4: T. Tala, Core Density Peaking Experiments in JET, DIII-D and Cmod in Various Operational Scenarios Driven by Fuelling or Transport
EX/P6-5: S. Mordijck, Particle Transport from the Bottom Up
TH/P6-14: P. Strand, Towards a Predictive Modelling Capacity for DT Plasmas European Transport Simulator (ETS) Verification and Validation
TH/P5-27: R. Coelho, Plasma Equilibrium Reconstruction of JET Discharges Using the IMAS Modelling Infrastructure
TH/P2-15: Y. V. Yakovenko, Simulations of the Sawtooth-Induced Redistribution of Fast Ions in JET and ITER
FIP/P7-42: J. Figueiredo, JET Upgraded Diagnostic Capabilities and Scientific Exploitation in Support of Deuterium-Tritium Operation
EX/8-1: Y. O. Kazakov, Recent Advances in ICRF Heating of Mixture Plasmas: Survey of JET and AUG Experiments and Extrapolation to JETDT and ITER
TH/P7-22: C.-S. Chang, Wide Divertor Heat-Flux Width in ITER from Self-Organization between the Neoclassical and Turbulent Transports across the Separatrix Surface
TH/7-1: F. Militello, Predicting Scrape-Off Layer Profiles and Filamentary Transport for Reactor Relevant Devices
TH/P5-22: P. Zanca, A Power-Balance Model of Density Limit in Fusion Plasmas
TH/P6-24: G. Telesca, Numerical Simulation of High Neutron Rate JET-ILW DD Pulses in View of Extension to DT Experiments
TH/P7-5: M. Wischmeier, The Physics Basis for a Solution to the Power and Particle Exhaust Problem of a Next Step Device
EX/P1-16: B. Viola, The Impact of Poloidal Flux Expansion on JET Divertor Radiation Performance
EX/P1-31: V. Huber, The Software and Hardware Architecture of the Real-Time Protection of In-Vessel Components in JET-ILW
FIP/2-4: D. Iglesias, Advances in Predictive Thermo-Mechanical Modelling for the JET Divertor Experimental Interpretation, Improved Protection, and Reliable Operation
EX/P1-15: M. Mayer, Erosion and Deposition in the JET Divertor During the ITER Like Wall Campaigns
EX/P1-14: D. Borodin, Extrapolation of Be Erosion Modelling from JET and PISCESB to ITER

## Slide 30: Impurity seeding and sweeping: the way to minimise heat load
C. Challis EPS 2017
S. Silburn, PFMC 2017
C. Giroud, EX/
M. Wischmeier, TH/P7-5
Power
(W)
ROSP
[m]
Max surface temp rise
[°C]
Time since heating turn-on (s)
0.0
1.0
2.0
3.0
Radiation
NBI Input
Ne seeding impacts on neutron rates
Sweeping amplitude mitigates target temperature

## Slide 31
“Hybrid” and “baseline” are both showing confinement of H98y2=1 or above.
Hybrid scenario
With pellets
Without pellets
Baseline scenario
Pellet injection leads to lower gas injection rate and higher rotation
Higher rotation and Ti>Te amplifies ITG stabilization
Electro-magnetic effect can stabilize turbulence at higher b
Fast particle (alpha) can further stabilize turbulence
GENE GK simulations
H.T. Kim, this FEC conference & Nuc. Fus. 2018
J. Garcia, PoP 2018

## Slide 32
Significant isotope effect on the access from type III to type I ELM
Access to H=1 type I
Power threshold for type I ELMs doubles from D to H
We could expect that this power threshold will be further increased in Tritium and D-T
1.4MA/1.7T – low d plasma shape
C. Maggi, Nucl. Fusion 2017
Deuterium
Tritium?

## Slide 33
CRONOS + TGLF
Ti (DT)
Te (DT)
Ti (DD)
Te (DD)
#86614
JETTO + QUALIKIZ
Ti (DT)
Te (DT)
Ti (DD)
Te (DD)
#92398
PFUS~15MW
PNBI=32MW
PICRH= 8MW
PFUS=16MW
PNBI=32MW
PICRH= 8MW
Pedestal scales as ~ mi0.0
With electron temperature gradients (ETG);
Ion-electron collisional energy exchange decreases with isotope mass
Higher confinement may impact on W transport
Pedestal scales as ~ mi0.2
No electron temperature gradient scales (ETG)
Isotope dependence in the core from ExB shear
Alpha power contribution included.
First principle DT fusion power prediction showing similar results ~15MW, despite different hypothesis

## Slide 34: ITER scenarios with JET ITER-Like Wall
The remaining challenge is to extend these results to maximum input power (40 MW), high magnetic field (3.85 T) and high plasma current (4 MA)
Demonstrate that the maximum performance (in D-D plasmas) is compatible with the ITER-like Wall
2018/19
Objective
[bN>1.8]
[L. Garzotti FEC 2018, I. Nunes et al Nucl. Fusion 2015]

## Slide 35
Isotope effects on JET pedestal pressure
Lower pedestal density in H than in D  lower plasma density in H
Larger pe,PED in D than in H at the same heating power
Hydrogen type I pedestals evolve along same isobar at all gas rates
1.4MA/1.7T
Power and gas scans
H
D
Gas puffing rate
Heating power
Type III
Pheat~15MW
[C. Maggi 26th ITC Conference, Toki, Japan, December 5th 2017, L Horvath et al. EPS 2017 ]

## Slide 36: ITER Non-Active Operation: H-mode Access
Non-linear mass dependence on L-H power threshold
[Hillesheim et al EPS 2017]
Fine mass scan 2→1 via H/(H+D) control
Large variation at high and low H/(H+D)
Little variation 0.2<H/(H+D)<0.8
Trace He quantity in H-plasma:
  Significant PL-H reduction
Impact on ITER non-active phase to be investigated
  helium campaign ?
2
1.5
1
H-H
D-D
Meff
[Pscal from ITPA scaling J. Phys. (2008)]
ICRH heating H & D
NBI heating H & He4
Notes: Red with ICRH only –
Blue with NBI
sharp variation in PLH with trace quantity

## Slide 37: Impact of wall materials and seeding gases on the pedestal and on core plasma performance
Outward shift of density profile degrades pedestal top
  Nitrogen seeding can partially reversed this effect (AUG)
  JET-ILW tends to have larger relative shift than JET-C
[Stefanikova et al EPS 2016, Frassinetti et al PPCF 2016]
Normalised pedestal pressure, a
Pedestal density shift (% y)
Low d, n*~0.1-0.35
JET-ILW
JET-C
0
1
2
3
2
4
6
8
0
[Dunne et al PPFC 2016, Wolfrum 2017]