## Slide 1
Test of the ITER-like RMP Configurations
for ELM-crash-suppression on KSTAR
Yongkyoon In1,2, A. Loarte3, H.H. Lee2, K. Kim2, J.W. Ahn4,
Y.M. Jeon2, J.K. Park5, G.Y. Park2, M.W. Kim1,2, H. Park1,2,
and the 3D Physics Task Force in KSTAR
1 Ulsan National Institute of Science and Technology (UNIST), Ulsan, Korea
2 National Fusion Research Institute (NFRI), Daejeon, Korea
3 ITER Organization
4 Oak Ridge National Laboratory, Oak Ridge, U.S.
5 Princeton Plasma Physics Ridge Laboratory, Princeton, U.S.
IAEA-FEC, October 22 - 27, 2018, Gandhinagar, India
In acknowledgement of the supports by Ministry of Science and ICT for the KSTAR project and by the Research Funds (180056 & 180245) of UNIST(Ulsan National Institute of Science & Technology)
“ITER is the Nuclear Facility INB no. 174. The views and opinions expressed herein do not necessarily reflect those of the ITER Organization.”

## Slide 2
ITER requires a scheme to spread the divertor heat fluxes with minimum electromagnetic cycling of coils, while sustaining the RMP-driven, ELM-crash-suppression
Application of ELM control coils leads to localized power fluxes at divertor and main wall by thermal plasma and by fast particles (NBI + a’s)
Excerpted from O. Schmitz et al, NF (2016)
Loarte (2014) “Rigid rotation of the perturbation solves the problem but causes large EM cycling of the control coils”

## Slide 3: KSTAR has secured robust RMP-driven ELM-crash-suppression, equipped with the capability to measure the divertor heat fluxes
As of 2017, KSTAR accomplished the longest sustainment of RMP-driven ELM-crash-suppression !
Ultimately, the RMP-driven ELM-crash-suppression would be one of the critical tools to warrant the divertor lifetime with a minimal cost of confinement
Toroidally varying striation pattern needs to be diagnosed even during RMP-driven ELM-crash-suppression
Above 30 sec  wall
q95~5.0

## Slide 4: The 3-row in-vessel coils in KSTAR can accommodate various 3-D configurations in ITER-RMP, including “intentionally misaligned configurations (IMC)”
ITER RMP coils
Up to n=4 with 9 coils in each row
KSTAR In-vessel Control Coils (IVCC): Top/Mid/Bot
Uniquely equipped with in-vessel mid-RMP coils
Courtesy of G.T.A. Huijsmans
Courtesy of K.S. Lee
Up to n=2 with 4 coils in each row

## Slide 5: Outline
Introduction
  Divertor heat flux measurement diagnostic
  Intentionally misaligned 3-D configurations (IMC)
Impact of 3-D field configurations on divertor heat flux profiles
  3-rows vs 2-rows (Upper/Lower RMPs)
Simple-model comparison (preliminary)
Progress in the compatibility study of RMP-driven, ELM-crash-suppression with detached plasmas
Discussion and Summary

## Slide 6
Time-resolved ELMy burst has been diagnosed
to be peaked up to 50 MW/m2 near divertor
The ELM heat load has been measured with fast IR camera acquisition frequency
of ~ 9 kHz (integration time: 0.1 ms) on KSTAR
Note that ELM rise time is two times longer than the parallel convection time ()
H.H. Lee et al, FEC (2016)

## Slide 7
† K. Kim PoP 24 052506 (2017)
Vacuum (before phase rotating)
Ideal plasma response (before phase rotating)
Divertor heat flux striation pattern during rotating n=1 RMP is consistent with the field line tracing calculation, including plasma response
H.H. Lee et al, IAEA-TM (2017)
Also, refer to K. Kim et al, PoP (2017)

## Slide 8: Intentionally misaligned configurations, with minimal EM loads, have been proposed to reduce EM loading on coils, while effectively diffusing the divertor heat fluxes
 | + |  | 
 |  |  | 
 |  | + - | +
Df =+90 ⁰
f
q
180º
0º
Reference phasing (fUM = fML= 90 deg):
default n=1 RMP
Misaligned configurations: 3 types
“distorted” (fUM ≠ fML )
II. “away” (fUM = fML> 90 ⁰): kink-aligned
III. “toward” (fUM = fML< 90 ⁰)
IV. 2-row (without mid-row):
Upper/Lower rows: nearly orthogonal to
the 3-D configuration of 90 deg phasing in vacuum
Phasing (= phase difference between rows)
[e.g. fUM = fM - fU = 0⁰ – (-90 ⁰ ) = 90 ⁰ ]
-180º
U
M
L

## Slide 9: Intentionally misaligned configurations, with minimal EM loads, have been proposed to reduce EM loading on coils, while effectively diffusing the divertor heat fluxes
 | + |  | 
 |  |  | 
 |  | + - | +
Df =+90 ⁰
f
q
180º
0º
Reference phasing (fUM = fML= 90 deg):
default n=1 RMP
Misaligned configurations: 3 types
“distorted” (fUM ≠ fML )
II. “away” (fUM = fML> 90 ⁰): kink-aligned
III. “toward” (fUM = fML< 90 ⁰)
IV. 2-row (without mid-row):
Upper/Lower rows: nearly orthogonal to
the 3-D configuration of 90 deg phasing in vacuum
Phasing (= phase difference between rows)
[e.g. fUM = fM - fU = 0⁰ – (-90 ⁰ ) = 90 ⁰ ]
-180º
U
M
L
Y. In et al, APS-DPP (2017); submitted for publication (2018)

## Slide 10: “Away” phasing might have been greatly influenced by kink-associated contributions, but what about “toward” phasing?
3-D phase space mapping has been successfully benchmarked for RMP-driven, ELM-crash-suppression
[J.K. Park et al, Nature Physics (2018)]
Divertor heat flux broadening has been observed in the “away” phasing
Coil current (kA) IT=IM=IB
Y. In et al, APS-DPP (2017);
submitted for publication (2018)
“Away Phasing”
“Toward Phasing”
Locking
Dominantly
non-resonant

## Slide 11: “Away” phasing might have been greatly influenced by kink-associated contributions, but what about “toward” phasing?
3-D phase space mapping has been successfully benchmarked for RMP-driven, ELM-crash-suppression
[J.K. Park et al, Nature Physics (2018)]
Divertor heat flux broadening has been observed in the “away” phasing
Coil current (kA) IT=IM=IB
Y. In et al, APS-DPP (2017);
submitted for publication (2018)
“Away Phasing”
“Toward Phasing”
Locking
Dominantly
non-resonant

## Slide 12: Outline
Introduction
  Divertor heat flux measurement diagnostic
  Intentionally misaligned 3-D configurations (IMC)
Impact of 3-D field configurations on divertor heat flux profiles
  3-rows vs 2-rows (Upper/Lower RMPs)
Simple-model comparison (preliminary)
Progress in the compatibility study of RMP-driven, ELM-crash-suppression with detached plasmas
Discussion and Summary

## Slide 13: “Toward” Phasing in n=1 RMP appears as equally effective as “Away” phasing in terms of ELM-crash-suppression, suggesting a broad optimal phasing
No
RMP
“Toward” each other at Upper/Lower rows
(fUM, fML)= (-90,90); (-85,85);(-80,80);(-75,75);(-70,70)
w.r.t. fM =0 deg [e.g. +90deg phasing (-90,90)]
+ | + | - | -
- | + | + | -
- | - | + | +
U
M
L
0º
-180º
180º
Rotating RMP
3-rows

## Slide 14: “Toward” phasing in n=1 RMP appears as equally effective in dispersing divertor heat flux as found in “Away” phasing (kink-aligned)
“Toward” dephasing benefits are clearly observed in
terms of divertor heat flux dispersal, prior to the loss of ELM-crash-suppression, avoiding mode-locking!
Realigned divertor heat flux (19212)
Rotating RMP
lq =1.9 mm
3-rows
Normalized
Radial position at the maximum [mm]
Radial position at the maximum [mm]

## Slide 15: Newly achieved RMP ELM-crash-suppression using n=1 off-midplane coils has been configured to be operationally perpendicular to conventional RMP configuration
ELM suppression has been demonstrated with a range of phasings of UL = -70 ~ -90 , and sustained during rigid rotation
q95 ~ 5.0
TB = -90 -85 
-80 -75  -70 
Upper/Lower rows (without mid-row):
: nearly orthogonal to the configuration of
3-row 90 deg phasing in vacuum
 | + |  | 
 |  | + - | +
DULf =+180 ⁰
q
0º
-180º
U
M
L
180º
DULf =-90 ⁰
2-rows

## Slide 16: ITER-like 3-row RMPs have broadened the divertor heat flux during ELM-crash-suppression at the near SOL, which cannot be seen with 2-rows
19214
A
A’
19212
3-row
Additional degree of freedom in 3-rows in RMPs, beyond usual 2-rows, appears responsible for the broadening of the heat flux near SOL, favorable to the ITER system
3-rows
2-rows
Radial position at the maximum [mm]
Radial position at the maximum [mm]

## Slide 17: Outline
Introduction
  Divertor heat flux measurement diagnostic
  Intentionally misaligned 3-D configurations (IMC)
Impact of 3-D field configurations on divertor heat flux profiles
  3-rows vs 2-rows (Upper/Lower RMPs)
Simple-model comparison (preliminary)
Progress in the compatibility study of RMP-driven, ELM-crash-suppression with detached plasmas
Discussion and Summary

## Slide 18: Field-line-tracing suggests minimum yn surface, possibly corresponding to the vicinity of the outer striking point
Refer to K. Kim et al, PoP (2017)
No effect on power loads in narrow regions of long connection lengths, attributable to a ‘smearing’ effect due to perpendicular transport
[Kobayashi et al, NF (2007);
Stangeby & Mitteau,
JNM (2009)]

## Slide 19: Although a simple modeling with 3 rows predicts heat flux reduction based on field-line-tracing, the broadened profiles have not been numerically confirmed yet
Simple models
No spike observed in experiment
 Need more sophisticated modelling (e.g. EMC3-EIRENE) and nonlinear approaches, as well as perpendicular transport
e-folding length ~ 15mm (unperturbed)
- Sheath-limited heat flux
- Conduction-limited heat flux
where

## Slide 20
High density ELM-crash-suppression has been achieved for n=2 RMP with substantial reduction of divertor heat flux, despite no detachment yet
3 4 5 6 7 8 9
Time (sec)
1.0
0.5
0
2.5
2.0
1.5
4.0
3.5
3.0
6.0
4.0
2.0
2
1
0
[1019m-3]
Da (arb.)
b N
q95
Vdiv (V)
19261 19279
RMP
RMP
q95 = 3.4
qpeak = 1.8 MW/m2 (19261): typical density
vs
0.8 MW/m2 (19279): high density
J.W. Ahn et al, APS-DPP (2017)
Measured during the outer strike point sweep
at t=9.0 sec (19261)
7.5 sec (19279)

## Slide 21: Simple linear and parallel transport analysis is not sufficient to explain the divertor heat flux broadening mechanism, requiring more sophisticated modeling
Although the 3-row RMP appears effective in broadening the divertor heat flux, it is possible that the mid-row might have played a bigger role than the other off-mid rows (scheduled for experiments in 2018)
Further study needs to demonstrate the RMP-driven, ELM-crash-suppression even with
i) low-rotation, ii) ITER-similar-shape (ISS), iii) partially detached plasmas
At the same time, the physics mechanism responsible for the broadening of near-SOL heat flux needs to be answered (in need of more detailed simulations (e.g. EMC3-EIRENE) and nonlinear approach)
 Pure 3-D field effect or plasma response (e.g. kink or peeling (?))

## Slide 22: Intentionally misaligned configurations are not only compatible with ELM-crash-suppression, but also effective in dispersing the divertor heat flux, while minimizing EM loads on RMP coils
Demonstrated a divertor heat flux broadening by dephasing
during RMP-driven, ELM-crash-suppression without driving mode-locking
3-row RMPs appeared more effective in broadening divertor heat fluxes than 2-row RMPs
Simple linear and parallel transport analysis is not sufficient to explain the divertor heat flux broadening mechanism, possibly requiring more sophisticated modelling (e.g. EMC3-EIRENE) and nonlinear approaches
ITER-like 3-row RMPs could be judiciously configured to broaden divertor heat fluxes with minimal EM loads on coils using IMC

## Slide 23
Back-up

## Slide 24: Seemingly dominantly non-resonant configuration in vacuum may turn out to be dominantly resonant configuration in plasma response
IM=0kA subspace
(off-midplane only)
- | - | + | +
- | + | + | -
Seemingly ‘Kink-orthogonal’ in vacuum
appears dominantly
‘kink-aligned’ in plasma response ( = 270)
( = -90)
K. Kim et al, NF (2017)
Ideal plasma response calculation “predicted first” the ELM-crash-suppression of n=1 ‘off-midplane’ RMPs

## Slide 25: Slowly decaying nature of n=1 field could be potentially a merit, rather than an obstacle in RMP ELM control in future reactors
Previously, ITER RMP control has discarded the option of n=1 RMP due to
1) wide spacing between adjacent islands
  high field strength required to meet sChirikov > 1
2) hardly decaying into the core plasma, susceptible to mode-locking
 correct, but not a major hindrance in KSTAR due to low-intrinsic EF !
Likely, KSTAR would be the most suitable device to address the validity of n=1 RMP ELM-control
[Schaffer et al, NF (2008)]
KSTAR specializes in low-n RMP ELM control challenges !!!
Y. In et al, KSTAR conference (2015)

## Slide 26
Intentionally misaligned configurations
II. “away” from each row (fUM = fML> 90 ⁰): kink-aligned
 | + |  | 
 |  |  | 
 |  | + - | +
Df =+90 ⁰
f
q
0º
-180º
U
M
L
180º

## Slide 27: Phasing increase toward kink-resonance in n=1 RMP configurations appears quite effective in sustaining the RMP ELM suppression
+ | + | - | -
- | + | + | -
- | - | + | +
U
M
L
0º
-180º
180º
(fUM, fML)= (-90,90);(-95,95);(-100,100);(-105,105)
w.r.t. fM =0 deg [e.g. +90deg phasing (-90,90)]
Away from each other (Top/Bot) (19211)
Y. In et al, APS-DPP (2017); submitted for publication (2018)

## Slide 28: As long as mode-locking is avoided, the kink-aligned configuration has been observed to be effective in broadening the divertor heat flux
Realigned divertor heat flux contour (19211)
Reduced peak of heat flux, along with broadened
shape, during RMP-driven, ELM suppression is quite favorable to ITER, similarly observed during RMP-driven, ELM mitigation [Y. In et al, NF (2017)]
Rotating RMP
Normalized
lq =1.9 mm
Y. In et al, APS-DPP (2017); submitted for publication (2018)

## Slide 29
 30 sec  wall
 15 sec
n=1,  = +90
n=2,  = +90
Robust ELM-crash-suppression has been successfully developed using either n=1 or n=2 RMPs
+ | + | - | -
- | + | + | -
- | - | + | +
+ | - | + | -
- | + | - | +
+ | - | + | -
q95 ~ 5.0
q95 ~ 3.8
Y.M. Jeon et al, APS-DPP (2017)

## Slide 30
Intentionally misaligned configurations
I. “distorted” (fUM ≠ fML )
 | + |  | 
 |  |  | 
 |  | + - | +
Df =+90 ⁰
f
q
0º
-180º
U
M
L
180º
ELM-crash-suppression
Y. In et al, APS-DPP (2017)
ELM-crash-mitigation
Y. In et al, FEC (2016); NF (2017)

## Slide 31: Intentionally misaligned n=1 RMP configurations have been confirmed to be effective in suppressing ELM-crashes
(fUM, fML)= (-90,90);(-95,85);(-100,80);(-105,75);(-110,70)
w.r.t. fM =0 deg [e.g. +90deg phasing (-90,90)]
+ | + | - | -
- | + | + | -
- | - | + | +
U
M
L
0º
-180º
180º
Fully sustained ELM-crash-suppression during rotating n=1 RMP is attributable to the low intrinsic EF in KSTAR
Y. In et al,
APS-DPP (2017)

## Slide 32: Given various uncertainties in fixing the outer strike point, the realigned heat flux patterns would help us assess the most stringent conditions on divertor
Hitting the same spot with the peaked heat flux throughout the discharge would be the most severe conditions, which could be regarded as the maximal heat flux on divertor
IR camera

## Slide 33: During RMP ELM suppression, the misaligned configurations has reduced the peaks, but no broadening was seen in both static and rotating RMPs
NOTE that the exactly same 3-D configuration during ELM mitigation led to a lowered peak, along with broadened heat flux
Divertor heat flux
dispersal cannot be extrapolated
from ELM mitigation
to ELM suppression
Attributable to
bifurcated state of ELM suppression
Excerpted from
Y. In et al, NF (2017)
lq =1.9 mm
Normalized
During ELM mitigation
During ELM suppression
Rotating RMP

## Slide 34: An order of magnitude lower level of intrinsic non-axisymmetry enables us to address 3D field physics and its uncertainties more rigorously
In a typical tokamak
[intrinsic EF : dB/B0 ~ 10-4; TF field ripple : dTF 0.5%]
  Resonant Magnetic Perturbation (RMP): dB/B0 ~ up to 10-3
  [e.g. 6x10-4 for n=4 suppression in ITER design]
  Requires actively controlled (removed) non-axisymmetry
  No matter what we do, the presence of “non-axisymmetric fields” cannot be completely eliminated => multiple “uncorrected EFs”
In an extremely low EF (dB/B0 ~ 10-5) and TF field ripple (dTF = 0.05%) in KSTAR, the application of dB can be controlled in an unprecedented level of precision!
dB/B0
10-5
10-3
10-2
10-4
Stellerator
Conv. Tokamaks
KSTAR
What about ITER or future reactors ?
Y. In et al, NF (2015)

## Slide 35: The effectiveness of misalignment is easily understood in the comparison of “wet areas”, leading up to ~20% increase
Using “intentionally misaligned” RMP configurations, the merit of dephasing is shown in reducing the peak, as well as dispersing heat flux on a wider area

## Slide 36: Lower q95 ELM-crash-suppressions, close to ITER (q95~3.1) have been newly established in KSTAR using low-n RMPs
q95 = 3.4
q95 = 4.0
Demonstrated the established methodology of low-n RMP-driven, ELM-crash-suppression would be applicable to ITER-relevant low-q95 regime
n=1,  = +90
n=2,  = +90
ECE density cutoff
+ | + | - | -
- | + | + | -
- | - | + | +
+ | - | + | -
- | + | - | +
+ | - | + | -

## Slide 37: Edge resonant components decoupled from core counterparts allow us to predict an optimal window for n=1 RMP-driven ELM-crash suppression, while avoiding mode-locking
+ | + | - | -
- | + | + | -
- | - | + | +
Polar plot of (IMID, ϕ)
with IU=IL=5kA and ϕ=ϕUM=ϕML
Minimize resonant
dB impacts in core,
while maximizing
RMP at edge
Y. In et al, NF (2017); J.K. Park et al, to appear in Nature physics (2018)
n=1,  = +90