## Slide 1: Pitch Angle Dynamics and Synchrotron Emission of Runaway Electrons in Quiescent and Disrupted DIII-D Plasmas
D. del-Castillo-Negrete, L. Carbajal, M. Cianciosa1
C. Paz-Soldan2
E. Hollmann, R.A. Moyer3
C. J. Lasnier4
1 Oak Ridge National Laboratory
2 General Atomics
3 University of California, San Diego
4 Lawrence Livermore National Laboratory
Presented at
IAEA Fusion Energy Conference
Ahmedabad, India
October 25th, 2018

## Slide 2: Introduction
There is a pressing need to develop modeling and simulation tools with predictive capabilities for the avoidance, mitigation, and dissipation of runaway electrons (RE).
Synchrotron emission (SE) measurements and simulations play a key role in model validation.
We present a numerical study of SE in DIII-D plasmas with emphasis on pitch-angle dynamics and RE energy distributions that significantly depart from current Fokker-Planck models.
We focus on visible SE of quiescent RE, and visible and infrared SE in mid-plateau RE in disrupted plasmas.

## Slide 3
There are significant discrepancies between experimentally inferred runaway electron (RE) distribution functions and current theoretical & computational models
Understanding this is key for the development of a predictive
simulation capability of RE generation, avoidance, and mitigation
[Hollmann, et al. (2015)]
[Paz-Soldan, et al (2017)]

## Slide 4: Synchrotron emission (SE) is a key diagnostic that can be used to understand these discrepancies.
Orbit dynamics:
  - Single particle (0D) - Phase space (2D)
  - Guiding center - Full-orbit (6D)
Radiation: curvature and pitch angle dependence
  - Single particle - Drift orbit correction
  - Exact curvature
Synthetic camera: direction and symmetry of emission
  - Cone models - Full-angular dependence
  - 2D (Axisymmetric B fields ) - 3D (islands & stochastic B)
Different levels of description

## Slide 5: Kinetic Orbit Runaway electron Code (KORC)
Synchrotron emission synthetic diagnostic incorporates exact curvature, and direction of emission and camera geometry.
[Carbajal, et al, (2017),
del-Castillo-Negrete et al, (2018) ]
KORC computes the full-orbit dynamics of large ensembles of particles in prescribed 3D magnetic and electric fields including radiation damping and collisions.
SE synthetic camera
Applicable to non-axisymmetric (3D) B field configurations (islands and stochasticity)

## Slide 6: Approximations can compromise the accuracy of SE and lead to underestimate or overestimate RE parameters
P(l)=Radiation power per particle per wavelength
P(l)
l
l
P(l)
l
P(l)
Approximation
Full-orbit
3D B fields with islands
Measured by the camera
“Cone” model
Full angular
dependence
Trapped-orbit effects
trapped
passing
Approximation
Full-orbit:
[Carbajal, et al, (2017),
del-Castillo-Negrete et al, (2018) ]

## Slide 7: Orbit induced (“collisionless”) pitch angle dispersion
The pitch angle is not a constant of motion and an initial distribution will evolve due to orbit-effects even without pitch angle collisional scattering
An initial spatially uniform pitch distribution with < q >=20o will “segregate” and become spatially dependent
mono-pitch angle and spatially-independent pitch angle distributions
are idealizations inconsistent with orbit dynamics
An initial mono-pitch distribution
will spread around qo
q
f(q)
R
Z
RE cross section
This collisionless dispersion effect [Carbajal, et al, (2017)] is different
to the colissionless scattering discussed in [Jian et al, (2016)].
,

## Slide 8: Modeling of synchrotron emission of quiescent RE (QRE)
Measured SE in DIII-D
Here we use the energy distribution from a direct fit of the hard-x-ray emission measurements
Previous studies [Hoppe et al (2018)] have shown that using the energy distribution from the Fokker-Planck model does not reproduce the observed SE
R
Z
Our goal is to apply KORC synthetic diagnostic to reproduce the SE in DIII-D
Focus on DIII-D quiescent flattop discharge shot # 165826

## Slide 9: Initial spatial and pitch angle distributions
We assume an initial spatially homogeneous toroidal
distribution of RE
As expected, the radial drifts
shift the distribution to the low
field side
For the pitch angle distribution we use the model in [Hollmann et al (2015)]
.
The model assumes a steady-state equilibration of pitch angle scattering and E field acceleration
Zeff= 4.5 effective Z seen by the RE
E = 4.0 electric field normalized to ECH
r0 = minor RE radius
=1 Fokker-Planck theoretical value
> 1 Faster decay of pitch angle PDF tail
Model parameters

## Slide 10: For numerical efficiency limit sampling of RE to region contributing to 95% of the radiation observed by the camera at a given wavelength
q
0o 20o 40o 60o
0 5 10 15 20 25 30
Energy [MeV]
0
-1
-2
-3
-4
-5
-6
.
Total radiation power
Radiation density
RE pdf
Radiation per particle
95% of SE at l=890 nm
Comes from this region

## Slide 11: There is agreement between the computed and the measured SE shape for quiescent runaways
Simulation
Experiment
Z
Qualitatively similar shapes for a wide range of and r0 values
Dependence on r0 stronger than
Optimal range of r0 ~0.25—0.35 m
Z
R
del-Castillo-Negrete et al, (2018)

## Slide 12: Dependence on pitch angle and energy fall-off
=1 exhibits good match but optimal match for shape reconstruction observed for > 1
=1 Fokker-Planck theoretical value
> 1 bigger fall-off of pitch angle PDF tail
r0= minor RE radius
Reconstruction error D
large D
small D
Fokker-Planck model for pitch angle PDF
However, >1 can significantly reduce the emission intensity
The emission intensity also depends on the energy range which in
the model used exhibits a sharp fall-off
Further studies needed to find the optimal parameters for shape
and intensity reconstruction

## Slide 13: Modeling of synchrotron emission of RE in disrupted plasmas (DRE)
Our study of SE of RE in disrupted plasmas
involves comparisons with visible and infrared
cameras as well as visible spectrometers.
Standard RE mid-plateau in DIII-D, IP=270 kA with ~1/3 Ar and ~2/3 D.
This provides a unique opportunity to to test
different ranges of the energy distribution.
Similar to the QRE case, our methodology is
to run KORC simulations using as initial conditions ensembles of RE sampled from the experimentally inferred energy distributions.
For the pitch angle distribution we use the standard Fokker-Planck model.
Layout of diagnostics used in disruptions experiments

## Slide 14: RE distribution function models and sampling box
For the pitch angle distribution we use
.
For the energy we use the reconstructed model in [Hollmann et al (2015)]
Visible
l=890 nm
Infrared
l=4 m m
Maximum energy in simulations for VIS = 50 MeV
Maximum energy in simulations for IR = 35 MeV
E=11 ECH Zeff = 5
nRE=4.5 x 1016 m-3

## Slide 15: Simulation of Visible (l=790 nm) Synchrotron Emission
Maximum RE energy in simulation=50 MeV
Brightness [1013 photons/cm2/s/ster/nm]
Z
Z
Measured
Simulation
45
35
25
15
5
R
R
l=790 nm
1013 photons/cm2/s/ster/nm
Visible spectrum in DIII-D
Wavelength [nm]
100
90
70
50
30
10
800
600
700
Measured
Simulated
900

## Slide 16: Simulation of Infrared (l=4 mm) Synchrotron Emission
Maximum RE energy in simulation=35 MeV
Measured
Simulation
Brightness (1013 photons/cm2/s/ster/nm)
R
Z
R
Measured
Simulation
400
300
200
100
Z
l=4 mm
Blind spot
1/10
1/10

## Slide 17: Conclusions
We have applied the Kinetic Orbit Runaway electron Code (KORC) to model synchrotron emission (SE) of RE in quiescent (QRE) and disrupted plasmas (DRE) in DIII-D.
KORC SE synthetic diagnostic incorporates the RE full-orbit, emission and camera geometry.
Orbit-induced (collisionless) pitch angle dispersion plays a key role.
For both, QRE and DRE, agreement has been found between measurements and simulations when using RE energy distributions that significantly depart from current Fokker-Planck models.
QRE with pitch angle distributions with faster fall-off rate than Fokker-Planck model also reproduce the radiation shape but underestimate the intensity.